Lab 3b. CONTINUITY EQUATION

Problem:  How long will it take for the water in the tank (below figure) to drop from ho to h?

- Ideal Gas Law

(1)

- Bernoulli’s Equation  (to be covered soon in the class)

Where P1 and P2 are absolute pressures

Assume that v1 ~ 0 (since v1At=v2Ah ( v1=v2(Ah/At) << v2), then  we have

Then                                                                                                            (2)

- Continuity Equation

Given a control volume as shown in the figure above, we have

With our case =0, thus

(3)

From Equations 1, 2, and 3, we have

(4)

WITHOUT THE LID ON then P=0,     and   Equation 4 can be rewritten as

We integrate the differential equation and get

WITH THE LID ON,

From Equation 4 we have

[5]

It is too difficult to integrate Equation 5.

In this case, we can determine when the water in the tank will stop running out of the hole

(using  hydrostatic law, since water is standing)

(from ideal gas law, since mass of air=constant and T=constant)

Thus, Equation 6 can be written as:

or

Given H=0.2m, and h0=0.15m

( h is very close to h0 !!!

m/s

m/s

sec

(this is time it takes for the water to stop running out of the hole)

# Text boxes

h0=0.15 m

h=0.1492 m