## Slide 1: CE 394K.2 Mass, Momentum, Energy
Begin with the Reynolds Transport Theorem
Momentum – Manning and Darcy eqns
Energy – conduction, convection, radiation
Energy Balance of the Earth
Atmospheric water
Reading: Applied Hydrology Sections 3.1 to 3.4 on Atmospheric Water and Precipitation

## Slide 2: Reynolds Transport Theorem
Total rate of change of B in the fluid system
Rate of change of B stored in the control volume
Net outflow of B across the control surface

## Slide 3: Continuity Equation
B = m; b = dB/dm = dm/dm = 1; dB/dt = 0 (conservation of mass)
r = constant for water
or
hence

## Slide 4: Continuous and Discrete time data
Continuous time representation
Sampled or Instantaneous data
(streamflow)
truthful for rate, volume is interpolated
Pulse or Interval data
(precipitation)
truthful for depth, rate is interpolated
Figure 2.3.1, p. 28 Applied Hydrology
Can we close a discrete-time water balance?
j-1
j
Dt

## Slide 5
Ij
Qj
DSj = Ij - Qj
Sj = Sj-1 + DSj
Continuity Equation, dS/dt = I – Q
applied in a discrete time interval [(j-1)Dt, jDt]
j-1
j
Dt

## Slide 7: Momentum
B = mv; b = dB/dm = dmv/dm = v; dB/dt = d(mv)/dt = SF (Newtons 2nd Law)
so
For steady flow
For uniform flow
In a steady, uniform flow

## Slide 8: Surface and Groundwater Flow Levels are related to Mean Sea Level
Earth surface
Ellipsoid
Sea surface
Geoid
Mean Sea Level is a surface of constant
gravitational potential called the Geoid

## Slide 9
http://www.csr.utexas.edu/ocean/mss.html

## Slide 10: GRACE Mission Gravity Recovery And Climate Experiment
http://www.csr.utexas.edu/grace/
Creating a new map of the earth’s gravity field every 30 days
http://www.csr.utexas.edu/grace/gallery/animations/measurement/measurement_qt.html
Water Mass of Earth

## Slide 11: Vertical Earth Datums
A vertical datum defines elevation, z
NGVD29 (National Geodetic Vertical Datum of 1929)
NAVD88 (North American Vertical Datum of 1988)
takes into account a map of gravity anomalies between the ellipsoid and the geoid

## Slide 12: Energy equation of fluid mechanics
Datum
z1
y1
bed
water
surface
energy
grade line
hf
z2
y2
L
How do we relate friction slope,
to the velocity of flow?

## Slide 13: Open channel flow Manning’s equation
Channel Roughness
Channel Geometry
Hydrologic Processes
(Open channel flow)
Physical environment
(Channel n, R)
Hydrologic conditions
(V, Sf)

## Slide 14: Subsurface flow Darcy’s equation
Hydraulic conductivity
Hydrologic Processes
(Porous medium flow)
Physical environment
(Medium K)
Hydrologic conditions
(q, Sf)
A
q
q

## Slide 15: Comparison of flow equations
Open Channel Flow
Porous medium flow
Why is there a different power of Sf?

## Slide 16: Energy
B = E = mv2/2 + mgz + Eu; b = dB/dm = v2/2 + gz + eu;
dE/dt = dH/dt – dW/dt (heat input – work output) First Law of Thermodynamics
Generally in hydrology, the heat or internal energy component
(Eu, dominates the mechanical energy components (mv2/2 + mgz)

## Slide 17: Heat energy
Energy
  Potential, Kinetic, Internal (Eu)
Internal energy
  Sensible heat – heat content that can be measured and is proportional to temperature
  Latent heat – “hidden” heat content that is related to phase changes

## Slide 18: Energy Units
In SI units, the basic unit of energy is Joule (J), where 1 J = 1 kg x 1 m/s2
Energy can also be measured in calories where 1 calorie = heat required to raise 1 gm of water by 1°C and 1 kilocalorie (C) = 1000 calories (1 calorie = 4.19 Joules)
We will use the SI system of units

## Slide 19: Energy fluxes and flows
Water Volume [L3] (acre-ft, m3)
Water flow [L3/T] (cfs or m3/s)
Water flux [L/T] (in/day, mm/day)
Energy amount [E] (Joules)
Energy “flow” in Watts [E/T] (1W = 1 J/s)
Energy flux [E/L2T] in Watts/m2
Energy flow of
1 Joule/sec
Area = 1 m2

## Slide 20: MegaJoules
When working with evaporation, its more convenient to use MegaJoules, MJ (J x 106)
So units are
  Energy amount (MJ)
  Energy flow (MJ/day, MJ/month)
  Energy flux (MJ/m2-day, MJ/m2-month)

## Slide 21: Internal Energy of Water
Heat Capacity (J/kg-K) Latent Heat (MJ/kg)
Ice 2220 0.33
Water 4190 2.5
Ice
Water
Water vapor
Water may evaporate at any temperature in range 0 – 100°C
Latent heat of vaporization consumes 7.6 times the latent heat of fusion (melting)
2.5/0.33 = 7.6

## Slide 22: Water Mass Fluxes and Flows
Water Volume, V [L3] (acre-ft, m3)
Water flow, Q [L3/T] (cfs or m3/s)
Water flux, q [L/T] (in/day, mm/day)
Water mass [m = rV] (Kg)
Water mass flow rate [m/T = rQ] (kg/s or kg/day)
Water mass flux [M/L2T = rq] in kg/m2-day
Water flux
Area = 1 m2

## Slide 23: Latent heat flux
Water flux
  Evaporation rate, E (mm/day)
Energy flux
  Latent heat flux (W/m2), Hl
Area = 1 m2
r = 1000 kg/m3
lv = 2.5 MJ/kg
28.94 W/m2 = 1 mm/day
Temp | Lv | Density | Conversion
0 | 2501000 | 999.9 | 28.94
10 | 2477300 | 999.7 | 28.66
20 | 2453600 | 998.2 | 28.35
30 | 2429900 | 995.7 | 28.00
40 | 2406200 | 992.2 | 27.63

## Slide 24: Radiation
Two basic laws
  Stefan-Boltzman Law
    R = emitted radiation (W/m2)
    e = emissivity (0-1)
    s = 5.67x10-8W/m2-K4
    T = absolute temperature (K)
  Wiens Law
    l = wavelength of emitted radiation (m)
Hot bodies (sun) emit short wave radiation
Cool bodies (earth) emit long wave radiation
All bodies emit radiation

## Slide 25: Net Radiation, Rn
Ri Incoming Radiation
Ro =aRi Reflected radiation
= albedo (0 – 1)
Rn Net Radiation
Re
Average value of Rn over the earth and
over the year is 105 W/m2

## Slide 26: Net Radiation, Rn
Rn Net Radiation
Average value of Rn over the earth and
over the year is 105 W/m2
G – Ground Heat Flux
LE – Evaporation
H – Sensible Heat

## Slide 27: Energy Balance of Earth
http://www.uwsp.edu/geo/faculty/ritter/geog101/textbook/energy/radiation_balance.html
6
4
100
70
51
21
26
38
6
20
15
Sensible heat flux 7
Latent heat flux 23
19

## Slide 28: Net Radiation
Mean annual net radiation over the earth and over the year is 105 W/m2
http://geography.uoregon.edu/envchange/clim_animations/flash/netrad.html

## Slide 29: Energy Balance in the San Marcos Basin from the NARR (July 2003)
Average fluxes over the day
310
72
415
495
3
61
112
Net Shortwave = 310 – 72 = 238; Net Longwave = 415 – 495 = - 80
Note the very large amount of longwave radiation exchanged between land and atmosphere

## Slide 30
Increasing carbon dioxide in the atmosphere (from about 300 ppm in preindustrial times)
We are burning fossil carbon (oil, coal) at 100,000 times the rate it
was laid down in geologic time

## Slide 31: Absorption of energy by CO2

## Slide 32: Heating of earth surface
Heating of earth surface is uneven
  Solar radiation strikes perpendicularly near the equator (270 W/m2)
  Solar radiation strikes at an oblique angle near the poles (90 W/m2)
Emitted radiation is more uniform than incoming radiation
Amount of energy transferred from equator to the poles is approximately 4 x 109 MW

## Slide 33: Hadley circulation
Warm air rises, cool air descends creating two huge convective cells.
Atmosphere (and oceans) serve to transmit heat energy from the equator to the poles

## Slide 34: Atmospheric circulation
Tropical Easterlies/Trades
Westerlies
Polar easterlies
Intertropical convergence zone (ITCZ)/Doldrums
Horse latitudes
Subpolar low
Polar high
Ferrel Cell
Polar Cell
Hadley cell
Ferrel Cell
Polar cell
Latitudes
Winds
Circulation cells

## Slide 35: Shifting in Intertropical Convergence Zone (ITCZ)
Owing to the tilt of the Earth's axis in orbit, the ITCZ shifts north and south.
Southward shift in January
Northward shift in July
Creates wet Summers (Monsoons) and dry winters, especially in India and SE Asia

## Slide 36: Structure of atmosphere

## Slide 37: Atmospheric water
Atmospheric water exists
  Mostly as gas or water vapor
  Liquid in rainfall and water droplets in clouds
  Solid in snowfall and in hail storms
Accounts for less than 1/100,000 part of total water, but plays a major role in the hydrologic cycle

## Slide 38: Water vapor
Suppose we have an elementary volume of atmosphere dV and
we want quantify how much water vapor it contains
Atmospheric gases:
Nitrogen – 78.1%
Oxygen – 20.9%
Other gases ~ 1%
http://www.bambooweb.com/articles/e/a/Earth's_atmosphere.html
dV
ma = mass of moist air
mv = mass of water vapor
Water vapor density
Air density

## Slide 39: Specific Humidity, qv
Specific humidity measures the mass of water vapor per unit mass of moist air
It is dimensionless

## Slide 40: Vapor pressure, e
Vapor pressure, e, is the pressure that water vapor exerts on a surface
Air pressure, p, is the total pressure that air makes on a surface
Ideal gas law relates pressure to absolute temperature T, Rv is the gas constant for water vapor
0.622 is ratio of mol. wt. of water vapor to avg mol. wt. of dry air (=18/28.9)

## Slide 41: Saturation vapor pressure, es
Saturation vapor pressure occurs when air is holding all the water vapor
that it can at a given air temperature
Vapor pressure is measured in Pascals (Pa), where 1 Pa = 1 N/m2
1 kPa = 1000 Pa

## Slide 42: Relative humidity, Rh
es
e
Relative humidity measures the percent
of the saturation water content of the air
that it currently holds (0 – 100%)

## Slide 43: Dewpoint Temperature, Td
e
Dewpoint temperature is the air temperature
at which the air would be saturated with its current
vapor content
T
Td

## Slide 44: Water vapor in an air column
We have three equations describing column:
  Hydrostatic air pressure, dp/dz = -rag
  Lapse rate of temperature, dT/dz = - a
  Ideal gas law, p = raRaT
Combine them and integrate over column to get pressure variation elevation
Column
Element, dz
1
2

## Slide 45: Precipitable Water
In an element dz, the mass of water vapor is dmp
Integrate over the whole atmospheric column to get precipitable water,mp
mp/A gives precipitable water per unit area in kg/m2
Column
Element, dz
1
2
Area = A

## Slide 46: Precipitable Water
http://geography.uoregon.edu/envchange/clim_animations/flash/pwat.html
25 mm precipitable water divides frontal from thunderstorm rainfall
Frontal rainfall in the winter
Thunderstorm rainfall in the summer