## Slide 1: CE 374K Hydrology
Review for First Exam
February 15, 2011

## Slide 2: Hydrology as a Science
“Hydrology is the science that treats the waters of the earth, their occurrence, circulation and distribution, their chemical and physical properties, and their reaction with their environment, including their relation to living things. The domain of hydrology embraces the full life history of water on the earth”
From “Opportunities in Hydrologic Science”, National Academies Press, 1992
http://www.nap.edu/catalog.php?record_id=1543
The “Blue Book”
Has this definition evolved in recent years? Are new issues important?

## Slide 3: Hydrology as a Profession
A profession is a “calling requiring specialized knowledge, which has as its prime purpose the rendering of a public service”
What hydrologists do:
  Water use – water withdrawal and instream uses
  Water Control – flood and drought mitigation
  Pollution Control – point and nonpoint sources
Have these functions changed in recent years? Are priorities different now?

## Slide 4: Global water balance (volumetric)
Land (148.7 km2)
(29% of earth area)
Ocean (361.3 km2)
(71% of earth area)
Precipitation
100
Evaporation
61
Surface Outflow
38
Subsurface Outflow
1
Precipitation
385
Evaporation
424
Atmospheric moisture flow 39
Units are in volume per year relative to precipitation on land (119,000 km3/yr) which is 100 units
What conclusions can we draw from these data?

## Slide 5: Global water balance
Land (148.7 km2)
(29% of earth area)
Ocean (361.3 km2)
(71% of earth area)
Precipitation
800 mm (31 in)
Evaporation
480 mm (19 in)
Outflow
320 mm (12 in)
Precipitation
1270 mm (50 in)
Evaporation
1400 mm (55 in)
Atmospheric moisture flow 316 mm (12 in)
What conclusions can we draw from these data?
Applied Hydrology, Table 1.1.2, p.5
(Values relative to land area)

## Slide 6: Global Water Resources
105,000 km3 or 0.0076% of total water

## Slide 7: Hydrologic System
Take a watershed and extrude it vertically into the atmosphere
and subsurface, Applied Hydrology, p.7- 8
A hydrologic system is “a structure or volume in space surrounded by a boundary, that accepts water and other inputs, operates on them internally, and produces them as outputs”

## Slide 8: Views of Motion
Eulerian view (for fluids – e is next to f in the alphabet!)
Lagrangian view (for solids)
Fluid flows through a control volume
Follow the motion of a solid body

## Slide 9: Reynolds Transport Theorem
A method for applying physical laws to fluid systems flowing through a control volume
B = Extensive property (quantity depends on amount of mass)
b = Intensive property (B per unit mass)
Total rate of
change of B in fluid system (single phase)
Rate of change of B stored within the Control Volume
Outflow of B across the Control Surface

## Slide 10: Mass, Momentum Energy
 | Mass | Momentum | Energy
B | m | mv | 
b = dB/dm | 1 | v | 
dB/dt | 0 |  | 
Physical Law | Conservation of mass | Newton’s Second Law of Motion | First Law of Thermodynamics

## Slide 11: Continuity Equation
B = m; b = dB/dm = dm/dm = 1; dB/dt = 0 (conservation of mass)
r = constant for water
or
hence

## Slide 12: Continuous and Discrete time data
Continuous time representation
Sampled or Instantaneous data
(streamflow)
truthful for rate, volume is interpolated
Pulse or Interval data
(precipitation)
truthful for depth, rate is interpolated
Figure 2.3.1, p. 28 Applied Hydrology
Can we close a discrete-time water balance?
http://waterservices.usgs.gov/nwis/iv?sites=08158000&period=P7D&parameterCd=00060

## Slide 13: Momentum
B = mv; b = dB/dm = dmv/dm = v; dB/dt = d(mv)/dt = SF (Newtons 2nd Law)
so
For steady flow
For uniform flow
In a steady, uniform flow

## Slide 14: Energy equation of fluid mechanics
Datum
z1
y1
bed
water
surface
energy
grade line
hf
z2
y2
L
How do we relate friction slope,
to the velocity of flow?

## Slide 15: Open channel flow Manning’s equation
Channel Roughness
Channel Geometry
Hydrologic Processes
(Open channel flow)
Physical environment
(Channel n, R)
Hydrologic conditions
(V, Sf)

## Slide 16: Subsurface flow Darcy’s equation
Hydraulic conductivity
Hydrologic Processes
(Porous medium flow)
Physical environment
(Medium K)
Hydrologic conditions
(q, Sf)
A
q
q

## Slide 17: Internal Energy of Water
Heat Capacity (J/kg-K) Latent Heat (MJ/kg)
Ice 2220 0.33
Water 4190 2.5
Ice
Water
Water vapor
Water may evaporate at any temperature in range 0 – 100°C
Latent heat of vaporization consumes 7.6 times the latent heat of fusion (melting)
2.5/0.33 = 7.6

## Slide 18: Radiation
Basic laws
  Stefan-Boltzman Law
    R = emitted radiation (W/m2)
    T = absolute temperature (K),
    and s = 5.67x10-8W/m2-K4
    with e = emissivity (0-1)
      Water, Ice, Snow (0.95-0.99)
      Sand (0.76)
“Gray bodies emit a proportion of the radiation of a black body
Valid for a Black body or “pure radiator”

## Slide 19: Net Radiation, Rn
Ri Incoming Radiation
Ro =aRi Reflected radiation
= albedo (0 – 1)
Rn Net Radiation
Re
Average value of Rn over the earth and
over the year is 105 W/m2

## Slide 20: Energy Balance of Earth
http://www.uwsp.edu/geo/faculty/ritter/geog101/textbook/energy/radiation_balance.html
6
4
100
70
51
21
26
38
6
20
15
Sensible heat flux 7
Latent heat flux 23
19

## Slide 21: Atmospheric circulation
Tropical Easterlies/Trades
Westerlies
Polar easterlies
Intertropical convergence zone (ITCZ)/Doldrums
Horse latitudes
Subpolar low
Polar high
Ferrel Cell
Polar Cell
Hadley cell
Ferrel Cell
Polar cell
Latitudes
Winds
Circulation cells

## Slide 22: Structure of atmosphere

## Slide 23: Specific Humidity, qv
Specific humidity measures the mass of water vapor per unit mass of moist air
It is dimensionless

## Slide 24: Vapor pressure, e
Vapor pressure, e, is the pressure that water vapor exerts on a surface
Air pressure, p, is the total pressure that air makes on a surface
Ideal gas law relates pressure to absolute temperature T, Rv is the gas constant for water vapor
0.622 is ratio of mol. wt. of water vapor to avg mol. wt. of dry air (=18/28.9)

## Slide 25: Saturation vapor pressure, es
Saturation vapor pressure occurs when air is holding all the water vapor
that it can at a given air temperature
Vapor pressure is measured in Pascals (Pa), where 1 Pa = 1 N/m2
1 kPa = 1000 Pa

## Slide 26: Relative humidity, Rh
es
e
Relative humidity measures the percent
of the saturation water content of the air
that it currently holds (0 – 100%)

## Slide 27: Frontal Lifting
Boundary between air masses with different properties is called a front
Cold front occurs when cold air advances towards warm air
Warm front occurs when warm air overrides cold air
Cold front (produces cumulus cloud)
Cold front (produces stratus cloud)

## Slide 28: Orographic lifting
Orographic uplift occurs when air is forced to rise because of the physical presence of elevated land.

## Slide 29: Convective lifting
Hot earth surface
Convective precipitation occurs when the air near the ground is heated by the earth’s warm surface. This warm air rises, cools and creates precipitation.

## Slide 30: Terminal Velocity
Terminal velocity: velocity at which the forces acting on the raindrop are in equilibrium.
If released from rest, the raindrop will accelerate until it reaches its terminal velocity
Raindrops are spherical up to a diameter of 1 mm
For tiny drops up to 0.1 mm diameter, the drag force is specified by Stokes law
Fd
Fd
Fb
Fg
D
V
At standard atmospheric pressure (101.3 kpa) and temperature (20oC), rw = 998 kg/m3 and ra = 1.20 kg/m3

## Slide 31: Incremental Rainfall
Rainfall Hyetograph

## Slide 32: Cumulative Rainfall
Rainfall Mass Curve

## Slide 33: Evaporation
  Evaporation – process by which liquid water becomes water vapor
  Transpiration – process by which liquid water passes from liquid to vapor through plant metabolism
  Evapotranspiration – evaporation through plants and trees, and directly from the soil and land surface
  Potential Evaporation – evaporation from an open water surface or from a well-watered grass surface

## Slide 34: ET -Eddy covariance method
Measurement of vertical transfer of water vapor driven by convective motion
Directly measure flux by sensing properties of eddies as they pass through a measurement level on an instantaneous basis
Statistical tool

## Slide 35: Energy Balance Method
Can directly measure these variables
How do you partition
H and E??

## Slide 36: Energy Balance Method
The maximum radiative evaporation rate Er =

## Slide 37: Aerodynamic Method
Often only available at 1 elevation
Simplifying
Net radiation
Evaporation
Air Flow

## Slide 38: Combined Method
Evaporation is calculated by
  Aerodynamic method
    Energy supply is not limiting
  Energy method
    Vapor transport is not limiting
Normally, both are limiting, so use a combination method
Priestley & Taylor

## Slide 39: Example
  Net Radiation = 200 W/m2,
  Air Temp = 25 degC,
Use Priestly-Taylor Method to find Evaporation rate for a water body
Priestly & Taylor

## Slide 40: Soil Texture Triangle
Source: USDA Soil
Survey Manual Chapter 3

## Slide 41: Soil Water Content
Soil Water Content

## Slide 42: Soil Water Flux, q
q = Q/A

## Slide 43: Soil Water Tension, y
Measures the suction head of the soil water
Like p/g in fluid mechanics but its always a suction (negative head)
Three key variables in soil water movement
  Flux, q
  Water content, q
  Tension, y
Total energy head = h
z=0
z1
z2
q12

## Slide 45: Richard’s Equation
Recall
  Darcy’s Law
  Total head
So Darcy becomes
Richard’s eqn is:
Soil water diffusivity

## Slide 46: Infiltration
Infiltration rate
  Rate at which water enters the soil at the surface (in/hr or cm/hr)
Cumulative infiltration
  Accumulated depth of water infiltrating during given time period

## Slide 47: Green – Ampt Infiltration
Wetted Zone
Wetting Front
Ponded Water
Ground Surface
Dry Soil

## Slide 48: Green – Ampt Infiltration (Cont.)
Apply finite difference to the derivative, between
  Ground surface
  Wetting front
Wetted Zone
Wetting Front
Ground Surface
Dry Soil

## Slide 49: Green – Ampt Infiltration (Cont.)
Wetted Zone
Wetting Front
Ground Surface
Dry Soil
Nonlinear equation, requiring iterative solution.

## Slide 51: Ponding time
Elapsed time between the time rainfall begins and the time water begins to pond on the soil surface (tp)

## Slide 52: Ponding Time
Up to the time of ponding, all rainfall has infiltrated (i = rainfall rate)
Potential
Infiltration
Actual Infiltration
Rainfall
Accumulated
Rainfall
Infiltration
Time
Time
Infiltration rate, f
Cumulative
Infiltration, F