## Slide 1
David Maidment, Harry Evans, David Arctur, Xing Zheng
University of Texas at Austin
Dean Djokic, ESRI; and Matt Ables, Kisters North America
Presentation for West Gulf River Forecast System, 3 March 2017
Acknowledgments: Yan Liu, University of Illinois; David Tarboton, Utah State University;
Texas Division of Emergency Management; City of Austin, National Weather Service, NCAR,
National Science Foundation, Colleagues and students at UT Austin.
Texas Flood Response System

## Slide 2: Information Flow During a Flood Emergency
Weather and
Flood Forecasting
Flood Impacts
Assessment of
Conditions
Emergency
Response
Communications
Cycle
TDEM Area coordinators
Disaster District coordinators
County emergency managers
State Operations Center
West Gulf River
Forecast Center

## Slide 3: Current Information Flow
Flood Impacts
Assessment of
Conditions
Emergency
Response
Communications
cycle
Rain maps
Hydrographs
at forecast points
TDEM Area coordinators
Disaster District coordinators
County emergency managers
State
Operations
Center
Verbal
Discussion

## Slide 4: Future Information Flow
Rain maps
Hydrographs
from National
Water Model
TDEM Area Coordinators
Disaster District Coordinators
County Emergency Management Coordinators
Reporting impacts:
Strategic Flood
Response Map
Real-Time
Inundation Map
Flood Impact
Assessment System
ESRI-Kisters Service
State Operations Center
Metrics
Assessment
of Conditions
Emergency
Response
Discussion

## Slide 5: Automated workflow for short term and medium term forecasts
Summary of Impacts for Disaster Districts
Inundation mapping and local impact assessment
National Water Model discharge forecasts
Conversion of discharge to depth using rating curves
ESRI

## Slide 6: Proposed Approach
Strategic Flood
Response Map
Assessment
of Conditions
Emergency
Response
Discussion
Real-Time
Inundation Map
Flood Impact
Assessment System
Three key elements:
Strategic Flood Response Map
Real-Time Inundation Map
Flood Impact Assessment System
Texas Flood Response System

## Slide 7: Real-Time Flood Inundation Mapping Onion Creek at Highway 183
http://water.weather.gov/ahps2/inundation/inundation_google.php?gage=atit2

## Slide 8: USGS Rating Curve at a Stream Gage
Measure
Water Level
Determine Discharge
Onion Creek at Highway 183

## Slide 9: Real Time Charts for Discharge and Depth for all of Texas
Discharge Forecast
Water Level Forecast
cfs
ft

## Slide 10: Method for Determining Flood Risk: Height Above Nearest Drainage (HAND)
HAND
Flood
Normal
Flooding occurs when Water Depth is greater than HAND
Address Point

## Slide 11: Texas Address Points
8.7 million points
Used for dispatching emergency
response vehicles in 911 systems

## Slide 12: Address points attributed with HAND using LIDAR Austin, Texas: A data rich community

## Slide 13: Detailed engineering modeling on creeks Austin, Texas: A data rich community

## Slide 14
Collaboration between Austin Fire Dept and Flood Early Warning System
Flood operational maps for 21 Austin creeks
Tested in six table top exercises over last 2 years
Now deployed in fire trucks in paper and pdf format

## Slide 15: Flood Operational Maps
Flood depth in houses
3ft
6” – 3 ft
< 6”
Potentially flooded
neighborhoods

## Slide 16: FEMA National Flood Hazard Layer in Texas (~ 120 counties)
Wharton County
Large areas of Texas
lack flood information

## Slide 17: Paper Map of Wharton County

## Slide 18: Strategic Flood Base Map for Wharton County
Prepared using standard Texas GIS data

## Slide 19: Potentially Impacted Features in Wharton County
(21)
(176)
(189)
(12)
(3)
(20,342)
Add Selected Features to the Base Map with the help of:
County Emergency Management Coordinator
TDEM Disaster District Coordinator

## Slide 20: Common Operating Picture for each County
Travis
Wharton
… Buildings
Identify neighborhoods at risk from flooding
using FEMA flood maps and interaction
with county Emergency Management Coordinator
Summarize information for
urban counties
Prepare information for
rural counties

## Slide 21: LIDAR Terrain Mapping
Wharton County
Source of Images: Joey Thomas, TNRIS
4 points per square meter
0.5 points per square meter

## Slide 22: River Toolbox – Integrity Checking and Database Adjustment
Minimum channel elevation – adjustment to get to bottom of the channel
Channel hydraulic properties – comparison with HEC-RAS geometries
Reach rating curves – comparison with USGS ratings
Inundation mapping extent – compare with FEMA flood maps
Checking water depth – Compare to USGS measurements in Kisters NWM viewer

## Slide 23: HEC-RAS Minimum Channel Elevation vs NED Waller Creek, Austin, Texas
DEM is 4.8 ft above HEC-RAS on average
DEM is 1.89 ft above HEC-RAS at this cross-section

## Slide 24: Error in Depth Predictions at USGS Gage Sites
Depth Error = Water Depth from Synthetic Rating Curve – Gage Water Depth (USGS)
Gage Water Depth (USGS) = Observed Gage Height – Gage Height of Zero Flow
Depth Error (ft)
(weekly average)
Average Depth Error = - 0.7 ft

## Slide 25: March 28 Exercise
Introduction
Exercise 1: Building a strategic flood response map
Exercise 2: Inundation mapping and impact assessment
Conclusion and recommendations
May 2015 flood in Blanco basin

## Slide 26: Questions for WGRFC
Do you want to be involved in the March 28 exercise?
Guidance on how to translate NWM forecasts to maps?
Participate in integrity checking the TFRS?
Suggestions and recommendations for us?