GIS in Water Resources	Exercise #3   Solution

Part 1.

1.1 Slope at grid cell A

Grid cell size 100m

| 52.5 a | 48.4 b | 48 c |
| --- | --- | --- |
| 64 d | 54.2 e | 50.2 f |
| 49 g | 44.7 h | 42 i |

(i) standard slope function

standard slope = 0.0532

atan(0.0489/(-0.0211)) = -66.6o  + 180 = aspect of 113.4o

Aspect = 113.4 o

(ii)  The 8 direction pour point model

(This in an Excel Object so you can click on it to see formula's)

Note that the steepest 8 direction pour point model slope in direction 4 is:

The neighboring cell in direction 2 is lower, but due to the diagonal distance being further the slope is less, so it is not the steepest direction.

D8 slope = 0.095

D8 flow direction = 4

(iii)  The D( algorithm

The diagram above indicates the interpretation of each of the angles on the trianglular facets.  Slope was evaluated for each triangular facet using

Angle was evaluated using

The slope on a triangular facet is valid only if it is in the range 0 to 45(.  The facets where this occurs have angles illustrated in red above.  Facets where the slope direction resides outside the 0 to 45( are illustrated in blue above.  When the angle is outside this range the slope down one of the D8 directions needs to be selected.  This may be either the diagonal or adjacent direction, depending which is the steepest in the downslope direction.  The largest slope from all 8 triangular facets and the corresponding direction is selected as the D( slope and angle.  The yellow highlight shows the slopes from which the largest is selected.  In this case it is the slope value of 0.099 associated with the facet 0-7-8 and angle 15.9( which corresponds to 285.9( = 4.989 radians counter clockwise from east (blue highlight).  The D( slope is therefore 0.099.

Comments

The standard slope function gives, in this case, a smaller slope than the other methods and a direction more to the east than the other methods, due to it using surrounding higher elevation grid cells.  This is reasonable if the surface is smooth, and is appropriate for calculations such as radiation exposure, but for calculating the direction that water will flow I think that only lower neighboring grid cells should be used.  The D8 and D( methods only use lower neighbors.  The D( method is preferable in my (biased) opinion because it does not limit flow to one of eight directions.

1.2.  Checking with ArcGIS.

b)  (i) Slope.  Be sure to use the percent option

The value at cell A of 5.32 % corresponds to the hand calculation of 0.0532.

Other values are obtained similarly from identifying values in the ArcMap output.

Table of ArcGIS computed quantities

| Cell | A | B |
| --- | --- | --- |
| Slope | 5.32% | 8.09% |
| Aspect | 113.4 | 144.1 |
| Flow Direction | 4 | 4 |
| Hydrologic Slope (Percentage drop) | 9.5% | 5.5% |
| D( Slope | 0.0988 | 0.055 |
| D( direction (radians) | 4.9893 | 4.712 |
| D( direction (degrees) | 285.9 | 270 |

These values corresponds with hand calculations

1.3  Model Builder model to do the above.

This tool is available on http://www.engineering.usu.edu/dtarb/giswr/2008/Ex3.tbx if you want to download and look at it.

Table of data ranges from model output using the file demo.asc

| Grid | Minimum | Maximum |
| --- | --- | --- |
| Aspect (-1 designates flat) | -1 | 360 |
| Slope | 0 | 56.09o (148.8%) |
| Flow Direction | 1 | 128 |
| Hydrologic Slope (percentage drop) | 0.067% | 146.67% |

Part 2.

1. Loading the Data

The number of columns and rows are 4800 and 2580 respectively,

cell size in the N-S directions in m = , where in rad and Re (Earth radius)

.

cell size in E-W direction must be adjusted for latitude.

cell size =  where, = longitude difference, use =29.82° (average of top and bottom latitudes) and = 0.0002778;

cell size E-W = 26.8 m

Spatial reference information for the San Marcos elevation dataset DEM ‘smdem_raw’ is;

2. Projecting the DEM

1305 columns, 823 rows. The minimum and maximum elevations in the San Marcos elevation dataset DEM ‘smdem_raw’ as well as the projected one ‘smdem’ are shown below. The difference in min and max is due to interpolation to a coarse grid.

3. Exploring the DEM

4. Contours, Hillshade and Slope

The layout above uses 100 m contours and the hillshade effect associated with the DEM to illustrate the San Marcos Topography.

5. Zonal Average Calculation

| HydroID | USGSID | Name | Elevation range (m) | Elevation mean (m) | Slope Mean % |
| --- | --- | --- | --- | --- | --- |
| 330 | 8172400 | Plum Ck at Lockhart, TX | 137.17 | 189.99 | 2.42 |
| 331 | 8171000 | Blanco Rv at Wimberley, TX | 371.76 | 418.74 | 5.81 |
| 332 | 8171300 | Blanco Rv nr Kyle, TX | 207.99 | 288.71 | 6.80 |
| 333 | 8170500 | San Marcos Rv at San Marcos, TX | 215.89 | 266.11 | 3.96 |
| 334 | 8172500 | Plum Ck nr Lockhart, TX | 78.42 | 150.23 | 1.92 |
| 335 | 8173000 | Plum Ck nr Luling, TX | 112.73 | 152.98 | 1.94 |
| 336 | 8172000 | San Marcos Rv at Luling, TX | 307.47 | 183.59 | 2.42 |
| 337 | 8173500 | San Marcos Rv at Ottine, TX | 115.67 | 131.47 | 2.36 |
| 338 |  | San Marcos Subbasin | 113.58 | 115.39 | 2.30 |

The subwatershed with highest mean elevation is Blanco above Wimberley (Note the point with the highest elevation is near the upper end of this subwatershed). The largest elevation range is found in the Blanco above Wimberley, too. The largest mean slope is noted in the Blanco above Kyle subwatershed.

6. Calculation of Area Average Precipitation using Thiessen Polygons

| HydroID | Name | Mean Precip (in) by Thiessen Polygons |
| --- | --- | --- |
| 330 | Plum Ck at Lockhart, TX | 36.37 |
| 331 | Blanco Rv at Wimberley, TX | 37.82 |
| 332 | Blanco Rv nr Kyle, TX | 40.48 |
| 333 | San Marcos Rv at San Marcos, TX | 40.48 |
| 334 | Plum Ck nr Lockhart, TX | 36.45 |
| 335 | Plum Ck nr Luling, TX | 36.56 |
| 336 | San Marcos Rv at Luling, TX | 37.59 |
| 337 | San Marcos Rv at Ottine, TX | 35.80 |
| 338 | San Marcos Subbasin | 34.49 |

The highest mean precipitation is found for the San Marcos River at San Marcos and Blanco River near Kyle watersheds.  These are identical, because they are both in the same polygon.

7. Estimate basin average mean annual precipitation using Spatial Interpolation/Surface fitting

| HydroID | Name | Mean Precip (in) by Tension Spline |
| --- | --- | --- |
| 330 | Plum Ck at Lockhart, TX | 36.22 |
| 331 | Blanco Rv at Wimberley, TX | 37.89 |
| 332 | Blanco Rv nr Kyle, TX | 39.79 |
| 333 | San Marcos Rv at San Marcos, TX | 39.66 |
| 334 | Plum Ck nr Lockhart, TX | 35.97 |
| 335 | Plum Ck nr Luling, TX | 36.74 |
| 336 | San Marcos Rv at Luling, TX | 37.99 |
| 337 | San Marcos Rv at Ottine, TX | 35.87 |
| 338 | San Marcos Subbasin | 34.52 |

Blanco Rv nr Kyle, TX has the highest mean precipitation estimated from Tension Spline Interpolation.

I also used Natural Neighbor Interpolation

| HydroID | Name | Mean Precip (in) by Natual Neighbor method |
| --- | --- | --- |
| 330 | Plum Ck at Lockhart, TX | 36.56 |
| 331 | Blanco Rv at Wimberley, TX | 37.58 |
| 332 | Blanco Rv nr Kyle, TX | 39.24 |
| 333 | San Marcos Rv at San Marcos, TX | 38.70 |
| 334 | Plum Ck nr Lockhart, TX | 36.21 |
| 335 | Plum Ck nr Luling, TX | 36.79 |
| 336 | San Marcos Rv at Luling, TX | 37.26 |
| 337 | San Marcos Rv at Ottine, TX | 36.18 |
| 338 | San Marcos Subbasin | 35.07 |

8.  Runoff Coefficients

The following map shows stream gages at the outlet of each subwatershed

This indicates the following subwatersheds which comprise each watershed

| Watershed | Subwatersheds |
| --- | --- |
| Plum Ck at Lockhart, TX | Plum Ck at Lockhart, TX |
| Blanco Rv at Wimberley, TX | Blanco Rv at Wimberley, TX |
| Blanco Rv nr Kyle, TX | Blanco Rv nr Kyle, TX Blanco Rv at Wimberley, TX |
| San Marcos Rv at San Marcos, TX | San Marcos Rv at San Marcos, TX |
| Plum Ck nr Lockhart, TX | Plum Ck nr Lockhart, TX Plum Ck at Lockhart, TX |
| Plum Ck nr Luling, TX | Plum Ck nr Luling, TX Plum Ck nr Lockhart, TX Plum Ck at Lockhart, TX |
| San Marcos Rv at Luling, TX | Blanco Rv nr Kyle, TX Blanco Rv at Wimberley, TX San Marcos Rv at San Marcos, TX San Marcos Rv at Luling, TX |
| San Marcos Rv at Ottine, TX | San Marcos Rv at Ottine, TX Blanco Rv nr Kyle, TX Blanco Rv at Wimberley, TX San Marcos Rv at San Marcos, TX San Marcos Rv at Luling, TX Plum Ck nr Luling, TX Plum Ck nr Lockhart, TX Plum Ck at Lockhart, TX |

Runoff ratio calculations are in the following spreadsheet (embedded object so you can see calculations in electronic version)

In the top table Precip volume is Mean precip * Area divided by 12 x 0.30482 to obtain volume in ft3.  In the bottom table Flow volume is obtained from flow in cfs by multiplying by 365.25*24*3600*3600.  The subwatersheds that comprise each watershed are identified and precip volume obtained by summing these.  Runoff ratio is then flow volume/precip volume.

The runoff ratio for the San Marcos river at San Marcos is anomalously high due to flow from springs that originates outside the watershed.  This anomalous high flow attenuates downstream.  Plum Creek at Lockhart is also in the vicinity of where the Edwards aquifer outcrops and has a slightly higher runoff ratio so likely gets some spring contributions too.  Over all the other watersheds, runoff ratio is pretty consistent between 0.11 and 0.15, which seems about right for this region.

# Text boxes

Two subwatersheds in the same polygon have identical estimated precipitation