## Slide 1: Yellowstone Fires and Their Hydrologic Effects
Patrick Sejkora
November 17, 2009
GIS in Water Resources

## Slide 2: Yellowstone National Park 1988 Fires
1988 driest summer on record
7 major fires burned June-September 1988
3,215 km2 (36% of park) burned
  485 km2 on August 20 alone!
Fires extinguished in September by rain/snow

## Slide 3: Objectives
Did fires augment surface water runoff regimes in Yellowstone?
Hypothesis: Evapotranspiration and infiltration rates decrease in burned areas1, increasing runoff
Evaluate using runoff ratio:
Is runoff ratio post-fires higher than pre-fires?
1. Robichaud 2000

## Slide 4: GIS DATA
Park outline and Digital Elevation Map (DEM)
NHD Flowlines and USGS Gage Sites
Burn Type Raster
Compare runoff ratios between heavily burned and unaffected (control) watersheds
  Before Fire
  After Fire
Firehole River
Boundary Creek

## Slide 5: Firehole River (burned/ experimental watershed)
Baseflow 7.37 m3/s
724 km2 watershed (obtained with ArcHydro Terrain Preprocessing)
288 km NHD flowline
Drainage Density of 0.40/km
4th order stream at gage
Chart: Flow (m3/sec)
| January | February | March | April | May | June | July | August | September | October | November | December
Mean flow | 7.4457 | 7.3778 | 7.6172 | 9.2331 | 13.7959 | 12.1406 | 8.2373 | 7.6046 | 7.5941 | 7.8449 | 7.7587 | 7.5449

## Slide 6: Boundary Creek (unburned/ control watershed)
Baseflow 1.94 m3/s
224 km2 watershed
151 km NHD flowline
Drainage Density of 0.68/km
3rd order stream at gage
Chart: Flow (m3/sec)
| January | February | March | April | May | June | July | August | September | October | November | December
Mean flow | 2.0363 | 1.9404 | 1.9805 | 3.5118 | 7.5865 | 6.4602 | 2.8803 | 2.3849 | 2.292 | 2.2659 | 2.2508 | 2.1502

## Slide 7
Chart: 
| Canopy burn | Mixed burn | Nonforested burn | Undifferentiated burn | Water | Unburned
 | 3521 | 3691 | 1052 | 899 | 17 | 80258
Chart: 
| Canopy burn | Mixed burn | Nonforested burn | Undifferentiated burn | Water | Unburned
 | 61659 | 41548 | 2192 | 2470 | 329 | 181555
Firehole River
Boundary Creek

## Slide 8: Precipitation Data
Find similar precipitation events before and after 1988 fires
Obtain data from National Climactic Data Center
Interpolate rainfall across park via Spline

## Slide 9: Pre-1988 Precipitation Event
Spline raster can be used to estimate rainfall across watersheds
  Zonal Statistics Tool in Spatial Analyst
July 10, 1987
July 11, 1987
September 18, 1989
0.6 cm
1.6 cm
1.6 cm
0.5 cm
1.7 cm
1.6 cm
Average Precipitation Across Watersheds

## Slide 10: Storm Event Flow Conditions
Chart: Discharge (m3/sec)
| 31962 | 31963 | 31964 | 31965 | 31966 | 31967 | 31968 | 31969 | 31970 | 31971 | 31972 | 31973 | 31974
Boundary Creek Flow | 1.9822 | 1.9539 | 1.9539 | 1.9539 | 1.9822 | 1.9822 | 2.1238 | 2.237 | 2.0671 | 2.0105 | 1.9822 | 1.9255 | 1.9255
Chart: Discharge (m3/sec)
| 32764 | 32765 | 32766 | 32767 | 32768 | 32769 | 32770 | 32771 | 32772
Boundary Creek Flow | 2.0105 | 2.0105 | 2.0105 | 2.0105 | 2.0671 | 2.322 | 2.0954 | 2.0388 | 2.0388
Boundary Creek
Pre-Fire
Post-Fire
Chart: Discharge (m3/s)
| 32764 | 32765 | 32766 | 32767 | 32768 | 32769 | 32770 | 32771 | 32772 | 32773
 | 7.2491 | 7.1925 | 7.1925 | 7.1642 | 7.3624 | 8.58 | 7.3907 | 7.2774 | 7.2208 | 7.1925
Chart: Discharge (m3/s)
| 31962 | 31963 | 31964 | 31965 | 31966 | 31967 | 31968 | 31969 | 31970 | 31971 | 31972 | 31973 | 31974
 | 7.2208 | 7.0792 | 6.9659 | 6.9943 | 7.0792 | 7.2774 | 7.6455 | 8.58 | 7.6739 | 7.3057 | 7.1925 | 7.1075 | 7.0509
Firehole River

## Slide 11: Runoff Ratios
Boundary Creek
Pre-Fire RR = 1.1%
Post Fire RR = 0.9%
Firehole River
Pre-Fire RR = 1.1%
Post Fire RR = 0.9%
Runoff Ratio Example Calculation (Boundary Creek 9/18/1989)
These Runoff Ratios aren’t very different!

## Slide 12: Conclusions
Runoff Ratios before and after fire are indistinguishable in burned watershed
An event’s runoff ratio same for both watershed
Suggests other factors besides landcover may influence runoff regimes
  Antecedent dry period, storm intensity, etc.?

## Slide 13: Future Work
Evaluate other storm events using same methodology
  NEXRAD precipitation data for recent events
Similar effects for snow melt?

## Slide 14: Questions?

## Slide 15
Firehole River
Boundary Creek
Chart: 
| Lodgepole Pine, post disturbance | Lodgepole Pine, climax | Nonforested | Lodgepole Pine, successional | Engelmann Spruce & Subalpine Fir, climax | Douglas Fir, climax | Pygmy Lodgepole Pine | Aspen | Water
 | 977 | 7636 | 12487 | 32732 | 1800 | 1354 | 32385 | 50 | 17
Chart: 
| Lodgepole Pine, climax | Lodgepole Pine, post disturbance | Nonforested | Lodgepole Pine, successional | Engelmann Spruce & Subalpine Fir, climax | Whitebark Pine, climax | Douglas Fir, climax | Pygmy Lodgepole Pine | Water
 | 71676 | 434 | 15772 | 191857 | 5942 | 142 | 94 | 3507 | 329

## Slide 16
Chart: 
| Lodgepole Pine, climax | Douglas Fir, post disturbance | Nonforested | Lodgepole Pine, post disturbance | Lodgepole Pine, successional | Engelmann Spruce & Subalpine Fir, climax | Whitebark Pine, climax | Pygmy Lodgepole Pine | Water
 | 58859 | 59 | 16134 | 110269 | 97414 | 3780 | 142 | 2793 | 303
Firehole River
Boundary Creek
Chart: 
| Lodgepole Pine, post disturbance | Lodgepole Pine, climax | Nonforested | Lodgepole Pine, successional | Engelmann Spruce & Subalpine Fir, climax | Douglas Fir, climax | Pygmy Lodgepole Pine | Aspen | Water
 | 977 | 7636 | 12487 | 32732 | 1800 | 1354 | 32385 | 50 | 17