## Slide 1: Revolution in Earth Measurement
Traditional Surveying uses benchmarks as reference points
Global Positioning uses fixed GPS receivers as reference points (Continuously Operating Reference System, CORS)
Some images and slides from Michael Dennis, National Geodetic Survey and Lewis Lapine, South Carolina Geodetic Survey

## Slide 2: Differential GPS
Differential GPS uses the time sequence of observed errors at fixed locations to adjust simultaneous measurements at mobile receivers
A location measurement accurate to 1 cm horizontally and 2cm vertically is now possible in 3 minutes with a mobile receiver
More accurate measurements if the instrument is left in place longer

## Slide 3
{Latitude (f), Longitude (l), Elevation (z)}
Survey Benchmark
This leads to adjustments in locations of the national network of survey benchmarks

## Slide 4: Adjustments of the NAD83 Datum
Slightly different (f, l) for benchmarks
Continuously Operating Reference System
Canadian Spatial Reference System
National Spatial Reference System
High Accuracy Reference Network

## Slide 5: THE GEOID AND TWO ELLIPSOIDS
GRS80-WGS84
(NAD83)
CLARKE 1866 (NAD27)
GEOID
Earth Mass
Center
Approximately
236 meters

## Slide 6: WGS 84 and NAD 83
International Terrestrial Reference Frame (ITRF) includes updates to WGS-84 (~ 2 cm)
North American Datum of 1983 (NAD 83) (Civilian Datum of US)
Earth Mass
Center
2.2 m (3-D)
dX,dY,dZ
GEOID
World Geodetic System of 1984 (WGS 84) is reference frame for Global Positioning Systems

## Slide 7
Slide: Lewis Lapine
http://www.ngs.noaa.gov/faq.shtml
High Accuracy Reference Network
Continuously Operating Reference System

## Slide 9
Adjustment using Triangulation of Reference Locations of Various Accuracies

## Slide 10: Tectonic Motions
From Sella et al., 2002
This has to take Tectonic Motions into account

## Slide 11: HORIZONTAL TECTONIC MOTIONS
Pacific Plate
North American Plate
Motion in cm/year
When is California not in North America …
…. when its on the Pacific Plate!

## Slide 12: What’s in a name?
NAD 83(2011) epoch 2010.00
  “2011” is datum tag  year adjustment complete
  “2010.00” is “epoch date” (January 1, 2010)
    Date associated with coordinates of control station
  Frame fixed to North American tectonic plate
    Includes California, Alaska, Puerto Rico, and US Virgin Islands
NAD 83(PA11) epoch 2010.00
  Frame fixed to Pacific tectonic plate (Hawaii and American Samoa)
NAD 83(MA11) epoch 2010.00
  Frame fixed to Mariana tectonic plate (Guam and CNMI)
That which we call a datum By any other name would smell as sweet…
The latest datum adjustments are referenced to location on a particular tectonic plate