## Slide 1: Waller Creek Flooding along 45th Street
Design Project
C E 365K- Hydraulic Engineering Design
Group 11: Scott Cameron, Matthew Strumeyer, Juhn-Yuan Su
Dr. D. R. Maidment

## Slide 2: Overview
Discussion on Location
Hydrodesign Process:
  Representation
  Process
  Evaluation
  Change
  Impact
  Decision
Recommendations

## Slide 3: Waller Creek
Flooding as a Fundamental Problem (Primary focus of Project)
  2/3 of Natural Disasters due to Flooding
  Examples of Flooding Disasters: Halloween Flood (10/31/2013), Sandy (2012); a lot of them over the world!
Water Quality another issue (will not be the primary focus of project)
  Buildings simply “getting rid of water as quickly as possible”
  NOT the primary emphasis for this project

## Slide 4: Area of Study
FOCUS OF PROJECT: 45th Street and Avenue F Area
  Apartment Complex
Apartment Complex

## Slide 5: Representation
How can the Study Area be Described?
Waller Creek through Avenue F and 45th Street
Approximately 22,500 feet from downstream of Waller Creek Reach
Apartment on one side of creek and road on another

## Slide 6: PROCESS
How does the Study Area Operate?
Waller Creek flows downstream along the route indicated
Flows through the park
Two Bridges:
  45th Street
  Avenue F
Bridges

## Slide 7: Evaluation
Is the Study Area Working Well?
NO!!!
The Apartment Complex Directly in the 25-year AND 100-year Floodplain
Karl McArthur: Flooding Problems between 41st and 47th Street
  Particularly Area on the right

## Slide 8: EVALUATION

## Slide 9
Cross Section to Modify

## Slide 11: CHANGE
How might the Study Area be Altered?
SOLUTIONS PROPOSED:
  Do Nothing
  Get Rid of the Apartment
  Elevate the Apartment
  Elevate BOTH the Apartment and the Road
USE HEC-RAS for the Simulation Models

## Slide 12: SOLUTION 1: DO NOTHING

## Slide 13: SOLUTION 1: DO NOTHING
Return Period | Q total | Min. Ch. El. | WS El. | Crit. W.S. | E.G. El. | EG slope | V | Flow A | T | Nf
years | cfs | ft | ft | ft | ft | ft/ft | ft/s | ft^2 | ft | 
2-year | 1240 | 602.46 | 609.57 | 607.76 | 610.34 | 0.01087 | 7.03 | 186.49 | 109.35 | 0.56
5-year | 1680 | 602.46 | 610.21 | 608.69 | 611.08 | 0.011313 | 7.78 | 278.66 | 188.62 | 0.58
10-year | 1990 | 602.46 | 610.35 | 610.29 | 611.43 | 0.01391 | 8.77 | 305.47 | 200.22 | 0.64
25-year | 2440 | 602.46 | 610.83 | 610.83 | 611.86 | 0.013036 | 8.96 | 411.96 | 240.75 | 0.63
50-year | 2800 | 602.46 | 611.13 | 611.13 | 612.13 | 0.012696 | 9.12 | 486.5 | 259.1 | 0.63
100-year | 3260 | 602.46 | 611.37 | 611.37 | 612.45 | 0.013606 | 9.67 | 549.15 | 272.32 | 0.66

## Slide 14: SOLUTION 2: Elevate the Apartment (Right OverBank)
Raise the Apartment by 2.5 Feet
In HEC-RAS, Raise the Right Overbank (ROB)
  Decreases the Flow Area

## Slide 15: Solution 2: Raise the Apartment
ROB | Q total | Min. Ch. El. | WS El. | Crit. W.S. | E.G. El. | EG slope | V | Flow A | T | Nf
2.5 ft up | cfs | ft | ft | ft | ft | ft/ft | ft/s | ft^2 | ft | 
2-year | 1240 | 602.46 | 609.57 | 607.76 | 610.34 | 0.010868 | 7.03 | 186.52 | 109.36 | 0.56
5-year | 1680 | 602.46 | 610.2 | 608.69 | 611.09 | 0.011539 | 7.85 | 263.31 | 135.57 | 0.58
10-year | 1990 | 602.46 | 610.33 | 610.14 | 611.46 | 0.014522 | 8.93 | 280.22 | 141.95 | 0.66
25-year | 2440 | 602.46 | 610.76 | 610.76 | 611.95 | 0.014774 | 9.46 | 347.47 | 165.9 | 0.67
50-year | 2800 | 602.46 | 611.09 | 611.09 | 612.27 | 0.014379 | 9.66 | 404.02 | 177.41 | 0.67
100-year | 3260 | 602.46 | 611.38 | 611.38 | 612.63 | 0.015005 | 10.16 | 456.41 | 185.55 | 0.69

## Slide 16: SOLUTION 2 Results
Pros
Lowered Top Width by 45 Feet for 5-year Return Period
Allows greater Flow Velocity THOUGH Smaller Flow Area
Cons
Requires People to Move Out and then Move Back In
Need a Machine to Literally Elevate the Apartment
Need Soil Fill to Add Below the Apartment

## Slide 17: Solution 3: Destroy the Obstruction
NO Change in Elevation of LOB or ROB
Water Surface Elevations still the same

## Slide 18: SOLUTION 3: Destroy the Obstruction
Destroy | Q total | Min. Ch. El. | WS El. | Crit. W.S. | E.G. El. | EG slope | V | Flow A | T | Nf
Apartment | cfs | ft | ft | ft | ft | ft/ft | ft/s | ft^2 | ft | 
2-year | 1240 | 602.46 | 609.57 | 607.76 | 610.33 | 0.010857 | 7.03 | 188.34 | 127.75 | 0.56
5-year | 1680 | 602.46 | 610.26 | 608.69 | 611.03 | 0.010376 | 7.49 | 326.45 | 261.92 | 0.56
10-year | 1990 | 602.46 | 610.43 | 610.39 | 611.34 | 0.012021 | 8.23 | 374.12 | 277.41 | 0.6
25-year | 2440 | 602.46 | 610.83 | 610.83 | 611.7 | 0.01169 | 8.48 | 490.42 | 310.3 | 0.6
50-year | 2800 | 602.46 | 611.05 | 611.03 | 611.94 | 0.011974 | 8.78 | 561.98 | 324.64 | 0.61
100-year | 3260 | 602.46 | 611.36 | 611.29 | 612.21 | 0.011636 | 8.93 | 663.81 | 341.84 | 0.61

## Slide 19: SOLUTION 3: Destroy the OBSTRUCTION
Pros
Flow Velocity has Decreased due to Larger Flow Area
Less Worries on People along Waller Creek at Avenue F getting Flooded
Cons
Top Width Increased Significantly
Where are all those people in the apartment going to go?
  MIGHT BE UT STUDENTS!!

## Slide 20: SOLUTION 4: Raise the Left and Right Overbanks
Raise Both Sides of the Channel by 2.5 feet
  Road
  Apartment Complex
Helps solve issue on Flooding along Apartment and Road

## Slide 21: Solution 4: Raise the left and right overbanks
Elevate LOB and ROB by 2.5 feet | Q total | Min. Ch. El. | WS El. | Crit. W.S. | E.G. El. | EG slope | V | Flow A | T | Nf
 | cfs | ft | ft | ft | ft | ft/ft | ft/s | ft^2 | ft | 
2-year | 1240 | 602.46 | 609.57 |  | 610.34 | 0.010909 | 7.04 | 179.09 | 42.77 | 0.56
5-year | 1680 | 602.46 | 610.09 |  | 611.22 | 0.014106 | 8.56 | 201.65 | 43.64 | 0.64
10-year | 1990 | 602.46 | 610.13 |  | 611.68 | 0.019369 | 10.07 | 203.13 | 43.7 | 0.76
25-year | 2440 | 602.46 | 610.06 | 610.03 | 612.47 | 0.030396 | 12.52 | 200.21 | 43.58 | 0.95
50-year | 2800 | 602.46 | 610.54 | 610.54 | 613.15 | 0.029632 | 13.08 | 221.53 | 44.39 | 0.95
100-year | 3260 | 602.46 | 611.18 | 611.18 | 613.98 | 0.028059 | 13.62 | 249.89 | 45.45 | 0.94

## Slide 22: SOLUTION 4: Raise the Left and Right Overbanks
Pros
Significantly decreased the Top Width
  All to Top Width in the 40s feet
Increased Flow Velocity though with Much Smaller Flow Area
Cons
Traffic Accidents due to Elevated Road???
  Means: Need to Raise 45th Street Upstream (cost-inefficient)
Soil Fill Needed
Cost- High; Need to Raise Apartment and Road

## Slide 23: Solution Choice
Conclude: Solution 2 (Elevate Apartment by 2.5 feet) is the most cost-effective solution
2.5 Feet- Neutral Selection for Elevation
  Water-Surface Level for 100-year Storm Still Below Apartment

## Slide 24: Photo of HeC-RAS model

## Slide 25: Progress
Auto-CAD Drawing of Waller Creek and Raised Apartment Elevation Needed!
Incorporation into ArcGIS with the Raised HEC-RAS Model
FOR MATT AND SCOTT: Please add any of the AutoCAD or GIS models with the solution if updated.

## Slide 26: QUESTIONS?
Thank you!