## Slide 1: Stormwater Best Management Practices
Michael Barrett, Ph.D., P.E.
University of Texas at Austin

## Slide 2: Cuyahoga River, Cleveland

## Slide 3: Dates to Remember
1948 Federal Water Pollution Control Act passed by Congress
1972 Clean Water Act prohibits any discharge of pollutants without NPDES permit - (fishable and swimmable)
1987 Clean Water Act amended to require permits for stormwater discharges
2003 NPDES Phase II permits required

## Slide 4: Clean Water Act
Requires NPDES permit for stormwater from cities, industry, construction sites
Requires assessment of beneficial uses and impairments of receiving waters
Impaired segments reported to EPA – 303(d) list.
Development of TMDL (total maximum daily load) for impaired segments

## Slide 5: Common Impairments
Constituent/Parameter | Number of Water Bodies Impaired
Bacteria | 418
Low Dissolved Oxygen Concentration | 130
PCBs | 104
Salinity | 102
Dioxins | 90
Mercury | 75

## Slide 7: Impervious Cover and Runoff

## Slide 8: Channel Degradation
Bear Creek
ShoalCreek
Fort Branch
Boggy Creek

## Slide 9: Constituents in Urban Runoff
Bacteria
Nutrients
Insecticides
Herbicides
Metals – zinc, copper, lead
Hydrocarbons – PAHs
Sediment

## Slide 10: Sources of Pollutants
Vehicles – Tires, Brake pads, Fluids, Tracking
Atmospheric Deposition
Fertilizers
Pesticides
Pets
Pavement abrasion
Channel Erosion

## Slide 11: Requirements for Stormwater Treatment
City of Austin – Required since 1981, mainly sand filters
TCEQ – Requires removal of 80% of sediment in stormwater for Edwards Aquifer
LCRA – Requires 70-75% removal of sediment, phosphorus, and oil & grease for Highland Lakes

## Slide 12: Treatment Difficulties
Runoff occurs on an irregular basis
Volume and rate of runoff from storms is highly variable
Quality of runoff varies from storm to storm
Concentrations of constituents of concern often very low

## Slide 13: “First Flush” of Pollutants
Stenstrom & Kayhanian, 2005

## Slide 14: Best Management Practice (BMP) Selection
End-of-pipe
  Fewer facilities to manage, inspect, and maintain
  Little volume control
  Little redundancy
Onsite
  Maintain pre-development hydrology
  Low Impact Development (LID) – “Green Infrastructure”
  Lower cost
  More facilities

## Slide 15
Loop 360 TxDOT Pond
1,000 ft
Courtesy Matt Hollon
Notes: Extreme example of end of pipe.

## Slide 16: Conventional Development

## Slide 17: LID Development
Disconnected Decentralized Distributed Multi-functional
Multiple Systems

## Slide 18: Pollutant Removal Mechanisms
Particle settling
Filtration
Biological uptake/degradation
Infiltration
Volatilization
Photodegradation
Oxidation

## Slide 19: Typical LID Practices
Bioretention/rain gardens
Porous Pavement
Vegetated swales and buffer strips
Green roofs

## Slide 20: Bioretention

## Slide 21: Bioretention

## Slide 23
10th & Rio Grande
Image courtesy Tom Franke

## Slide 24: Curbside Bioretention

## Slide 25: Setback Bioretention

## Slide 26
Sand Beach
Biofiltration Pond
March 2009
October 2011

## Slide 27: Types of Porous Pavement
Pervious Concrete
Porous Asphalt
Pavers

## Slide 28: Pervious Concrete
Generally has a lower strength
Water content is critical for proper installation
Requires specialized crew for installation
Each batch tends to have a different color/texture
Tends to ravel in high traffic areas

## Slide 29: Porous Asphalt
Created by omitting fine material from asphalt
Asphalt is considered flexible pavement, so low strength is not as much an issue.
Less expensive than concrete
No specialized training needed for installation

## Slide 30: Source of Raveling

## Slide 31: Porous Pavement only in Parking Stalls

## Slide 32: Pavers
Most expensive option
Decorative element
Easily removed and replaced if needed

## Slide 33: Permeable Pavers
If 2 inch thick porous overlays gives 90+% pollutant removal, why not permeable pavers?
Most research has focused on volume reduction
Very few studies have quantified the pollutant reduction

## Slide 35: Plan View

## Slide 36: Pavement Section

## Slide 37: Comparison of Effluent Quality
Constituent | Paver Underdrain | Sand Filter
TSS (mg/L) | 10.0 | 20.6
Total Phosphorus (mg/L) | 0.02 | 0.099
Total Nitrogen (mg/L) | 0.97 | 1.07
COD (mg/L) | 7.8 | 22
E. Coli (MPN/100mL) | 423 | 4,895
Total Lead (mg/L) | <1 | 5.7
Total Zinc (mg/L) | 5.6 | 22.9
Total Organic Carbon (mg/L) | 2.2 | 7.3

## Slide 38: Schematic of Swale and Strip

## Slide 42: Vegetated Filter Strips

## Slide 43: Falconhead West Development
Ozark Path Site
Swiss Alps Site
SH 71

## Slide 45: Green Roofs

## Slide 46: Summary
Substantial environmental impacts of urbanization
Objectives of BMPs are to reduce concentrations of pollutants and runoff volumes
Move towards LID practices from end-of-pipe
Stormwater treatment is an integral part of urban runoff management