## Slide 1: Open Channel Flow in Pipes CE 365K Hydraulic Engineering Design
Reading: “Stormwater Conveyance..” Sec 7.1, pp. 218-223

## Slide 2: “Modeling Stormwater Sewer Systems using High Resolution Data”
Austin, Texas Spring 2014
Hydraulic Engineering Design
Carlos Galdeano

## Slide 3: Introduction and Scope

## Slide 4: Introduction and Scope Introduction
More than 54% of the world population lives in urban areas, and this percentage is projected to increase rapidly in future years. This growth significantly affects the hydrological cycle, which translates into social and economic costs due to urban flooding

## Slide 5: Introduction and Scope Scope
The main scope is to develop a procedure to evaluate the current storm water infrastructure using Airborne LiDAR data. Airborne LiDAR data provides the elevation data necessary to characterize the elements involved in the storm water system.
The stormwater sewer system in northwest area of The University of Texas at Austin main campus is the region analyzed in this project.

## Slide 6: Methodology

## Slide 7: Methodology General Methodology
Airborne LiDAR Data
Create LAS Dataset
Point File Toolbox
LAS to Multipoint
Create a TIN
Inputs
ArcMap
StormCAD
Results
Ratio of Flow to the Total Capacity at pipeline
Invert Elevation
Create the Feature Classes of the stormwater sewer system
Digitize the stormwater sewer system’s elements
Import CAD Files to ArcMap
Characterize the elements of the system
CAD files of Stormwater Sewer Systems
Austin’s
IDF Table
StormCAD Catalog Conduit
Import characterized elements to StormCAD
Add Gutters
Define Headloss coefficient
Run Model

## Slide 8: Methodology TIN Methodology
Airborne LiDAR Data
Create LAS Dataset
Point File Toolbox
LAS to Multipoint
Create a TIN
Inputs
ArcMap

## Slide 9: Methodology TIN Methodology

## Slide 10: Methodology TIN Methodology
View of nodes and edges that form the TIN
View of face elevation with graduated color ramp of the TIN

## Slide 11: Methodology Characterizing elements in the stormwater sewer system
11
Airborne LiDAR Data
Create LAS Dataset
Point File Toolbox
LAS to Multipoint
Create a TIN
Inputs
ArcMap
StormCAD
Results
Ratio of Flow to the Total Capacity at pipeline
Invert Elevation
Create the Feature Classes of the stormwater sewer system
Digitize the stormwater sewer system’s elements
Import CAD Files to ArcMap
Characterize the elements of the system
CAD files of Stormwater Sewer Systems
Austin’s
IDF Table
StormCAD Catalog Conduit
Import characterized elements to StormCAD
Add Gutters
Define Headloss coefficient
Run Model

## Slide 12: Methodology Characterizing elements in the stormwater sewer system
Invert Elevation
Create the Feature Classes of the stormwater sewer system
Digitize the stormwater sewer system’s elements
Import CAD Files to ArcMap
Characterize the elements of the system
CAD files of Stormwater Sewer Systems
Inputs
ArcMap

## Slide 13: Methodology Characterizing elements in the stormwater sewer system
Elements’ characteristics of the Stormwater Sewer System
Point feature Classes | Data | Header | Manhole | Junction | Curb Inlet
 | Label | 1000000 | 1010001 | 1020001 | 1030001
 | Elevation (Ground) in ft. | 538.42 | 610.17 | 593.55 | 570.96
 | Elevation (Invert) in ft. | 530.64 | 599.32 | 580.12 | 555.87
Polyline feature Classes | Data | Pipelines
 | Label | 1040001
 | Diameter in inches | 24
 | Conduit Type (Label) | Catalog Conduit
 | Section Type (Label) | Circle
 | Section Size (Catalog Conduit) (Label) | 24 inch
 | Material | Concrete
Polygon feature Classes | Data | Catchments
 | Label | 1030001
 | Area (User Defined) in acres | 0.426193
 | Time of Concentration in min. | 5
 | Rational C | 0.602657

## Slide 14: Methodology Running Model in StormCAD
Airborne LiDAR Data
Create LAS Dataset
Point File Toolbox
LAS to Multipoint
Create a TIN
Ratio of Flow to the Total Capacity at pipeline
Invert Elevation
Create the Feature Classes of the stormwater sewer system
Digitize the stormwater sewer system’s elements
Import CAD Files to ArcMap
Characterize the elements of the system
CAD files of Stormwater Sewer Systems
Inputs
ArcMap
StormCAD
Results
Austin’s
IDF Table
StormCAD Catalog Conduit
Import characterized elements to StormCAD
Add Gutters
Define Headloss coefficient
Run Model

## Slide 15: Methodology Running Model in StormCAD
Austin’s
IDF Table
StormCAD Catalog Conduit
Import characterized elements to StormCAD
Add Gutters
Define Headloss coefficient
Run Model
Inputs
StormCAD
Inlets at the end of the line are defined by the standard method with a headloss coefficient of 1.25
Inlets in the middle of the line, manholes, and joints are defined by the HEC-22 Energy method with a flat HEC-22 benching method.
Add gutters for those inlets that are On Grade. Since they don’t capture all the water that flows over them, a gutter has to be drawn to connect the Inlet On Grade to the next Inlet. This will help to indicate where the water that was not captured will end.

## Slide 16: Methodology Generating Results
Airborne LiDAR Data
Create LAS Dataset
Point File Toolbox
LAS to Multipoint
Create a TIN
Inputs
ArcMap
StormCAD
Results
Results and Conclusions
Invert Elevation
Create the Feature Classes of the stormwater sewer system
Digitize the stormwater sewer system’s elements
Import CAD Files to ArcMap
Characterize the elements of the system
CAD files of Stormwater Sewer Systems
Austin’s
IDF Table
StormCAD Catalog Conduit
Import characterized elements to StormCAD
Add Gutters
Define Headloss coefficient
Run Model

## Slide 17: Results and Conclusions

## Slide 18: Results Ratio of Flow to the Total Capacity for each pipeline
Pipeline Label | Ratio of Flow to the Total Capacity (%) |  |  | 
 | 2-yr | 10-yr | 25-yr | 100-yr
1040008 | 0.40% | 0.60% | 0.80% | 1.20%
2040015 | 1.00% | 1.60% | 2.00% | 3.10%
1040011 | 2.20% | 3.60% | 4.50% | 6.00%
1040033 | 1.90% | 3.30% | 4.20% | 6.00%
1040018 | 2.40% | 3.90% | 4.90% | 6.80%
1040020 | 2.40% | 4.00% | 5.10% | 7.10%
1040006 | 2.70% | 4.60% | 5.70% | 7.80%
1040005 | 3.00% | 5.00% | 6.30% | 8.60%
1040014 | 4.80% | 6.60% | 7.50% | 8.90%
2040008 | 4.30% | 7.00% | 8.80% | 11.40%
1040036 | 4.30% | 7.10% | 8.80% | 11.50%
1040022 | 7.70% | 10.00% | 11.20% | 13.00%
2040009 | 5.10% | 8.50% | 10.60% | 13.70%
1040010 | 8.10% | 10.80% | 12.20% | 14.40%
1040032 | 5.50% | 9.20% | 11.40% | 14.70%
1040003 | 5.30% | 9.00% | 11.30% | 15.70%
1040028 | 8.10% | 12.20% | 14.30% | 17.50%
1040019 | 6.60% | 11.20% | 14.10% | 19.70%
2040003 | 8.50% | 14.70% | 17.80% | 22.60%
1040035 | 9.00% | 14.90% | 18.40% | 24.20%
2040010 | 12.60% | 17.80% | 20.40% | 24.40%
1040013 | 11.10% | 16.80% | 20.20% | 25.80%
1040004 | 12.80% | 18.40% | 21.30% | 26.80%
1040023 | 13.30% | 18.60% | 22.00% | 27.40%
1040031 | 10.70% | 16.90% | 21.40% | 28.70%
1040027 | 14.50% | 20.30% | 24.00% | 29.90%
Pipeline Label | Ratio of Flow to the Total Capacity (%) |  |  | 
 | 2-yr | 10-yr | 25-yr | 100-yr
1040009 | 16.10% | 22.40% | 25.80% | 31.40%
1040017 | 14.70% | 21.10% | 25.20% | 31.80%
1040021 | 14.70% | 21.50% | 25.90% | 33.10%
1040037 | 15.60% | 22.70% | 27.40% | 35.10%
2040014 | 11.90% | 21.20% | 26.70% | 36.30%
2040006 | 12.90% | 21.60% | 27.10% | 37.40%
1040024 | 18.30% | 25.60% | 30.30% | 37.70%
1040012 | 16.50% | 24.80% | 29.80% | 38.60%
1040007 | 20.30% | 28.50% | 33.00% | 40.60%
2040017 | 15.80% | 25.90% | 31.10% | 41.20%
2040004 | 24.00% | 33.30% | 37.90% | 45.20%
1040001 | 15.60% | 26.20% | 32.80% | 45.50%
2040012 | 20.60% | 31.70% | 37.00% | 47.40%
1040040 | 22.30% | 32.40% | 39.10% | 50.10%
2040013 | 17.80% | 29.40% | 36.80% | 50.50%
1040030 | 24.90% | 35.10% | 41.50% | 51.70%
1040029 | 25.00% | 35.30% | 41.70% | 51.80%
1040016 | 25.20% | 36.90% | 43.70% | 54.80%
2040007 | 19.00% | 31.80% | 39.90% | 55.30%
1040002 | 20.30% | 34.00% | 42.70% | 58.90%
2040005 | 27.80% | 42.50% | 49.80% | 61.10%
1040039 | 27.50% | 40.00% | 48.20% | 62.00%
1040038 | 28.70% | 41.70% | 50.20% | 64.40%
1040034 | 29.60% | 42.40% | 51.00% | 65.00%
2040011 | 33.80% | 52.20% | 61.40% | 80.10%
2040016 | 32.70% | 52.90% | 63.50% | 83.70%

## Slide 19: Results Location of Max Values
Max value 2-yr storm event = 33.80%
Pipeline at intersection of Dean Keaton and Speedway
Max value for:
10-yr storm event = 52.90%
25-yr storm event = 63.50%
100-yr storm event = 83.70%
Pipeline at intersection of Dean Keaton and footbridge

## Slide 20: Acknowledgments
CONACyT
Dr. David Maidment
Gonzalo, Denny, Amanda, and Georges
The EWRE faculty and students
Watershed Protection and Development Review Department of The City of Austin

## Slide 21: Questions?