## Slide 1: Hemphill Park Channel
Ethan Earl
Kiersten Holms
Mallory Stallings
Shelby Wiedrich
Notes: Ethan

## Slide 2
Study Area
Water Source
Problem Overview
Possible Solutions
Proposed Plan
Overview
Notes: Ethan

## Slide 3: Study Area
How should the study area be described?
Part of the Waller Creek Watershed
Located north of campus in Hemphill Park
Begins at 33rd street and runs until it spills into Waller Creek
Masonry channel
Focusing Specifically at 32nd St Bridge
Subject Site
Notes: Ethan

## Slide 4: Study Area (Cont’d)
Channel designed and Built in the 1930s
Notes: Ethan

## Slide 5: Water Sources
How does the study area operate?
Underground stormwater tunnels (main source)
Inlets from street drains
Sheet flow directly into the channel
Notes: Ethan

## Slide 6: Problem Overview Floodplain for Hemphill Park Channel courtesy of FEMA
Is the current study area working well?
Prone to flooding at 32nd St Bridge
  Channel narrowing after initial inlet
  Impervious channel bottom
Notes: Kiersten

## Slide 7: Problem Overview (Cont’d)
Erosion
  Very old channel
  parts of channel bottom missing
Aesthetics
  In a local neighborhood
  Channel looks dirty and eroded
Notes: Kiersten

## Slide 8: Current Flow Conditions
Discharge: 1709.6 cfs
33rd Street Bridge
HEC- RAS Model
Notes: Shelby
Put in modflow calculations and schematics of new channel and bridge at 33rd

## Slide 9
32nd Street Bridge
33rd Street Bridge
Notes: Kiersten

## Slide 10: Possible Solutions How might the study area be altered? What differences would the changes cause?
Notes: Mallory

## Slide 11: Alternative 1: Install Pervious Bottom
Change the Bottom of the Channel to Pervious Pavement
Pros:
  Increased flow through infiltration
  Helps recharge the water table
Cons:
  Soil underneath cannot infiltrate, Classified by class C and D hydrological groups:
    D: Houston Black soils and Urban land (HsD)
    C: Urban land, Austin, and Whitewright soils (UtD)
    C: Urban land (Ur)
Notes: Mallory

## Slide 12: Alternative 2: Modify Channel Geometry
Modify the Channel Geometry
Pros:
  Decreased velocity
  Helps reduce water overflow (flooding)
Cons:
  Widening of the channel would cut into the surrounding park area
Notes: Mallory

## Slide 13: Alternative 3: Install Detention Pond
Implement a detention pond upstream of 32nd Street bridge
Pros:
  Detains flow
  Increases Quality
Cons:
  Requires a large amount of space
  No way to completely verify where the runoff is coming from (because of complex pipe system shown before)
Notes: Mallory

## Slide 14: Proposed Solution How should the study area be changed?
Notes: Shelby

## Slide 15: Design of Modified Channel
Modify bridge at 32nd street
Change to a rectangular cross-section
Notes: Shelby
Enter a Schematic of the channel here, talk about how it reduces flooding

## Slide 16: Revised Flow Calculations
Discharge: 711.83 cfs
Discharge: 2654.17 cfs
32nd Street Bridge (current)
32nd Street Bridge (after)
This is acceptable as the new 32nd street bridge only needs to handle 1709.6 cfs, the discharge from 33rd street bridge
Notes: Shelby
Put in modflow calculations and schematics of new channel and bridge at 33rd

## Slide 17: New Bridge Schematic
New 32nd St Bridge Design
Notes: Shelby
Put in modflow calculations and schematics of new channel and bridge at 33rd

## Slide 18: Channel Modifications
Current channel holds correct amount of water but is highly eroded
Reline entire channel with smooth concrete
  increases Flow through channel
  Helps prevent future erosion
Schematic of Channel Relining between 33rd and 32nd St
Notes: INSERT PICTURE OF OUR SCHEMATIC OF CHANNEL RELIGNING

## Slide 19: Aesthetics of Design
Limestone Rocks along the edge of the channel
  Keep with Limestone theme in channel
  Helps keep water in channel
  Space 2” Apart to also allow water to flow in
Imitation Concrete
  Helps the channel look more natural, less like concrete
  Glaze with help with preservation
Limestone Bridge
  Will withstand erosion
  Aesthetically pleasing
Notes: Shelby

## Slide 20: Slope Amendments along Channel
Current slope: 0.012
New slope: 0.016
El: 576 ft
El: 572 ft
El: 570.5 ft
1.5 ft
Notes: Shelby
talk about hwat ever you did wit hthe slope!

## Slide 21: Questions?
Notes: Shelby