## Slide 1: Review Slides for Exam 1
CE 365K Spring 2015
Some class material was presented primarily on the board, and you should refer to your class notes for that material
The balance and emphasis in the Review Sheet is what you should consider definitive for the various topics covered in class so far.

## Slide 2: HydroDesign Process
How should the study area be described?
How does the study area operate?
Is the current study area working well?
How might the study area be altered?
What differences would the changes cause?
How should the study area be changed?
Representation
Process
Evaluation
Change
Impact
Decision
Structure your reports (oral and written) using this framework

## Slide 3: Evolution of Hydraulic Design
Stormwater runoff disposal
  Get the water off the site as quickly and efficiently possible
Stormwater detention
  Slow down the stormwater so that peak flow after development is not more than before
Water Quality Control
  Retain and filter water on site so that bacteria are reduced and water quality improves
Low Impact Development
  Dispersed onsite infiltration, filtration and retention schemes

## Slide 4: Bentley Computer Programs
Flow Master
  Design of pipes, gutters, inlets, ditches, open channels, weirs and orifices
Culvert Master
  Design and analyze culvert hydraulics
StormCAD
  Design and analyze storm sewer systems
PondPack
  Pre- and Post-developed watershed conditions
  Sizing ponds
  Outlet structure rating curves
Steady Flow
Unsteady Flow

## Slide 5: City of Austin Drainage Criteria Manual
https://www.municode.com/library/#!/tx/austin/codes/drainage_criteria_manual

## Slide 6: Rational Method
Source: Austin Drainage Criteria Manual, Chapter 2

## Slide 7
Source: Austin Drainage Criteria Manual, Chapter 2

## Slide 8: Intensity-Duration-Frequency Curves
Chart: Duration (Mins)
| 5 | 15 | 30 | 60 | 120 | 180 | 360 | 720 | 1440
2-yr | 5.76 | 3.92 | 2.64 | 1.72 | 1.08 | 0.773 | 0.445 | 0.255 | 0.143
5-yr | 7.39 | 5.04 | 3.42 | 2.28 | 1.45 | 1.04 | 0.593 | 0.339 | 0.208
25-yr | 10.1 | 7.04 | 4.72 | 3.28 | 2.1 | 1.52 | 0.857 | 0.492 | 0.318
100-yr | 12.5 | 9.16 | 6.08 | 4.37 | 2.83 | 2.04 | 1.14 | 0.663 | 0.424

## Slide 9: Gutter Flow
d
T
Sx
1
Q = flow in gutter (cfs)
Kc = coefficient (0.56 for US units, 0.376 for SI units
SL = longitudinal slope
T = spread (ft)
Sx = transverse slope
Ref: Haested p. 99

## Slide 10: Flow into a Curb Inlet
LT = required length to intercept all flow (ft)
Q = flow in gutter (cfs)
Kc = coefficient (0.60 for US units, 0.817 for SI units)
SL = longitudinal slope
Sx = transverse slope
Ref: Haested p. 103
E = efficiency (proportion of flow captured
L = actual length (ft) (for L < LT)
LT

## Slide 11: Weir Coefficients
Source: “Computer Applications in Hydraulic Engineering”, 8th Ed. Haested Methods, 2013

## Slide 12: Vena Contracta
http://en.wikipedia.org/wiki/Vena_contracta
A1
A2
Contraction = ~ 0.64

## Slide 13: Road Culvert

## Slide 14: Flow through a Circular Pipe
a
y
D

## Slide 15
Culvert Flow Control
Haested Methods Water Solutions “Computer Applications in Hydraulic Engineering, 8th Edition

## Slide 16: Example Problem: Solve for Size

## Slide 17: Example Problem: Solve for Headwater

## Slide 18: Example Problem: Solve for Discharge

## Slide 19: Stream Gaging, Onion Creek at Highway 183
For method see: http://water.usgs.gov/edu/measureflow.html

## Slide 20: ADCP
Acoustic Doppler Current Profiler

## Slide 21: ADCP Velocity Profile – Colorado River at La Grange

## Slide 22: What is GIS
A geographic information system (GIS) is a system designed to capture, store, manipulate, analyze, manage, and present all types of geographical data. -- Wikipedia
maps
data
tools
computers

## Slide 23: Vector data represent discrete features
map
data
polygons
lines
points

## Slide 24: Raster data form a grid of cells or pixels
map
data

## Slide 25
Data Model based on a collection of data themes

## Slide 26: Shape of the Earth
We think of the
earth as a sphere
It is actually a spheroid, slightly larger in radius at the equator than at the poles

## Slide 27: Representations of the Earth
Earth surface
Ellipsoid
Sea surface
Geoid
Mean Sea Level is a surface of constant
gravitational potential called the Geoid

## Slide 28: Definition of Latitude, f
(1) Take a point S on the surface of the ellipsoid and define there the tangent plane, mn
(2) Define the line pq through S and normal to the
tangent plane
(3) Angle pqr which this line makes with the equatorial
plane is the latitude f, of point S
O
f
S
m
n
q
p
r

## Slide 29: Cutting Plane of a Meridian
P
Meridian
Equator
plane
Prime Meridian

## Slide 30: Definition of Longitude, l
0°E, W
90°W
(-90 °)
180°E, W
90°E
(+90 °)
-120°
-30°
-60°
-150°
30°
-60°
120°
150°
l
l = the angle between a cutting plane on the prime meridian
and the cutting plane on the meridian through the point, P
P

## Slide 31: Geoid and Ellipsoid
Ocean
Geoid
Earth surface
Ellipsoid
Gravity Anomaly
Gravity anomaly is the elevation difference between
a standard shape of the earth (ellipsoid) and a surface
of constant gravitational potential (geoid)

## Slide 32: Definition of Elevation
Elevation Z
•
P
z = zp
z = 0
Mean Sea level = Geoid
Land Surface
Elevation is measured from the Geoid

## Slide 33
3D Buildings for Campus and Central Austin
Stormwater drainage infrastructure in the Waller Creek watershed
Data for Digital Campus
Digital Campus and Waller Creek Drainage Infrastructure

## Slide 34: Drainage Patterns at UT-Austin

## Slide 35: ECJ and Waller Creek

## Slide 36: TIN of a portion of Dean Keaton St

## Slide 37: Vehicle-based LIDAR collection at UT-Austin
Mandli Communications

## Slide 38: Dean Keaton St
CrossSection 56
Location

## Slide 39: Road CrossSections from LIDAR
Airborne LIDAR (ft)
(City of Austin data)
Vehicle LIDAR (vertical in meters, horizontal in ft)
Location 5-6 is shown
in previous slides
Its clear that the vehicle-based
LIDAR gives a better definition
of the road Cross-Section

## Slide 40: Stormwater Best Management Practices
Michael Barrett, Ph.D., P.E.
University of Texas at Austin

## Slide 42: Impervious Cover and Runoff

## Slide 43: Conventional Development

## Slide 44: LID Development
Disconnected Decentralized Distributed Multi-functional
Multiple Systems

## Slide 45: Bioretention

## Slide 46: Porous Asphalt and Concrete
Porous Mix
Conventional Mix

## Slide 47: Splash and Spray
Conventional Asphalt
PFC

## Slide 48: Water Quality at TX1
Constituent | Conventional Asphalt | PFC | Reduction % | p-value
TSS | 118 | 8.8 | 92 | 0.016
Total P | 0.13 | 0.07 | 48 | 0.047
Total Copper | 27 | 13 | 50 | 0.010
D. Copper | 6 | 10 | -77 | 0.045
Total Lead | 13 | 1 | 91 | 0.025
Total Zinc | 167 | 29 | 83 | 0.002
Dissolved Zinc | 47 | 22 | 53 | 0.139

## Slide 49: Porous Pavement only in Parking Stalls

## Slide 50: Schematic of Swale and Strip

## Slide 52: Vegetated Filter Strips

## Slide 53: Austin Filter Bed

## Slide 54: Central Park Wet Pond (TX)