## Slide 1: Hydrograph Computation
CE 365K Hydraulic Engineering Design
Spring 2015

## Slide 2: Depth-Duration-Frequency Table

## Slide 3
Source: SCS TR-55 Manual, 1986

## Slide 4
Source: SCS TR-55 Manual, 1986

## Slide 6: Hydrologic Analysis
Change in storage w.r.t. time = inflow - outflow
In the case of a linear reservoir, S = kQ
Transfer function for a linear system (S = kQ).

## Slide 7: Proportionality and superposition
Linear system (k is constant in S = kQ)
  Proportionality
    If I1  Q1 then C*I2  C*Q2
  Superposition
    If I1  Q1 and I2  Q2, then I1 +I2 Q1 + Q2

## Slide 8: Impulse response function
Impulse input: an input applied instantaneously (spike) at time t and zero everywhere else
An unit impulse at t produces as unit impulse response function u(t-t)
Principle of proportionality and superposition

## Slide 9: Unit Hydrograph Theory
Direct runoff hydrograph resulting from a unit depth of excess rainfall occurring uniformly on a watershed at a constant rate for a specified duration.
Unit pulse response function of a linear hydrologic system
Can be used to derive runoff from any excess rainfall on the watershed.

## Slide 10: Unit hydrograph assumptions
Assumptions
  Excess rainfall has constant intensity during duration
  Excess rainfall is uniformly distributed on watershed
  Base time of runoff is constant
  Ordinates of unit hydrograph are proportional to total runoff (linearity)
  Unit hydrograph represents all characteristics of watershed (lumped parameter) and is time invariant (stationarity)

## Slide 11
Application of convolution to the output from a linear system

## Slide 12: Need for synthetic UH
UH is applicable only for gauged watershed and for the point on the stream where data are measured
For other locations on the stream in the same watershed or for nearby (ungauged) watersheds, synthetic procedures are used.

## Slide 13: SCS dimensionless hydrograph
Synthetic UH in which the discharge is expressed by the ratio of q to qp and time by the ratio of t to Tp
If peak discharge and lag time are known, UH can be estimated.
Tc: time of concentration
C = 2.08 (483.4 in English system)
A: drainage area in km2 (mi2)
tp = lag time in HEC-HMS

## Slide 14: Example
Construct a 10-min SCS UH. A = 3.0 km2 and Tc = 1.25 h
Multiply y-axis of SCS hydrograph by qp and x-axis by Tp to get the required UH, or construct a triangular UH
q
t
0.833 h
2.22 h
7.49 m3/s.cm

## Slide 15: Watersheds upstream of Dam 6

## Slide 16: Subbasin BUT_060

## Slide 17: Flow along the longest path
Sheet Flow
Shallow Flow
Channel Flow
Sum travel times over each segment

## Slide 18: Modeling Runoff from BUT_060
How much runoff?
How quickly does it move?
How to characterize this subbasin?

## Slide 19: Results for Run “10”
24 hour design storm of 10” total precipitation in 10 min increments