## Slide 1: National Flood Interoperability Experiment
David R. Maidment

## Slide 2
David R. Maidment
Center for Research in Water Resources
University of Texas at Austin
UT Austin Flood Symposium, Austin, Texas, 11 February 2016
Acknowledgements: UT Austin Colleagues and Students, National Weather Service,
City of Austin, ESRI, Kisters, Microsoft Research
This research is supported in part by NSF EarthCube grant 1343785
National Flood Interoperability Experiment

## Slide 3: The Opportunity
New National Water Center established on the Tuscaloosa campus of University of Alabama by the National Weather Service and federal agency partners
Has a mission to assess hydrology in a new way at the continental scale for the United States

## Slide 4: NWS River Forecast Centers (RFCs)
  Prepare river and flood forecasts using models based on average basin characteristics
  Provide forecast guidance to Weather Forecast Offices (WFOs)
  Issue daily stage and streamflow forecasts, rainfall and drought data and information, and flash flood guidance
  Work with water managers and other Federal Agencies
4
6600 sub-basins in continental US
Notes: RFC Summary

## Slide 5
FY15 Centralized Water Forecasting
Centralized Data Archive – all RFC data
Modeling Evaluation Service
  RFC and NWC modeling and forecasts
Modeling Testbed – new NWC capabilities
Centralized Water Forecasting Demonstration
National Water Center
Notes: TRANSITION INTO METHODS
FY15 PROJECT HAS FOUR CORE COMPONENTS
RFC archive
Model evaluation service
Modeling testbed
Centralized modeling demonstration

## Slide 6: Transformative Research (NSF)
Transformative research involves ideas, discoveries, or tools that radically change our understanding of an important existing scientific or engineering concept or educational practice or leads to the creation of a new paradigm or field of science, engineering, or education. Such research challenges current understanding or provides pathways to new frontiers.
http://www.nsf.gov/about/transformative_research/definition.jsp
How to move from evolutionary change
to transformative change?

## Slide 7: National Flood Interoperability Experiment (NFIE) (Sept 2014 to August 2015)
Partnership between NWS and the academic community (Interagency Agreement between NSF and NOAA)
Included a Summer Institute for 44 graduate students from 19 Universities at the National Water Center, June 1 to July 17, 2015

## Slide 8: Goal of the Experiment
Close the gap between National Flood Forecasting and Local Emergency Response
Demonstrate forecasting of flood impacts at “stream and street level”
National
Local
Weather and Hydrology
National Weather Service and federal agencies
National Water Center
River Flooding and Emergency Response
Local, State and Regional Agencies
Citizens

## Slide 9: NHDPlus Version 2.1
National Elevation Dataset
National Hydrography Dataset
National Land Cover Dataset
Watershed Boundary Dataset
NHDPlus
Foundation for a Geospatial Hydrologic Framework for the United States
2.7 million reach catchments in US
average area 3 km2
reach length 2 km
Uniquely labelled

## Slide 10: Flood Information for Fritz Hughes Park Rd
National Hydrography Dataset Plus
catchment for Bear Creek
(area = 5.71 km2)
Low water crossing at
3400 Fritz Hughes Park Rd

## Slide 11
500,000 processors operating in parallel
Stampede
1.2 million gallon cooling tank

## Slide 12: WRF-Hydro Forecasting Model
Runoff
Streamflow
RAPID flow routing (for continental US)
Probabilistic flood forecasts
Weather model and forecasts (HRRR)
Land-Atmosphere Model (NOAH-MP)
Precipitation
Weather
Catchment-level forecasts
Computed for 2.7 million stream reaches of the continental US in 10 minutes
at Texas Advanced Computing Center

## Slide 13
RAPID River Routing Model
River Application for Parallel ComputatIon of Discharge
Flow
Legend
Dam
Junction
Catchment
Computational Unit for Rivers
Forcing: Runoff and reservoir releases
http://rapid-hub.org/
NHDPlus Catchment

## Slide 14
Grid to
catchment
NHDPlus
to RAPID
Forcing
WRF-Hydro
HRRR
ECMWF
NFIE-Hydro – Flood Forecasting Models
TACC

## Slide 15: Probability of Flooding on Shoal Ck, Austin, Tx
Ensemble of 50 flood forecasts
ECMWF-RAPID flow forecasts
Deterministic flood maps
Probabilistic flood maps
HEC-RAS model
Rating curves library

## Slide 16: Progression of Memorial Day Flood on Shoal Creek

## Slide 17: Flow Continuum Model – a national stream network, atmosphere to oceans, coast to coast
130 Catchments and Flowlines
uniquely labelled
Two basins and one forecast point
becomes
Current: 6600 basins and 3600 forecast points
NFIE: 2.7 million stream reaches and catchments
A national flow network
Blanco River at Wimberley
Basin ~ 400 Sq Mile
Reach Catchment ~ 1 Sq Mile
Watershed Hydrology – basins and outlet points
Continental Hydrology – network flow continuum

## Slide 18: Linear Referencing on Flowlines
Lat.
Long.
Measure
Bridge and Stream Gage at RR 12 is at Measure 70.246
on Flowline 1630223
Measure is the % distance upstream from most downstream point on line
Using measures, the flow can be estimated at any point along the line

## Slide 19: Next Step: National Water Model
Short-Range
‘Flood Prediction’
Long Range
‘Water Resources’
Analysis & Assimilation
Hourly
3-Hourly
~Daily (x16)
- 3 hrs
Cycling Frequency
WRF-Hydro Configurations – June 2016
0-2 days
0-30 days
Forecast Duration
1km/250m/NHDPlus Reach
1km/250m/NHDPlus Reach
1 km/catchment /NHDPlus Reach
Spatial Discretization & Routing
MRMS blend/ HRRR-NAM bkgnd.
Downscaled HRRR /RAP/NAM blend
Downscaled & bias-corrected CFS
Meteorological Forcing
Medium Range
‘Flow Prediction’
Daily
0-10 days
1km/250m/NHDPlus Reach
Short-range + Downscaled GFS

## Slide 20
Multi-Year Strategic
Science and Services Plan
Total Water Prediction and National Water Center
FY 15-20
FY 16-21
FY 17-22
FY 18-23
FY 19-24
Centralized Water Forecasting
Flash Flood and Urban Hydrology
Coastal Total Water Level
Dry Side: Drought and Post-Fire
Water Quality
National Water Model (NWM) operational May 2016
  Water forecasts for 2.7 million stream reaches in U.S.
  100 million people get a terrestrial water forecast for first time
  National Water Center (NWC) begins providing daily situational awareness and guidance to NWS field offices
Enhance NWM with nested hyper- resolution zoom capability and urban hydrologic processes
  Heightened focus on regions of interests (e.g. follow storms)
  Street level flood inundation forecasts for selected urban demonstration areas
  NWC increases guidance to NWS field offices to improve consistency and services for flash floods
Core Capability
Key Enhancement
Major Integration
Couple NWM with marine models to predict combined storm surge, tide, and riverine effects
  More complete picture of coastal storm impacts
  Water prediction information linked to geospatial risk and vulnerability
  New service delivery model implemented – increased stakeholder engagement and integrated information
  NWC operations center opens and provides national decision support services and situational awareness
Couple NWM with groundwater and transport models to predict low flows, drought and fire impacts
  Add NWM processes that affect subsurface water movement and storage during dry conditions
  Add NWM ability to track constituents (e.g. sediment, contaminants, nutrients) through stream network
  New decision support services for water shortage situations and waterborne transport
  NWC operations center expands to include drought and post-fire decision support services
Key Enhancement
Major Integration
Integrate enhanced NWM with key water quality data sets, models and tools to begin water quality prediction
  Incorporate water quality data from federal and State partners into NWM
  Link NWM output to NOAA ecological forecasting operations
  New decision support services for predicting water quality issues such as Harmful Algal Blooms
  New decision support services for emergencies such as chemical spills
  NWC operations center expands to include water quality decision support services

## Slide 21: Improvements in Flood Response Planning
Federal
State
Local
Citizen
GIS database and flood discharge forecasts
for 2.67 million stream reaches in
continental US from National Water Center
Conversion to water level forecasts and
inundation maps for 102,000 reaches in Texas
using 10m terrain data. Address points for flood
emergency response planning in each reach
Flood impact on transportation system
Flood response planning for stream reaches
and critical infrastructure. Inundation mapping
using LIDAR terrain data, if available.
Flood response portal for citizens (ATXFlood)
Automated flood warnings from cell-phone
towers to phones in flood risk zones

## Slide 22: Situational Awareness For Everyone (SAFE)
Flood SAFE Viewer: http://arcg.is/1LPOHnE
Source: Jared Allen, NWS Austin-San Antonio Weather Forecast Office

## Slide 23: NWS Flood Inundation Maps for the US (130 in total)
33 maps in Texas (one quarter of total)

## Slide 24: Real-Time Flood Inundation Mapping (USGS/NWS)
http://water.weather.gov/ahps2/inundation/inundation_google.php?gage=atit2

## Slide 25: Reach Hydraulic Parameters
Comid | H | A | R | P | T | V | Ab | As
5781175 | 3 |  |  |  |  |  |  | 
5781175 | 4 |  |  |  |  |  |  | 
Wetted Bed Area
L
As
Ab
V
T
P
A
h
Surface Area
Volume
Depth
T
P
Cross Section Area
Wetted Perimeter
Top Width
R
Hydraulic Radius

## Slide 26: Flood Inundation Mapping
Catchments and Flowlines
Digital Elevation Model
Height Above Nearest
Drainage (HAND) (relative elevation of land
surface cell above cell in
stream to which it flows)
Inundation map (Depth to stream < 15 ft)

## Slide 27: Reach Catchment 5781289
Eanes Creek, Rollingwood, Texas
Drainage area = 3.13 mi2
Reach Length = 4.3 miles

## Slide 28: Discharge Computation
Hydraulic Radius, R
n = 0.035 Manning roughness of channel
So = 0.0163 Bed slope
Crossection Area, A
Flood Depth, h (ft)
Flood Discharge, Q (cfs)

## Slide 29: Rating Curve for Eanes Creek
Chart: Rating Curve for Eanes Creek, ComID = 5781289
| 0 | 607.56406134719509 | 2490.8796015163871 | 5785.1592347077531 | 10565.65567829302 | 16808.943658196447 | 24277.138771673799
Stage Height, h (ft) | 0 | 2.0669 | 3.937 | 5.807 | 7.6443 | 9.4159 | 10.9907
Forecast Discharge, Q, from National Water Model
Flood Depth, h (ft)

## Slide 30: SPRNT Model – flow and water depth on large networks
Very Large Scale Integrated (VLSI) design of computer chips – solve 100 million equations each night to check on effects of design changes on electricity flow in chip
Dynamic wave routing
Compute water flow by analogy with electricity flow in chips
Open source code in Github

## Slide 31: Rating the Landscape using SPRNT
Total 540 flowlines in Travis County.
Catchment Area: 2942.76 km2
Rainfall increased in uniform
increments of 1 mm/hr
Flow reaches equilibrium
in Travis County in 200 hours
Time
Rainfall
Mannings “n” = 0.05

## Slide 32: Rating Curves for Stream Gages in Travis County
USGS Rating
SPRNT

## Slide 34: Community Flood Response Map Book
Source: Tomas Rodriguez, City of Austin

## Slide 35: Flood Emergency Response Mapping
Table Top Exercise
Pre-planning Flood Maps
Detailed information about flood area
Used “on a blue sunny day”
Review what the flood could do
and how to respond
Operation Flood Map
Incident/Area Command
  Flood info at an area command level
  Laminated for recording situational awareness
  Able to log where units are assigned
Strategic
  Overview map of entire area
  Used at Emergency Operations Center
  Used to keep track of several area commands, groups of units
More information about this at Thursday Morning Flood Symposium

## Slide 36: Strategic Overview Map
One area of risk

## Slide 37: Incident/Area Command Map
Onion Creek at Pleasant Valley/William Cannon

## Slide 38: Pre-Planning Flood Map
Actions, Indicators, Road Closures and Depth

## Slide 39: Connecting with Local Decision Makers
Work with the first response community to define flood strategy for stream reaches
https://www.youtube.com/watch?v=ympaR6YUxiA&feature=youtube