## Slide 1: Hydraulic Routing in Rivers
Reading: Applied Hydrology Sections 9.1, 9.2, 9.3, 9.7, 10.1, 10.2
Reference: HEC-RAS Hydraulic Reference Manual, Version 4.1, Chapters 1 and 2
  Reading: HEC-RAS Manual pp. 2-1 to 2-12
http://www.hec.usace.army.mil/software/hec-ras/documents/HEC-RAS_4.1_Reference_Manual.pdf

## Slide 2: Flood Inundation

## Slide 3: Floodplain Delineation
Notes: The channel and floodplain are both integral parts of the natural conveyance of a stream. The floodplain carries flow in excess of the channel capacity. The greater the discharge, the greater the extent of inundation. …. Because of its devastating nature, flooding poses serious hazards to human populations in many parts of the world. “The Flood Disaster Protection Act of 1973” required the identification of all floodplain areas in the United States and the establishments of flood-risk zones within those areas.

## Slide 4: Steady Flow Solution

## Slide 5
Right Overbank
Left Overbank
Channel centerline
and banklines
Cross-section
One-Dimensional Flow Computations

## Slide 6: Flow Conveyance, K
Left Overbank
Right Overbank
Channel

## Slide 7: Reach Lengths
(1)
(2)
Lob
Rob
Lch
Floodplain
Floodplain
Left to Right looking downstream

## Slide 8: Energy Head Loss

## Slide 9: Velocity Coefficient, 

## Slide 10: Solving Steady Flow Equations
All conditions at (1) are known, Q is known
Select h2
compute Y2, V2, K2, Sf, he
Using energy equation (A), compute h2
Compare new h2 with the value assumed in Step 2, and repeat until convergence occurs
h2
(2)
(1)
h1
Q is known throughout reach
(A)

## Slide 11: Flow Computations
Reach 2
Reach 3
Reach 1
Start at the downstream end (for subcritical flow)
Treat each reach separately
Compute h upstream, one cross-section at a time
Use computed h values to delineate the floodplain

## Slide 12: Floodplain Delineation
Notes: Ideally should have Two D Models…... A floodplain delineation process determines inundation extent by comparing water levels with ground surface elevations. We start with a DTM or topomap. > Water levels are computed based on cross-sections. During normal condition, flow remains within the main channel, but > during flood, water spill over the bank. In these cases it’s important to extent cross-section over the floodplain. > We then bring back water levels on the topomap. > Extent water levels until hit contour of higher elevations. > Finally delineate floodplain following the contours. The accuracy largely depends on water levels and in turns on the cross-section used for computation.

## Slide 13: Unsteady Flow Routing in Open Channels
Flow is one-dimensional
Hydrostatic pressure prevails and vertical accelerations are negligible
Streamline curvature is small.
Bottom slope of the channel is small.
Manning’s equation is used to describe resistance effects
The fluid is incompressible

## Slide 14: Continuity Equation
Q = inflow to the control volume
q = lateral inflow
Elevation View
Plan View
Rate of change of flow with distance
Outflow from the C.V.
Change in mass
Reynolds transport theorem

## Slide 15: Momentum Equation
From Newton’s 2nd Law:
Net force = time rate of change of momentum
Sum of forces on the C.V.
Momentum stored within the C.V
Momentum flow across the C. S.

## Slide 16: Forces acting on the C.V.
Elevation View
Plan View
Fg = Gravity force due to weight of water in the C.V.
Ff = friction force due to shear stress along the bottom and sides of the C.V.
Fe = contraction/expansion force due to abrupt changes in the channel cross-section
Fw = wind shear force due to frictional resistance of wind at the water surface
Fp = unbalanced pressure forces due to hydrostatic forces on the left and right hand side of the C.V. and pressure force exerted by banks

## Slide 17: Momentum Equation
Sum of forces on the C.V.
Momentum stored within the C.V
Momentum flow across the C. S.

## Slide 18: Momentum Equation(2)
Local acceleration term
Convective acceleration term
Pressure force term
Gravity force term
Friction force term
Kinematic Wave
Diffusion Wave
Dynamic Wave

## Slide 19: Momentum Equation (3)
Steady, uniform flow
Steady, non-uniform flow
Unsteady, non-uniform flow

## Slide 20: Solving St. Venant equations
Analytical
  Solved by integrating partial differential equations
  Applicable to only a few special simple cases of kinematic waves
Numerical
  Finite difference approximation
  Calculations are performed on a grid placed over the (x,t) plane
  Flow and water surface elevation are obtained for incremental time and distances along the channel
x-t plane for finite differences calculations

## Slide 21: Applications of different forms of momentum equation
Kinematic wave: when gravity forces and friction forces balance each other (steep slope channels with no back water effects)
Diffusion wave: when pressure forces are important in addition to gravity and frictional forces
Dynamic wave: when both inertial and pressure forces are important and backwater effects are not negligible (mild slope channels with downstream control, backwater effects)

## Slide 22: Kinematic Wave
Kinematic wave celerity, ck is the speed of movement of the mass of a flood wave downstream
  Approximately, ck = 5v/3 where v = water velocity

## Slide 23: Muskingum-Cunge Method
A variant of the Muskingum method that has a more physical hydraulic basis
This is what Dean Djokic has used in the Brushy Creek HEC-HMS models
, where Δx = reach length or an increment of this length
, where B = surface width, S0 is the bed slope

## Slide 24: Dynamic Wave Routing
Flow in natural channels is unsteady, non-uniform with junctions, tributaries, variable cross-sections, variable resistances, variable depths, etc etc.

## Slide 25
∆x
∆x
∆t
h0, Q0, t0
h1, Q1, t0
h2, Q2, t0
h0, Q0, t1
h1, Q1, t1
h2, Q2, t2
∆x
∆x
∆t
i, j
i-1, j
i+1, j
i-1, j+1
i-1, j+1
i+1, j+1
x-t plane
Cross-sectional view in x-t plane