## Slide 1: Hydrologic Routing
Reading: Applied Hydrology Sections 8.1, 8.2, 8.4

## Slide 2: Flow Routing
Procedure to determine the flow hydrograph at a point on a watershed from a known hydrograph upstream
As the hydrograph travels, it
  attenuates
  gets delayed
Q
t
Q
t
Q
t
Q
t

## Slide 3: Why route flows?
Account for changes in flow hydrograph as a flood wave passes downstream
This helps in
  Accounting for storages
  Studying the attenuation of flood peaks
Q
t

## Slide 4: Watershed – Drainage area of a point on a stream
Connecting rainfall input with streamflow output
Rainfall
Streamflow

## Slide 5: Flood Control Dams
Dam 13A
Flow with a Horizontal Water Surface

## Slide 6: Floodplain Zones
1% chance
< 0.2% chance
Main zone of water flow
Flow with a Sloping Water Surface

## Slide 7: Types of flow routing
Lumped/hydrologic
  Flow is calculated as a function of time alone at a particular location
  Governed by continuity equation and flow/storage relationship
Distributed/hydraulic
  Flow is calculated as a function of space and time throughout the system
  Governed by continuity and momentum equations

## Slide 8: Hydrologic Routing
Upstream hydrograph
Downstream hydrograph
Input, output, and storage are related by continuity equation:
Discharge
Inflow
Discharge
Outflow
Transfer
Function
Q and S are unknown
Storage can be expressed as a function of I(t) or Q(t) or both
For a linear reservoir, S=kQ

## Slide 9: Lumped flow routing
Three types
Level pool method (Modified Puls)
  Storage is nonlinear function of Q
Muskingum method
  Storage is linear function of I and Q
Series of reservoir models
  Storage is linear function of Q and its time derivatives

## Slide 10: S and Q relationships

## Slide 11: Level pool routing
Procedure for calculating outflow hydrograph Q(t) from a reservoir with horizontal water surface, given its inflow hydrograph I(t) and storage-outflow relationship

## Slide 12: Level pool methodology
Discharge
Time
Storage
Time
Inflow
Outflow
Unknown
Known
Need a function relating
Storage-outflow function

## Slide 13: Level pool methodology
Given
  Inflow hydrograph
  Q and H relationship
Steps
  Develop Q versus Q+ 2S/Dt relationship using Q/H relationship
  Compute Q+ 2S/Dt using
  Use the relationship developed in step 1 to get Q

## Slide 14: Ex. 8.2.1
Given I(t)
Given Q/H
Area of the reservoir = 1 acre, and outlet diameter = 5ft

## Slide 15: Ex. 8.2.1 Step 1
Develop Q versus Q+ 2S/Dt relationship using Q/H relationship

## Slide 16: Step 2
Compute Q+ 2S/Dt using
At time interval =1 (j=1), I1 = 0, and therefore Q1 = 0 as the reservoir is empty
Write the continuity equation for the first time step, which can be used to compute Q2

## Slide 17: Step 3
Use the relationship between 2S/Dt + Q versus Q to compute Q
Use the Table/graph created in Step 1 to compute Q
What is the value of Q if 2S/Dt + Q = 60 ?
So Q2 is 2.4 cfs
Repeat steps 2 and 3 for j=2, 3, 4… to compute Q3, Q4, Q5…..

## Slide 18: Ex. 8.2.1 results

## Slide 19: Ex. 8.2.1 results
Inflow
Outflow
Peak outflow intersects with the receding limb of the inflow hydrograph
Outflow hydrograph

## Slide 20: Q/H relationships
http://www.wsi.nrcs.usda.gov/products/W2Q/H&H/Tools_Models/Sites.html
Program for Routing Flow through an NRCS Reservoir

## Slide 21: Hydrologic river routing (Muskingum Method)
Wedge storage in reach
Advancing
Flood
Wave
I > Q
Receding
Flood
Wave
Q > I
K = travel time of peak through the reach
X = weight on inflow versus outflow (0 ≤ X ≤ 0.5)
X = 0  Reservoir, storage depends on outflow, no wedge
X = 0.0 - 0.3  Natural stream

## Slide 22: Muskingum Method (Cont.)
Recall:
Combine:
If I(t), K and X are known, Q(t) can be calculated using above equations

## Slide 23: Muskingum - Example
Given:
  Inflow hydrograph
  K = 2.3 hr, X = 0.15, Dt = 1 hour, Initial Q = 85 cfs
Find:
  Outflow hydrograph using Muskingum routing method

## Slide 24: Muskingum – Example (Cont.)
C1 = 0.0631, C2 = 0.3442, C3 = 0.5927

## Slide 25: HEC-HMS Model of Brushy Creek
Dam 7
Walsh Dr

## Slide 26: Watershed W1820

## Slide 27: Junction J329
W1820
R580
J329
W1820
J329

## Slide 28: Reach R580