## Slide 1: CE 374K Hydrology
Review for First Exam
February 21, 2012

## Slide 2: Hydrology as a Science
“Hydrology is the science that treats the waters of the earth, their occurrence, circulation and distribution, their chemical and physical properties, and their reaction with their environment, including their relation to living things. The domain of hydrology embraces the full life history of water on the earth”
From “Opportunities in Hydrologic Science”, National Academies Press, 1992
http://www.nap.edu/catalog.php?record_id=1543
The “Blue Book”
Has this definition evolved in recent years? Are new issues important?

## Slide 3: Hydrology as a Profession
A profession is a “calling requiring specialized knowledge, which has as its prime purpose the rendering of a public service”
What hydrologists do:
  Water use – water withdrawal and instream uses
  Water Control – flood and drought mitigation
  Pollution Control – point and nonpoint sources
Have these functions changed in recent years? Are priorities different now?

## Slide 4: Global water balance (volumetric)
Land (148.7 km2)
(29% of earth area)
Ocean (361.3 km2)
(71% of earth area)
Precipitation
100
Evaporation
61
Surface Outflow
38
Subsurface Outflow
1
Precipitation
385
Evaporation
424
Atmospheric moisture flow 39
Units are in volume per year relative to precipitation on land (119,000 km3/yr) which is 100 units
What conclusions can we draw from these data?

## Slide 5: Global water balance
Land (148.7 km2)
(29% of earth area)
Ocean (361.3 km2)
(71% of earth area)
Precipitation
800 mm (31 in)
Evaporation
480 mm (19 in)
Outflow
320 mm (12 in)
Precipitation
1270 mm (50 in)
Evaporation
1400 mm (55 in)
Atmospheric moisture flow 316 mm (12 in)
What conclusions can we draw from these data?
Applied Hydrology, Table 1.1.2, p.5
(Values relative to land area)

## Slide 6: Capital Area Counties

## Slide 7: Floodplains in Williamson County
Area of County = 1135 mile2
Area of floodplain = 147 mile2
13% of county in floodplain

## Slide 8: Floodplain Zones
1% chance
< 0.2% chance
Main zone of water flow
Flow with a Sloping Water Surface

## Slide 9: Flood Control Dams
Dam 13A
Flow with a Horizontal Water Surface

## Slide 10: Watershed – Drainage area of a point on a stream
Connecting rainfall input with streamflow output
Rainfall
Streamflow

## Slide 11: Hydrologic System
Take a watershed and extrude it vertically into the atmosphere
and subsurface, Applied Hydrology, p.7- 8
A hydrologic system is “a structure or volume in space surrounded by a boundary, that accepts water and other inputs, operates on them internally, and produces them as outputs”

## Slide 12: Reynolds Transport Theorem
A method for applying physical laws to fluid systems flowing through a control volume
B = Extensive property (quantity depends on amount of mass)
b = Intensive property (B per unit mass)
Total rate of
change of B in fluid system (single phase)
Rate of change of B stored within the Control Volume
Outflow of B across the Control Surface

## Slide 13: Mass, Momentum Energy
 | Mass | Momentum | Energy
B | m | mv | 
b = dB/dm | 1 | v | 
dB/dt | 0 |  | 
Physical Law | Conservation of mass | Newton’s Second Law of Motion | First Law of Thermodynamics

## Slide 14: Continuity Equation
B = m; b = dB/dm = dm/dm = 1; dB/dt = 0 (conservation of mass)
r = constant for water
or
hence

## Slide 15: Continuous and Discrete time data
Continuous time representation
Sampled or Instantaneous data
(streamflow)
truthful for rate, volume is interpolated
Pulse or Interval data
(precipitation)
truthful for depth, rate is interpolated
Figure 2.3.1, p. 28 Applied Hydrology
Can we close a discrete-time water balance?
j-1
j
Dt

## Slide 16
Ij
Qj
DSj = Ij - Qj
Sj = Sj-1 + DSj
Continuity Equation, dS/dt = I – Q
applied in a discrete time interval [(j-1)Dt, jDt]
j-1
j
Dt

## Slide 17: Momentum
B = mv; b = dB/dm = dmv/dm = v; dB/dt = d(mv)/dt = SF (Newtons 2nd Law)
so
For steady flow
For uniform flow
In a steady, uniform flow

## Slide 18: Energy equation of fluid mechanics
Datum
z1
y1
bed
water
surface
energy
grade line
hf
z2
y2
L
How do we relate friction slope,
to the velocity of flow?

## Slide 19: Open channel flow Manning’s equation
Channel Roughness
Channel Geometry
Hydrologic Processes
(Open channel flow)
Physical environment
(Channel n, R)
Hydrologic conditions
(V, Sf)

## Slide 20: Subsurface flow Darcy’s equation
Hydraulic conductivity
Hydrologic Processes
(Porous medium flow)
Physical environment
(Medium K)
Hydrologic conditions
(q, Sf)
A
q
q

## Slide 21: Internal Energy of Water
Heat Capacity (J/kg-K) Latent Heat (MJ/kg)
Ice 2220 0.33
Water 4190 2.5
Ice
Water
Water vapor
Water may evaporate at any temperature in range 0 – 100°C
Latent heat of vaporization consumes 7.6 times the latent heat of fusion (melting)
2.5/0.33 = 7.6

## Slide 22: Radiation
Basic laws
  Stefan-Boltzman Law
    R = emitted radiation (W/m2)
    T = absolute temperature (K),
    and s = 5.67x10-8W/m2-K4
    with e = emissivity (0-1)
      Water, Ice, Snow (0.95-0.99)
      Sand (0.76)
“Gray bodies emit a proportion of the radiation of a black body
Valid for a Black body or “pure radiator”

## Slide 23: Net Radiation, Rn
Ri Incoming Radiation
Ro =aRi Reflected radiation
= albedo (0 – 1)
Rn Net Radiation
Re
Average value of Rn over the earth and
over the year is 105 W/m2

## Slide 24: Latent heat flux
Water flux
  Evaporation rate, E (mm/day)
Energy flux
  Latent heat flux (W/m2), Hl
Area = 1 m2
r = 1000 kg/m3
lv = 2.5 MJ/kg
28.94 W/m2 = 1 mm/day
Temp | Lv | Density | Conversion
0 | 2501000 | 999.9 | 28.94
10 | 2477300 | 999.7 | 28.66
20 | 2453600 | 998.2 | 28.35
30 | 2429900 | 995.7 | 28.00
40 | 2406200 | 992.2 | 27.63

## Slide 25: Energy Balance of Earth
http://www.uwsp.edu/geo/faculty/ritter/geog101/textbook/energy/radiation_balance.html
6
4
100
70
51
21
26
38
6
20
15
Sensible heat flux 7
Latent heat flux 23
19

## Slide 26: Atmospheric circulation
Tropical Easterlies/Trades
Westerlies
Polar easterlies
Intertropical convergence zone (ITCZ)/Doldrums
Horse latitudes
Subpolar low
Polar high
Ferrel Cell
Polar Cell
Hadley cell
Ferrel Cell
Polar cell
Latitudes
Winds
Circulation cells

## Slide 27: Structure of atmosphere

## Slide 28: Specific Humidity, qv
Specific humidity measures the mass of water vapor per unit mass of moist air
It is dimensionless

## Slide 29: Vapor pressure, e
Vapor pressure, e, is the pressure that water vapor exerts on a surface
Air pressure, p, is the total pressure that air makes on a surface
Ideal gas law relates pressure to absolute temperature T, Rv is the gas constant for water vapor
0.622 is ratio of mol. wt. of water vapor to avg mol. wt. of dry air (=18/28.9)

## Slide 30: Saturation vapor pressure, es
Saturation vapor pressure occurs when air is holding all the water vapor
that it can at a given air temperature
Vapor pressure is measured in Pascals (Pa), where 1 Pa = 1 N/m2
1 kPa = 1000 Pa
T is in °C

## Slide 31: Relative humidity, Rh
es
e
Relative humidity measures the percent
of the saturation water content of the air
that it currently holds (0 – 100%)

## Slide 32: Frontal Lifting
Boundary between air masses with different properties is called a front
Cold front occurs when cold air advances towards warm air
Warm front occurs when warm air overrides cold air
Cold front (produces cumulus cloud)
Cold front (produces stratus cloud)

## Slide 33: Orographic lifting
Orographic uplift occurs when air is forced to rise because of the physical presence of elevated land.

## Slide 34: Convective lifting
Hot earth surface
Convective precipitation occurs when the air near the ground is heated by the earth’s warm surface. This warm air rises, cools and creates precipitation.

## Slide 35: Incremental Rainfall
Rainfall Hyetograph

## Slide 36: Cumulative Rainfall
Rainfall Mass Curve

## Slide 37: Rainfall maps in GIS
Nearest Neighbor “Thiessen” Polygon Interpolation
Spline Interpolation

## Slide 38: NEXRAD
NEXRAD Tower
NEXt generation RADar: is a doppler radar used for obtaining weather information
A signal is emitted from the radar which returns after striking a rainfall drop
Returned signals from the radar are analyzed to compute the rainfall intensity and integrated over time to get the precipitation
Working of NEXRAD

## Slide 39: Evaporation
  Evaporation – process by which liquid water becomes water vapor
  Transpiration – process by which liquid water passes from liquid to vapor through plant metabolism
  Evapotranspiration – evaporation through plants and trees, and directly from the soil and land surface
  Potential Evaporation – evaporation from an open water surface or from a well-watered grass surface

## Slide 40: ET -Eddy covariance method
Measurement of vertical transfer of water vapor driven by convective motion
Directly measure flux by sensing properties of eddies as they pass through a measurement level on an instantaneous basis
Statistical tool

## Slide 41: Energy Balance Method
Can directly measure these variables
How do you partition
H and E??

## Slide 42: Energy Balance Method
The maximum radiative evaporation rate Er =
Conversion valid at 20°C
Temp | Lv | Density | Conversion
0 | 2501000 | 999.9 | 28.94
10 | 2477300 | 999.7 | 28.66
20 | 2453600 | 998.2 | 28.35
30 | 2429900 | 995.7 | 28.00
40 | 2406200 | 992.2 | 27.63

## Slide 43
http://www.uga.edu/srel/kidsdoscience/soils-planets/soil-particle-size.pdf

## Slide 44: Soil Texture is defined by % of silt, sand, clay
Silty Clay Loam
~ 55% silt, 10% sand, 35% clay

## Slide 45: Soil Water Content
Soil Water Content

## Slide 46: Soil Water Flux, q
q = Q/A

## Slide 47: Soil Water Tension, y
Measures the suction head of the soil water
Like p/g in fluid mechanics but its always a suction (negative head)
Three key variables in soil water movement
  Flux, q
  Water content, q
  Tension, y
Total energy head = h
z=0
z1
z2
q12

## Slide 49: Richard’s Equation
Recall
  Darcy’s Law
  Total head
So Darcy becomes
Richard’s eqn is:
Soil water diffusivity

## Slide 50: Infiltration
Infiltration rate, f(t)
  Rate at which water enters the soil at the surface (in/hr or cm/hr)
Cumulative infiltration, F(t)
  Accumulated depth of water infiltrating during given time period
t
f, F
F
f

## Slide 51: Green – Ampt Infiltration
Wetted Zone
Wetting Front
Ponded Water
Ground Surface
Dry Soil

## Slide 52: Green – Ampt Infiltration (Cont.)
Apply finite difference to the derivative, between
  Ground surface
  Wetting front
Wetted Zone
Wetting Front
Ground Surface
Dry Soil

## Slide 53: Conductivity and Suction Head (Data from Table 4.3.1)
Chart: 
| 4.95 | 6.13 | 11.01 | 8.89 | 16.68 | 21.85 | 20.88 | 27.3 | 23.9 | 29.22 | 31.63
Conductivity | 11.78 | 2.99 | 1.09 | 0.34 | 0.65 | 0.15 | 0.1 | 0.1 | 0.06 | 0.05 | 0.03
Suction Head, ψ (cm)
Conductivity, K
(cm/hr)
Sand
Clay
Silt Loam
Silty Clay Loam
Loamy Sand
Sandy Clay
Sandy Loam
Loam
Sandy Clay Loam
Clay Loam
Silty Clay

## Slide 54: Green-Ampt Parameters (Data from Table 4.3.1)
Texture | Porosity n | Residual Porosity ϴr | Effective Porosity ϴe | Suction Head ψ (cm) | Conductivity K (cm/hr)
Sand | 0.437 | 0.020 | 0.417 | 4.95 | 11.78
Loamy Sand | 0.437 | 0.036 | 0.401 | 6.13 | 2.99
Sandy Loam | 0.453 | 0.041 | 0.412 | 11.01 | 1.09
Loam | 0.463 | 0.029 | 0.434 | 8.89 | 0.34
Silt Loam | 0.501 | 0.015 | 0.486 | 16.68 | 0.65
Sandy Clay Loam | 0.398 | 0.068 | 0.330 | 21.85 | 0.15
Clay Loam | 0.464 | 0.155 | 0.309 | 20.88 | 0.10
Silty Clay Loam | 0.471 | 0.039 | 0.432 | 27.30 | 0.10
Sandy Clay | 0.430 | 0.109 | 0.321 | 23.90 | 0.06
Silty Clay | 0.470 | 0.047 | 0.423 | 29.22 | 0.05
Clay | 0.475 | 0.090 | 0.385 | 31.63 | 0.03

## Slide 55: Green-Ampt Porosity (Data from Table 4.3.1)
Chart: 
| Sand | Loamy Sand | Sandy Loam | Loam | Silt Loam | Sandy Clay Loam | Clay Loam | Silty Clay Loam | Sandy Clay | Silty Clay | Clay
Residual Porosity | 0.02 | 0.036 | 0.041 | 0.029 | 0.015 | 0.068 | 0.155 | 0.039 | 0.109 | 0.047 | 0.09
Effective Porosity | 0.417 | 0.401 | 0.412 | 0.434 | 0.486 | 0.33 | 0.309 | 0.432 | 0.321 | 0.423 | 0.385
0.09
0.45
0.03
Total porosity ~ 0.45
Clay soils retain water in ~ 20% of voids when dry
Other soils retain water in ~ 6% of voids when dry
ϴe
ϴr

## Slide 56: Ponding time
Elapsed time between the time rainfall begins and the time water begins to pond on the soil surface (tp)

## Slide 57: Ponding Time
Up to the time of ponding, all rainfall has infiltrated (i = rainfall rate)
Potential
Infiltration
Actual Infiltration
Rainfall
Accumulated
Rainfall
Infiltration
Time
Time
Infiltration rate, f
Cumulative
Infiltration, F

## Slide 58: Infiltration after ponding has occured
At ponding time, tp, the cumulative infiltration is equal to the amount of rainfall that has fallen up to that time, Fp = i*tp
After that time, the cumulative infiltration is given by
  )

## Slide 59: Hortonian Flow
Sheet flow described by Horton in 1930s
When i<f, all i is absorbed
When i > f, (i-f) results in rainfall excess
Applicable in
  impervious surfaces (urban areas)
  Steep slopes with thin soil
  hydrophobic or compacted soil with low infiltration
Rainfall, i
Infiltration, f
i > q
Later studies showed that Hortonian flow rarely occurs on vegetated surfaces in humid regions.

## Slide 60: Subsurface flow
Lateral movement of water occurring through the soil above the water table
primary mechanism for stream flow generation when f>i
  Matrix/translatory flow
    Lateral flow of old water displaced by precipitation inputs
    Near surface lateral conductivity is greater than overall vertical conductivity
    Porosity and permeability higher near the ground
  Macropore flow
    Movement of water through large conduits in the soil

## Slide 61: Saturation overland flow
Soil is saturated from below by subsurface flow
Any precipitation occurring over a saturated surface becomes overland flow
Occurs mainly at the bottom of hill slopes and near stream banks

## Slide 62: Streamflow hydrograph
Graph of stream discharge as a function of time at a given location on the stream
Perennial river
Ephemeral river
Snow-fed River
Direct runoff
Baseflow

## Slide 63: SCS method
Soil conservation service (SCS) method is an experimentally derived method to determine rainfall excess using information about soils, vegetative cover, hydrologic condition and antecedent moisture conditions
The method is based on the simple relationship that Pe = P - Fa – Ia
Pe is runoff depth, P is precipitation depth, Fa is continuing abstraction, and Ia is the sum of initial losses (depression storage, interception, ET)
Time
Precipitation

## Slide 64: Abstractions – SCS Method
In general
After runoff begins
Potential runoff
SCS Assumption
Combining SCS assumption with P=Pe+Ia+Fa
Time
Precipitation

## Slide 65: SCS Method (Cont.)
Experiments showed
So
Surface
  Impervious: CN = 100
  Natural: CN < 100

## Slide 66: CN Table

## Slide 67: Hydrologic Measurement
Precipitation, Climate, Stream Gaging
Water Quality Sampling

## Slide 68: Stream Flow Rate
Discharge at a cross-section
Water Surface
Depth
Averaged
Velocity
Height
above
bed
Velocity
Velocity profile in stream

## Slide 69: Rating Curve
It is not feasible to measure flow daily.
Rating curves are used to estimate flow from stage data
Rating curve defines stage/streamflow relationship
http://nwis.waterdata.usgs.gov/nwis/measurements/?site_no=08158000

## Slide 70: Digital Elevation Model (DEM)
Contours
720
700
680
740
680
700
720
740
720
720

## Slide 71: LIDAR surveying
LIDAR (Light Detection and Ranging; or Laser Imaging Detection and Ranging) is a technology that determines distance to an object or surface using laser pulses. Like the similar radar technology, which uses radio waves instead of light, the range to an object is determined by measuring the time delay between transmission of a pulse and detection of the reflected signal.

## Slide 72
3-D detail of the Tongue river at the WY/Mont border from LIDAR.
Roberto Gutierrez
University of Texas at Austin