## Slide 1: CE 374K Hydrology
Review for Second Exam
April 17, 2012

## Slide 2: Hydrologic Analysis
Change in storage w.r.t. time = inflow - outflow
In the case of a linear reservoir, S = kQ
Transfer function for a linear system (S = kQ).

## Slide 3: Proportionality and superposition
Linear system (k is constant in S = kQ)
  Proportionality
    If I1  Q1 then C*I2  C*Q2
  Superposition
    If I1  Q1 and I2  Q2, then I1 +I2 Q1 + Q2

## Slide 4: Impulse response function
Impulse input: an input applied instantaneously (spike) at time t and zero everywhere else
An unit impulse at t produces as unit impulse response function u(t-t)
Principle of proportionality and superposition

## Slide 5: Step and pulse inputs
A unit step input is an input that goes from 0 to 1 at time 0 and continues indefinitely thereafter
A unit pulse is an input of unit amount occurring in duration Dt and 0 elsewhere.
Precipitation is a series of pulse inputs!

## Slide 6: Unit Hydrograph Theory
Direct runoff hydrograph resulting from a unit depth of excess rainfall occurring uniformly on a watershed at a constant rate for a specified duration.
Unit pulse response function of a linear hydrologic system
Can be used to derive runoff from any excess rainfall on the watershed.

## Slide 7: Discrete Convolution
Continuous
Discrete
Q is flow, P is precipitation and U is unit hydrograph
M is the number of precipitation pulses, n is the number of flow rate intervals
The unit hydrograph has N-M+1 pulses

## Slide 8
Application of convolution to the output from a linear system

## Slide 9: SCS dimensionless hydrograph
Synthetic UH in which the discharge is expressed by the ratio of q to qp and time by the ratio of t to Tp
If peak discharge and lag time are known, UH can be estimated.
Tc: time of concentration
C = 2.08 (483.4 in English system)
A: drainage area in km2 (mi2)

## Slide 10: Flow Routing
Procedure to determine the flow hydrograph at a point on a watershed from a known hydrograph upstream
As the hydrograph travels, it
  attenuates
  gets delayed
Q
t
Q
t
Q
t
Q
t

## Slide 11: Hydrologic Routing
Upstream hydrograph
Downstream hydrograph
Input, output, and storage are related by continuity equation:
Discharge
Inflow
Discharge
Outflow
Transfer
Function
Q and S are unknown
Storage can be expressed as a function of I(t) or Q(t) or both
For a linear reservoir, S=kQ

## Slide 12: Level pool methodology
Discharge
Time
Storage
Time
Inflow
Outflow
Unknown
Known
Need a function relating
Storage-outflow function

## Slide 13: Level pool methodology
Given
  Inflow hydrograph
  Q and H relationship
Steps
  Develop Q versus Q+ 2S/Dt relationship using Q/H relationship
  Compute Q+ 2S/Dt using
  Use the relationship developed in step 1 to get Q

## Slide 14: Hydrologic river routing (Muskingum Method)
Wedge storage in reach
Advancing
Flood
Wave
I > Q
Receding
Flood
Wave
Q > I
K = travel time of peak through the reach
X = weight on inflow versus outflow (0 ≤ X ≤ 0.5)
X = 0  Reservoir, storage depends on outflow, no wedge
X = 0.0 - 0.3  Natural stream

## Slide 15: Muskingum Method (Cont.)
Recall:
Combine:
If I(t), K and X are known, Q(t) can be calculated using above equations

## Slide 16: Types of flow routing
Lumped/hydrologic
  Flow is calculated as a function of time alone at a particular location
  Governed by continuity equation and flow/storage relationship
Distributed/hydraulic
  Flow is calculated as a function of space and time throughout the system
  Governed by continuity and momentum equations

## Slide 17: Hydraulic Routing in Rivers
Reference: HEC-RAS Hydraulic Reference Manual, Version 4.1, Chapters 1 and 2
Reading: HEC-RAS Manual pp. 2-1 to 2-12
Applied Hydrology, Sections 10-1 and 10-2
http://www.hec.usace.army.mil/software/hec-ras/documents/HEC-RAS_4.1_Reference_Manual.pdf

## Slide 18: Flood Inundation

## Slide 19: Steady Flow Solution

## Slide 20
Right Overbank
Left Overbank
Channel centerline
and banklines
Cross-section
One-Dimensional Flow Computations

## Slide 21: Solving Steady Flow Equations
All conditions at (1) are known, Q is known
Select h2
compute Y2, V2, K2, Sf, he
Using energy equation (A), compute h2
Compare new h2 with the value assumed in Step 2, and repeat until convergence occurs
h2
(2)
(1)
h1
Q is known throughout reach
(A)

## Slide 22: Unsteady Flow Routing in Open Channels
Flow is one-dimensional
Hydrostatic pressure prevails and vertical accelerations are negligible
Streamline curvature is small.
Bottom slope of the channel is small.
Manning’s equation is used to describe resistance effects
The fluid is incompressible

## Slide 23: Continuity Equation
Q = inflow to the control volume
q = lateral inflow
Elevation View
Plan View
Rate of change of flow with distance
Outflow from the C.V.
Change in mass
Reynolds transport theorem

## Slide 24: Momentum Equation (3)
Steady, uniform flow
Steady, non-uniform flow
Unsteady, non-uniform flow

## Slide 25: Random Variable
Random variable: a quantity used to represent probabilistic uncertainty
  Incremental precipitation
  Instantaneous streamflow
  Wind velocity
Random variable (X) is described by a probability distribution
Probability distribution is a set of probabilities associated with the values in a random variable’s sample space

## Slide 27: Summary statistics
Also called descriptive statistics
  If x1, x2, …xn is a sample then
Mean,
Variance,
Standard deviation,
Coeff. of variation,
m for continuous data
s2 for continuous data
s for continuous data
Also included in summary statistics are median, skewness, correlation coefficient,

## Slide 29: Return Period
Random variable:
Threshold level:
Extreme event occurs if:
Recurrence interval:
Return Period:
  Average recurrence interval between events equalling or exceeding a threshold
If p is the probability of occurrence of an extreme event, then
or

## Slide 30: Probability distributions
Normal family
  Normal, lognormal, lognormal-III
Generalized extreme value family
  EV1 (Gumbel), GEV, and EVIII (Weibull)
Exponential/Pearson type family
  Exponential, Pearson type III, Log-Pearson type III

## Slide 31: Frequency Factors
Once a distribution has been selected and its parameters estimated, then how do we use it?
Chow proposed using:
where
x
fX(x)

## Slide 32: Flood Frequency Analysis

## Slide 33: HEC-SSP

## Slide 34: Hydrologic design level
Hydrologic design level – magnitude of the hydrologic event to be considered for the design or a structure or project.
Three approaches for determining design level
  Empirical/probabilistic
  Risk analysis
  Hydroeconomic analysis

## Slide 35: Estimated Limiting Value (ELV)
Lower limit on design value – 0
Upper limit on design value – ELV
ELV – largest magnitude possible for a hydrologic event at a given location, based on the best available hydrologic information.
  Length of record
  Reliability of information
  Accuracy of analysis
Probable Maximum Precipitation (PMP) / Probable Maximum Flood (PMF)

## Slide 37: Design Storms
Get Depth, Duration, Frequency Data for the required location
Select a return period
Convert Depth-Duration data to a design hyetograph.

## Slide 38
Depth Duration Data to Rainfall Hyetograph

## Slide 39: Example 14.2.1
Determine i and P for a 20-min duration storm with 5-yr return period in Chicago
From the IDF curve for Chicago,
i = 3.5 in/hr for Td = 20 min and T = 5yr
P = i x Td = 3.5 x 20/60 = 1.17 in

## Slide 40: SCS Method
SCS (1973) adopted method similar to DDF to develop dimensionless rainfall temporal patterns called type curves for four different regions in the US.
SCS type curves are in the form of percentage mass (cumulative) curves based on 24-hr rainfall of the desired frequency.
If a single precipitation depth of desired frequency is known, the SCS type curve is rescaled (multiplied by the known number) to get the time distribution.
For durations less than 24 hr, the steepest part of the type curve for required duraction is used

## Slide 41: Example: Alternating Block Method
Find: Design precipitation hyetograph for a 2-hour storm (in 10 minute increments) in Denver with a 10-year return period 10-minute

## Slide 42: Responding to drought (and megadrought!) in Texas
Robert E. Mace, Ph.D., P.G.
Texas Water Development Board
March 27, 2012

## Slide 44: How drought impacts water
Less rainfall
  Less runoff
    Less flow in rivers
      Less water in reservoirs
  Less recharge
    Less water in aquifers
      Less flow in rivers
        Less water in reservoirs

## Slide 45: How drought impacts water
Less rainfall
  More water use
    Less water in rivers
      Less water in reservoirs
    Less water in reservoirs
    Less water in aquifer
      Less flow in rivers
        Less water in reservoirs

## Slide 46: How drought impacts water
More evaporation
  Less runoff
    Less flow in rivers
      Less water in reservoirs
  Less recharge
    Less water in aquifers
      Less flow in rivers
        Less water in reservoirs
Bottom line: reservoirs get hit hard…

## Slide 47: O.H. Ivie Reservoir
  Owned and operated by the Colorado River Municipal Water District
  Purpose: Water Supply
  Supplies: Odessa, Big Spring, Snyder, Midland, Abilene, San Angelo, Ballinger and Millersview-Doole
  Storage Capacity: 554,339 acre-feet
  Current Storage: 98,400 acre-feet
  2011 Change in Storage: -81,820 acre-feet
M. Bewley

## Slide 49: HEC-HMS and HEC-RAS Modeling at the City of Austin
Karl McArthur, PE, CFM
City of Austin
Watershed Protection Department
www.austintexas.gov/department/watershed-protection

## Slide 50
Notes: Varying Complexity of Watershed Modeling
Simple (relatively) – Dry Creek East
Complex – Carson Creek
Unsteady – Colorado River
Two-Dimensional – Shoal Creek
Beyond HEC-RAS
  Waller Creek Tunnel
  2D – XPSWMM and InforWorks RS
  SWAT
  Complication of Model Versions
  HEC-RAS 2.2 through 4.1
  HEC-HMS 2.1.2 through 3.5

## Slide 51: Lives, Property and the Environment
P u b l i c I n v o l v e m e n t
Implementation
Solution
Development
Assessment
Master Plan Process
Property
Protection
Public
Safety
Flooding
Environmental
Protection
WQ Degradation
Erosion

## Slide 52: Flood Risk Products and Datasets
Three Flood Risk Products
  Flood Risk Database
  Flood Risk Report
  Flood Risk Map
Four Flood Risk Datasets
  Flood Depth & Analysis Grids
  Flood Risk Assessments
  Changes Since Last FIRM
  Areas of Mitigation Interest
Flood Risk Datasets
Flood Risk Report
Flood Risk Map
Flood Risk
Database
Notes: The 3 Flood Risk Products are 3 different ways to deliver the 4 Flood Risk Datasets. All the datasets are present in the database and elements of the datasets are shown on the map and described in the report.
52

## Slide 53: FEWS Automated Mapping Process
NEXRAD Radar
And Gauge Data
Ground-Truthed
Distributed Rainfall
Predictive H&H Model
Model Output
XML
GIS Processing
Internal Website
Notes: 53

## Slide 54
Notes: New LiDAR should be available in September, 2012.

## Slide 56: Lidar Terrain Measurement

## Slide 59: Tropical Storm Hermine in Texas Sept 7-8, 2010

## Slide 60: GIS Hydrology Analysis (HEC-GeoHMS) using 10ft cells derived from LIDAR

## Slide 61: HEC-HMS Flood Discharge Model

## Slide 62: Engineering Hydraulics
Personal – a flooded home

## Slide 63
Cross-Sections for HEC-RAS model
Flood Elevation Model (HEC-GeoRAS) using 1ft cells derived from LIDAR

## Slide 64: HEC-RAS Flood Water Surface Elevation Model

## Slide 65: Flood Inundation Map

## Slide 66: Flood Impact on Houses

## Slide 67: National Flood Insurance Program
Started in 1968 and administered by FEMA
Based on agreement between federal and local government
Federal government provides flood insurance
Local government regulates land use to minimize flood risk
Federal Government
(Flood insurance, flood mapping)
Local Government (Cities, Counties)
Floodplain regulation

## Slide 68: Flood Insurance Rate Map (FIRM)
Flood Hazard Zone
≥ 1% chance of flooding in any year

## Slide 69: Digital Flood Insurance Rate Map (DFIRM)
Old, paper FIRM
New, digital (D)FIRM
The ideal DFIRM: more accurate than paper FIRM, more flexible to use and update, more versatile for community use

## Slide 70
(x,y)
(z)

## Slide 71: Conclusions from 2007 Study
Basemap imagery is fine for floodplain mapping
Existing elevation data have about 1/10 accuracy needed for floodplain mapping and are too old
A new elevation coverage of the nation is needed
Most likely technology to produce this is Lidar
Cost for national coverage ~ $500-600 million
We need “Elevation for the Nation”