## Slide 1: Channel Flow Routing
Reading:
Applied Hydrology Sections 8.4, 9.1-9.4, 9.7

## Slide 2: Brushy Creek Watershed
Dam 7
Subbasin BUT_060
Reservoir
Routing
Subasin Rainfall
-Runoff

## Slide 3: Reach SBR_080 Downstream of Dam 7
How do we route the flow through Reach SBR_080?

## Slide 4: Hydrologic river routing (Muskingum Method)
Wedge storage in reach
Advancing
Flood
Wave
I > Q
Receding
Flood
Wave
Q > I
K = travel time of peak through the reach
X = weight on inflow versus outflow (0 ≤ X ≤ 0.5)
X = 0  Reservoir, storage depends on outflow, no wedge
X = 0.0 - 0.3  Natural stream

## Slide 5: Muskingum Method (Cont.)
Recall:
Combine:
If I(t), K and X are known, Q(t) can be calculated using above equations

## Slide 6: Muskingum - Example
Given:
  Inflow hydrograph
  K = 2.3 hr, X = 0.15, Dt = 1 hour, Initial Q = 85 cfs
Find:
  Outflow hydrograph using Muskingum routing method

## Slide 7: Muskingum – Example (Cont.)
C1 = 0.0631, C2 = 0.3442, C3 = 0.5927

## Slide 8: Unsteady Flow Routing in Open Channels
Flow is one-dimensional
Hydrostatic pressure prevails and vertical accelerations are negligible
Streamline curvature is small.
Bottom slope of the channel is small.
Manning’s equation is used to describe resistance effects
The fluid is incompressible

## Slide 9: Continuity Equation
Q = inflow to the control volume
q = lateral inflow
Elevation View
Plan View
Rate of change of flow with distance
Outflow from the C.V.
Change in mass
Reynolds transport theorem

## Slide 10: Momentum Equation
From Newton’s 2nd Law:
Net force = time rate of change of momentum
Sum of forces on the C.V.
Momentum stored within the C.V
Momentum flow across the C. S.

## Slide 11: Forces acting on the C.V.
Elevation View
Plan View
Fg = Gravity force due to weight of water in the C.V.
Ff = friction force due to shear stress along the bottom and sides of the C.V.
Fe = contraction/expansion force due to abrupt changes in the channel cross-section
Fw = wind shear force due to frictional resistance of wind at the water surface
Fp = unbalanced pressure forces due to hydrostatic forces on the left and right hand side of the C.V. and pressure force exerted by banks

## Slide 12: Momentum Equation
Sum of forces on the C.V.
Momentum stored within the C.V
Momentum flow across the C. S.

## Slide 13: Momentum Equation(2)
Local acceleration term
Convective acceleration term
Pressure force term
Gravity force term
Friction force term
Kinematic Wave
Diffusion Wave
Dynamic Wave

## Slide 14: Momentum Equation (3)
Steady, uniform flow
Steady, non-uniform flow
Unsteady, non-uniform flow

## Slide 15: Applications of different forms of momentum equation
Kinematic wave: when gravity forces and friction forces balance each other (steep slope channels with no back water effects)
Diffusion wave: when pressure forces are important in addition to gravity and frictional forces
Dynamic wave: when both inertial and pressure forces are important and backwater effects are not negligible (mild slope channels with downstream control, backwater effects)

## Slide 16: Kinematic Wave
Kinematic wave celerity, ck is the speed of movement of the mass of a flood wave downstream
  Approximately, ck = 5v/3 where v = water velocity

## Slide 17: Muskingum-Cunge Method
A variant of the Muskingum method that has a more physical hydraulic basis
This is what Dean Djokic has used in the Brushy Creek HEC-HMS models
, where Δx = reach length or an increment of this length
, where B = surface width, S0 is the bed slope

## Slide 18: Reach SBR_080 Downstream of Dam 7
How do we route the flow through Reach SBR_080?

## Slide 19: Longitudinal profile for reach SBR_080
0.0008
1
1545 ft

## Slide 20: Cross-Section for SBR_080
Station | Elevation
0 | 797.6057
118.1 | 790.0711
236.2 | 781.6702
284 | 777.0652
304 | 777.0652
323.42 | 783.5712
344.26 | 789.859
365.1 | 795.4788
Chart: Cross-Section
| 0 | 118.1 | 236.2 | 284 | 304 | 323.42 | 344.26 | 365.1
Elevation | 797.6056 | 790.0711 | 781.6702 | 777.0652 | 777.0652 | 783.5712 | 789.859 | 795.4788

## Slide 21: Routing in stream reach downstream of Dam 7