## Slide 1
“Note D is on water filtration. It includes a description of a new device that seems to simply and economically resolve the problem of filtering water to supply a large city. To obtain this result, I take into consideration the law of water flow through sand, a law that I have demonstrated experimentally….. I have not seen the documents that are included in Note D collected in any special book. In particular, to my knowledge at least, no one has experimentally determined the laws of water flow through sand.”
Bobeck translation, p. xxv
Darcy’s Law for Flow through Porous Medium, first published in 1856
Translation, Patrica Bobeck, 2004
Published in Paris by Victor Dalmont, Publisher for Imperial Corps of Bridges, Roads and Mines
Quai des Augustins, 49 1856

## Slide 2
“Thus, if we denote the thickness of the sand
layer by e, its surface area by s, atmospheric pressure by P, and the height of the water on the sand layer by h, we will have P+h for the pressure to which the upper end will be subjected. In addition, if P ± h0 is the pressure to which the lower surface is subjected, k is a coefficient that depends on the permeability of the layer and q is the volume discharge, we have
which reduces to
when h0 = 0 or pressure under the filter is equal to atmospheric pressure.”
Darcy’s Law
e
s
P+h
P ± h0
q
k
Pressurized water supply in a hospital
Description of experiments and equation, p. 455-459,
as part of Appendix D in the book of 506 pages.
Sand column is 2.3 m high
0.35m diameter
Diagram from Plate 24

## Slide 3
Tests conducted on 29-30 October, and 6 November, 1855
Test 1 – sand was not washed
Test 2 – sand was not washed
Test 3 – sand was washed
Test 4 – washed sand with a slightly larger grain size
“Thus, it appears that for an identical sand, it can be assumed that the volume discharged is proportional to the head and inversely proportional to the thickness of the sand layer that the water passes through.”
Ratio of discharge/pressure head ~ constant for each test

## Slide 4: Hydraulic Conductivity in Test 1, 29 Oct 1855
Darcy’s Law:
= = 0.09621m2
For Test 1, Q/Dh = 2.8357, L
These are reasonable numbers for “slow sand” filters
Modern “rapid sand” filters have conductivities of 5-12 m/hr
The Green-Ampt conductivity for sand is 12 cm/hr