## Slide 1: Hydrologic Design Storms
Reading: Applied Hydrology Sections 14-1 to 14-4

## Slide 2: Hydrologic design
Water control
  Peak flows, erosion, pollution, etc.
Water management
  Domestic and industrial use, irrigation, instream flows, etc
Tasks
  Determine design inflow
  Route the design inflow
  Find the output
    check if it is sufficient to meet the demands (for management)
    Check if the outflow is at safe level (for control)

## Slide 4: Return Period
Random variable:
Threshold level:
Extreme event occurs if:
Recurrence interval:
Return Period:
  Average recurrence interval between events equalling or exceeding a threshold
If p is the probability of occurrence of an extreme event, then
or

## Slide 5: More on return period
If p is probability of success, then (1-p) is the probability of failure
Find probability that (X ≥ xT) at least once in N years.

## Slide 6: Risk Analysis
Uncertainty in hydrology
  Inherent - stochastic nature of hydrologic phenomena
  Model – approximations in equations
  Parameter – estimation of coefficients in equations
Consideration of Risk
  Structure may fail if event exceeds T–year design magnitude
  R = P(event occurs at least once in n years)
    Natural inherent risk of failure

## Slide 7: Example 13.2.2
Expected life of culvert = 10 yrs
Acceptable risk of 10 % for the culvert capacity
Find the design return period
What is the chance that the culvert designed for an event of 95 yr return period will have its capacity exceeded at least once in 50 yrs?
The chance that the capacity will not be exceeded during the next 50 yrs is 1-0.41 = 0.59

## Slide 8: Hydroeconomic Analysis
Probability distribution of hydrologic event and damage associated with its occurrence are known
As the design period increases, capital cost increases, but the cost associated with expected damages decreases.
In hydroeconomic analysis, find return period that has minimum total (capital + damage) cost.

## Slide 10: Design Storms
Get Depth, Duration, Frequency Data for the required location
Select a return period
Convert Depth-Duration data to a design hyetograph.

## Slide 11
Depth Duration Data to Rainfall Hyetograph

## Slide 12: TP 40
Hershfield (1961) developed isohyetal maps of design rainfall and published in TP 40.
TP 40 – U. S. Weather Bureau technical paper no. 40. Also called precipitation frequency atlas maps or precipitation atlas of the United States.
  30mins to 24hr maps for T = 1 to 100
Web resources for TP 40 and rainfall frequency maps
  http://www.tucson.ars.ag.gov/agwa/rainfall_frequency.html
  http://www.erh.noaa.gov/er/hq/Tp40s.htm
  http://hdsc.nws.noaa.gov/hdsc/pfds/

## Slide 13: 2yr-60min precipitation GIS map

## Slide 14: 2yr-60min precipitation map
This map is from HYDRO 35 (another publication from NWS) which supersedes TP 40

## Slide 15
http://hdsc.nws.noaa.gov/hdsc/pfds/index.html

## Slide 16
An example of precipitation frequency estimates for a location in California
37.4349 N
120.6062 W

## Slide 17: Results of Precip Frequency Query

## Slide 18: Design areal precipitation
Point precipitation estimates are extended to develop an average precipitation depth over an area
Depth-area-duration analysis
  Prepare isohyetal maps from point precipitation for different durations
  Determine area contained within each isohyet
  Plot average precipitation depth vs. area for each duration

## Slide 19: Tropical Storm Allison

## Slide 20: TS Allison

## Slide 21: Depth-area curve
(World Meteorological Organization, 1983)

## Slide 22: TS Allison
Chart: Time (Hours)
 | 0 | 0.04 | 1.18 | 0.98 | 2.48 | 2.4 | 1.46 | 1.69 | 4.88 | 3.39 | 3.86 | 3.19 | 0 | 0.2 | 0.08 | 0.04 | 0
Chart: Cumulative Rainfall
 | 0 | 0 | 0.04 | 1.22 | 2.2 | 4.68 | 7.08 | 8.54 | 10.23 | 15.11 | 18.5 | 22.36 | 25.55 | 25.55 | 25.75 | 25.83 | 25.87 | 25.87

## Slide 23: Extreme Rainfalls, Station 1600
Chart: Cumulative Rainfall
 | 0 | 0 | 0.04 | 1.22 | 2.2 | 4.68 | 7.08 | 8.54 | 10.23 | 15.11 | 18.5 | 22.36 | 25.55 | 25.55 | 25.75 | 25.83 | 25.87 | 25.87
Time | Rainfall | 2-Hour | 3-Hour | 4-hour
1.00 | 0.00 |  |  | 
2.00 | 0.04 | 0.04 |  | 
3.00 | 1.18 | 1.22 | 1.22 | 
4.00 | 0.98 | 2.16 | 2.20 | 2.20
5.00 | 2.48 | 3.46 | 4.64 | 4.68
6.00 | 2.40 | 4.88 | 5.86 | 7.04
7.00 | 1.46 | 3.86 | 6.34 | 7.32
8.00 | 1.69 | 3.15 | 5.55 | 8.03
9.00 | 4.88 | 6.57 | 8.03 | 10.43
10.00 | 3.39 | 8.27 | 9.96 | 11.42
11.00 | 3.86 | 7.25 | 12.13 | 13.82
12.00 | 3.19 | 7.05 | 10.44 | 15.32
13.00 | 0.00 | 3.19 | 7.05 | 10.44
14.00 | 0.20 | 0.20 | 3.39 | 7.25
15.00 | 0.08 | 0.28 | 0.28 | 3.47
16.00 | 0.04 | 0.12 | 0.32 | 0.32
17.00 | 0.00 | 0.04 | 0.12 | 0.32
Depth | 4.88 | 8.27 | 12.13 | 15.32
Intensity | 4.88 | 4.13 | 4.03 | 3.83
Values in inches for depth
and inches per hour for intensity

## Slide 24: Depth (intensity)-duration-frequency
DDF/IDF – graph of depth (intensity) versus duration for different frequencies
  TP 40 or HYDRO 35 gives spatial distribution of rainfall depths for a given duration and frequency
  DDF/IDF curve gives depths for different durations and frequencies at a particular location
  TP 40 or HYDRO 35 can be used to develop DDF/IDF curves
Depth (P) = intensity (i) x duration (Td)

## Slide 25: IDF curve

## Slide 26: Example 14.2.1
Determine i and P for a 20-min duration storm with 5-yr return period in Chicago
From the IDF curve for Chicago,
i = 3.5 in/hr for Td = 20 min and T = 5yr
P = i x Td = 3.5 x 20/60 = 1.17 in

## Slide 27: Equations for IDF curves
IDF curves can also be expressed as equations to avoid reading from graphs
i is precipitation intensity, Td is the duration, and c, e, f are coefficients that vary for locations and different return periods
This equation includes return period (T) and has an extra coefficient (m)

## Slide 28: Example 14.2.4
Using IDF curve equation, determine 10-yr 20-min design rainfall intensities for Denver
From Table 14.2.3 in the text, c = 96.6, e = 0.97, and f = 13.9
Similarly, i = 4.158 and 2.357 in/hr for Td = 10 and 30 min, respectively

## Slide 29: IDF curves for Austin
Source: City of Austin, Watershed Management Division

## Slide 30: Design Precipitation Hyetographs
Most often hydrologists are interested in precipitation hyetographs and not just the peak estimates.
Techniques for developing design precipitation hyetographs
  SCS method
  Triangular hyetograph method
  Using IDF relationships (Alternating block method)

## Slide 31: TS Allison
Chart: Time (Hours)
 | 0 | 0.04 | 1.18 | 0.98 | 2.48 | 2.4 | 1.46 | 1.69 | 4.88 | 3.39 | 3.86 | 3.19 | 0 | 0.2 | 0.08 | 0.04 | 0

## Slide 32: SCS Method
SCS (1973) adopted method similar to DDF to develop dimensionless rainfall temporal patterns called type curves for four different regions in the US.
SCS type curves are in the form of percentage mass (cumulative) curves based on 24-hr rainfall of the desired frequency.
If a single precipitation depth of desired frequency is known, the SCS type curve is rescaled (multiplied by the known number) to get the time distribution.
For durations less than 24 hr, the steepest part of the type curve for required duraction is used

## Slide 33: SCS type curves for Texas (II&III)
SCS 24-Hour Rainfall Distributions |  |  |  | SCS 24-Hour Rainfall Distributions |  | 
T (hrs) | Fraction of 24-hr rainfall |  |  | T (hrs) | Fraction of 24-hr rainfall | 
 | Type II | Type III |  |  | Type II | Type III
0.0 | 0.000 | 0.000 |  | 11.5 | 0.283 | 0.298
1.0 | 0.011 | 0.010 |  | 11.8 | 0.357 | 0.339
2.0 | 0.022 | 0.020 |  | 12.0 | 0.663 | 0.500
3.0 | 0.034 | 0.031 |  | 12.5 | 0.735 | 0.702
4.0 | 0.048 | 0.043 |  | 13.0 | 0.772 | 0.751
5.0 | 0.063 | 0.057 |  | 13.5 | 0.799 | 0.785
6.0 | 0.080 | 0.072 |  | 14.0 | 0.820 | 0.811
7.0 | 0.098 | 0.089 |  | 15.0 | 0.854 | 0.854
8.0 | 0.120 | 0.115 |  | 16.0 | 0.880 | 0.886
8.5 | 0.133 | 0.130 |  | 17.0 | 0.903 | 0.910
9.0 | 0.147 | 0.148 |  | 18.0 | 0.922 | 0.928
9.5 | 0.163 | 0.167 |  | 19.0 | 0.938 | 0.943
9.8 | 0.172 | 0.178 |  | 20.0 | 0.952 | 0.957
10.0 | 0.181 | 0.189 |  | 21.0 | 0.964 | 0.969
10.5 | 0.204 | 0.216 |  | 22.0 | 0.976 | 0.981
11.0 | 0.235 | 0.250 |  | 23.0 | 0.988 | 0.991
 |  |  |  | 24.0 | 1.000 | 1.000

## Slide 34: Choice of Calibration Storms
    Representative?
      In temporal shape
2007 Storm
2010 Hermine Storm

## Slide 35: SCS Method Steps
Given Td and frequency/T, find the design hyetograph
  Compute P/i (from DDF/IDF curves or equations)
  Pick a SCS type curve based on the location
  If Td = 24 hour, multiply (rescale) the type curve with P to get the design mass curve
    If Td is less than 24 hr, pick the steepest part of the type curve for rescaling
  Get the incremental precipitation from the rescaled mass curve to develop the design hyetograph

## Slide 36: Example – SCS Method
Find - rainfall hyetograph for a 25-year, 24-hour duration SCS Type-III storm in Harris County using a one-hour time increment
a = 81, b = 7.7, c = 0.724 (from Tx-DOT hydraulic manual)
Find
  Cumulative fraction - interpolate SCS table
  Cumulative rainfall = product of cumulative fraction * total 24-hour rainfall (10.01 in)
  Incremental rainfall = difference between current and preceding cumulative rainfall
TxDOT hydraulic manual is available at:
http://manuals.dot.state.tx.us/docs/colbridg/forms/hyd.pdf

## Slide 37: SCS – Example (Cont.)
If a hyetograph for less than 24 needs to be prepared, pick time intervals that include the steepest part of the type curve (to capture peak rainfall). For 3-hr pick 11 to 13, 6-hr pick 9 to 14 and so on.

## Slide 38: Triangular Hyetograph Method
Given Td and frequency/T, find the design hyetograph
  Compute P/i (from DDF/IDF curves or equations)
  Use above equations to get ta, tb, Td and h (r is available for various locations)
Time
Rainfall intensity, i
h
ta
tb
Td
Td: hyetograph base length = precipitation duration
ta: time before the peak
r: storm advancement coefficient = ta/Td
tb: recession time = Td – ta = (1-r)Td

## Slide 39: Triangular hyetograph - example
Find - rainfall hyetograph for a 25-year, 6-hour duration in Harris County. Use storm advancement coefficient of 0.5.
a = 81, b = 7.7, c = 0.724 (from Tx-DOT hydraulic manual)
Time
Rainfall intensity, in/hr
2.24
3 hr
3 hr
6 hr

## Slide 40: Alternating block method
Given Td and T/frequency, develop a hyetograph in Dt increments
  Using T, find i for Dt, 2Dt, 3Dt,…nDt using the IDF curve for the specified location
  Using i compute P for Dt, 2Dt, 3Dt,…nDt. This gives cumulative P.
  Compute incremental precipitation from cumulative P.
  Pick the highest incremental precipitation (maximum block) and place it in the middle of the hyetograph. Pick the second highest block and place it to the right of the maximum block, pick the third highest block and place it to the left of the maximum block, pick the fourth highest block and place it to the right of the maximum block (after second block), and so on until the last block.

## Slide 41: Example: Alternating Block Method
Find: Design precipitation hyetograph for a 2-hour storm (in 10 minute increments) in Denver with a 10-year return period 10-minute