## Slide 1: CE 374K Hydrology
Frequency Factors

## Slide 2: Frequency Analysis using Frequency Factors
The magnitude of an extreme event can be thought of as a departure from the mean expressed as a number of standard deviations
The frequency factor, , is a number in the range (-1, 5) that depends on:
  Probability distribution
  Return period, T
  Coefficient of skewness, Cs
f(x)
x
xT
P( xT)

## Slide 3: Frequency Factors for Log Pearson Type III Distribution

## Slide 4: Example: 100 year flood on Colorado River
Colorado River at Austin, annual maximum flows, 1900 to 1940. What is the 100 year flood based on these data?
Take logs to base 10 of the annual flows
Compute the mean, standard deviation and coefficient of skewness of the data (Excel functions: Average, Stdev, Skew)
Results:
  Mean = 4.7546, Standard Dev = 0.3423, Skew = 0.6919
From Table 12.3.1,
  For T = 100 years, and Cs = 0.6, KT = 2.755;
  For T = 100 years, and Cs = 0.7, KT = 2.824;
By interpolation,
  For T = 100 years, and Cs = 0.6919, KT = 2.8184;

## Slide 5: Example continued …
Hence
  5.7193
  or
Result from HEC-SSP

## Slide 6: Results in HEC-SSP
QT = 524,000 cfs for T = 100 years or p = 0.01

## Slide 7: Probability Plotting
Goal is to assign an exceedance probability to each observed value
Rank all data from largest (m = 1) to smallest (m = n)
Use plotting formula (A= B= 0.3)
  )=
  )=
So, for largest value on n = 41 data, m = 1, so
  )= = 0.0169 or 1.69%
This means that the largest value in 41 years has a chance of being exceeded in any year of 1.69%

## Slide 8: Coefficient of Skewness, Cs
This has considerable uncertainty, especially for small datasets
Desirable to balance the value computed from sample data, Cs with an mapped value, Cm for flood peaks recorded in this region
Use weighted Skew
The variance of the weighted skewness for the US is V(Cm) = 0.3025
The variance of the sample skewness is

## Slide 9: Coefficient of Skewness (Cont.)
For Colorado River example (n = 41)
  Cs = 0.692
  A = - 0.33+0.08*0.692 = - 0.2746
  B = 0.94 – 0.26*0.692 = 0.7601
  V(Cs) = 0.182
If, for Austin, Texas, we assume that the mapped skew is -0.25
Then the weighted skew is
Or Cw = 0.338

## Slide 10: Mapped Skewness Values
-0.3
-0.2

## Slide 11: Coefficient of Skewness (Cont.)
If we repeat the frequency analysis using the weighted skewness

## Slide 12: Big impact on extreme flood estimates, less so for small ones
With sample skewness, 0.692
With the adjusted skewness, 0.338
100 year
10 year

## Slide 13: Additional Considerations
Confidence Limits
Outliers
Expected Probability

## Slide 14: Outliers
Frequency analysis of extreme events is based on an underlying probability model (LPIII in this case)
It is assumed the sample parameters, () are representative of the population values (µ,σ) (more data is better)
Test
  High Outliers:
  Low Outliers:
Is this value (481,000 cfs) representative of the rest of the data?

## Slide 15: Example
For Colorado River, 1900-1940
  () = (4.7546, 0.3423)
  N = 41, Kn = 2.692
= 474,320 cfs
Observed maximum is 481,000 cfs, hence it’s a high outlier, but we’ll keep it in the analysis anyway.

## Slide 16: Confidence Limits (90% of observed 100 year floods are expected to be between these limits)
906087 – 523817 = 382270 cfs
523817 – 353765 = 170052 cfs
170052 (32% smaller)
382270 (73% larger)
5 %
95 %

## Slide 17: Expected Probability
Skewed distribution
(non-central t distn)
Median
(50% above and below)
Mean
Expected Value of QT E(QT)
If there are lots of floods, average value is E(QT)
This what you need if you are insuring $6 billion in property over the US for lots of floods, as is the National Flood Insurance Program

## Slide 18: Flood discharge Vs Return Period
Chart: 
| 2 | 5 | 10 | 25 | 50 | 100 | 200
QT | 51924.4282 | 105995.8166 | 162455.2423 | 267365.0841 | 377707.3235 | 523969.2197 | 716584.205
Discharge
Return Period (Years)
Design discharge rises less than proportional to return period