## Slide 1: Atmospheric Water and Precipitation
Global energy balance
Atmospheric circulation
Atmospheric water vapor
Precipitation
Reading: Sections 3.1 to 3.4

## Slide 2: Radiation
Basic laws
  Stefan-Boltzman Law
    R = emitted radiation (W/m2)
    T = absolute temperature (K),
    and s = 5.67x10-8W/m2-K4
    with e = emissivity (0-1)
      Water, Ice, Snow (0.95-0.99)
      Sand (0.76)
“Gray bodies emit a proportion of the radiation of a black body
Valid for a Black body or “pure radiator”

## Slide 3: Net Radiation, Rn
Ri Incoming Radiation
Ro =aRi Reflected radiation
= albedo (0 – 1)
Rn Net Radiation
Re
Average value of Rn over the earth and
over the year is 105 W/m2

## Slide 4: Net Radiation, Rn
Rn Net Radiation
Average value of Rn over the earth and
over the year is 105 W/m2
G – Ground Heat Flux
LE – Evaporation
H – Sensible Heat

## Slide 5: Energy Balance of Earth
http://www.uwsp.edu/geo/faculty/ritter/geog101/textbook/energy/radiation_balance.html
6
4
100
70
51
21
26
38
6
20
15
Sensible heat flux 7
Latent heat flux 23
19

## Slide 6: Energy Balance in the San Marcos Basin from the NARR (July 2003)
Average fluxes over the day
310
72
415
495
3
61
112
Net Shortwave = 310 – 72 = 238; Net Longwave = 415 – 495 = - 80
Note the very large amount of longwave radiation exchanged between land and atmosphere

## Slide 7
Increasing carbon dioxide in the atmosphere (from about 300 ppm in preindustrial times)
We are burning fossil carbon (oil, coal) at 100,000 times the rate it
was laid down in geologic time

## Slide 8: Absorption of energy by CO2

## Slide 9: Heating of earth surface
Heating of earth surface is uneven
  Solar radiation strikes perpendicularly near the equator (270 W/m2)
  Solar radiation strikes at an oblique angle near the poles (90 W/m2)
Emitted radiation is more uniform than incoming radiation
Amount of energy transferred from equator to the poles is approximately 4 x 109 MW

## Slide 10: Hadley circulation
Warm air rises, cool air descends creating two huge convective cells.
Atmosphere (and oceans) serve to transmit heat energy from the equator to the poles

## Slide 11: Atmospheric circulation
Tropical Easterlies/Trades
Westerlies
Polar easterlies
Intertropical convergence zone (ITCZ)/Doldrums
Horse latitudes
Subpolar low
Polar high
Ferrel Cell
Polar Cell
Hadley cell
Ferrel Cell
Polar cell
Latitudes
Winds
Circulation cells

## Slide 12: Shifting in Intertropical Convergence Zone (ITCZ)
Owing to the tilt of the Earth's axis in orbit, the ITCZ shifts north and south.
Southward shift in January
Northward shift in July
Creates wet Summers (Monsoons) and dry winters, especially in India and SE Asia

## Slide 13: Structure of atmosphere

## Slide 14: Atmospheric water
Atmospheric water exists
  Mostly as gas or water vapor
  Liquid in rainfall and water droplets in clouds
  Solid in snowfall and in hail storms
Accounts for less than 1/100,000 part of total water, but plays a major role in the hydrologic cycle

## Slide 15: Water vapor
Suppose we have an elementary volume of atmosphere dV and
we want quantify how much water vapor it contains
Atmospheric gases:
Nitrogen – 78.1%
Oxygen – 20.9%
Other gases ~ 1%
http://www.bambooweb.com/articles/e/a/Earth's_atmosphere.html
dV
ma = mass of moist air
mv = mass of water vapor
Water vapor density
Air density

## Slide 16: Specific Humidity, qv
Specific humidity measures the mass of water vapor per unit mass of moist air
It is dimensionless

## Slide 17: Vapor pressure, e
Vapor pressure, e, is the pressure that water vapor exerts on a surface
Air pressure, p, is the total pressure that air makes on a surface
Ideal gas law relates pressure to absolute temperature T, Rv is the gas constant for water vapor
0.622 is ratio of mol. wt. of water vapor to avg mol. wt. of dry air (=18/28.9)

## Slide 18: Saturation vapor pressure, es
Saturation vapor pressure occurs when air is holding all the water vapor
that it can at a given air temperature
Vapor pressure is measured in Pascals (Pa), where 1 Pa = 1 N/m2
1 kPa = 1000 Pa

## Slide 19: Relative humidity, Rh
es
e
Relative humidity measures the percent
of the saturation water content of the air
that it currently holds (0 – 100%)

## Slide 20: Dewpoint Temperature, Td
e
Dewpoint temperature is the air temperature
at which the air would be saturated with its current
vapor content
T
Td

## Slide 21: Water vapor in an air column
We have three equations describing column:
  Hydrostatic air pressure, dp/dz = -rag
  Lapse rate of temperature, dT/dz = - a
  Ideal gas law, p = raRaT
Combine them and integrate over column to get pressure variation elevation
Column
Element, dz
1
2

## Slide 22: Precipitable Water
In an element dz, the mass of water vapor is dmp
Integrate over the whole atmospheric column to get precipitable water,mp
mp/A gives precipitable water per unit area in kg/m2
Column
Element, dz
1
2
Area = A

## Slide 23: Precipitable Water
http://geography.uoregon.edu/envchange/clim_animations/flash/pwat.html
25 mm precipitable water divides frontal from thunderstorm rainfall
Frontal rainfall in the winter
Thunderstorm rainfall in the summer

## Slide 24: Precipitation
Precipitation: water falling from the atmosphere to the earth.
  Rainfall
  Snowfall
  Hail, sleet
Requires lifting of air mass so that it cools and condenses.

## Slide 25: Mechanisms for air lifting
Frontal lifting
Orographic lifting
Convective lifting

## Slide 26: Frontal Lifting
Boundary between air masses with different properties is called a front
Cold front occurs when cold air advances towards warm air
Warm front occurs when warm air overrides cold air
Cold front (produces cumulus cloud)
Cold front (produces stratus cloud)

## Slide 27: Orographic lifting
Orographic uplift occurs when air is forced to rise because of the physical presence of elevated land.

## Slide 28: Convective lifting
Hot earth surface
Convective precipitation occurs when the air near the ground is heated by the earth’s warm surface. This warm air rises, cools and creates precipitation.

## Slide 29: Condensation
Condensation is the change of water vapor into a liquid. For condensation to occur, the air must be at or near saturation in the presence of condensation nuclei.
Condensation nuclei are small particles or aerosol upon which water vapor attaches to initiate condensation. Dust particulates, sea salt, sulfur and nitrogen oxide aerosols serve as common condensation nuclei.
Size of aerosols range from 10-3 to 10 mm.

## Slide 30: Precipitation formation
Lifting cools air masses so moisture condenses
Condensation nuclei
  Aerosols
  water molecules attach
Rising & growing
  0.5 cm/s sufficient to carry 10 mm droplet
  Critical size (~0.1 mm)
  Gravity overcomes and drop falls

## Slide 31: Forces acting on rain drop
Fd
Fd
Fb
Fg
D
Three forces acting on rain drop
  Gravity force due to weight
  Buoyancy force due to displacement of air
  Drag force due to friction with surrounding air

## Slide 32: Terminal Velocity
Terminal velocity: velocity at which the forces acting on the raindrop are in equilibrium.
If released from rest, the raindrop will accelerate until it reaches its terminal velocity
Raindrops are spherical up to a diameter of 1 mm
For tiny drops up to 0.1 mm diameter, the drag force is specified by Stokes law
Fd
Fd
Fb
Fg
D
V
At standard atmospheric pressure (101.3 kpa) and temperature (20oC), rw = 998 kg/m3 and ra = 1.20 kg/m3

## Slide 33: Rainfall patterns in the US

## Slide 34: Global precipitation pattern

## Slide 35: Spatial Representation
Isohyet – contour of constant rainfall
Isohyetal maps are prepared by interpolating rainfall data at gaged points.
Austin, May 1981
Wellsboro, PA 1889

## Slide 36: Texas Rainfall Maps

## Slide 37: Temporal Representation
Rainfall hyetograph – plot of rainfall depth or intensity as a function of time
Cumulative rainfall hyetograph or rainfall mass curve – plot of summation of rainfall increments as a function of time
Rainfall intensity – depth of rainfall per unit time

## Slide 38: Rainfall Depth and Intensity

## Slide 39: Incremental Rainfall
Rainfall Hyetograph

## Slide 40: Cumulative Rainfall
Rainfall Mass Curve

## Slide 41: Arithmetic Mean Method
Simplest method for determining areal average
P1
P2
P3
P1 = 10 mm
P2 = 20 mm
P3 = 30 mm
Gages must be uniformly distributed
Gage measurements should not vary greatly about the mean

## Slide 42: Thiessen polygon method
P1
P2
P3
A1
A2
A3
Any point in the watershed receives the same amount of rainfall as that at the nearest gage
Rainfall recorded at a gage can be applied to any point at a distance halfway to the next station in any direction
Steps in Thiessen polygon method
  Draw lines joining adjacent gages
  Draw perpendicular bisectors to the lines created in step 1
  Extend the lines created in step 2 in both directions to form representative areas for gages
  Compute representative area for each gage
  Compute the areal average using the following formula
P1 = 10 mm, A1 = 12 Km2
P2 = 20 mm, A2 = 15 Km2
P3 = 30 mm, A3 = 20 km2

## Slide 43: Isohyetal method
P1
P2
P3
10
20
30
Steps
  Construct isohyets (rainfall contours)
  Compute area between each pair of adjacent isohyets (Ai)
  Compute average precipitation for each pair of adjacent isohyets (pi)
  Compute areal average using the following formula
A1=5 , p1 = 5
A2=18 , p2 = 15
A3=12 , p3 = 25
A4=12 , p3 = 35

## Slide 44: Inverse distance weighting
P1=10
P2= 20
P3=30
Prediction at a point is more influenced by nearby measurements than that by distant measurements
The prediction at an ungaged point is inversely proportional to the distance to the measurement points
Steps
  Compute distance (di) from ungaged point to all measurement points.
  Compute the precipitation at the ungaged point using the following formula
d1=25
d2=15
d3=10
p

## Slide 45: Rainfall interpolation in GIS
Data are generally available as points with precipitation stored in attribute table.

## Slide 46: Rainfall maps in GIS
Nearest Neighbor “Thiessen” Polygon Interpolation
Spline Interpolation

## Slide 47: NEXRAD
NEXRAD Tower
NEXt generation RADar: is a doppler radar used for obtaining weather information
A signal is emitted from the radar which returns after striking a rainfall drop
Returned signals from the radar are analyzed to compute the rainfall intensity and integrated over time to get the precipitation
Working of NEXRAD

## Slide 48: NEXRAD WSR-88D Radars in Central Texas (Weather Surveillance Radar-1988 Doppler) scanning range = 230 km
Stage I: Just Radar
Stage II: gages, satellite, and surface temperature
Stage III: Continuous mosaic from radar overlaps
NEXRAD Products:
Source: PBS&J, 2003
EWX – NEXRAD Radar in New Braunfels
Notes: One of the strong motivation points for integration is the availability of
good quality precipitation estimates at higher temporal and spatial resolutions to feed engineering models!!
In particular the NEXRAD products of the NWS that now provide “true spatial realizations of rainfall fields”
With historical and real time sources

## Slide 49: NEXRAD data
NOAA’s Weather and Climate Toolkit (JAVA viewer)
  http://www.ncdc.noaa.gov/oa/wct/
West Gulf River Forecast Center
  http://www.srh.noaa.gov/wgrfc/
National Weather Service Precipitation Analysis
  http://www.srh.noaa.gov/rfcshare/precip_analysis_new.php