## Slide 1: Excess Rainfall
Reading for today’s material: Sections 5.3-5.8

## Slide 2: Excess rainfall
Rainfall that is neither retained on the land surface nor infiltrated into the soil
Graph of excess rainfall versus time is called excess rainfall hyetograph
Direct runoff = observed streamflow - baseflow
Excess rainfall = observed rainfall - abstractions
Abstractions/losses – difference between total rainfall hyetograph and excess rainfall hyetograph

## Slide 3: f-index
f-index: Constant rate of abstraction yielding excess rainfall hyetograph with depth equal to depth of direct runoff
Used to compute excess rainfall hyetograph when observed rainfall and streamflow data are available

## Slide 4: f-index method
Goal: pick Dt, and adjust value of M to satisfy the equation
Steps
  Estimate baseflow
  DRH = streamflow hydrograph – baseflow
  Compute rd, rd = Vd/watershed area
  Adjust M until you get a satisfactory value of f
  ERH = Rm - fDt

## Slide 5: Example
Time Observed
Rain Flow
in cfs
8:30 203
9:00 0.15 246
9:30 0.26 283
10:00 1.33 828
10:30 2.2 2323
11:00 0.2 5697
11:30 0.09 9531
12:00 11025
12:30 8234
1:00 4321
1:30 2246
2:00 1802
2:30 1230
3:00 713
3:30 394
4:00 354
4:30 303
No direct runoff until after 9:30
And little precip after 11:00
Have precipitation and streamflow data, need to estimate losses
Basin area A = 7.03 mi2

## Slide 6: Example (Cont.)
Estimate baseflow (straight line method)
  Constant = 400 cfs
baseflow

## Slide 7: Example (Cont.)
Calculate Direct Runoff Hydrograph
  Subtract 400 cfs
Total = 43,550 cfs

## Slide 8: Example (Cont.)
Compute volume of direct runoff
Compute depth of direct runoff

## Slide 9: Example (Cont.)
Neglect all precipitation intervals that occur before the onset of direct runoff (before 9:30)
Select Rm as the precipitation values in the 1.5 hour period from 10:00 – 11:30

## Slide 10: Example (Cont.)
fDt=0.27

## Slide 11: SCS method
Soil conservation service (SCS) method is an experimentally derived method to determine rainfall excess using information about soils, vegetative cover, hydrologic condition and antecedent moisture conditions
The method is based on the simple relationship that Pe = P - Fa – Ia
Pe is runoff depth, P is precipitation depth, Fa is continuing abstraction, and Ia is the sum of initial losses (depression storage, interception, ET)
Time
Precipitation

## Slide 12: Abstractions – SCS Method
In general
After runoff begins
Potential runoff
SCS Assumption
Combining SCS assumption with P=Pe+Ia+Fa
Time
Precipitation

## Slide 13: SCS Method (Cont.)
Experiments showed
So
Surface
  Impervious: CN = 100
  Natural: CN < 100

## Slide 14: SCS Method (Cont.)
S and CN depend on antecedent rainfall conditions
Normal conditions, AMC(II)
Dry conditions, AMC(I)
Wet conditions, AMC(III)

## Slide 15: SCS Method (Cont.)
SCS Curve Numbers depend on soil conditions
Group | Minimum Infiltration Rate (in/hr) | Soil type
A | 0.3 – 0.45 | High infiltration rates. Deep, well drained sands and gravels
B | 0.15 – 0.30 | Moderate infiltration rates. Moderately deep, moderately well drained soils with moderately coarse textures (silt, silt loam)
C | 0.05 – 0.15 | Slow infiltration rates. Soils with layers, or soils with moderately fine textures (clay loams)
D | 0.00 – 0.05 | Very slow infiltration rates. Clayey soils, high water table, or shallow impervious layer

## Slide 16: Example - SCS Method - 1
Rainfall: 5 in.
Area: 1000-ac
Soils:
  Class B: 50%
  Class C: 50%
Antecedent moisture: AMC(II)
Land use
  Residential
    40% with 30% impervious cover
    12% with 65% impervious cover
  Paved roads: 18% with curbs and storm sewers
  Open land: 16%
    50% fair grass cover
    50% good grass cover
  Parking lots, etc.: 14%

## Slide 17: Example (SCS Method – 1, Cont.)
 | Hydrologic Soil Group |  |  |  |  | 
 | B |  |  | C |  | 
Land use | % | CN | Product | % | CN | Product
Residential (30% imp cover) | 20 | 72 | 14.40 | 20 | 81 | 16.20
Residential (65% imp cover) | 6 | 85 | 5.10 | 6 | 90 | 5.40
Roads | 9 | 98 | 8.82 | 9 | 98 | 8.82
Open land: good cover | 4 | 61 | 2.44 | 4 | 74 | 2.96
Open land: Fair cover | 4 | 69 | 2.76 | 4 | 79 | 3.16
Parking lots, etc | 7 | 98 | 6.86 | 7 | 98 | 6.86
Total | 50 |  | 40.38 | 50 |  | 43.40
CN values come from Table 5.5.2

## Slide 18: Example (SCS Method – 1 Cont.)
Average AMC
Wet AMC

## Slide 19: Example (SCS Method – 2)
Given P, CN = 80, AMC(II)
Find: Cumulative abstractions and excess rainfall hyetograph
Time (hr) | Cumulative Rainfall (in) | Cumulative Abstractions (in) |  | Cumulative Excess Rainfall (in) | Excess Rainfall Hyetograph (in)
 | P | Ia | Fa | Pe | 
0 | 0 |  |  |  | 
1 | 0.2 |  |  |  | 
2 | 0.9 |  |  |  | 
3 | 1.27 |  |  |  | 
4 | 2.31 |  |  |  | 
5 | 4.65 |  |  |  | 
6 | 5.29 |  |  |  | 
7 | 5.36 |  |  |  | 

## Slide 20: Example (SCS Method – 2)
Calculate storage
Calculate initial abstraction
Initial abstraction removes
  0.2 in. in 1st period (all the precip)
  0.3 in. in the 2nd period (only part of the precip)
Calculate continuing abstraction
Time (hr) | Cumulative Rainfall (in)
 | P
0 | 0
1 | 0.2
2 | 0.9
3 | 1.27
4 | 2.31
5 | 4.65
6 | 5.29
7 | 5.36

## Slide 21: Example (SCS method – 2)
Cumulative abstractions can now be calculated
Time (hr) | Cumulative Rainfall (in) | Cumulative Abstractions (in) | 
 | P | Ia | Fa
0 | 0 | 0 | -
1 | 0.2 | 0.2 | -
2 | 0.9 | 0.5 | 0.34
3 | 1.27 | 0.5 | 0.59
4 | 2.31 | 0.5 | 1.05
5 | 4.65 | 0.5 | 1.56
6 | 5.29 | 0.5 | 1.64
7 | 5.36 | 0.5 | 1.65

## Slide 22: Example (SCS method – 2)
Cumulative excess rainfall can now be calculated
Excess Rainfall Hyetograph can be calculated
Time (hr) | Cumulative Rainfall (in) | Cumulative Abstractions (in) |  | Cumulative Excess Rainfall (in) | Excess Rainfall Hyetograph (in)
 | P | Ia | Fa | Pe | 
0 | 0 | 0 | - | 0 | 0
1 | 0.2 | 0.2 | - | 0 | 0
2 | 0.9 | 0.5 | 0.34 | 0.06 | 0.06
3 | 1.27 | 0.5 | 0.59 | 0.18 | 0.12
4 | 2.31 | 0.5 | 1.05 | 0.76 | 0.58
5 | 4.65 | 0.5 | 1.56 | 2.59 | 1.83
6 | 5.29 | 0.5 | 1.64 | 3.15 | 0.56
7 | 5.36 | 0.5 | 1.65 | 3.21 | 0.06

## Slide 23: Example (SCS method – 2)
Cumulative excess rainfall can now be calculated
Excess Rainfall Hyetograph can be calculated
Time (hr) | Cumulative Rainfall (in) | Cumulative Abstractions (in) |  | Cumulative Excess Rainfall (in) | Excess Rainfall Hyetograph (in)
 | P | Ia | Fa | Pe | 
0 | 0 | 0 | - | 0 | 0
1 | 0.2 | 0.2 | - | 0 | 0
2 | 0.9 | 0.5 | 0.34 | 0.06 | 0.06
3 | 1.27 | 0.5 | 0.59 | 0.18 | 0.12
4 | 2.31 | 0.5 | 1.05 | 0.76 | 0.58
5 | 4.65 | 0.5 | 1.56 | 2.59 | 1.83
6 | 5.29 | 0.5 | 1.64 | 3.15 | 0.56
7 | 5.36 | 0.5 | 1.65 | 3.21 | 0.06

## Slide 24: Time of Concentration
Different areas of a watershed contribute to runoff at different times after precipitation begins
Time of concentration
  Time at which all parts of the watershed begin contributing to the runoff from the basin
  Time of flow from the farthest point in the watershed
Isochrones: boundaries of contributing areas with equal time of flow to the watershed outlet

## Slide 25: Stream ordering
Quantitative way of studying streams. Developed by Horton and then modified by Strahler.
Each headwater stream is designated as first order stream
When two first order stream combine, they produce second order stream
Only when two streams of the same order combine, the stream order increases by one
When a lower order stream combines with a higher order stream, the higher order is retained in the combined stream