## Slide 1: Hydrologic Measurement
Precipitation
Evaporation
Streamflow
Channel Properties
Topography
GIS datasets
Reading: Applied Hydrology Chapter 6

## Slide 2: Hydrologic Measurement
Precipitation, Climate, Stream Gaging
Water Quality Sampling

## Slide 3: Precipitation Station
Tipping Bucket Raingage
  The gauge registers precipitation (rainfall) by counting small increments of rain collected.
  When rain falls into the funnel it runs into a container divided into two equal compartments by a partition
  When a specified amount of rain has drained from the funnel the bucket tilts the opposite way.
  The number and rate of bucket movements are counted and logged electronically.

## Slide 4: Tipping bucket rain gage

## Slide 5: Weather/climate station
Following variables are recorded
  Wind velocity/direction
  Rainfall
  Relative humidity and temperature
  Radiation

## Slide 6: Components of a weather station
Anemometer
Radiometer
Tipping bucket raingage
Relative humidity and temperature

## Slide 7: Precipitation (continued)
Snow Pillows
http://wsoweb.ladwp.com/Aqueduct/snow/pillow.htm

## Slide 8: Snow Pillows

## Slide 9: Evaporation pan

## Slide 10: Measuring streamflow

## Slide 11: Streamflow using a boat
Tag line

## Slide 12: Measurement at high flows
Using stream gaging cable car
From bridge

## Slide 13: Acoustic Doppler Current Profiler

## Slide 14: Schematic of a stilling well gaging station

## Slide 15: Pressure transducer gaging station

## Slide 16: Stream Flow Rate
Discharge at a cross-section
Water Surface
Depth
Averaged
Velocity
Height
above
bed
Velocity
Velocity profile in stream

## Slide 17: Example
Colorado River at Austin

## Slide 18: Example (Cont.)
Q = 3061 ft3/s
V = Q/A = 1.81 ft/s

## Slide 19: Rating Curve
It is not feasible to measure flow daily.
Rating curves are used to estimate flow from stage data
Rating curve defines stage/streamflow relationship
http://nwis.waterdata.usgs.gov/nwis/measurements/?site_no=08158000

## Slide 20: Water Watch
http://waterwatch.usgs.gov/new/

## Slide 21
http://www.drought.unl.edu/dm/archive.html

## Slide 22: Improvements from Senate Bill 2: Instream Flow requirements
Requires TPWD, TWDB, TCEQ to develop procedures for defining instream flow requirements
Implemented on priority study regions by 2010
Based on fish habitat analysis
Priority Study Regions
Guadalupe
San Antonio
Brazos
Trinity
Sabine

## Slide 23: Process Flowchart
Instream
Flow
Decision Making
Hydrodynamic
Model
Habitat
Descriptions
Habitat
Model
ArcGIS
SMS/RMA2
Data Collection and some statistics
Depth & velocity
Species groups
Criterion
Notes: This is just a flow chart of the process that I spoke in the last slide. We used SMS (Surface water modeling system) with RMA2 module for hydrodynamic modeling. From hydrodynamic modeling studies we get water depth and velocity for different flow-rates. For habitat descriptions, we collect data for different kind of fish species and since we cannot capture all the fishes that are available we used some confidence intervals. Once we have the hydraulic and biological data different criteria are developed. For example Fish of a particular type is found within a particular velocity and depth range. In ArcGIS you go through all the data and if you find a location that satisfy a particular criteria you assign some value to that location which will correspond to a particular fish type.

## Slide 24: Study Area (Guadalupe river near Seguin, TX)
1/2 meter Digital Ortho Photography
Notes: This is a DOQ of the study area which is near Seguin in Texas.

## Slide 25: Depth Sounder (Echo Sounder)
The electronic depth sounder operates in a similar way to radar It sends out an electronic pulse which echoes back from the bed. The echo is timed electronically and transposed into a reading of the depth of water.
Notes: The most important dataset for hydrodynamic modeling is the bathymetry data to define the channel bed. Depth sounder is used to find the water depth in the river channel. It shoots an electronic pulse into the water and depending on how much time it takes for the pulse to come back, it finds the water depth.

## Slide 26: Acoustic Doppler Current Profiler
Provides full profiles of water current speed and direction in the ocean, rivers, and lakes. Also used for discharge, scour and river bed topography.
Notes: Acoustic Doppler is used to find out the velocity. It uses the Doppler effect to measure current velocity by transmitting a short pulse of sound, listening to its echo and measuring the change in pitch or frequency of the echo.
Doppler Effect
You hear the Doppler effect whenever a train passes by - the change in pitch you hear tells you how fast the train is moving. The Aquadopp uses the Doppler effect to measure current velocity by transmitting a short pulse of sound, listening to its echo and measuring the change in pitch or frequency of the echo.

## Slide 27: Measurement System
GPS Antenna
Depth Sounder
Computer and power setup
Notes: This the final set-up. You can see that the depth sounder is attached to the GPS. So when the depth sounder shoots a pulse we get z for that point and the GPS gives the (x,y) location and so we get (x,y,z) for all the data points. The next slide that I’m going to show is prepared in ArcScene. You can see how we can produce some really cool stuff in ArcScene.

## Slide 28: Channel Bed Soundings
Notes: This slide shows the DOQ with the bathymetry data overlapped on top of it. The red dots are the bathymetry points.

## Slide 29: Bathymetry from Side-Scanning Sonar
Channel demo

## Slide 30: National Elevation Dataset
Digital Elevation Model with 1 arc-second (30m) cells
Seamless in 1° blocks for the United States
10 billion data
Derived from USGS 1:24,000 quadrangle sheets
http://seamless.usgs.gov/
Get the data:
http://ned.usgs.gov/

## Slide 31: Digital Elevation Model (DEM)
Contours
720
700
680
740
680
700
720
740
720
720

## Slide 32: Austin West 30 Meter DEM

## Slide 33
32
16
8
64
4
128
1
2
Eight Direction Pour Point Model
Water flows in the direction of steepest descent

## Slide 34: Flow Direction Grid
32
16
8
64
4
128
1
2

## Slide 35: Delineation of Streams and Watersheds on a DEM

## Slide 36: Watersheds of the US
2-digit water resource regions
8-digit HUC watersheds

## Slide 37: Hydrologic Unit Code Watersheds
~ 2000 for US, about the size of counties

## Slide 38: LIDAR surveying
LIDAR (Light Detection and Ranging; or Laser Imaging Detection and Ranging) is a technology that determines distance to an object or surface using laser pulses. Like the similar radar technology, which uses radio waves instead of light, the range to an object is determined by measuring the time delay between transmission of a pulse and detection of the reflected signal.

## Slide 39
3-D detail of the Tongue river at the WY/Mont border from LIDAR.
Roberto Gutierrez
University of Texas at Austin

## Slide 40
http://srtm.usgs.gov/

## Slide 41: HydroSheds derived from SRTM
http://hydrosheds.cr.usgs.gov/

## Slide 43
River networks
for 8-digit HUC
watersheds
http://nhd.usgs.gov/

## Slide 45
Lower West Fork, Trinity River Basin
HUC = 12030102

## Slide 46
http://www.horizon-systems.com/nhdplus/

## Slide 47: NHDPlus for a Portion of Oregon
http://www.horizon-systems.com/nhdplus/

## Slide 48: NHDPlus Reach Catchments ~ 3km2
About 1000 reach catchments in each 8-digit HUC
Average reach length = 2km
2.3 million reaches for continental US

## Slide 49
http://www.ncgc.nrcs.usda.gov/products/datasets/statsgo/
1:250,000 Scale Soil Information

## Slide 51: Ssurgo for Travis County
103 soil map units described by 7530 polygons of average area 35.37 ha (87 acres)

## Slide 52: National Land Cover Dataset
http://seamless.usgs.gov/
Get the data: