## Slide 1: CE 394K.2 Mass, Momentum, Energy
Begin with the Reynolds Transport Theorem
Mass – continuity equation
Momentum – Manning and Darcy eqns
Energy – conduction, convection, radiation
Reading: Applied Hydrology Sections 2.3 to 2.8

## Slide 2: Reynolds Transport Theorem
Total rate of change of B in the fluid system
Rate of change of B stored in the control volume
Net outflow of B across the control surface

## Slide 3: Continuity Equation
B = m; b = dB/dm = dm/dm = 1; dB/dt = 0 (conservation of mass)
r = constant for water
or
hence

## Slide 4: Continuous and Discrete time data
Continuous time representation
Sampled or Instantaneous data
(streamflow)
truthful for rate, volume is interpolated
Pulse or Interval data
(precipitation)
truthful for depth, rate is interpolated
Figure 2.3.1, p. 28 Applied Hydrology
Can we close a discrete-time water balance?
http://waterservices.usgs.gov/nwis/iv?sites=08158000&period=P7D&parameterCd=00060

## Slide 6: Momentum
B = mv; b = dB/dm = dmv/dm = v; dB/dt = d(mv)/dt = SF (Newtons 2nd Law)
so
For steady flow
For uniform flow
In a steady, uniform flow

## Slide 7: Surface and Groundwater Flow Levels are related to Mean Sea Level
Earth surface
Ellipsoid
Sea surface
Geoid
Mean Sea Level is a surface of constant
gravitational potential called the Geoid

## Slide 8
http://www.csr.utexas.edu/ocean/mss.html

## Slide 9: GRACE Mission Gravity Recovery And Climate Experiment
http://www.csr.utexas.edu/grace/
Creating a new map of the earth’s gravity field every 30 days
http://www.csr.utexas.edu/grace/gallery/animations/measurement/measurement_qt.html
Water Mass of Earth

## Slide 10: Vertical Earth Datums
A vertical datum defines elevation, z
NGVD29 (National Geodetic Vertical Datum of 1929)
NAVD88 (North American Vertical Datum of 1988)
takes into account a map of gravity anomalies between the ellipsoid and the geoid

## Slide 11: Energy equation of fluid mechanics
Datum
z1
y1
bed
water
surface
energy
grade line
hf
z2
y2
L
How do we relate friction slope,
to the velocity of flow?

## Slide 12: Open channel flow Manning’s equation
Channel Roughness
Channel Geometry
Hydrologic Processes
(Open channel flow)
Physical environment
(Channel n, R)
Hydrologic conditions
(V, Sf)

## Slide 13: Subsurface flow Darcy’s equation
Hydraulic conductivity
Hydrologic Processes
(Porous medium flow)
Physical environment
(Medium K)
Hydrologic conditions
(q, Sf)
A
q
q

## Slide 14: Comparison of flow equations
Open Channel Flow
Porous medium flow
Why is there a different power of Sf?

## Slide 15: Energy
B = E = mv2/2 + mgz + Eu; b = dB/dm = v2/2 + gz + eu;
dE/dt = dH/dt – dW/dt (heat input – work output) First Law of Thermodynamics
Generally in hydrology, the heat or internal energy component
(Eu, dominates the mechanical energy components (mv2/2 + mgz)

## Slide 16: Heat energy
Energy
  Potential, Kinetic, Internal (Eu)
Internal energy
  Sensible heat – heat content that can be measured and is proportional to temperature
  Latent heat – “hidden” heat content that is related to phase changes

## Slide 17: Energy Units
In SI units, the basic unit of energy is Joule (J), where 1 J = 1 kg x 1 m/s2
Energy can also be measured in calories where 1 calorie = heat required to raise 1 gm of water by 1°C and 1 kilocalorie (C) = 1000 calories (1 calorie = 4.19 Joules)
We will use the SI system of units

## Slide 18: Energy fluxes and flows
Water Volume [L3] (acre-ft, m3)
Water flow [L3/T] (cfs or m3/s)
Water flux [L/T] (in/day, mm/day)
Energy amount [E] (Joules)
Energy “flow” in Watts [E/T] (1W = 1 J/s)
Energy flux [E/L2T] in Watts/m2
Energy flow of
1 Joule/sec
Area = 1 m2

## Slide 19: MegaJoules
When working with evaporation, its more convenient to use MegaJoules, MJ (J x 106)
So units are
  Energy amount (MJ)
  Energy flow (MJ/day, MJ/month)
  Energy flux (MJ/m2-day, MJ/m2-month)

## Slide 20: Internal Energy of Water
Heat Capacity (J/kg-K) Latent Heat (MJ/kg)
Ice 2220 0.33
Water 4190 2.5
Ice
Water
Water vapor
Water may evaporate at any temperature in range 0 – 100°C
Latent heat of vaporization consumes 7.6 times the latent heat of fusion (melting)
2.5/0.33 = 7.6

## Slide 21: Water Mass Fluxes and Flows
Water Volume, V [L3] (acre-ft, m3)
Water flow, Q [L3/T] (cfs or m3/s)
Water flux, q [L/T] (in/day, mm/day)
Water mass [m = rV] (Kg)
Water mass flow rate [m/T = rQ] (kg/s or kg/day)
Water mass flux [M/L2T = rq] in kg/m2-day
Water flux
Area = 1 m2

## Slide 22: Latent heat flux
Water flux
  Evaporation rate, E (mm/day)
Energy flux
  Latent heat flux (W/m2), Hl
Area = 1 m2
r = 1000 kg/m3
lv = 2.5 MJ/kg
28.94 W/m2 = 1 mm/day

## Slide 23: Radiation
Two basic laws
  Stefan-Boltzman Law
    R = emitted radiation (W/m2)
    e = emissivity (0-1)
    s = 5.67x10-8W/m2-K4
    T = absolute temperature (K)
  Wiens Law
    l = wavelength of emitted radiation (m)
Hot bodies (sun) emit short wave radiation
Cool bodies (earth) emit long wave radiation
All bodies emit radiation

## Slide 24: Net Radiation, Rn
Ri Incoming Radiation
Ro =aRi Reflected radiation
= albedo (0 – 1)
Rn Net Radiation
Re
Average value of Rn over the earth and
over the year is 105 W/m2

## Slide 25: Net Radiation, Rn
Rn Net Radiation
Average value of Rn over the earth and
over the year is 105 W/m2
G – Ground Heat Flux
LE – Evaporation
H – Sensible Heat

## Slide 26: Energy Balance of Earth
http://www.uwsp.edu/geo/faculty/ritter/geog101/textbook/energy/radiation_balance.html
6
4
100
70
51
21
26
38
6
20
15
Sensible heat flux 7
Latent heat flux 23
19

## Slide 27: Net Radiation
Mean annual net radiation over the earth and over the year is 105 W/m2
http://geography.uoregon.edu/envchange/clim_animations/flash/netrad.html