## Slide 1: Assessment of Economic Benefits of the North Carolina Floodplain Mapping Program Hydrologic and Hydraulic Case Studies
Adapted from a Presentation to NRC Committee on FEMA Flood Maps January 14, 2008
by Thomas Langan, P.E., CFM
North Carolina Floodplain Mapping Program
Notes: test

## Slide 2: Purpose
Assess impacts to 100-yr water surface elevations (WSELs) and special flood hazard areas boundaries by changing:
  Physiographic region
  Hydrologic modeling methodology
  Hydraulic study type (Primary Goal)
  Topographic data source

## Slide 3: Site Selection Criteria
Physiographic Regions – Coastal, Piedmont, Mountains
  Should be in or near County w/ GIS building footprints
Hydrologic Methodology
  All locations should have stream gage
  One County with a rainfall runoff model
  Suburban/Rural land use
Hydraulic Study Type
  Existing detail study (DS) HEC-RAS model
    20 years of peak and average daily discharge record
Topography
  NC LiDAR or Equivalent Accuracy (2 ½ -ft contour)

## Slide 5
Length (mi) | 7.1
XSs | 80
Average XS Spacing | 472
Structures | 6
US Drainage Area (mi2) | 60
DS Drainage Area (mi2) | 136 (7545 cfs)

## Slide 6
Length (mi) | 5.7
XSs | 66
Average XS Spacing | 459
Structures | 4
US Drainage Area (mi2) | 8
DS Drainage Area (mi2) | 32 (4394 cfs)

## Slide 7
Length (mi) | 4.8
XSs | 59
Average XS Spacing | 496
Structures | 9
US Drainage Area (mi2) | 108
DS Drainage Area (mi2) | 133 (19710 cfs)

## Slide 8: Analytical Approach
Hydrologic Methodology
Hydraulic Study Type
Topography
Statistics
Hydraulics
Hydrology
Floodplain Mapping
Physiographic Region
Variables
Analyses

## Slide 9: Hydrologic Methodology
Flow estimate methods
  Rainfall-runoff (RR) – HEC-1 or HEC-HMS
  LPIII Weighted Adjusted Regional Regression (ADJREG)
  Rural Regional Regression (REG)
    Upper and Lower Limit of the Standard Error of Prediction of Regional Regression (REGUP & REGLOW) (+/- 42% Coast, Piedmont, Mountains - +/- 47%)
Parameters varied for only DS model runs and for 100-yr return period

## Slide 10: USGS Regional Regression Equations
For a 100 square mile drainage area, the 100-year flood discharge estimate is
13,250 cfs in the Blue Ridge-Piedmont,
6340 cfs in the coastal plain,
3400 cfs in the Sand Hills.
Blue Ridge - Piedmont
Sand Hills
Coastal Plain
95% Confidence interval is
+/- 42-47% of the estimated flow

## Slide 11
14-ft
WSEL
Downstream
Bottom of Bridge Deck

## Slide 13
15-ft

## Slide 15
19-ft

## Slide 17: Conclusions
All hydrologic methods are calibrated to results from frequency analysis at USGS gages so gage analysis drives results
Main effect is produced by stretching USGS regression equation results out to their limits (not realistic actually)
Varying hydrologic methods changes elevation by 1-2 ft

## Slide 18: Analytical Results Water Surface Elevation Profiles Hydraulic Study Type

## Slide 20
Changes SFHA

## Slide 25: Conclusions
Uncertainty induced by changing the terrain data dominates other hydraulic model uncertainties
There is a huge effect of terrain data uncertainty in the in the Long Creek example in Charlotte, NC
  Floodplain derived from the LIDAR data is underground when viewed on the National Elevation Dataset!