## Slide 1: CE 397 Flood Forecasting
University of Texas at Austin (David Maidment)
and University of Alabama (Andy Ernest)
Spring Semester, 2015
Lecture 1: Introduction to the National Flood Interoperability Experiment

## Slide 2
Inaugural Meeting – May, 2014
Proposal for National Flood Interoperability Experiment

## Slide 3: Nationally Synthesize Operations of Regional River Forecast Centers

## Slide 4: National Flood Interoperability Experiment (NFIE)
Will be led by the academic community coordinated by CUAHSI in collaboration with the IWRSS partners through the National Water Center
Run from September 2014 to August 2015
  Preparatory phase to May 2015
  Summer Institute at the National Water Center, June 1 to July 17 2015

## Slide 5: Technical Readiness Levels
The NFIE is a research effort
It will not create an operational system
It will not produce public forecast information
NFIE
http://en.wikipedia.org/wiki/Technology_readiness_level

## Slide 6: NFIE Goal: Connect National Scale Flood Modeling with Local emergency planning and response
How can near-real-time hydrologic simulations at high spatial resolution, covering the nation, be carried out using the NHDPlus or next generation hydro-fabric (e.g. data structure for hillslope, watershed scales)?
How can this lead to improved emergency response and community resilience?
How can an improved interoperability framework support the first two goals and lead to sustained innovation in the research to operations process?
Slide: Ed Clark, NWS

## Slide 7: National Flood Interoperability Experiment (NFIE): Five Components
NFIE-Services: Web services for flood information
NFIE-Geo: National geospatial framework for hydrology
NFIE-Hydro: National high spatial resolution hydrologic forecasting
NFIE-River: River channel information and real-time flood inundation mapping
NFIE-Response: Wide area planning for flood emergency response

## Slide 8: National Flood Interoperability Experiment (NFIE) Component One: NFIE-Geo
NFIE-Services: Web services for flood information
NFIE-Geo: National geospatial framework for hydrology
NFIE-Hydro: National high spatial resolution hydrologic forecasting
NFIE-River: River channel information and real-time flood inundation mapping
NFIE-Response: Wide area planning for flood emergency response

## Slide 9: NHDPlus Version 2
National Elevation Dataset
National Hydrography Dataset
National Land Cover Dataset
Watershed Boundary Dataset
NHDPlus
Geospatial foundation for a national water data infrastructure
2.67 million reach catchments in US
average area 3 km2
reach length 2 km

## Slide 10: NFIE-Geo for National Flood Interoperability Experiment
Enhanced geospatial database for a national water data infrastructure
NWS Basins and
Forecast Points
USGS Water Watch
Points
National Flood
Hazard Layer
NHDPlus
Feature classes:
Subwatershed (HUC12) Catchment
Flowline
Waterbody Dam
NFIE-Geo
9 feature classes
5 from NHDPlus
4 from IWRSS

## Slide 11: NHDPlus Reach Catchments and Subwatersheds
Each reach catchment has a single flow line
Uniquely labeled across the nation
Flood hazard zone defined by FEMA map
Catchment 5781369
HUC12 Subwatershed
Contains reach catchments
Base for Hydrologic modeling
and flood emergency response planning
Reach Catchment
Subwatershed

## Slide 12: NFIE-Geo in HydroShare
https://www.arcgis.com/home/webmap/viewer.html?webmap=2c30160429984a59873f26b9d118dbfe
David Tarboton, Utah State Univ
and Ray Idaszak, RENCI

## Slide 13
Need workflow here
HydroTerre: A Service for HUC12 Data Access
GSSURGO
Lorne Leonard and Chris Duffy
200 TB of information

## Slide 14
www.HydroTerre.psu.edu: Interface
Leonard, L., C. Duffy. 2013. Essential Terrestrial Variable data workflows for distributed water resources modeling,
Environmental Modelling & Software, 50, p. 85-96
200 TB of information

## Slide 15
HydroTerre: A Prototype fo Model-Data Access
Land Parcel Data; NHD: Stream, Lake, HUC’; USDA: Soils/Crops; NLCD: LU_LC;

## Slide 16
Need workflow here
HydroTerre: A Prototype Model-Data Workflow
Produce new hydrologic models at HUC12 scale

## Slide 17
Penn State Integrated Hydrolgic Model

## Slide 18
Xuan Yu Watershed Modeling with PIHM

## Slide 19: National Flood Interoperability Experiment (NFIE) Component Two: NFIE-Hydro
NFIE-Services: Web services for flood information
NFIE-Geo: National geospatial framework for hydrology
NFIE-Hydro: National high spatial resolution hydrologic forecasting
NFIE-River: River channel information and real-time flood inundation mapping
NFIE-Response: Wide area planning for flood emergency response

## Slide 20: Overarching WRF-Hydro Scientific Objectives (David Gochis, NCAR)
A community-based, supported coupling architecture designed to provide:
An extensible multi-scale & multi-physics land-atmosphere modeling capability for conservative, coupled and uncoupled assimilation & prediction of major water cycle components such as precipitation, soil moisture, snowpack, groundwater, streamflow, inundation
Streamflow prediction across scales (from 0-order headwater catchments to continental river basins & minutes to seasons)
A robust framework for land-atmosphere coupling studies

## Slide 21
Notes: Remember that LSM is only req’d when run ‘offline’, when run ‘coupled’ the land model with the atmo model can be used….

## Slide 22: Modeling of Weather, Hydrology, River Flow in WRF-Hydro
Observations Datasets, Numerical Weather Model
Land Surface Model
Forcing:
Radiation
Precipitation
Surface climate
Evaporation
Soil Moisture
Runoff
Recharge
Soil
Vegetation
Terrain
RAPID: River Routing on NHDPlus
Network River Flow

## Slide 23: WRF-Hydro and RAPID
NWS River Forecasts
WRF-Hydro Model
NHDPlus to
RAPID Conversion
Grid to Catchment Linking
Forecast services
Completed
Pending
NFIE-Hydro

## Slide 24: Soil Moisture Map (mm water in top 1 m of soil from NASA Land Data Assimilation System)
Map is created each day using NASA services
http://statsnldas.azurewebsites.net/
Include forecast soil moisture in NFIE

## Slide 25: Soil Moisture Anomaly Map (current value – mean for calendar day at each spatial point)
Map is created each day using NASA services
http://statsnldas.azurewebsites.net/

## Slide 26: Soil Moisture Percentile Map
http://statsnldas.azurewebsites.net/
Current value expressed as a percentile based on historical data [1979 to present] on this calendar day at this spatial point
Compare present soil moisture with past conditions

## Slide 27
European Center for Medium Range Weather Forecasting and European Joint Research Commission
15 Day ahead forecast ensemble (50 hydrographs) at each location

## Slide 28: Hydrologic Forecasting for the Texas-Gulf Region (from Brigham Young University)
http://demo.tethys.ci-water.org/
(67,313 NHDPlus reaches)
Source: Jim Nelson, BYU

## Slide 29: 50 Ensemble Forecasts
Source: Jim Nelson, BYU

## Slide 30: Ensemble Flow Forecast for Reach Catchment 5592208 made on Jan 13, 2015 (15 day horizon) Weather information source: European Center for Medium Range Weather Forecasting (ECMWF). Summary statistics compiled from 50 forecast hydrographs
Source: Jim Nelson, BYU

## Slide 31: National Flood Interoperability Experiment (NFIE) Component Three: NFIE-River
NFIE-Services: Web services for flood information
NFIE-Geo: National geospatial framework for hydrology
NFIE-Hydro: National high spatial resolution hydrologic forecasting
NFIE-River: River channel information and real-time flood inundation mapping
NFIE-Response: Wide area planning for flood emergency response

## Slide 32: Real-Time Flood Inundation Mapping (USGS/NWS)
http://water.weather.gov/ahps2/inundation/inundation_google.php?gage=atit2

## Slide 33
Gage is here
Another Gage up here
Another Gage down here…
Slide: Ken Ashe, NCFMP
Big gaps in flood inundation mapping between gages need to be filled in

## Slide 34
North Carolina Floodplain Mapping Program HEC- RAS Models
  5 Recurrence Intervals: 10, 25, 50, 100, 500
  300,000 cross-sections
  Each cross-section has a rating curve
Slide: Ken Ashe, NCFMP

## Slide 35: Our cross-sections give the ability to interpolate between gages expanding the real time information from ~200 locations to 10s of thousands to 100s of thousand of locations
Slide: Ken Ashe, NCFMP

## Slide 36: The Texas NHDPlus network looks complicated...
...with 105 river reaches.
Slide: Ben Hodges

## Slide 37: But silicon microchips can have a billion (109) or more transistors.
Electrical engineers routinely solve huge nonlinear circuit network problems during chip design.
Slide: Ben Hodges

## Slide 38: We don’t have to simplify!
Solve the full, nonlinear, unsteady, dynamic Saint-Venant equations (1D)
Diffusive Wave
Kinematic Wave
Slide: Ben Hodges

## Slide 39: SPRNT Simulation Program for River NeTworks
Using ideas from computer chip design for river network analysis for fast solution
Frank Liu
IBM Research Austin
Ben R. Hodges
Univ. of Texas at Austin
Slide: Ben Hodges

## Slide 40: We can solve the complete river network, ... but we need river geometry:
- cross-section area vs. depth
- cross-section perimeter vs. depth
- river bottom slope
- channel roughness
Slide: Ben Hodges

## Slide 41: Cross-sections from HEC-RAS models
Travis County
Hayes County
Onion Creek watershed
We need a national repository -- use HydroShare
Map: Xing Zheng
Data Source: City of Austin

## Slide 42: National Flood Interoperability Experiment (NFIE) Component Four: NFIE-Response
NFIE-Services: Web services for flood information
NFIE-Geo: National geospatial framework for hydrology
NFIE-Hydro: National high spatial resolution hydrologic forecasting
NFIE-River: River channel information and real-time flood inundation mapping
NFIE-Response: Wide area planning for flood emergency response

## Slide 43: Link with the First Response Community
https://www.youtube.com/watch?v=ympaR6YUxiA&feature=youtube
Harry Evans, Chief of Staff Austin Fire Department
Responsible for flood emergency response in Austin

## Slide 44: Address Points -- used for directing emergency response vehicles
All legal residences have an address point
Established when the lot is legally platted and registered with the county

## Slide 45: Address Points and the Flood Hazard Zone
495,000 Address points in the two counties
How many points are in the flood hazard zone?
Where are the high flood risk areas in these counties?
Travis County
Williamson County
Austin, Texas

## Slide 46: Address Points and the Floodplain

## Slide 47: Address Points in the Floodplain
Floodpoints
Address Points in Floodplain of Onion Creek

## Slide 48: Address Points in Floodplain of a Subwatershed
Number of Address Points in the Floodplain
A total of 12,052 address points are in the floodplain out of 495,468 in the study region (2.5%)

## Slide 49: Address Points and Roads in Floodplain of Onion Creek

## Slide 50: Length of Roads in Floodplain of a Subwatershed
Length of Roads in Floodplain (Km)
A total of 711 km of roads are in the floodplain out of 14,732 km in the study region (4.8%)

## Slide 51: National Flood Interoperability Experiment (NFIE) Component Five: NFIE-Services
NFIE-Services: Web services for flood information
NFIE-Geo: National geospatial framework for hydrology
NFIE-Hydro: National high spatial resolution hydrologic forecasting
NFIE-River: River channel information and real-time flood inundation mapping
NFIE-Response: Wide area planning for flood emergency response

## Slide 52: WaterML Web Services – CUAHSI, USGS, OGC, WMO …..
Water time series data on the internet
24/7/365 service
For daily and real-time data
. . . Operational water web services system for the United States
http://waterservices.usgs.gov/nwis/iv/?format=waterml,2.0&sites=08158000&period=P1D&parameterCd=00060

## Slide 53: Develop NWS Experimental Data Services
NWS CHPS Modeling Units: RFCs
Export Data elements from the simulation& forecast workflow including:
Inflow to the Channel (INFW)
Mean Areal Precipitation (MAP)
Streamflow (QINE) at ~3600 points
PI-XML to WaterML22
netCDF
to
NHD+
Data Services – local runoff
Experimental WRF-Hydro 1
1Responsibility of NCAR
Slide: Ed Clark, NWS

## Slide 54: NFIE: NWS Project ‘Elements’ or Functional Requirements
Acquire data from 13 CHPS Instances
  Establish hosting system – central FEWS data server at UoA
  Develop and implement extraction workflow (Based on WGRFC Export example)
  Develop and implement transmission capability – SFTP to UoA
Serve (make data available) constituent CHPS elements
  Publish geospatial--topology relationship corresponding to the time-series identifiers in CHPS extracted data sets1 (metadata)
  Data reformatting to WaterML22
  Provide access to CHPS data and metadata sets (data service)1
  Develop data service monitoring capability (TBD via NWC)
Support Data Service through Aug 2015.
  Monitor & maintain
1on going through OWDI
2 Via UoA FEWS-WaterML2-SOAP service
Slide: Ed Clark, NWS

## Slide 55: Align forecasts with those produced by regional NWS modeling
Color the reach catchment according to flood risk for all the reach catchments in the region
Produce a color-coded flood risk map service for a region

## Slide 56: Conclusions
NFIE-Geo is really solid
NFIE-Hydro is a work in progress but is achievable at the Summer Institute
NFIE-River has good input information in some regions but needs national structure and data
NFIE-Response needs further development
NFIE-Services are just beginning
Your contribution to advance these components is very welcome!!