## Slide 1: GeoNet: An automatic tool for channel network and channel head extraction from digital terrain data
Harish Sangireddy, Anna Kladzyk, Richard Carothers, and Paola Passalacqua

## Slide 2: https://sites.google.com/site/geonethome/

## Slide 3: History of GeoNet
GeoNet 1.0 (released beginning 2010)
  Paola Passalacqua
  Tien Do Trung (Ecole Normale Superieure de Cachan)
  Efi Foufoula-Georgiou (Univ. of Minnesota)
  Guillermo Sapiro (Univ. of Minnesota)
  Bill Dietrich (UC Berkeley)
  NSF Grants: EAR-0835789; EAR-0120914
GeoNet 1.0.1 (released September 2010)
  Paola Passalacqua
  Colin Stark (Columbia Univ.)
  Nachiket Gokhale (Univ. of Minnesota)
  Efi Foufoula-Georgiou (Univ. of Minnesota)
  Guillermo Sapiro (Univ. of Minnesota)
  Bill Dietrich (UC Berkeley)
  NSF Grants: BCS-1063231/1063228; EAR-0120914
GeoNet 2.0 (released November 2011)
  Paola Passalacqua
  Colin Stark
  Harish Sangireddy
GeoNet 2.1 (released Nov 2012)
Paola Passalacqua
Harish Sangireddy
GeoNet 2.0 and 2.1 (gdal) (May 2013)
Harish Sangireddy
Paola Passalacqua
PyGeoNet 1.0 ( November 2014)
Harish Sangireddy
Paola Passalacqua

## Slide 4: Workflow of GeoNet

## Slide 5: Workflow of GeoNet: Input DEM
GeoNet requires a bare earth lidar Digital Elevation Model (DEM)
  UTM projections are preferred and recommended.
Data sources of Lidar DEMs
  NCALM (National center for Airborne Laser Mapping) (http://ncalm.cive.uh.edu/ )
  OpenTopography (http://www.opentopography.org/index.php)
  USGS Click (http://lidar.cr.usgs.gov/ )
  Various State Agencies e.g. TNRIS (https://tnris.org/maps-and-data/)
  Interagency elevation Inventory (http://coast.noaa.gov/inventory/ )

## Slide 6: United States Interagency Elevation Inventory

## Slide 7: Important user-defined parameters
Filtering iterations
Flow accumulation area threshold
Search box size

## Slide 8: Workflow of GeoNet: Non linear Filtering: a critical step when using lidar data
  Errors in the representation of the landscape can be introduced several ways:
    Acquisition
    Preprocessing
    Point cloud classification

## Slide 9: Workflow of GeoNet: Filter Type Comparisons
Gaussian
Perona-Malik
Images: Passalacqua et al., 2010, DOI: 10.1029/2009JF001254 (top) Pelletier, 2013, DOI: 10.1029/2012WR012452 (bottom)
Nonlinear diffusion equation:

## Slide 10: Workflow of GeoNet: Filtering iterations
Filtering iterations impacts amount of noise reduction
What is the suggested number of filtering iterations?
50 iterations
200 iterations

## Slide 11: Workflow of GeoNet: Filtering iterations
What is the suggested number of filtering iterations?
  If the unknown noise ‘n’ is uncorrelated to the unknown signal F, it would be reasonable to minimize the covariance of the noise (u(0) – u(t)) with the signal u(t), or better employed in a normalized form, the correlation coefficient.
  The stopping time T (~ number of iterations) minimizes the correlation coefficient.
Mrázek, Pavel, and Mirko Navara. "Selection of optimal stopping time for nonlinear diffusion filtering." International Journal of Computer Vision 52.2-3 (2003): 189-203.

## Slide 12: Workflow of GeoNet: Filtering iterations
Number of iterations
Number of iterations
Correlation Coefficient
Correlation Coefficient
gradient of Correlation Coefficient
T ~ 25 iterations
T ~ 45 iterations
gradient of Correlation Coefficient
These results are shown for the Tennessee Valley, CA dataset

## Slide 13: Workflow of GeoNet: Filtering iterations
The Perona Malik conductance function (1) involving exponential function decreases much faster than the (2)
The first function prefers high contrast edges over low contrast ones
The second function prefers larger-scale edges (channel banks) to very small-scale edges (rocks).
By default GeoNet uses equation (2) as the function prefers wide regions over smaller ones
‘’ – the edge threshold is set to the 90th quantile of the slope values in the landscape.
  (Perona, Pietro, and Jitendra Malik. "Scale-space and edge detection using anisotropic diffusion." Pattern Analysis and Machine Intelligence, IEEE Transactions on 12.7 (1990): 629-639.)
-- (1)
-- (2)

## Slide 14: Workflow of GeoNet: Identification of likely channelized pixels
Ridges
Channels
Diffusive portion of the landscape
Geometric curvature

## Slide 15: Channel network extraction and bridge crossings (advantages)
By using Laplacian curvature, we can avoid the detection of roads and bridges in the skeleton map of likely channelized pixels
Indian Creek, OH

## Slide 16: Workflow of GeoNet: Identification of likely channelized pixels
divergent
planar
convergent
Clean the curvature threshold skeleton by using a small flow threshold determined from slope area plots

## Slide 17: Workflow of GeoNet: Identification of likely channelized pixels
Flow routing
D-infinity algorithm
Tells us the total number of cells which flow into a cell
Allows for flow divergence (flow can be directed into one or two neighboring cells depending on flow direction)
Image: Tarboton, 1997. http://www.neng.usu.edu/cee/faculty/dtarb/dinf.pdf

## Slide 18: Workflow of GeoNet: Geodesics and cost function
a
b
Channel head
Basin outlet
Geodesic curves
channel
Passalacqua et al. [2010] defined the cost function as a combination of surface curvature and flow accumulation area.
Geodesics are defined as curves of minimal cost among all the possible paths that connect two points a and b.

## Slide 19: Workflow of GeoNet: Geodesics and cost function
Fast Marching Algorithms are used to compute the geodesic distance by using the cost function for each of the outlets (identified as green dots).
The outlets are the starting point, and the draining basin is the region the fast marching can be done.
Big advantage: global operation using local information

## Slide 20: Workflow of GeoNet: channel head detection
The skeleton is not connected continuously
Each connected component is labeled
A histogram of the number of connected components is prepared and all components less than a small threshold are removed from the skeleton. This removes isolated skeleton pixels.

## Slide 21: Workflow of GeoNet: channel head detection
The hillslope length for each pixel is estimated and the median hillslope length is determined.
This median hillslope length is set as the search box size for finding channel heads.
Pixels with maximum geodesic distance and belonging to a particular connected component are identified as the channel heads.

## Slide 22: Workflow of GeoNet: Discrete Geodesics
Using the geodesic distance we do a gradient descent from channel heads to the outlet.
The map shows the comparison of the drainage network extracted by GeoNet against the digitized channel network by Montgomery and Dietrich 1989 for the Tennessee Valley basin, CA.

## Slide 23: Suggestions for parameters
Filtering iterations: 50
Start with a small source area: ~ 50 m^2
(resolution dependent)
Search box: the median hillslope length
***As of version 2.1.1 this is automatic

## Slide 24: Original xSection Extraction
GeoNet extracts geodesic skeleton
Strikes xSections based on chosen parameters along longest centerline

## Slide 25: Original xSection Extraction
GeoNet extracts geodesic skeleton
Strikes xSections based on chosen parameters along longest centerline
Channel “banks” chosen based on maximum slope

## Slide 26: Challenges with Current Methodology
Relies on GeoNet extracted centerline, thus subject to processing limitations of larger program
Without mapping toolbox, skeleton, bank locations, etc exported as geotiff

## Slide 27: Adapted methodology
For research purposes, GeoNet’s bank location feature was adapted for user input centerlines

## Slide 28: Adapted methodology
For research purposes, GeoNet’s bank location feature was adapted for user input centerlines
Same general methodology used for channel bank identification

## Slide 29: Adapted methodology
For research purposes, GeoNet’s bank location feature was adapted for user input centerlines
Same general methodology used for channel bank identification
Banks locations output as a csv to facilitate GIS interface

## Slide 30: Generalizing the method further for NHD incorporation
Want to be able to extract cross sections from just the NHD and a DEM
Developed a model in ArcGIS preprocess the NHD and DEM and postprocess the csv results

## Slide 31: Generalizing the method further for NHD incorporation
Test study on San Antonio river basin section

## Slide 32: Generalizing the method further for NHD incorporation
Test study on San Antonio river basin section

## Slide 33: Generalizing the method further for NHD incorporation
Test study on San Antonio river basin section
Preprocessing in Arc

## Slide 34: Generalizing the method further for NHD incorporation
Test study on San Antonio river basin section
Preprocessing in Arc
GeoNet csv output

## Slide 35: Generalizing the method further for NHD incorporation
Postprocessing model creates feature of results
  Issues

## Slide 36: Generalizing the method further for NHD incorporation
Postprocessing model creates feature of results
  Issues
Work with just the endpoints

## Slide 37: Generalizing the method further for NHD incorporation
Postprocessing model creates feature of results
  Issues
Work with just the endpoints
Further postprocessing produces straight section

## Slide 38: Conclusion
Classical approaches to channel network extraction challenged by information in lidar data
GeoNet: open-source tool for channel extraction from lidar data
Good results achieved in channel network extraction and identification of channel initiation points
Improving method for larger watersheds. Upcoming GeoNet 3.0 release.
GeoNet approved as stream extraction tool and will be used by Forestry Corporation of New South Wales, Australia (press release March 2014 – implementation starts August 2014) over 1.3M hectares.