## Slide 1: CE 397 Flood Forecasting
Lecture 3: Review of Concepts and Definitions

## Slide 2: National Water Data Infrastructure for the NFIE
Enhanced geospatial database for a national water data infrastructure
NWS Basins and
Forecast Points
USGS Water Watch
Points
National Flood
Hazard Layer
NHDPlus
Feature classes:
Subwatershed Catchment
Flowline (Medium and High Resolution)
Waterbody Dam
NFIE-Geo
9 feature classes
5 from NHDPlus
4 from IWRSS

## Slide 3: NHDPlus Version 2
National Elevation Dataset
National Hydrography Dataset
National Land Cover Dataset
Watershed Boundary Dataset
NHDPlus
2.67 million catchments average area 3 km2,
reach length 2 km
(built 2004-2014)
Geospatial foundation for a national water data infrastructure

## Slide 4: NFIE-Hydro: flow computation over CONUS
NWS River Forecasts
WRF-Hydro Model
NHDPlus to
RAPID Conversion
Grid to Catchment Linking
Forecast services
Completed
Pending
NFIE-Hydro
Deltares and
University of Alabama
14-day historical period, 2.67 million reaches

## Slide 5
European Center for Medium Range Weather Forecasting and European Joint Research Commission
15 Day ahead forecast ensemble (50 hydrographs) at each location

## Slide 6: Hydrologic Forecasting for the Texas-Gulf Region (from Brigham Young University)
http://demo.tethys.ci-water.org/
(67,313 NHDPlus reaches)
Source: Jim Nelson, Nathan Swain, BYU

## Slide 7: Ensemble Flow Forecast for Reach Catchment 5592208 made on Jan 13, 2015 (15 day horizon) Weather information source: European Center for Medium Range Weather Forecasting (ECMWF). Summary statistics compiled from 50 forecast hydrographs
Source: Jim Nelson, Alan Snow BYU

## Slide 8
North Carolina Floodplain Mapping Program HEC- RAS Models
  5 Recurrence Intervals: 10, 25, 50, 100, 500
  300,000 cross-sections
  Each cross-section has a rating curve
Slide: Ken Ashe, NCFMP

## Slide 9: Our cross-sections give the ability to interpolate between gages expanding the real time information from ~200 locations to 10s of thousands to 100s of thousand of locations
Slide: Ken Ashe, NCFMP

## Slide 10: HEC-RAS CrossSections (from 31 separate models on parts of Onion Creek, Austin, Texas)
Onion Creek watershed
Travis County
Hays County
100K NHD (Med res)
24K NHD (High res)
Conclusion: We need 24K NHD flow lines to link cross-sections
Some cross-sections are on tributaries not in 100K NHD

## Slide 11: Conclusion
NFIE is making excellent progress, more rapidly than I anticipated when I proposed it last May
Academic engagement of other universities is growing
NFIE requests from SSWD one more geospatial layer: a national coverage of high resolution NHD Flowlines
  NFIE-Hydro is supported by Medium Res NHDPlus nationally
  NFIE-River is supported by High Res NHD locally

## Slide 12: NFIE Conceptual Framework (modified)
NFIE-Services : Web services for flood information
NWDI: National water data infrastructure for hydrology
NFIE-Hydro: National high spatial resolution hydrologic forecasting
NFIE-River: River channel information and real-time flood inundation mapping
NFIE-Response: Wide area planning for flood emergency response
NFIE-Geo: Geospatial database for local application of NFIE

## Slide 13: NFIE Conceptual Framework (modified)
NFIE-Services : Web services for flood information
NWDI: National water data infrastructure for hydrology
NFIE-Hydro: National high spatial resolution hydrologic forecasting
NFIE-River: River channel information and real-time flood inundation mapping
NFIE-Response: Wide area planning for flood emergency response
NFIE-Geo: Geospatial database for local application of NFIE
National High Spatial
Resolution Hydrology

## Slide 14: NFIE Conceptual Framework (modified)
NFIE-Services : Web services for flood information
NWDI: National water data infrastructure for hydrology
NFIE-Hydro: National high spatial resolution hydrologic forecasting
NFIE-River: River channel information and real-time flood inundation mapping
NFIE-Response: Wide area planning for flood emergency response
NFIE-Geo: Geospatial database for local application of NFIE
Local, Regional River Hydraulics
and Flood Response Planning

## Slide 15: NFIE Goal
Connect “National” flood forecasting with “local” flood emergency response
National
Local
National Water Data Infrastructure
Local and regional GIS information
Weather and Hydrology
River Hydraulics and flood emergency response
NFIE-Hydro
NFIE-River and Response
NFIE-Geo

## Slide 16: National Water Data Infrastructure for the NFIE
Enhanced geospatial database for a national water data infrastructure
NWS Basins and
Forecast Points
USGS Water Watch
Points
National Flood
Hazard Layer
NHDPlus
Feature classes:
Subwatershed Catchment
Flowline (Medium and High Resolution)
Waterbody Dam
NFIE-Geo
9 feature classes
5 from NHDPlus
4 from IWRSS

## Slide 17: Reach Connectivity (100K NHD)
83
88
81
82
85
All node numbers are preceded by 6300348
So Node 81 is actually 630034881
All flowlines have a From_Node and a To_Node in the downhill flow direction
These node numbers are attributes of the flowline and not actual points in the database

## Slide 18: Line-Node Topology
A
B
C
D
1
3
4
2
Line | FromNode | ToNode
1 | A | B
2 | A | C
3 | B | D
4 | C | D
Flow Direction
Diverging reaches
Converging reaches

## Slide 19: Line-Node Topology for a loop
Line | FromNode | ToNode
1 | A | B
2 | A | B
Flow Direction
A
B
1
2
This means that there is a flow split
Each reach has its own local reach catchment

## Slide 20: 24K National Hydrography Dataset – Connectivity by geometric network
Geometric network
Feature Types
No FromNode and ToNode as attributes on the lines
No catchment associated with each individual line

## Slide 21: In 24K NHD, each reach is made up of “features” Indexed by a “ReachCode”
ReachCode 12090205000078 means that this is segment 78 in HUC8 Subbasin 12090205