## Slide 1
Distributed Catchment Modeling
Christopher Duffy, Penn State University
Essential Terrestrial Variables
Automating the Model Workflow
National Geospatial Data
Hydrologic Basis for Earth System Models
PIHM development
Climate Reanalysis & IPCC Projections
Detecting Decadal Ecosystem Change
Topics
Notes: 1

## Slide 2
  Why High Resolution Distributed Catchment Modeling?
  Hydrologic Basis for Earth System Modeling (e.g. CZO’s)
  Cyberinfrastructure for Virtual Data-Model Sharing
  Climate reanalysis and future scenario reconstructions
  Scaling up from HUC-12 to River Basin Scales
  All flood, drought and water supply impacts are local

## Slide 3
Motivating the Need for Water-Cycle Models
Drinking Water
Energy
Agriculture
Floods
Ecosystem Services
Drought
Notes: * Water is key to sustainability. It is used for drinking, in power generation, for agriculture and support of the whole ecosystem. But too much of it can lead to floods and too little of it cause drought.

## Slide 4: Essential Terrestrial Variables Necessary for Catchment Modeling Anywhere in CONUS
Atmospheric Forcing (precipitation, snow cover, wind, relative humidity, temperature, net radiation, albedo, photosynthestic atmospheric radiation)
Digital elevation models (30, 10, 3, 1m resolution)
River/Stream discharge, stage, cross-section
Soil (texture, C/N, organic, hydrologic & thermal properties)
Groundwater (levels, extent, hydrogeologic properties, 3D Architecture)
Land Cover (biomass/leaf area index, phenology,……. )
Land Use (human infrastructure, demography, ecosystem disturbance, property & political boundaries)
Environmental Tracers- stable isotopes
Water Use and Water Transfers
Lake/Reservoir/Diversion (levels, extent, discharge, operating rules)
…to be cont’d……..??

## Slide 5
  ETV’s -> National Data Supporting Catchment Models
  Fast access to high resolution data is a requirement for model development at relevant scales
  Detection and attribution of change for climate, landuse and ecosystem impacts is critical for resource management and policy
  National (continental) geospatial data for catchments is served by multiple nations/federal agencies/organizations
  A community-driven exercise in developing a high resolution data and models

## Slide 6
2,268 USGS
HUC 8
watersheds
103,444 USGS
HUC 12
watersheds
The Hydrologic Unit Code (HUC)
A Basis For Catchment Model-Data Sharing

## Slide 7
  An Initial ETV Bundle

## Slide 8
Need workflow here
HydroTerre: High Resolution ETV

## Slide 10
HydroTerre: A Prototype for Model-Data Access
Land Parcel Data; NHD: Stream, Lake, HUC’; USDA: Soils/Crops; NLCD: LU_LC;

## Slide 11
Need workflow here
HydroTerre: A Prototype Model-Data Workflow

## Slide 12
HydroTerre Prototype: Data and Modeling Hardware

## Slide 13
  A Time Line for the Penn State Model PIHM
1998-04 SAHRA NSF Science & Technology Center
    Duffy sabbatical at Los Alamos
    Yizhong Qu first PhD & early architect
    Finite volume model first steps
2006-08 NSF Waters/CUAHSI Project
Duffy and Reed
Mukesh Kumar-redesign PIHM, Data-Model
Gopal Bhatt, PIHMgis
Shuangcai Li, PIHM_hydro
2008-13 NSF Critical Zone Observatory
Duffy, Brantley, and CZO teams
Kumar-PIHM_3D
Gopal Bhatt/Duffy- Solute, Age Modeling
Yuning Shi, Ken Davis Flux_PIHM
Lorne Leonard: Hydroterre
Soil TrEC European Community funding
2013-16 NSF EarthCube GeoSoft BB
NSF INSPIRE Project Lake-Catchment Age of Water

## Slide 14
    Why & How of Integrated Models
  New sensors, communication networks, and characterization tools
  have made it possible to examine spatial and temporal
  phenomena over an unprecedented
  range of scales
  Multiphysics analysis is a unifying modeling strategy that allow scientists and engineers to explore
  fully-coupled effects of complex
  physical phenomena
  Goal: to develop an evolvable approach to hydrologic simulation,
  to advance predictive understanding &
  to develop the next generation
  of environmental forecasting tools

## Slide 15
Architecture for Multiphysics Modeling
Mike Heath UIUC, 2008
Sequential Coupling Approach one process or field is partially solved and then passed to the next physics field to form an initial solution. The iteration process continues until a final solution is achieved. The integration interface provides the services for subsystem interaction, data handling, mesh generation, parallel I/O, visualization, etc.

## Slide 16
Kumar, Bhatt, Duffy, 2008; Bhatt, Kumar, Duffy, 2014; Leonard and Duffy, 2014
Direct Coupling assembles all the physics equations in one matrix and solves all equations together. In this example an open-source GIS and Geodatabase is used for data management, mesh generation, space-time data analysis, and interface to the system solver and visualization.
ETV-Geodata
(Schema, Data, Relationships)
Field, Feature Objects, Non-Spatial Data
User Interface
Vector Processing
Raster Processing
Data Model Loader
Parameterization
Data Management
Kernel Physics
Numerical Solver
PIHM
Spatial
Temporal
Data Analytics
Spatio-Temporal
Uncertainty
Static: Conformed, constrained Delaunay & nested triangulation
Dynamic: Adaptive triangulations
Domain Decomposition
(Grid-Shp/ Dbf) Read, (Grid-Shp/ Dbf) Write
Data Access Tool
Architecture for Multiphysics Modeling

## Slide 17: Open Source Programming Tools
QGIS
  an open source and free "Programmable Geographic Information System"
  a mapping tool, a GIS modeling system, and a GIS application programming interface (API) all in one
  a platform independent Open Source Geographic Information System that runs on Linux, Unix, Mac OSX, and Windows
  libraries for raster and vector geospatial formats
  Object relational database is handled using PostgreSQL
  GRASS compatible
Qt/C++
- tools for programming the interface and visualization

## Slide 18
Fully coupled processes but with reduced physics (ASAP)
Qu and Duffy 2007. Kumar, Bhatt, Duffy 2009
NOAH Land
Surface
Model

## Slide 19: Semi-Discrete Finite Volume Formulation

## Slide 20
Desktop Data-Model Workflow
Gopal Bhatt author

## Slide 21
PIHM GIS: Open Source tool
for Desktop Model Setup with Tools for
A-Priori Parameters

## Slide 22
Conceptual Model + ETV data = A Priori Parameters
Example of the GIS for the surface geology coverage.
Conceptual Model Groundwater
flow in the Allegheny Plateau Section.

## Slide 23: PIHM GIS Framework
Geodata
(Schema, Data, Relationships)
Field, Feature Objects, Non-Spatial Data
User Interface
Vector Processing
Raster Processing
Data Model Loader
Parameterization
Data Management
Kernel Definition
Numerical Solver
PIHM
Spatial
Temporal
Data Analysis
Spatio-Temporal
Uncertainty
Static: Conformed, constrained Delaunay & nested triangulation
Dynamic: Adaptive triangulations
Domain Decomposition
(Grid-Shp/ Dbf) Read, (Grid-Shp/ Dbf) Write
Data Access Tool

## Slide 24
PIHM GIS Interface: Domain Decomposition

## Slide 25
Land Cover
Soil Classes
Elevations
Irregular Mesh &
Stream Network

## Slide 26
Hydroclimatic Process Scales
HUC-12 Scale

## Slide 27
GCM Grid Box
Resolve Uplands In Large Scale Simulations

## Slide 28
Unfolding A Multi-Scale
Experiment

## Slide 29
Generating Grids: resolution depends on purpose

## Slide 30
Advancing interdisciplinary studies of earth surface processes
Chris Duffy, PI 07-13
Sue Brantley
Rudy Slingerland
David Eissenstat
Henry Lin
Ken Davis
Kamini Singha
Laura Toran
Pat Reed
Karen Salvage
Eric Kirby
Tim White
Kevin Dressler
Doug Miller
Brian Bills
Beth Boyer
Colin Duffy
Chris Graham
Jennifer Williams
CZEN
Model Development & Testing
The Shale Hills/Susquehanna
Critical Zone Observatory
Ray Fletcher
Michelle Tuttle
Paul Bierman
Peter Lichtner
Carl Steefel
Rich April
Ryan Mather
David Harbor
Larry McKay
Teferi Tsegaye
HernanSantos
Evan Thomas
Xuan Yu
Yu Zhang
Ryan Jones
Beth Boyer

## Slide 31
b) Shaver Creek catchment

## Slide 34: CZO Data ->lidar, Soil, Regolith,Veg

## Slide 35
PIHM

## Slide 36
Basic Output: Water balance

## Slide 37
CZO Reanalysis:
Shale Hills Storm Library
1979-2011
Shale Hills CZO: 1979-2010 Reanalysis Storm Library

## Slide 38: http://www.pihm.psu.edu/applications.html CZO Catchment Reanalysis time series: 1979-Present

## Slide 39
Stream-Groundwater Interaction

## Slide 40
30 km^2 Meso-Scale Experiment
Integrated Modeling in a Coastal Watershed
Freshwater Discharge: Groundwater or Surface Water?
Gopal Bhatt
In cooperation with the Smithsonian
Environmental Research Center

## Slide 41
Domain used in decomposition

## Slide 42
Triangular Irregular Mesh
(Number of Mesh = 1862)

## Slide 43
SSURGO Soil Classification

## Slide 44
30m NLCD Data

## Slide 45
Stream Gauge Locations

## Slide 47
Freshwater Discharge to the Chesapeake

## Slide 48: Physically-based land surface hydrologic model: Flux-PIHM
Penn State Integrated Hydrologic Model (PIHM)
Flux-PIHM

## Slide 49: Flux-PIHM data assimilation system
Initial Conditions
Flux-PIHM
Perturbation
Observations
Ensemble Members
Ensemble Members
Ensemble Members
Ensemble Members
EnKF
Quality Control
Ensemble Members
Ensemble Members
Ensemble Members
Forecast
Ensemble Members
Ensemble Members
Ensemble Members
Analysis
Ensemble Members
Ensemble Members
Ensemble Members
Constrained Vrbls & Prmts
Notes: Data assimilation system for parameter and state estimation

## Slide 50: Flux-PIHM
Coupled land surface hydrologic model
Noah land surface + PIHM hydrology
Physically-based
Spatially-distributed
Notes: Blue arrows are Noah processes, and red arrows are PIHM processes.

## Slide 53
Spatial pattern of soil water content
Calibrated only using outlet discharge and SWC and WTD at one location, and driven by spatially uniform forcing data

## Slide 54: Flux-PIHM DA system for parameter estimation
Notes: Results from synthetic experiments. Solid lines represent estimated evolution of estimated parameter values when starting from different first guesses. Dashed lines are true parameter values. The DA system provide accurate estimates of parameter values.

## Slide 55: Flux-PIHM
Flux-PIHM provides accurate predictions of water and energy fluxes both in time and space
It is now being coupled with different models to explore watershed processes:
  Weathering models (Flux-PIHM-WITCH)
  Reactive transport models (RT-Flux-PIHM)
  Biogeochemistry models (Flux-PIHM-BBGC)
  …

## Slide 56: Wetland Vulnerability to Climate Change
Team
Chris Duffy
Xuan Yu
Gopal Bhatt
Ray Najaar
Michael Nassry
Denice Wardrop
Watersheds (7)
Muddy Creek
Kettle Creek
Shaver’s Creek
Young Womans Creek
East Mahantango Creek
Little Juniata River
Lackawanna River
Ecoregions (4)
Ridge and Valley
Piedmont
Unglaciated Plateau
Glaciated Plateau
20-Year Climate Scenarios (2)
Historical: 1979 - 1998
Future: 2046 - 2065

## Slide 60: Workflow
Use relative gwl change to measure wetland vulnerability
Set up models using HydroTerre data
Calibrate catchments on historic data (1979-1998)
Run IPCC future climate scenario (2046-2065)
HydroGeoMorphic (HGM) classification of wetlands
        Riverine
        Slope
        Depression

## Slide 61
Catchment-Wetland Response

## Slide 62
Historical - IPCC Precip-Temp

## Slide 63: Historical vs IPCC Simulations
1979-1998
2046-2065
Evapotranspiration
Recharge
2046-2065
1979-1998

## Slide 64
“Constrain” Model on Streamflow & NWI Wetlands

## Slide 65
FDC Young Woman’s Creek
Future:
peak flows - increase
low flows - lower

## Slide 66
FDC Shaver Creek
Future:
peak flows - increase
low flows - increase slightly

## Slide 67
FDC Lackawanna
Future:
peak flows increase
low flows increase

## Slide 68
Simulated-Observed Wetlands
Working definition: wetland is defined as having a water table within 30 cm of the surface

## Slide 69
Seasonal GW Change Anomaly Shavers Creek
Drier
Stable
Wetter
Winter
Annual
Spring
Summer
Fall

## Slide 70
Drier
Stable
Wetter
Seasonal GW Change Anomaly: Muddy Creek
Winter
Spring
Summer
Fall
Annual

## Slide 71: Catchment-Wide Results
 | NWI Wetlands |  | PIHM Depression |  | 
 | Drier | Wetter | Drier | Wetter | Ecoregion
Lackawanna River | 74% | 26% | 71% | 29% | Glaciated Plateau
Young Womans Creek | 62% | 38% | 63% | 37% | Unglaciated Plateau
Kettle Creek | 47% | 53% | 62% | 38% | Unglaciated Plateau
East Mahantango Creek | 40% | 60% | 50% | 50% | Ridge and Valley
Shaver’s Creek | 20% | 80% | 27% | 73% | Ridge and Valley
Little Juniata River | 71% | 29% | 64% | 36% | Ridge and Valley
Muddy Creek | 35% | 65% | 35% | 65% | Piedmont

## Slide 72
Scaling Concepts and Models From HUC-12’S to Major River Basins
Future Large Scale, High Resolution Model-Data Access & Scalability

## Slide 73
Essential Terrestrial Variables
Automating the Model Workflow
National Geospatial Data
Hydrologic Basis for Earth System Models
PIHM development
Climate Reanalysis & IPCC Projections
Detecting Decadal Ecosystem Change
Other examples
Topics
http://www.pihm.psu.edu/announcement_20141026.html
https://www.youtube.com/watch?v=1uRpMR6SpoI&feature=youtu.be