## Slide 1: CE 397 Flood Forecasting
Review Slides for the Midterm Exam
David Maidment
Spring 2015

## Slide 2: The Opportunity…
New National Water Center established on the Tuscaloosa campus of University of Alabama by the National Weather Service and federal agency partners
Has a mission to assess hydrology in a new way at the continental scale for the United State

## Slide 3: Partnership with the academic community …
National Weather Service has joined with CUAHSI to conduct a one-year National Flood Interoperability Experiment (NFIE)
Includes a Summer Institute for students and faculty at the National Water Center, June 1 to July 17, 2015

## Slide 4: Nationally Synthesize Operations of Regional River Forecast Centers

## Slide 5: Goal of the Experiment …
Close the gap between National Flood Forecasting and Local Emergency Response
Demonstrate forecasting of flood impacts at “stream and street level”
National
Local
Weather and Hydrology
National Weather Service and federal agencies
National Water Center
River Flooding and Emergency Response
Local, State and Regional Agencies
Citizens

## Slide 6: NFIE Goal: Connect National Scale Flood Modeling with Local emergency planning and response
How can near-real-time hydrologic simulations at high spatial resolution, covering the nation, be carried out using the NHDPlus or next generation hydro-fabric (e.g. data structure for hillslope, watershed scales)?
How can this lead to improved emergency response and community resilience?
How can an improved interoperability framework support the first two goals and lead to sustained innovation in the research to operations process?
Slide: Ed Clark, NWS

## Slide 7: Conceptual Framework Paper…

## Slide 8: National Flood Interoperability Experiment (NFIE): Five Components
NFIE-Services: Web services for flood information
NFIE-Geo: National geospatial framework for hydrology
NFIE-Hydro: National high spatial resolution hydrologic forecasting
NFIE-River: River channel information and real-time flood inundation mapping
NFIE-Response: Wide area planning for flood emergency response

## Slide 9: National Flood Interoperability Experiment (NFIE) Component One: NFIE-Geo
NFIE-Services: Web services for flood information
NFIE-Geo: National geospatial framework for hydrology
NFIE-Hydro: National high spatial resolution hydrologic forecasting
NFIE-River: River channel information and real-time flood inundation mapping
NFIE-Response: Wide area planning for flood emergency response

## Slide 10: Conceptual Framework Paper…

## Slide 11: National Flood Interoperability Experiment (NFIE): Five Components
NFIE-Services: Web services for flood information
NFIE-Geo: National geospatial framework for hydrology
NFIE-Hydro: National high spatial resolution hydrologic forecasting
NFIE-River: River channel information and real-time flood inundation mapping
NFIE-Response: Wide area planning for flood emergency response

## Slide 12: National Flood Interoperability Experiment (NFIE) Component One: NFIE-Geo
NFIE-Services: Web services for flood information
NFIE-Geo: National geospatial framework for hydrology
NFIE-Hydro: National high spatial resolution hydrologic forecasting
NFIE-River: River channel information and real-time flood inundation mapping
NFIE-Response: Wide area planning for flood emergency response

## Slide 13: Assumptions…
High spatial resolution hydrologic modeling at continental scale
Built upon NFIE-Geo: A national geospatial framework for hydrology
  Continental landscape divided into 2.67 million local catchments, each containing a single stream reach
  Stream reaches connect to form a national stream network
2.67 million catchments
Average area 3 km2
Average reach length 2 km

## Slide 14: NHDPlus Version 2
National Elevation Dataset
National Hydrography Dataset
National Land Cover Dataset
Watershed Boundary Dataset
NHDPlus
Geospatial foundation for a national water data infrastructure
2.67 million reach catchments in US
average area 3 km2
reach length 2 km

## Slide 15: NFIE-Geo for National Flood Interoperability Experiment
Enhanced geospatial database for a national water data infrastructure
NWS Basins and
Forecast Points
USGS Water Watch
Points
National Flood
Hazard Layer
NHDPlus
Feature classes:
Subwatershed (HUC12) Catchment
Flowline
Waterbody Dam
NFIE-Geo
9 feature classes
5 from NHDPlus
4 from IWRSS

## Slide 16: NHDPlus Reach Catchments and Subwatersheds
Each reach catchment has a single flow line
Uniquely labeled across the nation
Flood hazard zone defined by FEMA map
Catchment 5781369
HUC12 Subwatershed
Contains reach catchments
Base for Hydrologic modeling
and flood emergency response planning
Reach Catchment
Subwatershed

## Slide 17: NFIE-Geo in HydroShare
https://www.arcgis.com/home/webmap/viewer.html?webmap=2c30160429984a59873f26b9d118dbfe
David Tarboton, Utah State Univ
and Ray Idaszak, RENCI

## Slide 18: Reach Connectivity (100K NHD)
83
88
81
82
85
All node numbers are preceded by 6300348
So Node 81 is actually 630034881
All flowlines have a From_Node and a To_Node in the downhill flow direction
These node numbers are attributes of the flowline and not actual points in the database

## Slide 19: Line-Node Topology
A
B
C
D
1
3
4
2
Line | FromNode | ToNode
1 | A | B
2 | A | C
3 | B | D
4 | C | D
Flow Direction
Diverging reaches
Converging reaches

## Slide 20: Line-Node Topology for a loop
Line | FromNode | ToNode
1 | A | B
2 | A | B
Flow Direction
A
B
1
2
This means that there is a flow split
Each reach has its own local reach catchment

## Slide 21: 24K National Hydrography Dataset – Connectivity by geometric network
Geometric network
Feature Types
No FromNode and ToNode as attributes on the lines
No catchment associated with each individual line

## Slide 22: In 24K NHD, each reach is made up of “features” Indexed by a “ReachCode”
ReachCode 12090205000078 means that this is segment 78 in HUC8 Subbasin 12090205

## Slide 23: NFIE-Geo for a county….
http://www.caee.utexas.edu/prof/maidment/CE397Flood/Assignment2/NFIEGeo.pdf
Map courtesy of Cyndi Castro
UT Austin
County subset of national geospatial data layers

## Slide 24: What have we learned?
NFIE-Geo is a solid information base for building a national flow forecasting system
National level data yields local data description that is detailed enough for “stream and street” level impacts
24K data is too detailed for a national model – better to stick to 100K flowline data

## Slide 25: National Flood Interoperability Experiment (NFIE) Component Two: NFIE-Hydro
NFIE-Services: Web services for flood information
NFIE-Geo: National geospatial framework for hydrology
NFIE-Hydro: National high spatial resolution hydrologic forecasting
NFIE-River: River channel information and real-time flood inundation mapping
NFIE-Response: Wide area planning for flood emergency response

## Slide 26: NFIE-Hydro Forecasting Model…
Runoff
Streamflow
Channel flow routing (for continental US)
Probabilistic flood forecasts
Weather model and forecasts
Land-Atmosphere Model
Precipitation
Weather
Catchment-level forecasts

## Slide 27: Modeling of Weather, Hydrology, River Flow in WRF-Hydro
Observations Datasets, Numerical Weather Model
Land Surface Model
Forcing:
Radiation
Precipitation
Surface climate
Evaporation
Soil Moisture
Runoff
Recharge
Soil
Vegetation
Terrain
RAPID: River Routing on NHDPlus
Network River Flow

## Slide 28: NFIE-Hydro Workflow
Implemented in Microsoft Azure

## Slide 29: High Resolution Rapid Refresh (HRRR)
NOAA NCEP real-time 3 km resolution model
- Nested WRF model (cloud resolving atmospheric model)
Updated hourly
15 hour forecast
3 km radar assimilation
Initialized by RUC model
Variables of interest: Temp at 2 m, U and V wind at 2 m, relative humidity, specific humidity, precipitation rate, surface pressure

## Slide 30: Accessing Real-time HRRR Forecasts
Time (Hours)
0
3
6
Forecast run at Hour 0
Forecast run at Hour 6
15
Time (Hours)
http://thredds-jumbo.unidata.ucar.edu/thredds/ncss/grib/HRRR/CONUS_3km/surface/Best?var=Temperature_height_above_ground&north=45&west=-134&east=-61&south=21&disableProjSubset=on&horizStride=1&time_start=2015-02-05T00:00:00Z&time_end=2015-02-09T17:00:00Z&timeStride=1&vertCoord=&accept=netcdf

## Slide 31: Overarching WRF-Hydro Scientific Objectives (David Gochis, NCAR)
A community-based, supported coupling architecture designed to provide:
An extensible multi-scale & multi-physics land-atmosphere modeling capability for conservative, coupled and uncoupled assimilation & prediction of major water cycle components such as precipitation, soil moisture, snowpack, groundwater, streamflow, inundation
Streamflow prediction across scales (from 0-order headwater catchments to continental river basins & minutes to seasons)
A robust framework for land-atmosphere coupling studies

## Slide 32: GEOGRID
HGT_M : Topographic elevation (units of meters) on the ‘mass grid’.
XLAT_M : Latitude coordinates, in decimal degrees, on the mass grid.
XLONG_M : Longitude coordinates, in decimal degrees, on the mass grid.
LANDUSEF : Land use fraction, in units of fraction.
SOILCTOP: Top layer soil texture category, in units of fraction
GREENFRAC : Monthly mean green vegetation fraction values (units of fraction).
ALBEDO12M : Monthly mean surface albedo values (units of %) not including snow effects.

## Slide 33: Soil Moisture Map (mm water in top 1 m of soil from NASA Land Data Assimilation System)
Map is created each day using NASA services
http://statsnldas.azurewebsites.net/
Include forecast soil moisture in NFIE

## Slide 34: Soil Moisture Anomaly Map (current value – mean for calendar day at each spatial point)
Map is created each day using NASA services
http://statsnldas.azurewebsites.net/

## Slide 35: Soil Moisture Percentile Map
http://statsnldas.azurewebsites.net/
Current value expressed as a percentile based on historical data [1979 to present] on this calendar day at this spatial point
Compare present soil moisture with past conditions

## Slide 36: How to connect gridded input runoff data (WRFHydro) to NHDplus network
Runoff Downscaling Weight Table
540
542
541
210
209
From: Deng Ding/Nawajish Noman (ESRI)

## Slide 37
RAPID River Routing Model
River Application for Parallel ComputatIon of Discharge
Flow
Legend
Dam
Junction
Catchment
Computational Unit for Rivers
Forcing: Runoff and reservoir releases
http://rapid-hub.org/
NHDPlus Catchment
Sprism = KQ
Swedge = KX (I – Q)
Muskingum
Method

## Slide 38: ArcGIS Tools for RAPID Model
13473525
13475951
13475949
Muskingum Parameters
Kfac = LENGTH_GEO x 3600
K = Kfac x λk
where λk = 0.35
X = λx x 0.1 (units:
where λx = 3
Flowline
Flowline

## Slide 39: Flow in the Texas Gulf Coast RAPID Model, 3 hour time steps
GIS data describes 64k river reaches . . .
. . . simulate flow in each reach in each time step
Atmosphere
Land Surface
Rivers
David et al (2013)
DOI: 10.1016/j.envsoft.2012.12.011

## Slide 40
European Center for Medium Range Weather Forecasting and European Joint Research Commission
15 Day ahead forecast ensemble (50 hydrographs) at each location

## Slide 41: Hydrologic Forecasting for the Texas-Gulf Region (from Brigham Young University)
http://demo.tethys.ci-water.org/
(67,313 NHDPlus reaches)
Source: Jim Nelson, BYU

## Slide 42: Ensemble Flow Forecast for Reach Catchment 5592208 made on Jan 13, 2015 (15 day horizon) Weather information source: European Center for Medium Range Weather Forecasting (ECMWF). Summary statistics compiled from 50 forecast hydrographs
Source: Jim Nelson, BYU

## Slide 43: What have we learned?
A high resolution flow forecasting model is feasible for the continental United States!
NFIE-Hydro is a work in progress that needs a complicated workflow system e.g. built in the Azure Data Factory to become operational
RAPID is a very useful flow model running over the NHD Flowlines
European GloFAS procedure is a more advanced than ours and easier to deploy locally

## Slide 44: National Flood Interoperability Experiment (NFIE) Component Three: NFIE-River
NFIE-Services: Web services for flood information
NFIE-Geo: National geospatial framework for hydrology
NFIE-Hydro: National high spatial resolution hydrologic forecasting
NFIE-River: River channel information and real-time flood inundation mapping
NFIE-Response: Wide area planning for flood emergency response

## Slide 45: Flood risk zones…
Each catchment has a flood hazard zone defined from FEMA flood data
Probabilistic forecast from NFIE-Hydro defines flood risk
Color the zones according to risk

## Slide 46: More comprehensive solution…
NFIE-River: Dynamic flood modeling, forecasting and inundation mapping in space and time
Requires LIDAR terrain data so can only be done for particular regions
Iowa Flood Information System
North Carolina Floodplain Mapping Program

## Slide 47: CrossSections on Lower Mississippi River
173 cross-sections over 543 km, or 3.1 km between cross-sections, on average
41,479 cross-section points (x,y,z) of bed elevation, or 240 points per cross-section, on average

## Slide 48: NFIE-Hydro and NFIE-River
Junction
XSIntersect
Tributary inflow
Catchment inflow

## Slide 49: Cross-sections from HEC-RAS models
Travis County
Hayes County
Onion Creek watershed
We need a national repository -- use HydroShare
Map: Xing Zheng
Data Source: City of Austin

## Slide 50: Real-Time Flood Inundation Mapping (USGS/NWS)
http://water.weather.gov/ahps2/inundation/inundation_google.php?gage=atit2

## Slide 51
North Carolina Floodplain Mapping Program HEC- RAS Models
  5 Recurrence Intervals: 10, 25, 50, 100, 500
  300,000 cross-sections
  Each cross-section has a rating curve
Slide: Ken Ashe, NCFMP

## Slide 52: Flood Alert and Mapping Network How it works
Rain Gage
Stream Gage
Output of Flood Forecast Model
Library of Flood Profiles
Flood Forecast and Flood Inundation Maps available to Emergency Managers and Public
Now
3hr
6hr
9hr
12hr
24hr
NWS SE River Forecast Center
FMIS

## Slide 53: Return Period – Discharge – Stage Height – Water Surface Elevation

## Slide 54: Automated “integrated Simplified Inundation Mapping (iSIM)” – CG3i Software Service
CG3I UT Dallas Feb 2015
Johnstown, PA – May 31, 1889

## Slide 55: Step 2 & 3 – Create Cut-lines
The most important input for the RAS software is the cross sections, which are derived from the cut-lines
  Innovative automation of cut-line placement
  Placement regularly spaced at perpendicular angles to the river flow
  Created in 2D first (cut-lines), then…

## Slide 56: Cross-section Geometry Rules
A stream must be drawn from upstream to downstream.
A stream is composed of one or more reaches, and each reach must have unique combination of stream ID and reach ID.
All reaches must be connected at junctions.
A junction is an intersection of two or more streams.
A stream cannot contain parallel flow path. If three reaches connected at a junction, only two can have the same stream ID.
XS cut lines must be digitized from the left to the right side of a stream centerline.
XS cut lines cannot cross a stream centerline more than once.
XS cut lines cannot cross each other.
Moreover, HEC-­‐RAS itself also has limitations:
XS cut lines cannot have more than 500 stations (elevation points).
XS cut lines cannot have more than 20 variations in Manning’s N values.
There must be no vertical drop in elevation (two stations overlapping at the same location and having different elevation values), especially at the end of the line.

## Slide 57: Our Solution
Offset lines are created along stream centerline
XS cut lines are generated with the aid of offset lines

## Slide 58: Step 4 – Transforming 2D to 3D

## Slide 59: Step 5 - Land Use Data in GIS

## Slide 60: Step 3 – Final Inundation Shapefile
Notes: Redo this slide

## Slide 61: Workflow of GeoNet

## Slide 62: Workflow of GeoNet: Non linear Filtering: a critical step when using lidar data
  Errors in the representation of the landscape can be introduced several ways:
    Acquisition
    Preprocessing
    Point cloud classification

## Slide 63: Workflow of GeoNet: Filter Type Comparisons
Gaussian
Perona-Malik
Images: Passalacqua et al., 2010, DOI: 10.1029/2009JF001254 (top) Pelletier, 2013, DOI: 10.1029/2012WR012452 (bottom)
Nonlinear diffusion equation:

## Slide 64: Workflow of GeoNet: Identification of likely channelized pixels
Ridges
Channels
Diffusive portion of the landscape
Geometric curvature

## Slide 65: Workflow of GeoNet: Identification of likely channelized pixels
Flow routing
D-infinity algorithm
Tells us the total number of cells which flow into a cell
Allows for flow divergence (flow can be directed into one or two neighboring cells depending on flow direction)
Image: Tarboton, 1997. http://www.neng.usu.edu/cee/faculty/dtarb/dinf.pdf

## Slide 66: Workflow of GeoNet: Geodesics and cost function
Fast Marching Algorithms are used to compute the geodesic distance by using the cost function for each of the outlets (identified as green dots).
The outlets are the starting point, and the draining basin is the region the fast marching can be done.
Big advantage: global operation using local information

## Slide 67: Generalizing the method further for NHD incorporation
Postprocessing model creates feature of results
  Issues

## Slide 68: Adapted methodology
For research purposes, GeoNet’s bank location feature was adapted for user input centerlines
Same general methodology used for channel bank identification
Banks locations output as a csv to facilitate GIS interface

## Slide 69: The Texas NHDPlus network looks complicated...
...with 105 river reaches.
Slide: Ben Hodges

## Slide 70: But silicon microchips can have a billion (109) or more transistors.
Electrical engineers routinely solve huge nonlinear circuit network problems during chip design.
Slide: Ben Hodges

## Slide 71: We can solve the complete river network, ... but we need river geometry:
- cross-section area vs. depth
- cross-section perimeter vs. depth
- river bottom slope
- channel roughness
Slide: Ben Hodges

## Slide 72: What have we learned?
We need hydraulic modeling on the main rivers and streams (SPRNT!)
Key connection is to add river cross-sections to NFIE-Geo dataset and derive flow properties from
Cross-sections can come from existing HEC-RAS models
Cross-sections can be derived from terrain data using GeoNet or ArcGIS

## Slide 73: National Flood Interoperability Experiment (NFIE) Component Four: NFIE-Response
NFIE-Services: Web services for flood information
NFIE-Geo: National geospatial framework for hydrology
NFIE-Hydro: National high spatial resolution hydrologic forecasting
NFIE-River: River channel information and real-time flood inundation mapping
NFIE-Response: Wide area planning for flood emergency response

## Slide 74: Link with the First Response Community
https://www.youtube.com/watch?v=ympaR6YUxiA&feature=youtube
Harry Evans, Chief of Staff Austin Fire Department
Responsible for flood emergency response in Austin

## Slide 75
Actual Rainfall Totals
Onion Creek watershed

## Slide 77
Incident Command Locations
11:30PM, Oct 30
4.25AM, Oct 31
5.50AM, Oct 31
6.00AM, Oct 31

## Slide 78: Address Points -- used for directing emergency response vehicles
All legal residences have an address point
Established when the lot is legally platted and registered with the county

## Slide 79: Address Points and the Flood Hazard Zone
495,000 Address points in the two counties
How many points are in the flood hazard zone?
Where are the high flood risk areas in these counties?
Travis County
Williamson County
Austin, Texas

## Slide 80: Address Points and the Floodplain

## Slide 81: Address Points in the Floodplain
Floodpoints
Address Points in Floodplain of Onion Creek

## Slide 82: Address Points in Floodplain of a Subwatershed
Number of Address Points in the Floodplain
A total of 12,052 address points are in the floodplain out of 495,468 in the study region (2.5%)

## Slide 83: Address Points and Roads in Floodplain of Onion Creek

## Slide 84: Length of Roads in Floodplain of a Subwatershed
Length of Roads in Floodplain (Km)
A total of 711 km of roads are in the floodplain out of 14,732 km in the study region (4.8%)

## Slide 85: Intersection of Streams and Roads
Both datasets at 24K resolution
5517 intersection points in Travis and Williamson Counties
Data: Xing Zheng

## Slide 86: Public Education
Community resilience
  Promoting self reliance
  Knowing areas of high risk
Public Awareness
  Timely notification of flood conditions
  Meaningful and actionable messaging
Public Notification
  Reverse Notification System (RNS)
  Social media
  News Media
  Subscription Services

## Slide 87: Emergency Response
Pre-planning
  Flood Prone areas – type of flooding – access and egress – critical infrastructure
Training and Equipment
  Swift Water Rescue – Flat Water Evac… What’s the threat?
Predictive Services
  NWS, NOAA, USGS…How bad is bad?
  Real time flood updates
Evacuations
  Timely Evacuations vs Protect in Place

## Slide 88: What have we learned?
Impact on people and on the transportation system are the two key factors linking flood forecasting with emergency response
Public education and awareness is critical
Hard to separate out all local flood issues from those related to improved flood forecasting
Communication of real-time information is key

## Slide 89: National Flood Interoperability Experiment (NFIE) Component Five: NFIE-Services
NFIE-Services: Web services for flood information
NFIE-Geo: National geospatial framework for hydrology
NFIE-Hydro: National high spatial resolution hydrologic forecasting
NFIE-River: River channel information and real-time flood inundation mapping
NFIE-Response: Wide area planning for flood emergency response

## Slide 90: Introduction to OGC & ISO Standards for Sharing Geographic Information
Focus on WaterML for Flood Forecasting
CE 397 Flood Forecasting, Feb 2015
by David K Arctur

## Slide 91: Geographic Features: Quick Overview
Perceived in context of …
Data capture
Feature: abstraction of a real-world phenomenon
Geographic Feature: a feature associated with a location relative to the Earth; digital representation of an aspect of the real world
Reality: phenomena
Geographic application
Feature Types
Feature Instances
Classified as …
Defining [0..n]
Universe of discourse
Digital Representation
Notes: Notes:
Source: OGC Reference Model
URL:

## Slide 92: Different phenomena call for different forms of exchange
Two broad categories of features: discrete and continuous
  Discrete: recognizable objects having distinct boundaries or spatial extent [vector]
    Buildings, streams, measurement stations, …
  Continuous: phenomena varying over space and time, with no specific extent [gridded, raster]
    Temperature, soil composition, land cover, elevation, …
    OGC “coverage”: defines a data model that associates spatio-temporal positions to data values or model outputs

## Slide 93: What different things about coverage features do we need to exchange?
Earth imagery; gridded data (OGC AS Topic 7; ISO 19121, 19129)
Coverage schema (OGC AS Topic 6; ISO 19123)
AS = Abstract Spec
Notes: Source: http://www.geo.cornell.edu/geology/classes/Geo101/graphics/ithaca_dem.jpg

## Slide 94: What different things about observations do we need to exchange?
Observations and Measurements: Related entities & their associations (OGC AS Topic 20, ISO 19156)
But this is very abstract… we need to create a profile for unambiguous use in hydrologic applications…
OM_Observation
+
phenomenonTime
+
resultTime
+
validTime [0..1]
+
resultQuality [0..*]
+
parameter [0..*]
GF_PropertyType
GFI_Feature
OM_Process
Any
+observedProperty
1
0..*
+featureOfInterest
1
0..*
+procedure
1
+result

## Slide 95: Using OGC O&M model for water level …
An Observation is an action whose result is an estimate of the value of some property of the feature-of-interest, obtained using a specified procedure
GF_PropertyType
OM_Observation
+
phenomenonTime
+
resultTime
+
validTime [0..1]
+
resultQuality [0..*]
+
parameter [0..*]
GFI_Feature
OM_Process
Any
+observedProperty
1
0..*
+featureOfInterest
1
0..*
+procedure
1
+result
Stage Height
Water level measurement
sampling feature
Stream Gage
River is a
sampled feature
Time series of values
Source: USGS
(WaterML2 Part 1)

## Slide 96: Workflows
Stage Height
Discharge Value
Rating Curve
Discharge Time Series
Measured with water level recorder
Measured with stream flow meter at a point in time
Derived from stage vs. discharge measurements over time at cross-section
Apply rating curve to convert stage height to discharge time series
1
2
3
4
Flood Maps
Stage Time Series
Rating Curve
Discharge Time Series
Extent of inundation modeled in GIS
Apply rating curve to convert discharge to stage height time series
Produced by hydraulic models & associated with cross-sections
Modeled by NFIE-Hydro for every NHDPlus Reach
8
7
6
5
Typical Case
Flood Forecasting

## Slide 97: Treating rating curves as a measurement …
(Stage, Discharge) pair
GF_PropertyType
OM_Observation
+
phenomenonTime
+
resultTime
+
validTime [0..1]
+
resultQuality [0..*]
+
parameter [0..*]
GFI_Feature
OM_Process
Any
+observedProperty
1
0..*
+featureOfInterest
1
0..*
+procedure
1
+result
Gage Location
Observation or Conversion Method
sampling feature
(Stage, Discharge) tuples
Source: USGS
(WaterML2 Part 2)
An Observation is an action whose result is an estimate of the value of some property of the feature-of-interest, obtained using a specified procedure
Notes: Rating curves are developed on infrequent, as-needed basis, by taking direct measurements of depth and flow, and plotting the curve from this data. The curve is then used to convert real-time measurements of depth into real-time values of discharge.
The object of WaterML 2.0 Part 2 is to apply the OGC O&M conceptual model and WaterML XML schema to convey the set of (stage, discharge) values.
Source: http://water.usgs.gov/edu/measureflow.html
See also: OGC 13-021r3 WaterML 2.0 – Part 2.

## Slide 98: The stream flow can then be determined from the rating curve
Discharge
GF_PropertyType
OM_Observation
+
phenomenonTime
+
resultTime
+
validTime [0..1]
+
resultQuality [0..*]
+
parameter [0..*]
GFI_Feature
OM_Process
Any
+observedProperty
1
0..*
+featureOfInterest
1
0..*
+procedure
1
+result
Stream Gage
Flow rate conversion
sampling feature
River is a
sampled feature
Time series of values
Source: USGS
(WaterML2 Part 1)
An Observation is an action whose result is an estimate of the value of some property of the feature-of-interest, obtained using a specified procedure
Notes: Graph source: http://waterdata.usgs.gov/nwis/uv?cb_00060=on&cb_00065=on&cb_00065=on&format=gif_default&site_no=08158000&period=&begin_date=2015-02-02&end_date=2015-02-16

## Slide 99: Workflows
Stage Height
Discharge Value
Rating Curve
Discharge Time Series
Measured with water level recorder
Measured with stream flow meter at a point in time
Derived from stage vs. discharge measurements over time at cross-section
Apply rating curve to convert stage height to discharge time series
1
2
3
4
Flood Maps
Stage Time Series
Rating Curve
Discharge Time Series
Extent of inundation modeled in GIS
Apply rating curve to convert discharge to stage height time series
Produced by hydraulic models & associated with cross-sections
Modeled by NFIE-Hydro for every NHDPlus Reach
8
7
6
5
Typical Case
Flood Forecasting

## Slide 100: Ensemble Flow Forecast for Reach Catchment 5592208 made on Jan 13, 2015 (15 day horizon) Weather information source: European Center for Medium Range Weather Forecasting (ECMWF). Summary statistics compiled from 50 forecast hydrographs
Source: Jim Nelson, BYU

## Slide 101: Going from discharge to stage height with simulated rating curves
An Observation is an action whose result is an estimate of the value of some property of the feature-of-interest, obtained using a specified procedure
(Stage, Discharge) pair
GF_PropertyType
OM_Observation
+
phenomenonTime
+
resultTime
+
validTime [0..1]
+
resultQuality [0..*]
+
parameter [0..*]
GFI_Feature
OM_Process
Any
+observedProperty
1
0..*
+featureOfInterest
1
0..*
+procedure
1
+result
Monitoring Point on x-section
Conversion Method
sampling feature
(Stage, Discharge) tuples
Source: USGS
Notes: We already have rating curves at gages, and we can determine rating curves for any cross-section developed for hydraulic models.
That still doesn’t give us rating curves for all the NHDPlus reaches.
We can work from NED 10m, or LIDAR where available, to extract cross-sections where needed. Accuracy may vary!
Can then take a large-scale hydraulic model (SPRNT) to develop rating curves for all known cross-sections.

## Slide 102: Flood Stage and Inundation

## Slide 103: OGC/WMO Hydrology Domain Working Group
2008
2009
2010
2011
2012
Hydrology Domain Working Group formed
OGC at WMO Commission for Hydrology
7+ Year International Effort – WaterML
2013
2014
Technical Meetings every 3 months
Five Interoperability Experiments (Surface water, groundwater, ratings-gaugings)
Annual week-long workshops
Involvement by many countries
WML2 Part 2 Ratings-Gaugings
Acknowledgements: OGC, WMO, GRDC, NWS, CUAHSI, BoM/CSIRO, USGS, GSC, Kisters, …….
Stage-Discharge values for one cross-section
A time series for one variable at one location
(draft pending)
Memorandum of Understanding between the World Meteorological Organization and the Open Geospatial Consortium
Sensor Observation Service 2.0
Hydrology Profile
Best Practice
Notes: (1) A four-year international effort has been undertaken to reconcile WaterML with international standards;
(2) This effort was initiated with the establishment of an Hydrology Domain Working Group by the Open Geospatial Consortium in September 2008;
(3) An OGC representative attended the WMO Congress of the Commission for Hydrology in 2008
(4) A formal agreement between Secretary General of WMO and President of OGC in 2009 to jointly develop standards for hydrology, climatology, oceanography and climatology;
(5) The joint OGC/WMO Hydrology Domain Working Group was supported by a large work effort, annual week-long workshops, four interoperability experiments for surface and groundwater data exchange, and participation by many countries;
(6) In June 2012, the OGC voted to adopt the revised version, WaterML2 as an international standard for exchange of water resources time series (the first such public standard that has existed);
(7) This Congress to the WMO Commission for Hydrology to whom I am speaking is considering WaterML2 for adoption as an official standard by WMO
(8) WaterML 2.0 Part 2 – Ratings and Gagings is ready for public comment, pending OGC approval to post.

## Slide 104: What is Time? … on the web?
ISO 8601:2004[E] – Data elements and interchange formats – Information interchange – Representation of dates and times
  Date and time values are ordered from the largest to smallest unit of time: year, month (or week), day, hour, minute, second, and fraction of second. This ordering corresponds to chronological order. This allows dates to be naturally sorted by computer file systems.
  Each date and time value has a fixed number of digits that must be padded with leading zeros. (The “format template” in figure below will achieve this in Excel spreadsheets)
  Two main formats – (1) a basic format with a minimal number of separators, or (2) an extended format with separators: hyphen between date values (year, month, week, and day) and colon between time values (hours, minutes, and seconds). Local time zone begins with + or – hours from UTC.
  http://en.wikipedia.org/wiki/ISO_8601
Date and time expressed according to ISO 8601: | 
Format template: | yyyy-m-dTh:mm:ssZ
Date: | 2015-02-15
Date and time in UTC: … as Zulu: | 2015-02-15T19:39:11+00:00
 | 2015-02-15T19:39:11Z
Date & time in Austin: with Daylight Savings: | 2015-02-15T13:39:11-06:00 2015-02-15T14:39:11-05:00
Week: | 2015-W07
Ordinal date: | 2015-046

## Slide 105: Time–Value Pairs: Building a time series for web exchange
How do you represent time series in a database?
Only precise instants are allowed.
<wml2:time>2015-02-02T23:55:00-06:00</wml2:time>
<wml2:value>12.25</wml2:value>
Notes: Table source: http://waterdata.usgs.gov/nwis/uv?cb_00065=on&cb_00065=on&format=html&site_no=08158000&period=&begin_date=2015-02-02&end_date=2015-02-16
Graph source: http://waterdata.usgs.gov/nwis/uv?cb_00060=on&cb_00065=on&cb_00065=on&format=gif_default&site_no=08158000&period=&begin_date=2015-02-02&end_date=2015-02-16

## Slide 106: WaterML Web Services CUAHSI, USGS, OGC, WMO…
Water time series data on the internet
24/7/365 service
For daily and real-time data
. . . Operational water web services system for the United States
http://waterservices.usgs.gov/nwis/iv/?format=waterml,2.0&sites=08158000&period=P1D&parameterCd=00060
Notes: Increasingly, national water data is being published using WaterML to describe time series of observations and model results. This is the current output from the US Geological Survey for one of their tens of thousands of river gauges (this one is on the Colorado River in Austin TX).

## Slide 107: Example: Global map of stream gauges for getting data and hydrograph at one gauge
Click to add layers
http://geoss.maps.arcgis.com/home/webmap/viewer.html?webmap=5efcdfb27d744e3ea65eaf58c06f9d0c
Esri ArcGIS Online web map viewer
http://bit.ly/1ERSyva
WMO GRDC (gauge descriptions only, no water data)
Kisters GRDC (WaterML 2 data for OGC Surface Water IE)
USGS NWIS (most have real-time data)
Mexico (some with historical data, hosted by Univ of Texas)
Dominican Republic (historical data hosted by BYU)
Italy & New Zealand (real-time data, developed for AIP-6)
Notes: Full link: http://geoss.maps.arcgis.com/home/webmap/viewer.html?webmap=5efcdfb27d744e3ea65eaf58c06f9d0c
Short link: http://bit.ly/1ERSyva
Here is a map of the world’s major rivers, and <click>
locations of about 20,000 stream gauges registered in WMO’s Global Runoff Data Center in Germany. While the yellow dots represent locations where data has been collected, that data is not available in a standardized format, nor is it necessarily available without restriction. <click>
The purple dots are mainly coastal sites where Kisters has developed a WaterML2 web service from the GRDC data. This was done for the OGC Surface Water Interoperability Experiment in 2011. <click>
The US <click> and Mexico maintain another 20,000 stream gauges, nearly all of which provide ongoing data services. <click>
The red dots are for Dominican Republic, which started publishing its water data in 2012. <click>
As a result of this project, we can now add regional agencies’ gauges and data in Italy and New Zealand. <click> (shows legends) <click> (next slide)

## Slide 108: NASA Land Data Assimilation System: Grid and time series globally
http://bit.ly/J2I43m
Notes: Full link: http://ec2-54-225-249-9.compute-1.amazonaws.com/MultidimensionalTemplate/index.html?appid=d73011dceb0e41d0af334912355bddd5
Short link: http://bit.ly/J2I43m

## Slide 109: Develop NWS Experimental Data Services
NWS CHPS Modeling Units: RFCs
Export Data elements from the simulation& forecast workflow including:
Inflow to the Channel (INFW)
Mean Areal Precipitation (MAP)
Streamflow (QINE) at ~3600 points
PI-XML to WaterML22
netCDF
to
NHD+
Data Services – local runoff
Experimental WRF-Hydro 1
1Responsibility of NCAR
Slide: Ed Clark, NWS

## Slide 110: What have we learned?
Existing water data exchange standards are sufficient to support the NFIE
Sensor Observation Service and WaterML2
Emerging work on a ratings and gagings standard
We need to connect the geospatial and temporal information frameworks

## Slide 111: Transformative for the nation…
Forecasts produced by
  Current system – 3600 locations
  NFIE system – 2.67 million locations
New Information to help emergency managers save lives and keep people safe
700 times more
Current
Proposed