## Slide 1: Texas Drought Planning
David R. Maidment Center for Research in Water Resources University of Texas at Austin
Updated from a presentation made at the TAMEST 2012 Texas Water Summit, May 20, 2012
Revised version: 30 July 2012

## Slide 2: Water Availability during the Drought
Drought Technology Steering Committee
Water balance of Texas
Drought in West Texas
Texas water and climate model

## Slide 3: Water Availability during the Drought
Drought Technology Steering Committee
Water balance of Texas
Drought in West Texas
Texas water and climate model

## Slide 4
Drought Forum, Feb 13, 2012
State water agencies and academic speakers
Formed a Drought Technology Steering Committee to continue dialog
  TWDB, TCEQ, TPWD, TDEM
  UT Austin, TAMU – College Station, Texas Tech
Acknowledgements: Brenner Brown, Kathy Alexander, David Bradsby, Mike Bewley, Byron Tapley, Himanshu Save, Gordon Wells, Teresa Howard, Johnnie Sullivan, Zong-Liang Yang, Xitian Cai, Jay Banner, Eric James, Charlie Kreitler, Cedric David, Dharhas Pothina
http://www.texasdroughtinfo.org

## Slide 5
About 1000 water systems
600 Groundwater
400 Surface water

## Slide 6: Water and Electric Power Generation
ERCOT Power Pool
Water flow, level and temperature issues

## Slide 7: Impact on Agriculture
Source: Texas Agrilife
Pasture in Burleson County

## Slide 8: Normalized Difference Vegetation Index (NDVI)
A measure (0-1) of the greenness of the land surface derived from remote sensing
Vegetative vigor is limited by soil moisture

## Slide 9
Normalized Difference
Vegetation Index
September 30, 2010
Source: 16-day cycle MODIS
UT Center for Space Research
NDVI on September 30, 2010

## Slide 10
Normalized Difference
Vegetation Index
September 30, 2011
Source: 16-day cycle MODIS
UT Center for Space Research
NDVI on September 30, 2011

## Slide 11
September 30
2010
September 30
2010

## Slide 12
September 30
2011
September 30
2011

## Slide 13
April 6
2012
April 6
2012

## Slide 14: Water Availability during the Drought
Drought Technology Steering Committee
Water balance of Texas
Drought in West Texas
Texas water and climate model

## Slide 15: Measuring Gravity Anomaly from Space (GRACE) Force of gravity responds to changes in water volume Water is really heavy!
Gravity Anomaly of Texas, 2002 – 2012
Normal
In 2011, we lost 100 Km3 of water or 70 Lake Travis’s

## Slide 16: GRACE and Texas Reservoir Water Storage
Surface Water Reservoirs
In 2011 we lost 9 Km3 of water from reservoirs
Grace Satellites
Surface water reservoir storage is closely correlated with the GRACE data
In 2011 we lost 100 Km3 of water overall
Normal
Normal

## Slide 17: GRACE and Edwards Aquifer Levels
Texas Drought
2011
Texas Drought
2005-2006
Edwards Aquifer
J-17 well
Grace Satellites
Edwards aquifer levels are also correlated with the GRACE data
Normal
Normal

## Slide 18: Soil Water In Texas
Soil Texture Map
First meter of Texas soil contains 11 cm of soil water and soil air
Soil Wetness Index
Solid Particles
Soil Water
Soil Air
0
100
Oven Dry
Saturated
Soil water system has 78 Km3 of water storage capacity in top 1m of soil

## Slide 19: Texas Soil Wetness Index
% soil water capacity
Average = 40%
Soil water storage in first meter of soil = 4 cm, or 31Km3 of water
1 June 2012

## Slide 20: Soil Wetness Index, Travis County, January 2011 - May 2012
Chart: 
| 41030 | 41000 | 40969 | 40940 | 40910 | 40878 | 40848 | 40817 | 40787 | 40756 | 40725 | 40695 | 40664 | 40634 | 40603 | 40575 | 40544
SWI_perc | 47.4231 | 66.4961 | 63.078 | 61.52 | 56.996 | 37.1359 | 25.1855 | 17.5296 | 18.8251 | 22.1838 | 30.1762 | 35.1765 | 37.9577 | 46.6336 | 55.1541 | 61.658 | 48.174
Effect of Spring Rains

## Slide 21: GRACE and Texas Soil Water Storage
Texas Soil Water Storage
We lost 25 Km3 of water from top 1m of soil
Grace Satellites
In 2011 we lost 100 Km3 of water overall
Normal
Normal

## Slide 22: Summary Water Balance of Texas
Overall changes in Texas water storage can be measured from space by the GRACE satellites
In 2011 drought we lost 100 Km3 of water (70 Lake Travis’s)
  About 9 Km3 from surface water reservoirs
  Approximately 25 Km3 from the soil water system
  About two thirds from shallow groundwater
We have regained most of this lost water
We need county level metrics of water availability for better drought management

## Slide 23: Water Availability during the Drought
Drought Technology Steering Committee
Water balance of Texas
Drought in West Texas
Texas water and climate model

## Slide 24: Drought in West Texas

## Slide 25
San Angelo
Odessa
Midland
Reservoirs

## Slide 26: Lake O.C. Fisher, August 2010

## Slide 27: Lake O.C. Fisher, Jan 2012

## Slide 28: Lake E.V. Spence, August 2010

## Slide 29: Lake E.V. Spence, Jan 2012

## Slide 30: O.H. Ivie Reservoir
  Owned and operated by the Colorado River Municipal Water District
  Purpose: Water Supply
  Supplies: Odessa, Big Spring, Snyder, Midland, Abilene, San Angelo, Ballinger
  Storage Capacity: 554,339 acre-feet
  Current Storage: 98,400 acre-feet
  2011 Change in Storage: -81,820 acre-feet
M. Bewley

## Slide 31
Drought in West Texas is chronic

## Slide 32: Saline Groundwaters of Texas
Pecos Alluvium

## Slide 33: Water Availability during the Drought
Drought Technology Steering Committee
Water balance of Texas
Drought in West Texas
Texas water and climate model

## Slide 34: Facing Drought in Texas
Texas population increased by 4.3 million in the last 10 years
  430,000 people per year
  1180 people per day
We have a Texas Water Plan but little money to implement it
The clock is ticking …..

## Slide 35: Texas Water and Climate Model
Last severe drought in 1996 led to Senate Bill 1 in 1997 and SB2, SB3 later
Great improvement in long term water planning (10 to 50 years in future)
The 2011 drought exposed
  We don’t have synthesized situational awareness of current condition of our water system state-wide
  We need to be able to see ahead 6-18 months for rational water decision making

## Slide 36: Drought Technology
Atmosphere
Groundwater
Soil Water
Surface Water
Water Cycle
Economic Development
Public Water Supply
Agricultural Production
Electric Power Generation
Ecological Integrity
Impacts
Observations – Modeling – Assessment – Prediction
Notes: The intent of the Drought Technology Steering Committee is to bring the best available science and technology to bear on quantifying the storage and flow of water in Texas, and the impacts of water shortage on key water functions in the state.

## Slide 37: Texas Water and Climate Model
Statistics from past
Current situation
Short-term predictions
Improve our state-wide, real-time situational awareness of water conditions

## Slide 38: Calculate the Soil Water Balance of Texas
Temperature
Precipitation
Wind speed
Specific humidity
Surface pressure
Downward SW radiation
Downward LW radiation
Noah-MP land surface model
Surface runoff
Sub-surface runoff
Soil moisture
Evapotranspiration
Water table ……
Soil
type
Soil
color
Green
vegetation fraction
Land
cover
Model output
NLDAS atmospheric forcing
Land surface features

## Slide 39
RAPID River Flow Model

## Slide 40: Synthesized Real-Time Water Models, Observations, Maps and Graphs
http://www.CentralTexasHub.org

## Slide 41: Conclusions
GRACE Satellites can directly measure overall change in water storage in Texas
In 2011, we lost 100 Km3 of water, but conditions have returned to nearly normal
County-based metrics are needed to quantify drought severity and its spatial patterns
Surface water storage is almost gone in West Texas – switching to groundwater supply
We need a Texas Water and Climate Model