## Slide 1
The University of Texas at Austin
US Geological Survey
KISTERS
ESRI
Quarterly
Review 1
TxDOT Project 0-7095-01
Flood Assessment System for TxDOT (FAST)
August 1, 2024

## Slide 2: Every project is a safety project.
Texas has lost at least one person every day on Texas roads since Nov. 7, 2000.
Notes: Texas has the highest number of roadway fatalities of any state in the country.

## Slide 3: FEMA Press Release NR209 (May 8, 2018) – All Texans are at risk for floods
No place is safe from flooding. If it can rain, it can flood. And nowhere is that truer than Texas.
Nearly every major city in Texas is vulnerable to Gulf Coast hurricanes or sits in “Flash Flood Alley,” one of the most flash flood-prone areas in the nation. More than 200,000 single-family homes in disaster-declared Texas counties were flooded by Hurricane Harvey last year, and many of them were in areas not considered high-risk for floods.
Don’t assume your area won’t flood because it hasn’t in the past: Risk of flooding can change considerably as factors like drought and urban development affect the ground’s surface. Nationwide, 26 percent of flood insurance claims come from properties outside high-risk zones.
Notes: We are especially vulnerable to flooding in Texas.

## Slide 4: Turn Around, Don’t Drown.
On average, over 50% of flood fatalities occur in cars.
Notes: TxDOT has a role to play in solving this problem. And we all do better, when we all do better.

## Slide 5: Reactive Proactive
Notes: Bird’s eye view of what we’re doing here

## Slide 6
  TxDOT Project Management Committee (PMC)
Rose Marie Klee – Lead Advisor TxDOT DES - H&H Section Director
Matthew Heinze – Lead Advisor
TxDOT MNT – Maintenance Support Section Manager
Chris Henry
TxDOT MNT – Deputy Director
Trenton Ellis
TxDOT H&H – H&H Engineer
Jared Browder
TxDOT MNT – TxMAP Specialist
Valerie Taylor
TxDOT HOU – Transportation Engineer
Omar DeLeon
TxDOT MNT/AUS – Director of Maintenance
Ryan Granger
TxDOT STR – Strategic Mgmt Analyst
Stephanie Marquez
TxDOT TTP-GIM - Statewide GIS Data Engineer
Mark Wallace
TxDOT BRG – State Bridge Inspection Program MGR
ChunHo Lee
TxDOT BRG – Geotechnical Engineer
Mauricio Moreno
TxDOT ITD – Information Security Architect
Allison Wood
TxDOT DES / Huitt-Zollars
Jade Adediwura – Project Manager
TxDOT RTI – Research Project Manager

## Slide 7
  TxDOT Technical Project Management Team (TPMT)
Rose Marie Klee – Lead Advisor TxDOT DES - H&H Section Director
Trenton Ellis
TxDOT DES - H&H Engineer
Allison Wood
TxDOT DES / Huitt-Zollars
Stephanie Marquez
TxDOT TTP-GIM - Statewide GIS Data Engineer

## Slide 8
  TxDOT Technical Stakeholders
Matthew Heinze – Lead Advisor
TxDOT MNT – Maintenance Support Section Manager
Carolyn Brooks
TxDOT PRO – Special Projects Coordinator
Missy Lowe
TxDOT MNT – Maintenance Field Support Manager
Jared Browder
TxDOT MNT – TxMAP Specialist
Mysti Tran
TxDOT ITD – IT Planning & Admin System Branch Manager
Joy Morales
TxDOT ITD – IT Applications Delivery Lead
Bijal Patel
TxDOT ITD – Management Analyst
Jason Henderson
TxDOT ITD – GIS Systems Architect
Mauricio Moreno
TxDOT ITD – Information Security Architect
Aiko Neill
TxDOT ITD – IT Contract Management Branch Manager
Lisa Ramirez
TxDOT ITD – Contract Administrator
Alonzo Balderaz
TxDOT ITD – GIS Development & Maintenance Lead
Priscillo Campos
TxDOT ITD – Management Analyst

## Slide 9
  Project Advisory Committee
NOAA Weather Forecast Office
Jonathan Brazzell
West Gulf River Forecast Center, Lake Charles Office
Katie Landry-Guyton
West Gulf River Forecast Center, Houston/Galveston Office
Amanda Schroeder
West Gulf River Forecast Center, Dallas/Fort Worth Office
State and Local Agencies
Jorge Urquidi
City of Austin, FEWS Team
Sam Marie Hermitte
TWDB, Water Science Conservations
Christina Bryant
City of Austin, FEWS Team
Peter Smith
former TxDOT Director TPP
TxDOT H&H Section
Ab Maamar-Tayeb
Davis Magenheimer
Edra Brashear
Harrison Smith
+ TxDOT Project Management Committee
Maria Thomas
Shu Gao
Zenia De Leon
NOAA National Weather Service
Jason Johnson
West Gulf River Forecast Center
Paul McKee
Southern Region HQ
Fernando Salas
Geo-Intelligence Division
Paul Yura
Austin/San Antonio WFO
US Corps of Engineers
Matthew Lepinski
Lead Hydraulics Engineer, Water Resources Branch FTW
Jeff Linder
HCFCD

## Slide 10
Task 2
Task 3
Task 4
Task 5
Task 6
Flood
Map Services
Flood Decision Support Gauges
Flood Transportation Geodatabase
Flood
Data Services
Forecast Data Analytics
Flood Map
Development
Flood Map Delivery
Field Mapping
Flood Emergency
Response Exercises
Gauge Operation and Maintenance
Gauge Calibration
RQ30 Flood Decision Support Toolbox Sites
Velocity – Stage Height Interaction
Synthetic Rating Curves
Road Elevation Model
Stream Hydrography
Road Inundation
Span Bridges
Bridge Class Culverts
Low Water Crossings
Bridge Warnings
Flooded Road Inundation
Flood Impact Assessment
Data Assimilation Implementation
Transportation Flood Impact Simulation
Probability of Road Overtopping
Assimilation in Space and Time
Regional Error Assessment
  Project Tasks and Subtasks
Task 1
Project Management
Organization, Coordination,
Reporting, and Communication
Dr. David Maidment
Kristine Blickenstaff

## Slide 11
Task Components
Task 6
Forecast Data Analytics
Subtask 6.1 Probability of Road Overtopping
Subtask 6.2 Assimilation in Space and Time
Subtask 6.3 Regional Error Assessment
Dr. Paola
Passalacqua
Dr. Matt Bartos

## Slide 12
  Task 6: Quantifying Forecast Error
Regional Error Assessment:
NWM 3.0 struggles to predict streamflow
accurately especially during major storm events.
Draft of paper for the regional error assessment for NWM 2.1 and 3.0 is ready, undergoing revisions for final submission for publishing.
NWM 3.0 struggles to predict streamflow accurately especially during major storm events.
Fig: Spatial Distribution of NNSE for NWM 3.0 during (a) Hurricane Harvey, (b) TS Imelda, and (c) Hurricane Hanna. NNSE<0.5 in most locations.
Dr. Paola
Passalacqua

## Slide 13
Streamflow prediction improves with Data Assimilation
DA improves the streamflow prediction at the validation site for 2018 Llano flood
  Task 6: Data Assimilation with the CFE Model
CFE (Conceptual Functional Equivalent) Model:
One of the hydrological models considered for the
NextGen Framework.
A simplified conceptual model designed to be functionally
equivalent to the NWM.

## Slide 14: Further Improvement of Data Assimilation in Space with Spatial Correlation
Quantifying the Spatial Correlation In Guadalupe Basin
Initial Results for Spatial Correlation in Guadalupe Basin for 2018 storm
  Task 6: Further Improvement of Data Assimilation
Topological Kriging: A geostatistical method used for predicting spatial variables along river networks where the flow path significantly influences spatial relationships.
Current study focuses on spatial correlation within
the Llano, Guadalupe, and San Antonio Basins.
2018-10-16 05:00:00
2018-10-16 10:00:00 (peak flow)

## Slide 15
  Task 6: Data assimilation with Kalman Filter
Data assimilation based on
Kalman Filtering extended to entire
USGS water resource region 12
(70,000 stream reaches)
Scaling to entire state facilitated by new parallelization scheme.
Positive correction
Negative correction
Dr. Matt Bartos
USGS water resource region 12

## Slide 16
  Task 6: Data assimilation
Tests on large river basins (San Antonio and Guadalupe) show that Kalman Filter greatly improves forecast accuracy
Kalman Filter
outperforms
Nudging
outperforms

## Slide 17
  Task 6: Data assimilation and False Flood Alarms
Reduce false alarms
Kalman Filter significantly reduces false flood alarms compared to raw National Water Model outputs

## Slide 18
  Task 6: Key Points: Knowledge Added and Operational Capabilities
We have quantified the performance of the current version of the NWM, providing a baseline for assessing improvements (Knowledge added)
We have developed an approach for scaling up the Data Assimilation approach over Texas (Operational capability achieved)
We are improving the DA approach temporal (forecasting) and spatial (spatial correlation) capabilities, which we will integrated in the scaled up approach (developing Knowledge and improving Operational capability)
National Water Model
Observations
Error assessment (baseline)
Data Assimilation over Texas
Spatial correlation
Improved forecasting
Quantified forecasting improvements

## Slide 19
  Task 1: USGS Gauge Network
What will we know about the gauge network that we do not know now?
  Building a lower cost gauging network
    Externalizing the black box of the RQ-30 gauge
    Number of site visits needed for O&M/calibration
    Updated USGS standards
  Data improvements
    Velocity
    Scour
    Backwater
    Early warning
    Velocity – stage – discharge relationships
    Synthetic rating curve standardization
    Flood inundation mapping libraries
Who will benefit? – “We all do better, when we all do better.” – RMK
Kristine
Blickenstaff

## Slide 20
  Task 1: All Roads Lead to Texas
RQ-30 Gauges
Flood Assessment System
for TxDOT (FAST)
Flood Decision
Support Toolbox
Base Level Engineering
StreamStats
Integrated Water
Science Basins

## Slide 21
FAST Project Agreement
UT Project Management Plan
Technical Project Management Team (TxDOT IT, UT Dev, USGS)
Weekly Status Reports
Monthly Progress Reports
Quarterly Review
Reports
Development & TACH
Research
USGS Project Management
UT’s Project
Management
TxDOT’s Project Management
  TASK 1: DEVELOPMENT of FAST
USGS Project Management Plan
Feedback
Flood Decision Support Gauges
Harry Evans
Tim Whiteaker
Andy Carter
Christine Thies
Harry Evans
TACH Team

## Slide 22
  Project Vision - Next Three Years
What is TxDOT receiving?
  Flood Gauges
  Flood Forecasting
  Bridge Warning & Flooded Road data
  Real-time flood maps
Who will use it?
  TxDOT State EOC
  TxDOT District EOC’s
  TxDOT Maintenance Offices
  TxDOT Field Staff during flood operations
Where will it be housed?
  Flood Gauge data – USGS National Water Information System
  Flood Forecasting – NWS National Water Prediction System
  Flood Data Services – KISTERS cloud system (Amazon East cloud services)
  Flood Map Services – TxDOT Information Technology Division (temporarily located at UT Austin)

## Slide 23
Task Components
Subtask 2.1 Flood Map Development
Subtask 2.2 Flood Map Delivery
Subtask 2.3 Field Mapping
Subtask 2.4 Flood Emergency Response Exercises
Task 2
FLOOD MAP SERVICES
Harry Evans
Christine Thies

## Slide 24
  Task 2: Progress since last Quarterly Review (Dec 2023)
Draft prototype of
Bridge Warnings & Flooded Roads
Incorporated changes to
draft layers based on TPMT input
Bridge
Warnings
Flooded Roads
Gave TxDOT Access to Initial Datasets
Harry Evans

## Slide 25
  Task 2: Progress since last Quarterly Review (Dec 2023)
Developed draft mobile and desktop applications
Provided to TPMT for internal review
TPMT provided feedback which has guided production
Try it out!
Created a ‘Sandbox’ for TxDOT & UT Interactions
https://bit.ly/4d0I7KI

## Slide 26
  Task 2: Mustang Chase at Walnut Creek
Mustang Chase @
West Branch of Walnut Creek
FLOODED ROAD
in Dashboard
UT Field Reconnaissance
Field check
contradicts Bridge Warning Layer

## Slide 27
  Task 2: Royal Forest Dr at Caney Creek
Royal Forest Dr @
Caney Creek
FLOODED BRIDGE
in Dashboard
Field check validates Bridge Warning Layer
USGS Field Reconnaissance
Jody Avant

## Slide 28
  Task 2: Garrett Road at Austin Bayou
Garrett Rd @
Austin Bayou
FLOODED BRIDGE
in Dashboard
Field check validates Bridge Warning Layer
USGS Field Reconnaissance

## Slide 29
  Task 2: Damon School Rd at Mound Creek
Damon School Rd @
Mound Creek
2-5FT to BRIDGE
in Dashboard
Field check validates Bridge Warning Layer
3.9ft to deck
USGS Field Reconnaissance

## Slide 30
  Task 2: Plans for Next Quarter
Flood Emergency Response Exercises
Exercise Work Group
Emergency Response Priorities
Create overall Exercise Plan

## Slide 31
  First Discussion

## Slide 32
Task Components
Task 3
FLOOD DECISION
SUPPORT GAUGES
Subtask 3.1 Gauge Operation and Maintenance
Subtask 3.2 Gauge Calibration
Subtask 3.3 RQ30 Flood Decision Support Toolbox Sites
Subtask 3.4 Velocity – Stage Height Interaction
Subtask 3.5 Synthetic Rating Curves
Kristine
Blickenstaff
Scott Grzyb
Jon Thomas

## Slide 33
  Task 3: Field Visits
  179 gage visits
  67 measurements
  31 verification surveys

## Slide 34
  Task 3: Hurricane Beryl
  6-hour response time
  15 flood measurements over a 3- day campaign
  Stress test on the network
  Data collection during windy conditions
  Telemetry issues identified

## Slide 35
  Task 3: Calibrations
  20 gages calibrated
  Continue verification measurements at calibrated gages

## Slide 36
  Task 3: Bathymetric Surveys
  2 surveys completed
  Data processing with iRIC
  Determine what level of accuracy is needed for model derived discharge rating curves
Jon Nelson is starting
hydrodynamic modeling
Notes: Add a headshot of jon

## Slide 37
  Task 3: Observed Limitations
  Average velocity issues once water reaches the low chord
  Road overflow
  Power issues = Connectivity issues

## Slide 38
  Task 3: RQ-30 Flood Decisions Support Toolbox (FDST) Sites
  1D modeling for FDST flood maps (On-going): 25* sites completed, yet to be validated
2D modeling for FDST flood maps (started)
Jon Thomas

## Slide 39
  Task 3: Synthetic Rating Curves and the FDST
FDST validated by comparing the modeled stage-discharge relationship (rating curve) to the USGS measured rating curve
RQ30 gages do not have the measurements to validate the FDST models in flood stage
We are developing a regionalized stage-discharge relationship using a GAM model based on 17,000+ discharge measurements in TX to provide an estimated rating curve for new gages based on stream:
  Cross-section area (A)
  Top width (B)
  Other regional parameters
Method can provide a synthetic rating curve for any* stream location in Texas
*Estimates may be less accurate in certain scenarios, such as mountainous terrain or highly urbanized channels
Method is based on William Asquith's 2013 paper http://dx.doi.org/10.1061/(ASCE)HE.1943-5584.0000635

## Slide 40
  Task 3: Plans for Next Quarter
  Continue flood measurements and calibrations
  Continue bathymetric surveys
  Experiment with increased transmission frequency for flood events
  2D (14 locations) and 1D (8 locations) remain for FDST to be modeled and evaluated in FY24
  Finalize regional regression equation for synthetic rating curve effort
  Start assessment uncertainty across FEMA Region 6

## Slide 41
Task Components
Task 4
Flood
Transportation Geodatabase
Subtask 4.1 Road Elevation Model
Subtask 4.2 Stream Hydrography
Subtask 4.3 Road Inundation
Subtask 4.4 Span Bridges
Subtask 4.5 Bridge Class Culverts
Subtask 4.6 Low Water Crossings
Andy Carter, P.E.
Dr. David
Maidment
Dr. Tim
Whiteaker

## Slide 42
Dynamic
Flood Map Service
Static
Flood Transportation
Geodatabase
Flood Forecast
Streamflow Measurement
Adjusted Forecast
Impact
Assessment
2D Roads
and bridges
Lidar terrain measurement
Quality Control and Checking
3D Roads
and bridges
  Flood Assessment System for TxDOT (FAST)
  Conceptual Framework
FY24 Austin District On-System
FY25 State-wide On-System
FY26 State-wide public roads

## Slide 43
  Task 4: Flood Transportation Geodatabase
Flood Transportation Geodatabase
Develop a geodatabase schema that relates the built world
(roads, culverts, bridges)
with the flood inundation modeling

## Slide 44
  Task 4: Flood Inundation Mapping
Flood Transportation Database
Flood Inundation Layers
Methods to extract flood inundation layers and rating curves
We have begun with HAND and will include HEC-RAS mapping later

## Slide 45
  Task 4: Flood Transportation Geodatabase Components
Road Lines
Pavement Limit Polygons
Streamlines
Streamline / Road Intersections
Road Elevation Model
(from LiDAR)
Culverts
Low Water Crossings
Bridges
A 3D geographically integrated database of roads, streams, bridges, culverts and low water crossings

## Slide 46
  Task 4: ESRI Team for Geodatabase Design and Quality Control Checking
Dean Djokic
Principal Technical Consultant
Water Resources Practice
Arc Hydro Lead
Michelle Johnson
Principal Technical Consultant
Geodata Engineering; QA/QC
Flood Transportation Database design
Flood Transportation
QA/QC design

## Slide 47
  Task 4: Flood Transportation Geodatabase Design
Translating concepts into integrated data system
  Raster
  Vector
  Tables
Key elements:
  Topography
  Hydrography
  Hydrology/hydraulics/forecasting
  Critical infrastructure
  Reporting units

## Slide 48
  Task 4: Flood Transportation Geodatabase Design
Key elements:
  Topography
  Hydrography
  Hydrology/hydraulics/forecasting
  Critical infrastructure
  Reporting units

## Slide 49
  Task 4: Geodatabase Design and Quality Control Checking

## Slide 50
  Task 4: Example: Road Crossing a Stream

## Slide 51
  Task 4: Composite Check being Configured in Data Reviewer

## Slide 52
  Task 4: Error Inspector used to Identify Issues

## Slide 53
Task Components
Task 5
Flood DATA SERVICES
Subtask 5.1 Road Elevation Model
Subtask 5.2 Stream Hydrography
Subtask 5.3 Road Inundation
Subtask 5.4 Span Bridges
Subtask 5.5 Bridge Class Culverts
Subtask 5.6 Low Water Crossings
Andy Carter, P.E.
Dr. Tim
Whiteaker
Dr. Attila Bibok

## Slide 54: Computed 1-meter Road Digital Elevation Model
  Task 5: Flooded Road and Bridge Services
For Austin District
Built from lidar
Supports flooded road computation
Dr. Tim
Whiteaker

## Slide 55: Published flooded road feature service in ArcGIS Online (AUS only)
  Task 5: Flooded Road Service

## Slide 56: Published bridge warnings service in ArcGIS Online and as GeoJSON (TX)
  Task 5: Bridge Warning Service

## Slide 57
  Task 5: Progress since last Quarterly Review (Dec 2023)
OLD - Bridge Warning Prototype
NEW – Draft bridge warning Dashboard
Stand-up an [DRAFT] operational web service, using Kisters backend servers, that deploys a flooded bridge and flooded road system.
Agnostic data endpoints: GeoJSON, GIS Feature Layers, FAST API, etc…
Andy Carter, P.E.

## Slide 58
  Task 5: Bridge Cross Section Service
Bridge Cross Section Service: How it works
Bridge definition
database
KISTERS AWS s3 bucket
NWPS
0,0,1000,2000,2000,….
User defined flow list
Streamflow sources
Datasphere
Bridge Warning Service
(on AWS - Kisters)
https://bridges.txdot.kisters.cloud/xs/?uuid=00a1d8c7-2ead-4fc4-ae9c-928146a4460c&source=datasphere&product=short_range
Interactive Bridge Cross Section view (Web page)
Example URL:

## Slide 59
  Task 5: Bridge Warning API
Deploy an agnostic API for bridge warnings
https://bridges.txdot.kisters.cloud/xs/?
uuid=00a1d8c7-2ead-4fc4-ae9c-928146a4460c
list_flows=0,0,0,0,0,0,0,100,1000,5000,28000,42000,50000,45000,42000,35000,30000,25000
first_utc_time=2023-10-26T02:00:00
Click to see requested bridge (kisters.cloud)
https://bridges.txdot.kisters.cloud/docs
Documented API – using SWAGGER

## Slide 60
  Task 5: Current Web Architecture
Bridge definition
database
Static Assets
Road Flooding Susceptibility
Realtime Streamflow sources
Datasphere
Flooded Road and bridge backend
Ingested to create Feature layers
Realtime warning raw data
What is predicted to flood?
Web Maps
Creating flooded road and bridge geospatial
layers hourly … Expose them in web maps
Notes: We have a solid base of services -> Now we have to upgrade them with DA
Make the first subcatchment operational with DA
Update the services to receive the DA adjusted forecasts
Gradually improve the lag of available forecasts and opbservations

## Slide 61
  Task 5: Plans for Next Quarter
Bridge definition
database
Static Assets
Road Flooding Susceptibility
Realtime Streamflow sources
Datasphere
Flooded Road and bridge backend
Ingested to create Feature layers
Realtime warning raw data
What is predicted to flood?
Web Maps
Data Assimilation
USGS Gages +
National Water Model +
Installed RQ-30 gages =
Improved flow estimates
Adding ‘Data Assimilation’ flow data to show
the difference in predicted impacts
Notes: We have a solid base of services -> Now we have to upgrade them with DA
Make the first subcatchment operational with DA
Update the services to receive the DA adjusted forecasts
Gradually improve the lag of available forecasts and opbservations

## Slide 62
  Second Discussion