## Slide 1: Mapping for Real-Time Flood Emergency Response From National … to … Local
Presented by David R. Maidment Center for Water and the Environment University of Texas at Austin
ESRI Water Resources and Hydro Meeting
San Diego, CA
10 July 2022
Acknowledgments: National Water Center, Texas Department of Transportation
Christine Thies, UT Austin

## Slide 2: Conversations in 2013 ̶ 2014
Jack Dangermond President, ESRI
Craig Fugate
FEMA
Administrator
“Can we
do better?”
“Yes, Jack,
but not yet”
Flood Inundation mapping
at some forecast points
Regional flood forecasting
for large watersheds
“We need a national system for flood forecasting
and real-time inundation mapping”

## Slide 3: National Flood Forecasting
National Water Center
Established in 2014 in Tuscaloosa, AL

## Slide 4: National Water Model
Four model outputs:
Assimilation (Current conditions)
Short Range Forecast (18 hours ahead)
Medium Range (10 days ahead)
Long Range Forecast (30 days ahead)
Water forecast like weather 24/7/365
Water flow forecasts on 190,000 miles
of streams and rivers in Texas

## Slide 6: Operations Room at the National Water Center

## Slide 7: Geospatial Systems Are Helping Us Understand
. . . Helping Us Make Better Decisions
Data
Information
Knowledge
Understanding
Mapping
Integration
Sharing and Collaboration
Slide: Jack Dangermond

## Slide 8: 40 New Water Forecast Map Services
https://maps.water.noaa.gov/server/rest/services
Free and publicly available

## Slide 9: Through open water services everyone can see …
… what is seen at the National Water Center
https://www.weather.gov/owp/operations

## Slide 10: Water Flow Anomaly – Comparison with Average Flow Conditions Average for last 7 days
2.7 million stream reaches
covering United States

## Slide 11: ESRI Living Atlas Water Flow Map -- Conditions at Local Scale
Barton Creek is near
my home in Austin, Texas
It is reach 5781265
in the national stream network

## Slide 12: A Storm Occurring in North Dakota this Morning (10 July 2022)

## Slide 13: Probability of High Water in Next 12 Hours
Flooding is expected here

## Slide 14: High Flow Magnitude Measured as Annual Exceedance Probability
High flood risk that threatens I-94

## Slide 15: High Water Arrival Time
Flooding will occur soon

## Slide 16: Ending Time of High Water (Short Range Forecast up to 18 hours ahead)
Flooding will continue for more than 18 hours

## Slide 17: Ending Time of High Water (Medium Range Forecast up to 10 days ahead)
Flooding near I-94 will continue for 4-5 days

## Slide 18: Flood Web Map Services for Texas Department of Transportation
https://www.arcgis.com/apps/instant/basic/index.html?appid=bb7cb731322d47f4bfee629ca148e053

## Slide 19: Texas Department of Transportation

## Slide 20: TxDOT wants to move from Reactive response to Proactive response
Maintenance Staff
observing current
flood conditions
EOC staff
Decisions based on
current conditions
Reactive Response

## Slide 21: TxDOT wants to move from Reactive response to Proactive response
Proactive Response
Maintenance Staff
observing current
flood conditions
Predictive Storm and Flood Maps
EOC staff
Advance warning of location, extent
and severity of flooding
Decisions based on
current and predicted conditions

## Slide 22: Some Thoughts I have Heard
“We want to move from being reactive to being proactive”
Chris Henry, Director of Maintenance, BMT
“It’s the guys in the field who tell us what’s going on”
Keith Horn, Logistics Coordinator, BMT
“I want technology to be my eyes on the landscape”
Martin Gonzalez, District Engineer, BMT
“We need all the data in one place”
Eliza Paul, District Engineer, HOU
“At the SOC, we need warning 24-48 hours in advance”
Jared Browder, Maintenance Assessment Specialist, MNT
“We could close IH-10 in 3-6 hours”
Chris Henry, Director of Maintenance, BMT
“I want to know if there’s going be another Harvey”
Eliza Paul, District Engineer, HOU

## Slide 23: Flood Forecasting Project with Texas Department of Transportation
Largest research project ever supported by TxDOT ($6.38 million)

## Slide 24
Forecast Rain Map
Observation Gauges
High Water Streams and
Flooded Roads (HCRS)
Flood Inundation Map
Web Communication
to TxDOT (TxERA)
Rainmap in the Sky to Floodmap on the Ground
Maps accessible through ESRI StoryMap
https://arcg.is/0LLLXX
Maps prepared for a
flood emergency response exercise
in Beaumont District of TxDOT
February 2022

## Slide 25
Top New Products
Flooded Road Estimates
Precipitation Forecast by Section
Bridge Warnings
Estimated Depth
Ok (>10ft to bridge)
Concern (5 to 10ft to bridge)
Warning (< 5ft to bridge)
Out of Service (gauge not working)
X
Notes: Larry

## Slide 26: Predictive and Observational Flood Inundation Mapping
West Gulf River
Forecast Center
Predictive Flood
Mapping
Observational
Flood Mapping
State Operations Center
State Operations Center
Local EOC
First responders in field

## Slide 27: NWC Flood Inundation Map Services are based on … Height Above Nearest Drainage (HAND)
HAND
Flood
Normal
Flooding occurs when Water Depth is greater than HAND

## Slide 28: Pin2Flood on Onion Creek 14 October 2021
Tee Box
Tee Box
Tree
Tree
Based on Height Above
Nearest Drainage (HAND)
and 1m LIIDAR DEM

## Slide 29
During Flood – Common Operating Picture
University of Texas Center for Water and the Environment
Emergency Management Flood Project – Pin2Flood

## Slide 30: During Flood – Common Operating Picture
The first responder knows the scope and extent of the flood before them!
Emergency Managers can support and resource the response
Provides Common Operating Picture
University of Texas Center for Water and the Environment
Emergency Management Flood Project – Pin2Flood
https://gis.tdem.texas.gov/pin2flood/#

## Slide 31: Adding Adjacent Flood Polygons
A function requested by first responders in field exercises

## Slide 32: Pin2Flood Dashboard for Emergency Operations Center
https://gis.tdem.texas.gov/portal/apps/dashboards/4520d2fb7ceb41e180cdf29d97b0d2eb

## Slide 33
Pin2Flood Vision
Arrival of Response Units
University of Texas Center for Water and the Environment
Emergency Management Flood Project – Pin2Flood

## Slide 34
Flood calls start coming in..
02:00
Notes: What if….
During a flood you were able to use your phone to drop a pin…

## Slide 35
Units Arrive on-scene
Flood calls start coming in..
02:05
Notes: What if….
During a flood you were able to use your phone to drop a pin…

## Slide 36
Units Arrive on-scene
Flood calls start coming in..
Pin dropped at water’s edge
02:07
Notes: What if….
During a flood you were able to use your phone to drop a pin…

## Slide 37
Flood inundation calculated
Units Arrive on-scene
Flood calls start coming in..
Pin dropped at water’s edge
02:09
Notes: What if….
During a flood you were able to use your phone to drop a pin…

## Slide 38
Able to identify….
  Homes Impacted
Flood inundation calculated
Units Arrive on-scene
Flood calls start coming in..
Pin dropped at water’s edge
02:10
Notes: What if….
During a flood you were able to use your phone to drop a pin…

## Slide 39
Able to identify….
  Homes Impacted
  Population
Flood inundation calculated
Units Arrive on-scene
Flood calls start coming in..
Pin dropped at water’s edge
02:10
Notes: What if….
During a flood you were able to use your phone to drop a pin…

## Slide 40
Able to identify….
  Homes Impacted
  Population
  Flooded Roads
Flood inundation calculated
Units Arrive on-scene
Flood calls start coming in..
Pin dropped at water’s edge
02:10
Notes: What if….
During a flood you were able to use your phone to drop a pin…

## Slide 41: Progress in 9 years ….
Jack Dangermond President, ESRI
“Can we
do better?”
“Ok, Jack
We’re doing
better now”
National
Local