## Slide 1: Unearthing the Unit Hydrograph
Rami Harfouch
Surface Water Hydrology
University of Texas at Austin, April 2010

## Slide 2
Peak flows (flood applications, channels design)
  Rationale method Q=C i A
Hydrograph (storage structures design)
  SCS triangular hydrograph
  SCS dimensionless hydrograph
  The Unit Hydrograph (UH)
Flow methods

## Slide 3
A UNIT HYDROGRAPH (UH) is
a direct runoff hydrograph resulting from 1 inch of excess rainfall generated uniformly over the drainage area at a constant rate for an effective duration

## Slide 4: Simple application of the UH
Applied Hydrology, Maidment

## Slide 5: Matrix Calculation
[P][U] = [Q]
Precipitation
UH
Discharge
Applied Hydrology, Maidment

## Slide 6: How to calculate the UH?
Solution by successive approximation (Collins 1939)
Solution by linear regression (Snyder 1955)
  [P] [U] = [Q]
  Transform [P] to a square matrix (because rectangular matrix don’t have an inverse)
  [P]T[P][U] = [P]T [Q]
  Let [Z] = [P]T[P]
  [U] = [Z]-1 [P]T [Q]
In excel,
=MMULT(MMULT(MINVERSE(MMULT(TRANSPOSE(L9:W25),L9:W25)),TRANSPOSE(L9:W25)),Y9:Y2)
=MMULT(MMULT(MINVERSE(MMULT(TRANSPOSE(L9:W25),L9:W25)),TRANSPOSE(L9:W25)),Y9:Y2)
It is easy…

## Slide 7
Selecting a watershed and the Gauging stations
Selecting the storm events
Modify the rainfall and flow events (excess rainfall, adequate time steps)
Computing the different Unit Hydrographs, and adapting them into one
Plug the UH for other storm events, calculate streamflow and compare them to the measured
1
2
3
4
5

## Slide 8: Watershed selection criteria
Flow and precipitation gages with real time information
Unregulated with Hortonian flow and no snow = No storage
Small watershed (to have a uniform distribution of rain) VS big watershed (where UH is usually used)
In Texas!

## Slide 9
Streamflow gagesRunoff coefficients
0- 0.15
0.15 – 1
1- 2.7
2.7 - 7.8
7.8 – 12.7
#
USGS precipitation gages
4
0
275
550
137.5
Kilometers
Precipitation and streamflow gages with available real time data

## Slide 10
Someplace in Texas

## Slide 11
No rain or no data?!
Edwards Aquifer = Non Hortonian Flow
Selection of the watershed depends on the runoff information

## Slide 12: Selection of the storms
Short and strong storms
Single-peaked hydrograph of short time base

## Slide 13: Case study: Guadalupe River at Hunt Texas

## Slide 14
Increasing the time step depending on the length of the event, and the response time
Calculating the excess rainfall Hyetograph using the Ф-index method
Raw data
Modified Data
One more Increase of the time step from 1h to 2hrs to create a continuous event

## Slide 15
t(h) | Excess Rainfall (in) | Q(cfs)
2 | 0.22 | 68.375
4 | 0.03 | 76
6 | 0.07 | 78.75
8 | 0.26 | 94
10 | 0.77 | 183.5
12 | 0.37 | 9595.12
13 | 0 | 24425
14 | 0 | 15150
15 | 0 | 6435
16 | 0 | 3708.75
17 | 0 | 3201.25
18 | 0 | 2043.75
19 | 0 | 1423.75
20 | 0 | 1079.75
21 | 0 | 876.875
22 | 0 | 781.75
23 | 0 | 692
  [U] = [Z]-1 [P]T [Q]
[P]
[Q]

## Slide 16: The result…
-6780.256
7333.716
21992
7301.544
4512.247
234.5135
4682.728
-486.1719
1222.673
1192.859
-279.9168
1356.144
“The resulting Unit Hydrograph may show erratic variatons and even have negative values”
Maidment, Applied Hydrology
Chart: Time hrs
| 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24
Calculated raw UH | -6504.2292 | 7225.5211 | 22047.5218 | 7283.2488 | 4525.7209 | 208.2438 | 4705.0397 | -500.9433 | 1227.1708 | 1197.6682 | -285.9693 | 1359.2377
UH (τ=2hrs,bf=500cfs)

## Slide 17
Chart: Time hrs
| 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24
Calculated raw UH | -6504.2292 | 7225.5211 | 22047.5218 | 7283.2488 | 4525.7209 | 208.2438 | 4705.0397 | -500.9433 | 1227.1708 | 1197.6682 | -285.9693 | 1359.2377
Modified UH | 500 | 7225.5211 | 22047.5218 | 7283.2488 | 3000 | 1500 | 750 | 200 | 0 | 0 | 0 | 0

## Slide 18
Impulse response functions
Measured VS calculated hydrograph

## Slide 19: …No other storm event to test the UH
Only 1 event near Hunt in the last 120 days…

## Slide 20
The UH is better calculated from strong and isolated storm events… Not many of them happened in the last 120 days
Next:
  Find THE watershed with the perfect storms and storm information
  Create a synthetic Hydrograph from the UH and test it for other stream gages in the watershed
  Compare the peak flows from the UH and the rationale method (C i A)