## Slide 1: Terrain Processing of Sanderson, Texas
Laura Hurd

## Slide 2: Overview
Terrain overview
Flood of 1965
Terrain Pre-Processing
Terrain Accuracy
Dams
Flooding

## Slide 3
Terrain overview: Sanderson HUC 8-13040208

## Slide 4: Terrain Overview: 2500ft drop over 30 miles= 1.7% Slope

## Slide 5: Terrain overview: Zoom-in of Sanderson Terrain (ft)

## Slide 6: Flood of 1965 (100,000cfs)

## Slide 7
Terrain Pre-Processing
NED data was 1/3 arcsecond (~10m) (http://seamless.usgs.gov)
  projected the grid with NAD 1983 UTM Zone 13N
Used 100K NHDPlus flow-lines
Used Basic Dentritic Terrain Processing tool to get flow accumulation, catchments etc.
  First Burned the NHD flowlines to get the AGREE-DEM

## Slide 8: Terrain Accuracy
Compared DEM with geodetic benchmarks
  benchmarks had A or B stability and an elevation datum of NAVD88
  Average difference is 6.1ft between the benchmarks and DEM
    Standard Deviation of the difference= 4.59ft
    The accuracy prescribed by FEMA is 2.4ft
Ortho-imagery quads used to compare terrain with DEM
  1:12,000 digital, mosaic 7.5 minute quads (http://datagateway.nrcs.usda.gov/)

## Slide 9: Terrain Accuray: 1:12,000 digital Ortho-imagery quads, mosaic 7.5 minute quads (http://datagateway.nrcs.usda.gov/)

## Slide 10: Dams: DEM (ft) with 11 dam sites

## Slide 11: Dam capacity

## Slide 12: Flooding: Water Surface elevation (meters) of 1965 Flood (100,000cfs)

## Slide 13: Flooding: Depth(meters) of 1965 Flood (100,000cfs)

## Slide 14
1965 Flood (100,000cfs)
100 yr. flood without dams (72,268 cfs)
100 yr. flood with dams (16,224 cfs)

## Slide 15: Flooding: NHD vs. Delineated stream without burning

## Slide 16: Flooding: Original DFIRM vs. Flow Produced in GIS

## Slide 17: Conclusion
Terrain is not accurate enough for this study
  Need more accurate LIDAR terrain data