## Slide 1
David R. Maidment and Harry R. Evans
Center for Research in Water Resources
University of Texas at Austin
Discussion with Hays County Emergency Response officials
San Marcos TX, 26 Aug 2015
Acknowledgements: Tomas Rodriguez, City of Austin
Community Flood Response System for Hays County

## Slide 2: The Opportunity
New National Water Center established on the Tuscaloosa campus of University of Alabama by the National Weather Service and federal agency partners
Has a mission to assess hydrology in a new way at the continental scale for the United States

## Slide 3: NWS River Forecast Centers (RFCs)
  Prepare river and flood forecasts using models based on average basin characteristics
  Provide forecast guidance to Weather Forecast Offices (WFOs)
  Issue daily stage and streamflow forecasts, rainfall and drought data and information, and flash flood guidance
  Work with water managers and other Federal Agencies
3
6000 sub-basins in continental US
Notes: RFC Summary

## Slide 4
FY15 Centralized Water Forecasting
Centralized Data Archive – all RFC data
Modeling Evaluation Service
  RFC and NWC modeling and forecasts
Modeling Testbed – new NWC capabilities
Centralized Water Forecasting Demonstration
National Water Center
Notes: TRANSITION INTO METHODS
FY15 PROJECT HAS FOUR CORE COMPONENTS
RFC archive
Model evaluation service
Modeling testbed
Centralized modeling demonstration

## Slide 5: Goal of the Experiment
Close the gap between National Flood Forecasting and Local Emergency Response
Demonstrate forecasting of flood impacts at “stream and street level”
National
Local
Weather and Hydrology
National Weather Service and federal agencies
National Water Center
River Flooding and Emergency Response
Local, State and Regional Agencies
Citizens

## Slide 6: NFIE Conceptual Framework
NFIE-Services: Web services for flood information
NFIE-Geo: National geospatial framework for hydrology
NFIE-Hydro: National high spatial resolution hydrologic forecasting
NFIE-River: River channel information and real-time flood inundation mapping
NFIE-Response: Community Flood Response System

## Slide 7: NHDPlus Version 2.1
National Elevation Dataset
National Hydrography Dataset
National Land Cover Dataset
Watershed Boundary Dataset
NHDPlus
Geospatial foundation for a national water data infrastructure
2.7 million reach catchments in US
average area 3 km2
reach length 2 km
Uniquely labelled

## Slide 8: Flood Information for Fritz Hughes Park Rd
National Hydrography Dataset Plus
catchment for Bear Creek
(area = 5.71 km2)
Low water crossing at
3400 Fritz Hughes Park Rd

## Slide 9: NFIE-Hydro Forecasting Model
Runoff
Streamflow
RAPID flow routing (for continental US)
Probabilistic flood forecasts
Weather model and forecasts (HRRR)
Land-Atmosphere Model (NOAH-MP)
Precipitation
Weather
Catchment-level forecasts
Computed for the continental US in 10 minutes at Texas Advanced Computing Center

## Slide 10: Next Step: National Water Prediction Model Configurations
Short-Range
‘Flood Prediction’
Long Range
‘Water Resources’
Analysis & Assimilation
Hourly
3-Hourly
~Daily (x16)
- 3 hrs
Cycling Frequency
WRF-Hydro IOC Configurations – May 2016
0-2 days
0-30 days
Forecast Duration
1km/250m/NHDPlus Reach
1km/250m/NHDPlus Reach
1 km/catchment /NHDPlus Reach
Spatial Discretization & Routing
MRMS blend/ HRRR-NAM bkgnd.
Downscaled HRRR /RAP/NAM blend
Downscaled & bias-corrected CFS
Meteorological Forcing
Medium Range
‘Flow Prediction’
Daily
0-10 days
1km/250m/NHDPlus Reach
Short-range + Downscaled GFS

## Slide 11: Current and NFIE Forecast Systems
130 Catchments and Flowlines
uniquely labelled
Two basins and one forecast point
becomes
Current: 6600 basins and 3600 forecast points
NFIE: 2.7 million stream reaches and catchments
A national flow network
Blanco River at Wimberley
Forecast Basin ~ 400 Square Miles
Reach Catchment ~ 1 Square Mile

## Slide 12: Linear Referencing on Flowlines
Lat.
Long.
Measure
Stream Gage at RR 12 is at Measure 70.246
on Flowline 1630223
Measure is the % distance upstream from most downstream point on line
Using measures, the flow can be estimated at any point along the line

## Slide 13: Improvements in Flood Response Planning
Federal
State
Local
Citizen
GIS database and flood discharge forecasts
for 2.67 million stream reaches in
continental US from National Water Center
Conversion to water level forecasts and
inundation maps for 102,000 reaches in Texas
using 10m terrain data. Address points for flood
emergency response planning in each reach
Flood impact on transportation system
Flood response planning for stream reaches
and critical infrastructure. Inundation mapping
using LIDAR terrain data, if available.
Flood response portal for citizens (ATXFlood)
Automated flood warnings from cell-phone
towers to phones in flood risk zones

## Slide 14: NFIE-Geo for Texas
102,000 NHDPlus reach catchments for Texas
Average area 7.1 km2
Average reach length 3 km
NHDPlus reach catchment
Uniquely labeled across nation

## Slide 15: NFIE-Geo for Hays County
264 Forecast Reaches within County Boundary

## Slide 16: 264 Forecast Reaches in Hays County

## Slide 17: Memorial Day Weekend Precipitation
Total Precip.
(inches)

## Slide 18: Flow in Blanco River at Wimberley
40 ft wall of water overwhelmed the gage

## Slide 19: Drought to Deluge!
Reservoir storage doubled in 10 days
Lake Travis near Austin, Texas, has been in drought for the last four years
How can this happen?

## Slide 22
Saturday, May 23, 6 AM
Storm Rainfall during Memorial Day Weekend
http://gis.ncdc.noaa.gov/map/viewer/#app=cdo&cfg=radar&theme=radar&display=nexrad
Saturday, May 23, noon
Saturday, May 23, 6 PM
Saturday, May 23, Midnight
Sunday, May 24, 6 AM
Sunday, May 24, noon
Sunday, May 24, 6 PM
Sunday, May 24, Midnight
Where are the corresponding flood maps on the ground?

## Slide 23: National Flood Hazard Layer in Texas (~ 120 counties)

## Slide 24: Real-Time Flood Inundation Mapping (USGS/NWS)
http://water.weather.gov/ahps2/inundation/inundation_google.php?gage=atit2

## Slide 25: Elevation-indexed flood mapping
Map sequence for each point
Center Points of Reaches
Hays County

## Slide 26: Flood warnings from cell-phone towers
Flood Risk Zone
Detect phone in flood zone
Send warning
Cell Phone Tower

## Slide 27: National Flood Interoperability Experiment (NFIE) Conceptual Framework
NFIE-Services: Web services for flood information
NFIE-Geo: National geospatial framework for hydrology
NFIE-Hydro: National high spatial resolution hydrologic forecasting
NFIE-River: River channel information and real-time flood inundation mapping
NFIE-Response: Community Flood Response System

## Slide 28: Community Flood Response Map Book
Source: Tomas Rodriguez, City of Austin

## Slide 31: Situational Awareness For Everyone (SAFE)
Flood SAFE Viewer: http://arcg.is/1LPOHnE
Source: Jared Allen, NWS Austin-San Antonio Weather Forecast Office

## Slide 32: SAFE Map for Blanco River near Wimberley, Tx
Source: Jared Allen, NWS Austin-San Antonio Weather Forecast Office
Blanco River Proof-of-concept Map: http://arcg.is/1GtObu3

## Slide 33: Flood Emergency Response
Action
Planning
Emergency Responders
Public
Incident Response
Warnings
Wide Area Flood Plan
Public Education
Current and forecast storm rainfall
Creates Flood Response Maps
Current and forecast flood conditions
Impact on homes, critical infrastructure, and transportation routes
Public notification and warnings
Current and anticipated road closures
Real-time and forecast flood maps
Evacuation routes
Static flood maps
Number of flooded homes, critical infrastructure and transportation routes for different risk conditions
Pre-planning of flood response mobilization
Location based risk
Evacuation routes
Putting together a “go bag” for evacuation
Flood hazard prevention methods

## Slide 34: Flood Response: 4 Critical Functions
Action
Planning
Pre-planning
Public Education
Real-Time Flood Maps
Warnings

## Slide 35: Flood Response: 4 Critical Functions
Action
Planning
Pre-planning
Public Education
Real-Time Flood Maps
Warnings

## Slide 36: Pre-Planning
Why: enhance disaster response
What: prepare for these types of floods:
  Flash flood – short duration pulse; high risk, high mortality
  Flat-water flood – chronic event; lower velocity, longer duration
Who: federal/state + local jurisdiction

## Slide 37: Pre-Planning
Identify, map & prioritize high risk areas
    Critical infrastructure
    Key resources
    Vulnerable population
    First-responder access routes
    Public evacuation routes

## Slide 38: Pre-Planning Outputs
Flood response maps
Roads, bridges, address points, low-water crossings (where available)
First-responder access & public evacuation routes
Go / no-go decision support data
    Blocked roads
    Reflex time (to evacuate a risk area)

## Slide 39: Flood Response: 4 Critical Functions
Action
Planning
Pre-planning
Public Education
Real-Time Flood Maps
Warnings

## Slide 40: Public Education
Why: more public awareness & readiness results in more effective flood response
    Plus much less costly than flood response!!!
What: professional materials & campaigns
    Educate on go / no-go decision process
    Warning message content (including disabilities, language barriers)
    Ready, Set, Go (public guidelines for action)

## Slide 41: Flood Response: 4 Critical Functions
Action
Planning
Pre-planning
Public Education
Real-Time Flood Maps
Warnings

## Slide 42: Real-Time Flood Response Maps
Pushed to emergency managers, and to first responders on maps and mobile devices
    Real time precipitation data
    Expected rise and flood level
    Address points affected
    Low-water crossings
    Threats to critical infrastructure & key resources
      Utilities, communications, roads
      Hospitals, schools, public safety, food & fuel

## Slide 43: Flood Response: 4 Critical Functions
Action
Planning
Pre-planning
Public Education
Real-Time Flood Maps
Warnings

## Slide 44: Public Warnings
Warnings must convey a credible threat, and be actionable
    Explanatory enough to not be ignored
    Go / no-go directions
    Flood maps available to the public
    Complement Integrated Public Alert and Warning System (IPAWS)
Must consider social media
    Twitter, Facebook, Instagram, etc.
    Cell phone alert in flood zone
    News media: need consistent messaging
    Monitor social media via hotspot mapping