## Slide 1
David R. Maidment and Harry R. Evans
Center for Research in Water Resources
University of Texas at Austin
Texas Division of Emergency Management
Austin, TX| 30 October 2015
Acknowledgements: Ed Clark, Fernando Salas, Marcelo Somos Valenzuela, Andy Ernest
ESRI, Kisters, Microsoft Research
National Flood Interoperability Experiment for the Texas Emergency Response

## Slide 2: The Opportunity
New National Water Center established on the Tuscaloosa campus of University of Alabama by the National Weather Service and federal agency partners
Has a mission to assess hydrology in a new way at the continental scale for the United States

## Slide 3: NWS River Forecast Centers (RFCs)
  Prepare river and flood forecasts using models based on average basin characteristics
  Provide forecast guidance to Weather Forecast Offices (WFOs)
  Issue daily stage and streamflow forecasts, rainfall and drought data and information, and flash flood guidance
  Work with water managers and other Federal Agencies
3
6600 sub-basins in continental US
Notes: RFC Summary

## Slide 4
FY15 Centralized Water Forecasting
Centralized Data Archive – all RFC data
Modeling Evaluation Service
  RFC and NWC modeling and forecasts
Modeling Testbed – new NWC capabilities
Centralized Water Forecasting Demonstration
National Water Center
Notes: TRANSITION INTO METHODS
FY15 PROJECT HAS FOUR CORE COMPONENTS
RFC archive
Model evaluation service
Modeling testbed
Centralized modeling demonstration

## Slide 5: Goal of the Experiment
Close the gap between National Flood Forecasting and Local Emergency Response
Demonstrate forecasting of flood impacts at “stream and street level”
National
Local
Weather and Hydrology
National Weather Service and federal agencies
National Water Center
River Flooding and Emergency Response
Local, State and Regional Agencies
Citizens

## Slide 6: NFIE Conceptual Framework
NFIE-Services: Web services for flood information
NFIE-Geo: National geospatial framework for hydrology
NFIE-Hydro: National high spatial resolution hydrologic forecasting
NFIE-River: River channel information and real-time flood inundation mapping
NFIE-Response: Wide area planning for flood emergency response

## Slide 7
Saturday, May 23, 6 AM
Storm Rainfall during Memorial Day Weekend
http://gis.ncdc.noaa.gov/map/viewer/#app=cdo&cfg=radar&theme=radar&display=nexrad
Saturday, May 23, noon
Saturday, May 23, 6 PM
Saturday, May 23, Midnight
Sunday, May 24, 6 AM
Sunday, May 24, noon
Sunday, May 24, 6 PM
Sunday, May 24, Midnight
Where are the corresponding flood maps on the ground?

## Slide 8: Memorial Day Weekend Precipitation
Total Precip.
(inches)

## Slide 9: Flow in Blanco River at Wimberley
40 ft wall of water overwhelmed the gage

## Slide 10: Current and New Forecast Systems
130 Catchments and Flowlines
uniquely labelled
Two basins and one forecast point
becomes
Current: 6600 basins and 3600 forecast points
NFIE: 2.7 million stream reaches and catchments
A national flow network
Blanco River at Wimberley
Basin ~ 400 Sq Mile
Reach Catchment ~ 1 Sq Mile

## Slide 11: Linear Referencing on Flowlines
Lat.
Long.
Measure
Bridge and Stream Gage at RR 12 is at Measure 70.246
on Flowline 1630223
Measure is the % distance upstream from most downstream point on line
Using measures, the flow can be estimated at any point along the line

## Slide 12: Probability of Flooding on Shoal Creek, Austin, TX
Ensemble of 50 flood forecasts
ECMWF-RAPID flow forecasts
Deterministic flood maps
Probabilistic flood maps
HEC-RAS model
Rating curves library

## Slide 13: Progression of Memorial Day Flood

## Slide 14
Multi-Year Strategic
Science and Services Plan
Total Water Prediction and National Water Center
FY 15-20
FY 16-21
FY 17-22
FY 18-23
FY 19-24
Centralized Water Forecasting
Flash Flood and Urban Hydrology
Coastal Total Water Level
Dry Side: Drought and Post-Fire
Water Quality
National Water Model (NWM) operational May 2016
  Water forecasts for 2.7 million stream reaches in U.S.
  100 million people get a terrestrial water forecast for first time
  National Water Center (NWC) begins providing daily situational awareness and guidance to NWS field offices
Enhance NWM with nested hyper- resolution zoom capability and urban hydrologic processes
  Heightened focus on regions of interests (e.g. follow storms)
  Street level flood inundation forecasts for selected urban demonstration areas
  NWC increases guidance to NWS field offices to improve consistency and services for flash floods
Core Capability
Key Enhancement
Major Integration
Couple NWM with marine models to predict combined storm surge, tide, and riverine effects
  More complete picture of coastal storm impacts
  Water prediction information linked to geospatial risk and vulnerability
  New service delivery model implemented – increased stakeholder engagement and integrated information
  NWC operations center opens and provides national decision support services and situational awareness
Couple NWM with groundwater and transport models to predict low flows, drought and fire impacts
  Add NWM processes that affect subsurface water movement and storage during dry conditions
  Add NWM ability to track constituents (e.g. sediment, contaminants, nutrients) through stream network
  New decision support services for water shortage situations and waterborne transport
  NWC operations center expands to include drought and post-fire decision support services
Key Enhancement
Major Integration
Integrate enhanced NWM with key water quality data sets, models and tools to begin water quality prediction
  Incorporate water quality data from federal and State partners into NWM
  Link NWM output to NOAA ecological forecasting operations
  New decision support services for predicting water quality issues such as Harmful Algal Blooms
  New decision support services for emergencies such as chemical spills
  NWC operations center expands to include water quality decision support services
Slide Source: Dr Donald Cline, National Weather Service

## Slide 15: Next Step: National Water Prediction Model Configurations
Short-Range
‘Flood Prediction’
Long Range
‘Water Resources’
Analysis & Assimilation
Hourly
3-Hourly
~Daily (x16)
- 3 hrs
Cycling Frequency
WRF-Hydro IOC Configurations – May 2016
0-2 days
0-30 days
Forecast Duration
1km/250m/NHDPlus Reach
1km/250m/NHDPlus Reach
1 km/catchment /NHDPlus Reach
Spatial Discretization & Routing
MRMS blend/ HRRR-NAM bkgnd.
Downscaled HRRR /RAP/NAM blend
Downscaled & bias-corrected CFS
Meteorological Forcing
Medium Range
‘Flow Prediction’
Daily
0-10 days
1km/250m/NHDPlus Reach
Short-range + Downscaled GFS

## Slide 16: Improvements in Flood Response Planning
Federal
State
Local
Citizen
GIS database and flood discharge forecasts
for 2.67 million stream reaches in
continental US from National Water Center
Conversion to water level forecasts and
inundation maps for 102,000 reaches in Texas
using 10m terrain data. Address points for flood
emergency response planning in each reach
Flood impact on transportation system
Flood response planning for stream reaches
and critical infrastructure. Inundation mapping
using LIDAR terrain data, if available.
Flood response portal for citizens (ATXFlood)
Automated flood warnings from cell-phone
towers to phones in flood risk zones

## Slide 17: NFIE-Geo for Texas
102,000 NHDPlus reach catchments for Texas
Average area 7.1 km2
Average reach length 3 km
NHDPlus reach catchment
Uniquely labeled across nation

## Slide 18: Flood Information for Fritz Hughes Park Rd
National Hydrography Dataset Plus
catchment for Bear Creek
(area = 5.71 km2)
Low water crossing at
3400 Fritz Hughes Park Rd

## Slide 19: FEMA National Flood Hazard Layer in Texas (~ 120 counties)
Hidalgo County, Population 774,000
Cameron County Population 420,000
Blanco County

## Slide 20: NWS Flood Inundation Maps for the US (130 in total)
33 maps in Texas (one quarter of total)

## Slide 21: NWS Flood Inundation Maps in Texas
33 maps
12079 flood inundation extent polygons
1 ft or 0.5 ft intervals of elevation

## Slide 22: Real-Time Flood Inundation Mapping (NWS/AHPS)
http://water.weather.gov/ahps2/inundation/inundation_google.php?gage=atit2

## Slide 23: NWS Flood Inundation Map – Onion Creek at Highway 183 (ATIT2)

## Slide 24: Flood Extent Map for each 1 ft of geodetic elevation (25 maps in all)

## Slide 25: LIDAR Terrain Data Available from TNRIS

## Slide 26: Situational Awareness For Everyone (SAFE)
Flood SAFE Viewer: http://arcg.is/1LPOHnE
Source: Jared Allen, NWS Austin-San Antonio Weather Forecast Office

## Slide 27: SAFE Map for Blanco River near Wimberley, Tx
Source: Jared Allen, NWS Austin-San Antonio Weather Forecast Office
Blanco River Proof-of-concept Map: http://arcg.is/1GtObu3

## Slide 28: Address Points and the Floodplain

## Slide 29: Address Points in the Floodplain
Floodpoints
Address Points in Floodplain of Onion Creek

## Slide 30: Dry Creek Transportation
Bee Cave Rd (FM 2244)
Identify streets with flood risk

## Slide 31: US National Grid Cells

## Slide 32: Address Points in a National Grid Cell

## Slide 33: Community Flood Response Map Book
Source: Tomas Rodriguez, City of Austin