## Slide 1
David R. Maidment
Center for Research in Water Resources
University of Texas at Austin
Webinar at US Army Corps of Engineers
Washington DC, 3 September 2015
Acknowledgements: Fernando Salas, Marcelo Somos Valenzuela, David Gochis, Ed Clark,
Don Cline, Jack Dangermond, Andy Ernest, Richard Hooper
This research is supported in part by NSF EarthCube grant 1343785
National Flood Interoperability Experiment

## Slide 2: The Opportunity
New National Water Center established on the Tuscaloosa campus of University of Alabama by the National Weather Service and federal agency partners
Has a mission to assess hydrology in a new way at the continental scale for the United States

## Slide 3: Integrated Water Resources Science and Services (IWRSS)
Weather
Rivers
Impact
Data
Formal partnership across these four agencies

## Slide 4: NWS River Forecast Centers (RFCs)
  Prepare river and flood forecasts using models based on average basin characteristics
  Provide forecast guidance to Weather Forecast Offices (WFOs)
  Issue daily stage and streamflow forecasts, rainfall and drought data and information, and flash flood guidance
  Work with water managers and other Federal Agencies
4
6600 sub-basins in continental US
Notes: RFC Summary

## Slide 5
100 million people on coast
No River Forecast
Notes: THERE’S A MAJOR GEOGRAPHIC GAP – WE DON’T FORECAST ALONG THE COAST

## Slide 6
FY15 Centralized Water Forecasting
Centralized Data Archive – all RFC data
Modeling Evaluation Service
  RFC and NWC modeling and forecasts
Modeling Testbed – new NWC capabilities
Centralized Water Forecasting Demonstration
National Water Center
Notes: TRANSITION INTO METHODS
FY15 PROJECT HAS FOUR CORE COMPONENTS
RFC archive
Model evaluation service
Modeling testbed
Centralized modeling demonstration

## Slide 7: RFC Forecast Point: Onion Creek at Highway 183
USGS Gage 08159000
NWS Forecast Point ATIT2
National Flood Interoperability Experiment
Geospatial data framework for Texas
NFIE-Geo Texas
NHDPlus Catchment 5781369

## Slide 8: WaterML2 Observations from USGS and Forecasts from NWS for this location
USGS Observed Flows, July 19
NWS Forecast Flows, July 19-20
USGS Gage 08159000
NWS Forecast Point ATIT2

## Slide 9
Inaugural Meeting – May, 2014

## Slide 10: Transformative Research (NSF)
Transformative research involves ideas, discoveries, or tools that radically change our understanding of an important existing scientific or engineering concept or educational practice or leads to the creation of a new paradigm or field of science, engineering, or education. Such research challenges current understanding or provides pathways to new frontiers.
http://www.nsf.gov/about/transformative_research/definition.jsp
How to move from evolutionary change
to transformative change?

## Slide 11: National Flood Interoperability Experiment (NFIE) (Sept 2014 to August 2015)
Partnership between NWS and the academic community (Interagency Agreement between NSF and NOAA)
Included a Summer Institute for 44 graduate students from 19 Universities at the National Water Center, June 1 to July 17, 2015

## Slide 12: Goal of the Experiment
Close the gap between National Flood Forecasting and Local Emergency Response
Demonstrate forecasting of flood impacts at “stream and street level”
National
Local
Weather and Hydrology
National Weather Service and federal agencies
National Water Center
River Flooding and Emergency Response
Local, State and Regional Agencies
Citizens

## Slide 13: NFIE Conceptual Framework
NFIE-Services: Web services for flood information
NFIE-Geo: National geospatial framework for hydrology
NFIE-Hydro: National high spatial resolution hydrologic forecasting
NFIE-River: River channel information and real-time flood inundation mapping
NFIE-Response: Community Flood Response System

## Slide 14: Open Water Data Initiative (OWDI)
Subcommittee on Spatial Water Data leads this effort
Al Rea (USGS) and Ed Clark (NWS) are co-chairs
This reports to both FGDC and ACWI
Sponsoring a series of “experiments” with water information services
NFIE is one of these experiments
Chair
Anne Castle, Former Asst Secretary for Water and Science, Dept of Interior

## Slide 15: NHDPlus Version 2.1
National Elevation Dataset
National Hydrography Dataset
National Land Cover Dataset
Watershed Boundary Dataset
NHDPlus
Foundation for a Geospatial Hydrologic Framework for the United States
2.7 million reach catchments in US
average area 3 km2
reach length 2 km
Uniquely labelled

## Slide 16: Flood Information for Fritz Hughes Park Rd
National Hydrography Dataset Plus
catchment for Bear Creek
(area = 5.71 km2)
Low water crossing at
3400 Fritz Hughes Park Rd

## Slide 17
500,000 processors operating in parallel
Stampede
1.2 million gallon cooling tank

## Slide 18: WRF-Hydro Forecasting Model
Runoff
Streamflow
RAPID flow routing (for continental US)
Probabilistic flood forecasts
Weather model and forecasts (HRRR)
Land-Atmosphere Model (NOAH-MP)
Precipitation
Weather
Catchment-level forecasts
Computed for the continental US in 10 minutes at Texas Advanced Computing Center

## Slide 19: High Resolution Rapid Refresh (HRRR)
Variables of interest: Temperature at 2 m, u and v-wind at 10 m, relative humidity, specific humidity, precipitation rate, surface pressure, radiation
13 km grid spacing
3 km grid spacing
Operational HRRR maintained by NCEP
  Nested WRF model with cloud resolving physics
15 hour forecast
  15 min time step
Updates issued hourly
Preceded by RAP and RUC models

## Slide 20
RAPID River Routing Model
River Application for Parallel ComputatIon of Discharge
Flow
Legend
Dam
Junction
Catchment
Computational Unit for Rivers
Forcing: Runoff and reservoir releases
http://rapid-hub.org/
NHDPlus Catchment
Sprism = KQ
Swedge = KX (I – Q)
Muskingum
Method

## Slide 21
Grid to
catchment
NHDPlus
to RAPID
Forcing
WRF-Hydro
HRRR
ECMWF
NFIE-Hydro
TACC

## Slide 22
08156800 Shoal Ck at W 12th St Austin TX (12 SQ KM)

## Slide 23
08055560 Elm Fk Trinity Rv at Spur 348, Irving, TX (2,537 SQ KM)

## Slide 24
08176500 Guadalupe Rv at Victoria, TX (5,198 SQ KM)

## Slide 25
08116650 Brazos Rv nr Rosharon, TX (45,339 SQ KM)

## Slide 26: Probability of Flooding on Shoal Ck, Austin, Tx
Ensemble of 50 flood forecasts
ECMWF-RAPID flow forecasts
Deterministic flood maps
Probabilistic flood maps
HEC-RAS model
Rating curves library

## Slide 27: Rating Curve Library
50 profiles with flows ranging from the 2-500 year return period flood were used to create rating curves at each of the cross-sections in the Shoal Creek (299 XS), Onion Creek (266 XS), and Brushy Creek (798 XS) Models.
These are stored in a look up table and used to interpolate
water surface elevations from the ECMWF\RAPID flow forecast
Shoal Creek Plan Shoal Creek 8/17/2015

## Slide 28: Inundation depth and probability rasters – Shoal Creek

## Slide 29: Progression of Memorial Day Flood on Shoal Creek

## Slide 30: Current and NFIE Forecast Systems
130 Catchments and Flowlines
uniquely labelled
Two basins and one forecast point
becomes
Current: 6600 basins and 3600 forecast points
NFIE: 2.7 million stream reaches and catchments
A national flow network
Blanco River at Wimberley
Basin ~ 400 Sq Mile
Reach Catchment ~ 1 Sq Mile

## Slide 31: Linear Referencing on Flowlines
Lat.
Long.
Measure
Bridge and Stream Gage at RR 12 is at Measure 70.246
on Flowline 1630223
Measure is the % distance upstream from most downstream point on line
Using measures, the flow can be estimated at any point along the line

## Slide 32: Next Step: National Water Prediction Model Configurations
Short-Range
‘Flood Prediction’
Long Range
‘Water Resources’
Analysis & Assimilation
Hourly
3-Hourly
~Daily (x16)
- 3 hrs
Cycling Frequency
WRF-Hydro IOC Configurations – May 2016
0-2 days
0-30 days
Forecast Duration
1km/250m/NHDPlus Reach
1km/250m/NHDPlus Reach
1 km/catchment /NHDPlus Reach
Spatial Discretization & Routing
MRMS blend/ HRRR-NAM bkgnd.
Downscaled HRRR /RAP/NAM blend
Downscaled & bias-corrected CFS
Meteorological Forcing
Medium Range
‘Flow Prediction’
Daily
0-10 days
1km/250m/NHDPlus Reach
Short-range + Downscaled GFS

## Slide 33: NFIE Conceptual Framework
NFIE-Services: Web services for flood information
NFIE-Geo: National geospatial framework for hydrology
NFIE-Hydro: National high spatial resolution hydrologic forecasting
NFIE-River: River channel information and real-time flood inundation mapping
NFIE-Response: Community Flood Response System
Worked Well
Needs Development

## Slide 34: Improvements in Flood Response Planning
Federal
State
Local
Citizen
GIS database and flood discharge forecasts
for 2.67 million stream reaches in
continental US from National Water Center
Conversion to water level forecasts and
inundation maps for 102,000 reaches in Texas
using 10m terrain data. Address points for flood
emergency response planning in each reach
Flood impact on transportation system
Flood response planning for stream reaches
and critical infrastructure. Inundation mapping
using LIDAR terrain data, if available.
Flood response portal for citizens (ATXFlood)
Automated flood warnings from cell-phone
towers to phones in flood risk zones

## Slide 35: NFIE-Geo for Texas
102,000 NHDPlus reach catchments for Texas
Average area 7.1 km2
Average reach length 3 km
NHDPlus reach catchment
Uniquely labeled across nation

## Slide 36: Connecting with Local Decision Makers
Work with the first response community to define flood strategy for stream reaches
https://www.youtube.com/watch?v=ympaR6YUxiA&feature=youtube

## Slide 37: Community Flood Response Map Book
Source: Tomas Rodriguez, City of Austin

## Slide 39: Situational Awareness For Everyone (SAFE)
Flood SAFE Viewer: http://arcg.is/1LPOHnE
Source: Jared Allen, NWS Austin-San Antonio Weather Forecast Office

## Slide 40: Memorial Day Weekend Precipitation in Blanco River Basin
Total Precip.
(inches)

## Slide 41: Flow in Blanco River at Wimberley
40 ft wall of water overwhelmed the gage

## Slide 42: NFIE-Geo for Hays County
264 Forecast Reaches within County Boundary

## Slide 43: 264 Forecast Reaches in Hays County

## Slide 44
Saturday, May 23, 6 AM
Storm Rainfall during Memorial Day Weekend
http://gis.ncdc.noaa.gov/map/viewer/#app=cdo&cfg=radar&theme=radar&display=nexrad
Saturday, May 23, noon
Saturday, May 23, 6 PM
Saturday, May 23, Midnight
Sunday, May 24, 6 AM
Sunday, May 24, noon
Sunday, May 24, 6 PM
Sunday, May 24, Midnight
Where are the corresponding flood maps on the ground?

## Slide 45: Real-Time Flood Inundation Mapping (USGS/NWS)
http://water.weather.gov/ahps2/inundation/inundation_google.php?gage=atit2

## Slide 46: Elevation-indexed flood mapping
Map sequence for each point
Center Points of Reaches
Hays County

## Slide 47
Flood Modeling: Geometry and Flow

## Slide 48: USACE Bathymetric Data for the Mobile-Alabama River System
Could USACE Bathymetric data be contributed to the
OWDI Geospatial Hydrologic Framework?

## Slide 49: Reach Hydraulic Parameters
Wetted Bed Area
L
As
Ab
V
T
R
A
T
R
Cross Section Area
Hydraulic Radius
Top Width
h
Surface Area
Volume
Depth
5781175
3
5781175
4

## Slide 50: Real-Time Water Surface Elevation: Two Methods
Each reach has a center point and a flow forecast
(1) Establish a rating curve at center point and use this to convert flow, Q, to water depth, h, and water surface elevation
(2) Use the SPRNT model to compute both flow and depth
Forecast, Q
h
Q
h
Depth
Rating Curve

## Slide 51
Solve 100 million equations each night
to check the effects of design changes
made during the day

## Slide 52
SPRNT model computes flow and depth in large river networks using VLSI design concepts

## Slide 53: Elevation-Indexed Flood Response Mapping
Coastal
Mapping
Riverine
Mapping
Treat these
in a common way
Elevation-indexed flood
inundation mapping
Flood water surface elevation
modeling and forecasting
Take blue line network, raise it and
flood it out, continue for increments
of elevation
Inundation map library for each NHDPlus Reach
for coastal and riverine reaches

## Slide 54: Corps of Engineers Modeling, Mapping and Consequences program
Source: R. Simrall, USACE

## Slide 55: NFIE-Geo for Guadalupe Basin
3240 NHDPlus Catchments Average area = 5.04 Km2
Average reach length = 2.9 Km
19 NWS Forecast Points 31 NWS Forecast Basins
33 Active USGS Stream Gages

## Slide 56: NFIE-HMS model of the Guadalupe Basin

## Slide 57: CrossSections on Lower Mississippi River
173 cross-sections over 543 km, or 3.1 km between cross-sections, on average
41,479 cross-section points (x,y,z) of bed elevation, or 240 points per cross-section, on average

## Slide 58: Conclusions
The National Flood Interoperability Experiment has been a significant success in rapidly prototyping a high spatial resolution flood forecasting system
NHDPlus and Geospatial Hydrologic Framework provide the information foundation for the continental scale modeling
This is a “flow continuum” model on the national stream network, like atmospheric and ocean models
There is a significant synergy with the USACE Modeling, Mapping and Consequences program
Need to synthesize riverine and coastal flood modeling and mapping
Similar Summer Institutes will be held in 2016 and 2017 at the National Water Center