## Slide 1
An Introduction to Remote Sensing
Ayse Irmak
University of Nebraska-Lincoln

## Slide 2: Remote Sensing: A Definition
The art and science of acquiring information about the earth and its environment using sensors mounted in aircraft and spacecraft

## Slide 3: Remote Sensing in the context of GIS
Aerial images taken from aircraft using film or digital cameras
Satellite images recorded with satellite scanners
Under most conditions, aerial images contain geometric distortion
  Imperfections in the camera, lens or film systems,
  Camera tilt or terrain variation
Satellite scanners may also contain errors due to imaging equipment or satellite platform

## Slide 4
Remotely sensed images have a number of features which make them ideal GIS data sources
Remote sensing provides a regional view
Remote sensing provides repetitive looks at the same area
Remote sensors "see" over a broader portion of the electromagnetic spectrum than the human eye

## Slide 5: Remote Sensing and GIS
Sensors can focus in on a very specific bandwidth in an image
They can also look at a number of bandwidths simultaneously
Remote sensors often record signals electronically and provide geo-referenced, digital data (i.e. aerial images)
Some remote sensors operate in all seasons, at night, and in bad weather
Permanent record (Image is fixed in time). Therefore, it is an accurate source of historical information

## Slide 6: Geospatial Data
Hydrography
Transportation
Elevation
Soils
Land Use
Digitized Quads
Aerial and satellite images are valuable source of spatial data in GIS!
Notes: Aerial images are used as a basis for surveying and topographic mapping to measure and identify horizontal and vertical locations of objects.
1:24,000 –scale quadrangle maps by USGS
Digital orthophotographs

## Slide 7: Processes involved in electromagnetic remote sensing of earth features
Notes: Camera tilt and terrain variations may cause large errors in aerial photos – stereophogtoraphic determination of elevations removes terrain caused image displacement.

## Slide 8: Overview of data acquisition by satellites
Source John R. Jensen
Notes: Overview of data acquisition
Data recorded by the sensor system are converted from an analog electrical signal to a digital values. It takes places on-board. Sensor system creates pixels with a brightness value of 8 bit to 12 bits
Data is transmitted to ground control stations
Radiometric correction: for sensor performance. Some sensor is not performing well over time
Geometric correction. Satellite is not always going up and down. There might be some tilting.
Ground processing removes geometric and radiometric distortions.
The data are then ready for visual or digital analysis to extract information on biophysical and landcove

## Slide 9
http://srtm.usgs.gov/

## Slide 10: Energy Sources and Radiation Principles
Light energy is the principal form detected
Common forms of RS is based on reflected electromagnetic energy. i.e. Sensing Electromagnetic Radiation
Light energy is characterized by its wavelengths
Different materials reflect different amounts of incoming energy. This differential reflectance gives objects a distinct appearance

## Slide 11: Electromagnetic Radiation
The distance between peaks in the electromagnetic stream is the wavelength
Each color of light has a distinctive wavelengths

## Slide 12: Energy pathways from source to sensor
Incident radiation = reflected + absorbed + transmitted
Notes: Light reflected from the surface and transmitted to the sensor is used to create an image
Light energy may be absorbed, transmitted or reflected, by the atmosphere
Light reflected from the surface and transmitted to the sensor is used to create an image
The image may be degraded by atmospheric scattering due to water vapor, dust, smoke, ant others
Absorbed energy may be re-radiated at longer wavelenghts, forming the basis for thermal remote sensing.

## Slide 13
USGS definition: ” Electromagnetic radiation is energy propagated through space between electric and magnetic fields. The electromagnetic spectrum is the extent of that energy ranging from cosmic rays to infrared radiation including microwave energy."
Categorize electromagnetic waves by their wavelenght location in electromagnetic spectrum (unit is micrometer).
Notes: USGS defines the electromagnetic spectrum as: Electromagnetic radiation is energy propagated through space between electric and magnetic fields. The electromagnetic spectrum is the extent of that energy ranging from cosmic rays, gamma rays, X-rays to ultraviolet, visible, and infrared radiation including microwave energy."

## Slide 14: The Electromagnetic Spectrum
Our eyes perceive light in the visible portion of spectrum
Satellites can operationally measure panchromatic imagery (variations in a waveband from 400 to 700nm as shades of grey) at a 1 m. Panchromatic sensors.
Satellites can operationally measure multi-spectral imagery (the simultaneous sensing of two or more wavebands) at 20 to 30 m. Multispectral sensors.
Hyperspectral sensors cover spectral bands narrower than multispectral
spectral bands (channels)

## Slide 15: Thermal Radiation Principles
Thermal infrared radiation refers to electromagnetic waves with a wavelength of between 3.5 and 20 micrometers
Most remote sensing applications make use of the 8 to 13 micrometer range
Thermal infrared is emitted energy, whereas the near infrared (photographic infrared) is reflected energy
Notes: Thermal energy
Heat is a form of energy. Heat energy is stored in matter just like electrical energy is stored in a battery. An object that contains no heat energy is very cold, and is said to be at absolute zero (-460 F or -273 C). As heat is added to the object, its temperature rises. The more heat energy an object contains the hotter the object becomes. infrared energy is emitted as a result of atomic and molecular vibration.
The total amount of infrared energy emitted by an object is proportional to temperature to the fourth power.
Stefan-Boltzmann Law
P/A = emissivity of the object X stefan bolzman constant (5.6703 10-8 watt/m2/K4). X T4
P= new radiated power; A =radiating area

## Slide 16: Atmospheric Windows (AW) in the Electromagnetic Spectrum
AW are caused when atmospheric gases/particles do not absorb the radiation
Only light in certain wavelength regions can penetrate the atmosphere well
Satellite are designed to operate on certain AW
Black if sensor is designed to operate on absorption bands
Jensen 2000
Notes: Absorption results in the effective loss of energy to the atmosphere
AW are caused when atmospheric gases/particles do not absorb the radiation
Only light in certain wavelength regions can penetrate the atmosphere well
Satellite are designed to operate on certain AW
Black if sensor is designed to operate on absorption bands

## Slide 17: Spectral Response Curve (“signature”)
Natural objects appear to be the color they most reflect!
Notes: Healthy green vegetation always manifest “peak and valley”
The valleys in the visible portion of spectrum are dictated by the pigments in the leaves. Chlorophyll absorbs energy centered at 0.45 and 0.67
That means high absorption of blue and red energy by plants
0.7 1.3, plant reflects as much as 50% of energy incident upon it
Dips (valleys) occur at 1.4, 1.9, and 2.7 because water in the leaves absorbs
Water: most distinctive characteristics. Absorption at near—IR and beyond
Soil shows less peak and valley because factors (moisture, texture, organic matter, surface roughness) affecting soil reflectance act less specific spectral bands

## Slide 18
Detect crop stress generally from moisture deficiency or disease and pests
Stress is indicated by a progressive decrease in Near-IR reflectance accompanied by a reversal in Short-Wave IR reflectance
http://rst.gsfc.nasa.gov/

## Slide 19: Major Components of Technology
Energy Source
  Passive System: Irradiance from earth's materials
  Active System: irradiance from artificially generated energy sources such as radar
Platforms: Vehicle to carry the sensor
Sensors: Device to detect electro-magnetic radiation
Detectors: Handling signal data (photographic, digital, etc.) Processing: Handling signal data
Institutionalization (international and national organizations, centers, universities for execution at all stages of remote-sensing technology)
Notes: The following are major components of Remote sensing System:
Energy Source
  Passive System: sun, irradiance from earth's materials; Active System: irradiance from artificially generated energy sources such as radar.
Platforms:(Vehicle to carry the sensor) (truck, aircraft, space shuttle, satellite, etc.)
Sensors:(Device to detect electro-magnetic radiation) (camera, scanner, etc.) Detectors: (Handling signal data) (photographic, digital, etc.) Processing (Handling Signal data) (photographic, digital etc.) Institutionalisation: (Organization for execution at all stages of remote-sensing technology: international and national orrganisations, centres, universities, etc.).

## Slide 20: Sensors
include cameras, scanners, radar
sensors are designed to address specific problems and data requirements
sensors complement one another; image fusion
Notes: image fusion: Process of combining relevant information from two or more images into a single image
Output: high spatial and high spectral resolution in a single image

## Slide 21: Platforms
field vehicles
light aircraft
high altitude aircraft
satellites (Landsat, SPOT, Ikonos, Terra)
space shuttle

## Slide 22: Some Sensors and Platforms
Platform | Sensor(s)
Ikonos | Ikonos
Landsat-7 | Enhanced Thematic Mapper + (ETM+)
SPOT-4 | High Resolution Visible -Infrared (HRVIR); Vegetation
Terra | MODIS; ASTER
EO-1 | Advanced Land Imager (ALI); Hyperion
Radarsat | Synthetic Aperture Radar (SAR)

## Slide 23: Remote Sensing Raster (Matrix) Data Format
Jensen 2000
Notes: Digital remote sensor data are stored as matrix of numbers
Each digital value is located at a specific row and column in that matrix
Sensor systems creates pixels with a brightness value (BV) range of 8 to 12 bits. This is called “Quantization” level of remote sensor data.
8 bits have BV that range from 0 to 255
Data quantized to 12 bits range from 0 to 1023
The greater the range of values, the more precise we may able to measure the amount of radiance recorded by the sensor

## Slide 24: Digital Image
Pixel (picture element)
25 | 22 | 19 | 47 | 44
22 | 18 | 25 | 22 | 44
19 | 21 | 22 | 23 | 42
21 | 116 | 121 | 125 | 134
118 | 125 | 123 | 135 | 126
125 | 133 | 136 | 221 | 234
244 | 243 | 212 | 232 | 178

## Slide 25: Selection of Imagery
Resolution
  spatial
  spectral
  radiometric
  temporal
Image coverage
Image availability/format
Cost

## Slide 26: Spatial Resolution
pixel size (instantaneous field of view)
smallest object one can discern/identify
commonly 1 meter to 1100 meters

## Slide 27: Spatial Resolution
Coarse (30 m, multispectral)
Fine (1 m, panchromatic, Ikonos)
Image of Lincoln, NE

## Slide 28: Spectral Resolution
how many spectral bands?
which bands?
band widths - narrow band vs broad band
http://geospatial.amnh.org/remote_sensing/widgets/spectral_curve/spectral.swf
Notes: Spectral resolution refers to the number of different frequency bands recorded - usually, this is equivalent to the number of sensors carried by the platform(s).
Current Landsat collection is that of seven bands, including several in the infra-red spectrum.
The MODIS satellites are the highest resolving at 31 bands

## Slide 29: LIDAR (Light Detection and Ranging)

## Slide 30: Radiometric Resolution
number of “brightness levels” (gray shades; bits)
commonly 256 - 2048 levels (8 - 11 bit)

## Slide 31: Temporal Resolution
how often is image available?
varies from 1 day to 26 days (phased?)
some sensors must be “tasked”; some are pointable
historical archive?
Notes: The temporal resolution is simply the frequency of flyovers by the satellite or plane, and is only relevant in time-series studies or those requiring an averaged or mosaic image as in deforesting monitoring.
Cloud cover over a given area or object makes it necessary to repeat the collection of said location.
Radiometric correction gives a scale to the pixel values, e.g. the monochromatic scale of 0 to 255 will be converted to actual radiance values.
Atmospheric correction eliminates atmospheric haze by rescaling each frequency band so that its minimum value (usually realised in water bodies) corresponds to a pixel value of 0. The digitizing of data also make possible to manipulate the data by changing gray-scale values.

## Slide 32: Comparing Resolution
Sensor | Spatial | Spectral | Radiometric | Temporal
Ikonos | 1-4 m | 4 + pan bands | 11 bit | 1-3 days
SPOT-5 HRG | 2.5-10 m | 4 + pan bands | 8 bit | 1-26 days
Landsat-7 ETM+ | 15-30 m | 7 + pan bands | 8 bit | 16 days
Terra MODIS | 250 m – 1000 m | 36 bands | 12 bit | 1 day

## Slide 33: LANDSAT
LANDSAT refers to a series of satellites put into orbit around the earth to collect environmental data about the earth's surface.
The LANDSAT program was initiated by the U.S. Department of Interior and NASA under the name ERTS, Earth Resources Technology Satellites.
ERTS-1 was launched on July 23, 1972, and was the first unmanned satellite designed solely to acquire earth resources data on a systematic, repetitive, multispectral basis.
Over time, the sensors carried by the LANDSAT satellites have varied as technologies improved and certain types of data proved more useful than others

## Slide 34: Principal applications of different wavelengths
1) 0.45-0.52. Blue. Designed for water body penetration, making it useful for coastal water mapping. Also useful for soil/vegetation discrimination, forest type mapping, and cultural feature identification.
2) 0.52-0.60. Green. Designed to measure green reflectance peak of vegetation for vegetation discrimination and vigor assessment. Also useful for cultural feature identification.
3) 0.63-0.69. Red. Designed to sense in a chlorophyll absorption region aiding in plant species differentiation. Also useful for cultural feature identification.
4) 0.76-0.90. Near-infrared. Useful for determining vegetation types, vigor, and biomass content, for delineating water bodies, and for soil moisture discrimination.
5) 1.55-1.75. Mid-infrared. Indication of vegetation moisture content and soil moisture. Also useful for differentiation of snow from clouds.
6) 10.4-12.5. Thermal infrared. Useful in vegetation stress analysis, soil moisture discrimination, and thermal mapping applications.
7) 2.08-2.35. Mid-infrared. Useful for discrimination of mineral and rock types. Also sensitive to vegetation moisture content.

## Slide 35: Landsat Images to Cover Nebraska
http://earthnow.usgs.gov/earthnow_app.html?sessionId=a0d0c8de12ec09f065837276c5d8ab6b4155

## Slide 36: Image Coverage
P33R30
10
P32R30
9
P31R30
10
P30R30
9
P29R30
10
P33R31
11
P32R31
10
P31R31
12
P30R31
9
P29R31
11
P28R31
8
P33R32
15
P32R32
8
P31R32
12
P30R32
10
P29R32
12
P28R32
10
P27R32
8
2005
Number of images to cover study area
Generally, higher spatial resolution = smaller area coverage per frame = more scenes

## Slide 37: Image processing Leica ERDAS Imagine

## Slide 40: Image processing to generate color composite
Spectral band | Color assignment
green (TM2) | blue
red (TM3) | green
near-infrared (TM4) | red
False Color Composite
Individual bands can be displayed in gray shades
Bands can be combined in color composites
Reds, depicting vegetation
Medium grayish-browns, mainly along the bright sun-facing slopes
Deep blue, depicting ocean and bay
Near the shore, a bit lighter blue where thicker sediments add reflectance

## Slide 41: Remote Sensing The Good News
sensors - spectral bands, higher resolution (< 1m)
lower data costs?
inexpensive, powerful software
global datasets
improved interface to GIS
biophysical analyses - biomass, soil moisture, turbidity

## Slide 42: Aerial or satellite images?
A number of factors including spectral range, price, availability, reliability and flexibility are important in deciding between aerial and satellite images.
Aerial images are the main source of coordinate and attribute data, and provide more detailed information than satellite images.
National, state, and local governments are the main source of aerial images.
The National Aerial Photography Program (NAPP) provides full coverage of the lower 48 United States at 1:40,000 scale at 5 to 10 year return intervals.
Satellite systems provide a broader range of spatial, spectral and temporal data relative to aerial images, and cover large areas.
Often used to create or update landcover classification, and to detect and monitor change over large areas.

## Slide 43: Remote Sensing Some Typical Applications
Mapping or monitoring land cover and land use
Measuring area, volume, trajectory

## Slide 44
Estimating biomass, surface temperature, turbidity
Extent/impacts of natural hazards (e.g., drought, fires)

## Slide 45: Mapping Invasive species (Albuquerque, NM)

## Slide 46: Vegetation Index: Infrared/Red Ratio Vegetation Index
The near-infrared (NIR) to red simple ratio (SR) is the first true vegetation index
It takes advantage of the inverse relationship between chlorophyll absorption of red radiant energy and increased reflectance of near-infrared energy for healthy plant canopies (Cohen, 1991)

## Slide 47: Vegetation Index
As plants grow, canopy and biomass increase
Green leaves absorb more red and blue light –
Increase in NIR reflectance
Vegetation indices express the difference between NIR and red reflectance
“Greenness” - associated with plant photosynthetic activity, biomass, fractional cover of vegetation
Normalized vegetation index (-1, 1)

## Slide 49: Global Normalized Difference Vegetation Index (NDVI) Image Produced Using (AVHRR) Imagery

## Slide 50: Leaf Area Index
The area of green leaf per unit area of ground

## Slide 51: Actual Evapotranspiration (ET) at Central Platte Natural Resources District , NE

## Slide 52
http://www.nasa.gov/vision/earth/lookingatearth/socal_wildfires_oct07.html
Witch Wildland fire, burned 198,000 acres north of San Diego, destroying 1125 homes, commercial structures, and outbuildings. Over 3,000 firefighters finally contained the fire two weeks after it started on October 21. Fire started on Oct 8th 2007
Witch Wildland fire San Diego
This ASTER image depicts the area after the fire, on November 6; vegetation is green, burned areas are dark red, and urban areas are blue. On the burn severity index image, calculated using infrared and visible bands, red areas are the most severely burned, followed by green and blue. This information can help the US Forest Service to plan post-fire activities.

## Slide 53
Three decades of Mississippi Delta sediment deposition from the Mississippi-Missouri River system eroded debris. The left image was acquired on January 16, 1973; the middle image on March 12, 1989; and the right image on January 6, 2003.
Landsat Images to study sediment deposition

## Slide 54
Photo credit: USGS
http://pubs.usgs.gov/fs/2010/3026/pdf/FS2010-3026.pdf
Remote Sensing in Forestry
Progression of deforestation in Bolivia from 1975 to 2000 using LANDSAT 2, 4, and 7 images. The image on the left was acquired on June 17, 1975; the middle image on July 10, 1992; and the right image on August 1, 2000.

## Slide 55
Airborne Remote Sensing to Support Precision Farming
Maturity Map of Brown Rice (Red: High, Purple: Low)
Protein Map of Brown Rice (Red: High, Purple: Low)
Detail Map (Red: High, Purple: Low)
http://www.esri.com/mapmuseum/mapbook_gallery/volume20/agriculture3.html
Hyperspectral airborne remote sensing can be used for leaf color analysis, soil classification, and monitoring the growth stage of rice in a large area.
Tokyo, Japan
By PASCO Corporation

## Slide 56
Mapping Riparian Vegetation with Lidar Data
The figure on the left is a 0.3048-meter-resolution aerial photograph of the Walker River in Nevada. The image on the right is the height-above- river map using a 300-meter kernel size and classified into 50-centimeter vertical intervals. In the upper left-hand corner is a eutrophic oxbow lake that is low lying yet disconnected from the river channel. Near the bottom of the map is a shallow river channel that periodically fills with water, cutting off the point bar. An irrigation ditch is visible on the right-hand side of the image.
http://www.esri.com/news/arcuser/0110/mapping-with-lidar.html

## Slide 57
http://remotesensing.usgs.gov/feature/description.php?id=190
Landsat 5 Image of the Oil Slick in the Gulf of Mexico
On April 20, 2010, an explosion at an oil well in the Gulf of Mexico resulted in a major oil spill. Since then, emergency response efforts have been underway to cap the leaking well system and contain the growing oil slick before it reaches wildlife refuges, fisheries, and beaches along the southern coast of the United States.
Landsat imagery, acquired by the U.S. Geological Survey on May 9 shows the extent of the oil slick. The Landsat data are being used by emergency response teams to monitor the extent and movement of the slick.
Notes: On April 20, 2010, an explosion at an oil well in the Gulf of Mexico resulted in a major oil spill. Since then, emergency response efforts have been underway to cap the leaking well system and contain the growing oil slick before it reaches wildlife refuges, fisheries, and beaches along the southern coast of the United States.
Landsat imagery, acquired by the U.S. Geological Survey on May 9 shows the extent of the oil slick. The Landsat data are being used by emergency response teams to monitor the extent and movement of the slick.

## Slide 58
http://landsat.gsfc.nasa.gov/images/archive/e0024.html
In this image the Mississippi Delta is displayed on the left and the oil spill can be seen on the right. The image colors have been enhanced to increase visibility of the oil spill. Vegetation appears green, sediment-laden effluence from the delta appears light blue, clouds are white, the Gulf of Mexico is magenta, and the oil spill is a deep to light purple.
This Landsat 7 false-color composite image was created using ETM+ bands 7,4, and 2. It was acquired on May 1, 2010. The image falls on Landsat WRS-2 Path 21 Row 40.
Gulf of Mexico Oil Spill 2010

## Slide 59
Remote Sensing for Land Use
http://calmit.unl.edu/2005landuse/

## Slide 60
http://www.nass.usda.gov/research/Cropland/CDL09_greatplains_l.png
http://www.nass.usda.gov/research/Cropland/sarsfaqs2.html#_What_satellite_sensors
The CDL Program uses medium resolution satellites. CDL products prior AWiFS to 2006 relied primarily on Landsat 4/5/7. Beginning with the 2006 CDL products, the CDL program transitioned to using the senor on the IRS-P6 Resourcesat-1 satellite.

## Slide 61
http://www.satimagingcorp.com/gallery/quickbird-pyramids-egypt.html
The Giza Pyramids were constructed around 2500 BC as monumental tombs. The largest and oldest pyramid was originally over 480 feet high and is made of 5.7 million tons of limestone.
QuickBird Satellite Sensor, February 2002

## Slide 63
Hurricane Katrina
Notes: Hurricane Katrina was the costliest and one of the five deadliest hurricanes in the history of the United States.
The storm surge caused severe damage along the Gulf Coast, devastating the Mississippi cities of Waveland, Bay St. Louis, Pass Christian, Long Beach, Gulfport, Biloxi, Ocean Springs, and Pascagoula

## Slide 64: Landsat Change Analysis
Las Vegas
September 13, 1972
Las Vegas
June 20, 1997
Notes: Urban development has expanded rapidly in Las Vegas, Nevada of the United States, over the last fifty years.
A major environmental change associated with this urbanization trend is the transformation of the landscape from natural cover types to increasingly anthropogenic impervious surface
--Total urban land-use increases approximately 110 percent from 1984 to 2002. Most of the increases are associated with medium-to high-density urban development.
---Places having significant increases in impervious surfaces are in the northwestern and southeastern parts of Las Vegas. Most high-density urban development, however, appears in central Las Vegas.

## Slide 65
Lake McConaughy
June 3, 2000
Landsat 7 ETM+ panchromatic 15m
Lake McConaughy
June 9, 2002
Landsat 7 ETM+ panchromatic 15m
The elevation level of Lake McConaughy of Nebraska dropped due to drought
Notes: Understanding nature of drought:
1. Large parts of Nebraska have experienced drought conditions since the
beginning of 2000
2. The elevation level of Lake McConaughy of Nebraska is dropping persistently
3. Lake McConaughy on the North Platte River. It is about 25 miles long
The precipitation in Wyoming and Colorado, the headwaters region of the lake, is stable over the period 1980-2004. With the projected warmer climate, the accumulation of the mountain snowpack would be affected significantly, resulting in declining water “storage
low levels of dissolved oxygen in the lake

## Slide 66
West end of
Lake McConaughy
June 3, 2000
Landsat 7 ETM+ panchromatic 15m
West end of
Lake McConaughy
June 9, 2002
Landsat 7 ETM+ panchromatic 15m

## Slide 67: NOAA Advanced Very High Resolution Radiometer (AVHRR)
  1 km spatial resolution
  5 spectral bands
  daily revisit
  inexpensive “real-time” data capture
  Defining hydrologic, oceanographic, and meteorological parameters
Notes: The AVHRR is a radiation-detection imager that can be used for remotely determining cloud cover and the surface temperature
The first AVHRR was a 4-channel radiometer, first carried on TIROS-N (launched October 1978). This was subsequently improved to a 5-channel instrument (AVHRR/2) that was initially carried on NOAA-7 (launched June 1981). The latest instrument version is AVHRR/3, with 6 channels, first carried on NOAA-15 launched in May 1998.
AVHRR/3 Channel Characteristics
Channel Number Resolution at Nadir Wavelength (um) Typical Use
1) 1.09 km 0.58 - 0.68 Daytime cloud and surface mapping
2) 1.09 km 0.725 - 1.00 Land-water boundaries
3A) 1.09 km 1.58 - 1.64 Snow and ice detection
3B) 1.09 km 3.55 - 3.93 Night cloud mapping, sea surface temperature
1.09 km 10.30 - 11.30 Night cloud mapping, sea surface temperature
1.09 km 11.50 - 12.50 Sea surface temperature
Measuring the same view, after processing, permits multi spectral analysis for more precisely defining hydrologic, oceanographic, and meteorological parameters. Comparison of data from two channels is often used to observe features or measure various environmental parameters. The three channels operating entirely within the infrared band are used to detect the heat radiation from and hence, the temperature of land, water, sea surfaces, and the clouds above them.

## Slide 68
Jensen, 2000
Three-day composite of thermal infrared data centered on March 4, 1999.
Each pixel as allocated the highest surface temperature that occurred during the three days.
Worldwide Sea-surface Temperature (SST) Map
Derived From NOAA-14 AVHRR Data

## Slide 69: Global Land Cover 1992

## Slide 70
Hyperspectral Assessment of Water Quality (Toxic algae (blue-green) alert procedure to provide early warning)
Notes: CALMIT scientists undertook a collaborative effort with the Nebraska Department of Environmental Quality aimed at developing a tool to identify lakes where blue-green algae populations are present. The overall purpose was to incorporate those affected lakes into a toxic-algae alert procedure to provide early warnings to the public about the potential danger.
Both in-situ (close-range) and remote techniques were employed to detect and quantify in real-time the algal phytoplankton pigment concentration and composition; i.e., chlorophyll-a and phycocyanin in the water column. Two criteria were used to identify lakes and reservoirs with high probability of toxic algae: (a) chlorophyll concentration above 50 mg/m3 and (b) existence of blue green algae (the phycocyanin absorption feature has been used to indicate remotely the presence of blue-green algae).

## Slide 71: Landsat 7 - Black Hills, SD
August 20, 2000
September 5, 2000
Leaf Area Index for Fire Consequences (August 24, 2000) of the Black Hills
Notes: The 2000 wildfire season was one of the worst ever recorded in the Western United States
The Black Hills of South Dakota is dominated by ponderosa pine forest characterized by low LAI values, allowing to avoid the saturation of vegetation indices that often occurs with higher LAI values.
In three days the fire covering an area of more than 70,000 acres.

## Slide 72: Monitoring Volcanic Eruptions
6,5,4
3,2,1
Mt. Etna, Sicily, Italy Bands 321 and 654. Here Band 6 is Red, Band 5 is Green, Band 4 is Blue. Notice how the thermal band 6 does not pick up the smoke, or the clouds. You can see where the hot lava flows underground in lava tubes. The hotter the signal the brighter the pixel.
Notes: Band Wavelength (micro-m) Nominal spectral
location Principal applications
1) 0.45-0.52 Blue Designed for water body penetration, making it useful for coastal water mapping. Also useful for soil/vegetation discrimination, forest type mapping, and cultural feature identification.
2) 0.52-0.60 Green Designed to measure green reflectance peak of vegetation for vegetation discrimination and vigor assessment. Also useful for cultural feature identification.
3) 0.63-0.69 Red Designed to sense in a chlorophyll absorption region aiding in plant species differentiation. Also useful for cultural feature identification.
4) 0.76-0.90 Near-infrared Useful for determining vegetation types, vigor, and biomass content, for delineating water bodies, and for soil moisture discrimination.
5) 1.55-1.75 Mid-infrared Indication of vegetation moisture content and soil moisture. Also useful for differentiation of snow from clouds.
6) 10.4-12.5 Thermal infrared Useful in vegetation stress analysis, soil moisture discrimination, and thermal mapping applications.
7) 2.08-2.35 Mid-infrared Useful for discrimination of mineral and rock types. Also sensitive to vegetation moisture content.