## Slide 1
Geospatial Representation of Bridge-Class Culverts
Presentation for TWDB FLOG/FIM Subcommittee, 6/30/2023
Presented by
David Maidment and Tim Whiteaker
Center for Water and the Environment, University of Texas at Austin
Yan Liu, Oak Ridge National Laboratory
Acknowledgements: Rose Marie Klee (H&H Director, DES), Trenton Ellis (H&H, DES),
Shelley Pridgen (Project Manager, RTI)
Research reported here is supported by TxDOT RTI Project 0-7095
Evaluate Improved Streamflow Measurement at TxDOT Bridges

## Slide 2: NWS/TXDOT Collaboration
Example NWS/FDOT Collaboration:
In order to provide actionable information to all of partners, FDOT & NWS determined four impacting points on or near a bridge that should be added as impact statements. These are:
Low member - Lowest structural beam across the river
Roadway Elevation - Lowest elevation of travel lane approach to the bridge
Water overtops deck - Elevation of travel lane on bridge
Traffic Barrier - Elevation of top of the guard rail on bridge
When using these four impacting points, common terminology has been developed to describe these impacts that can be implemented across all FDOT regions. The terminology we’ve selected is as follows:
Low Member | Water reaches the base of the <insert roadway name> bridge
Roadway Elevation | Water reaches the approach road surface to the <insert roadway name> bridge.
Water Overtops Deck | Water begins to flood the <insert road name> bridge travel lanes.
Traffic Barrier | Water reaches the top of the <insert road name> bridge railing
Jason Johnson
Hydrologist-in-Charge, WGRFC

## Slide 3: Span Bridges and Bridge-Class Culverts
If more than 20’ in length along the roadway, they have to be inspected every two years – National Bridge Inventory
24,928
10,309 (18%)
21,012
Total number of NBI Structures Over Water = 45,940 (82%)

## Slide 4: Culvert on Anderson Lane at Shoal Creek in Austin, Tx

## Slide 5: Views from Creek Level
Upstream
Downstream
Debris on
upstream side
Bed erosion and overfall
on downstream side

## Slide 6: Culvert Information from AssetWise
Internal database of TxDOT bridge and culvert assets
(Culvert condition 1-9)
Bridge Number
Maintenance
(On top of culvert)
10’
6’
72’
Five Box Culverts

## Slide 7: Culvert on Shoal Creek at West Anderson Lane, Austin, Tx

## Slide 8: DEM Resolution
3m DEM
1m DEM
Current TNRIS standard for individual data tiles
Fathom DEM that we used State-wide for Pin2Flood

## Slide 9: Elevation Profile along Road
Chart: Road Profile on Bare Earth DEM
Minimum elevation point on approach road is not on the bridge

## Slide 10: Culvert Template
Streamflow
Road Centerline
Stream Centerline
NBI Point
Width_Curb_Curb
Deck_width_Out_Out
Struct_Length
Sidewalk_Width

## Slide 11: Building Culvert Template
Create centerline of length 54’
Buffer by 36’ to get deck width out to out (72’/2)
Buffer by 28.5’ to get road curb to curb (57’/2)
Buffer by 33.5’ to get side walks (28.5’ + 5’)
Union these three polygons to create road, sidewalk, berm polys

## Slide 12: Relocate Culvert Template
Correct Position and Orientation
Start with the NBI Point
Create the Culvert Template
Translate and Rotate the Template

## Slide 13: Add LIDAR points Classified as Bridge
Bridge LIDAR points (5237)

## Slide 14
Ecopia Road
Road on Culvert
Sidewalks
Berms
Add Ecopia Road Polygons
They line up very well with the Culvert polygon

## Slide 15: Add all Road LIDAR points

## Slide 16: 3D Surface as a Triangulated Irregular Network

## Slide 17: Use LIDAR points to create 3D road centerline and 3D polygon extent and combine with TIN to create a 3D road surface (Yan Liu)
Culvert

## Slide 18: Registration Points at Four Corners of the Box Culvert (R1, R2, R3, R4) Transect along Sidewalk Gives Elevation
R3
R4
Where trees interfere with
LIDAR elevation values
Regression line is used to
estimate elevation at R4

## Slide 19: Critical Roadway Elevations on Bridge and Approach Road
Points in (x,y,z)

## Slide 20: Tape Down from Road Berm to top of Culvert
Rail
Low Member
Sidewalk
Bridge Rail
Offset (3’)
Low
Member
Offset
3 ft
698.37’
701.37’
696.79’
Sidewalk
Elevation
Tape down
(inches)
Z - Offset
Top – Culvert
Height (6’)

## Slide 21: Box Culvert Elevation
Berm supporting the rail is 4” above the sidewalk
Culvert pipes (five 10’x6’ box culverts)
Sidewalk elevation
32”
19”
Looking left to right from upstream
Road
Gutter
Sidewalk (5’ including berm)
Berm
Top of Culvert
4”
5”

## Slide 22: Box Culverts under road
Box culverts 72’ long
and 10’x6’ cross-section
LIDAR points profile over the road
1 m DEM

## Slide 23: Stream Bed Elevation Upstream of Culvert
Chart: Distance Along Profile (ft)
| 0 | 9.4653522833503594 | 18.930704553601331 | 28.395900450535521 | 37.861252720786489 | 47.326605004136852 | 56.791957267284957 | 66.257309537535932 | 75.722661820886287 | 85.187857711823327 | 94.652921580142319 | 104.11827385039329 | 113.5836261206443 | 123.0489784039946 | 132.51417428782921 | 141.9795265711796 | 151.44487884143061 | 160.91023112478089 | 170.3755833950319 | 179.8407792919661 | 189.30613156221699 | 198.77148384556739
ElevationFt | 699.6372 | 699.71 | 699.8619 | 699.731 | 698.9275 | 697.0906 | 694.1454 | 691.7314 | 691.1146 | 691.1816 | 690.9066 | 691.2718 | 694.1431 | 699.1815 | 700.2487 | 700.4633 | 700.6565 | 701.1155 | 701.4948 | 701.5279 | 701.5666 | 701.6814
Stream Cross-Section Upstream of Culvert
Left to right looking from upstream

## Slide 24: Culvert Wall Thickness
Length = 54’
Openings = 5 * 10’ = 50’
Walls = 54’ – 50’ = 4’ = 48”
4 interior walls + 2 end walls = 6
48” / 6 = 8” wall thickness
End walls are slightly thicker
7” wall
measured
Can be estimated from Structure Length, number and width of culvert pipes

## Slide 25: TxDOT Austin District NBI Bridges and Culverts
2210 (57%)
1684 (43%)

## Slide 26: District-Wide Culvert Template Creation (Tim Whiteaker)
Shoal Ck at West Anderson Lane
Culverts on Waller Creek
Culverts on Little Walnut Creek

## Slide 27: Roads in the TxDOT Austin District
4400 miles On-System
18,000 miles TxDOT Roadway Inventory
Purchased by TxDOT RTI to support
our Streamflow II research project
Flood Emergency Response Exercise, Jan 2023
38,000 miles Ecopia road coverage
1600 miles of TxDOT Roadway Inventory
are not located on pavement as defined by
Ecopia roads coverage