## Slide 1: Evaluate Improved Streamflow Measurement at TxDOT Bridges Project 0-7095 Being conducted for TxDOT by UT Austin and US Geological Survey with the support of Kisters North America and Aqua Strategies September 2020 to August 2023
Presentation for Third Quarterly Review Meeting, Monday 14 June 2021
Acknowledgements: Shelley Pridgen (RTI Project Manager), Rose Marie Klee (H&H Director, TxDOT),
Adam Jack (BMT, TxDOT), Michael Cunningham (TPP, TxDOT)

## Slide 2: TxDOT Priorities
SAFETY
        Our staff, our community
        Emergency response
CONNECTIVITY
        Reliability of the transportation network
  Asset management
        *BRIDGES*
  Efficiency and efficacy
        For TxDOT
        For other/all jurisdictions
Slide: Rose Marie Klee, TxDOT

## Slide 3: TxDOT Project Management Committee
Rose Marie Klee H&H Section Director, DES
Abderrahmane Maamar-Tayeb
H&H Section Team Lead, DES
Adam Jack Dir of Trans Plan & Development, BMT
Andrew Lee District Bridge Engineer, BMT
Jared Browder Maintenance Assess Spec, MNT
Trent Ellis Bridge Scour Coordinator, BRG
Shelley Pridgen Research Project Manager, RTI
Joseph Goessling
Lead Hydraulics Engineer, AUS

## Slide 4: Project Advisory Committee
Jason Johnson, NOAA National Weather Service Mark Lenz, NOAA National Weather Service
Paul Yura, NOAA National Weather Service
Sam Marie Hermitte, Texas Water Development Board
Jorge Urquidi, City of Austin, Flood Early Warning System
Justin Terry, Harris County Flood Control District
Peter Smith, former TxDOT Dir of Trans Planning and Programming
+ other members of the H&H Section, TxDOT Design Division:
Welcome to
the Discussion!
Sauda Ahmed | Ivanna Heigl-Maza
Hiruy Berhe | Lucinda Soto
Zenia De Leon | Jaime Villena-Morales
Tyler DeRose | Sarah Wildenstein

## Slide 5: Streamflow II Overview Meeting Agenda
Task 1: Project Management
Task 2: Watershed Selection and Site Evaluation Task 3: Gauge Installation, Operation and Maintenance Task 4: Flood Forecast System Operation Task 5: Forecast Model Assessment
Task 6: Flood Manual and Training

## Slide 6: Task 1: Project Management – Some Highlights for this Quarter
Meeting with Austin District Maintenance
Staff, 29 April
Learned about Area Offices and
Maintenance Sections
Meeting with Project Management
Committee, 5 May 2021
Approval of 30 sites for gauge
installation
Excellent data recorded at Cole Ck
during storms, 16 – 24 May
Datasphere Dashboard for Mason County
Live HEC-RAS model
embedded in Datasphere
Lower Colorado River
Concern Point
Low Water Crossing

## Slide 7: When is Hurricane Season?
Atlantic Hurricane Season: June 1 - November 30
Peak of season in August and September
You are here
Source: Melissa Huffman, NWS Corpus Christi

## Slide 8: Task 1: Project Management
Achievements during last Quarter
    Selected first 30 gauge sites
    Beginning collaboration with Austin District Maintenance
    Received first 12 gauge permits
    Advancements in Datasphere
    Advancements in Bridge Modeling
Challenges for Next Quarter
    Selection of second 30 gauge sites
    Begin collaboration with Beaumont District
    More gauge permits obtained
    Advancements in Data Assimilation and 3D road representation
    Cope with Hurricane Season!

## Slide 9: Streamflow II Overview Meeting Agenda
Task 1: Project Management
Task 2: Watershed Selection and Site Evaluation Task 3: Gauge Installation, Operation and Maintenance Task 4: Flood Forecast System Operation Task 5: Forecast Model Assessment
Task 6: Flood Manual and Training

## Slide 10: Prioritized Watershed Region Identified using Weighting Factors
Selecting Watersheds
Field Assessment
Desktop Assessment
Base set of Bridges
Site Selection
Coastal Gauging
Daily Vehicle
Miles Travelled
DMVT
Bridge Count
Flood Fatalities
Terrain Slope
Soil Drainage
100yr-24hr Precipitation

## Slide 11: Flood Risk Factors have a Combined Gradient from the Coast towards Inland
High
Rain
Poor Drainage
Flat
Slope

## Slide 12: 400 Potential Gauge Sites from Office Reconnaissance

## Slide 13: Divide the HUC6 Basins into Three Groups
Potential gauge sites
identified by USGS
HUC6 Group | Number of Potential Gauge Sites
Lower | 60
Middle | 100
Upper | 240
Total | 400
Upper
Middle
Lower

## Slide 14: Evacuation Routes
Evacuation Routes are in Lower and Middle basins

## Slide 15: Gauging Density in Middle Basins
Basin | Area SqKm | USGS Gauges | LCRA Gauges | Existing Gauges | Gauges/1000 SqKm
San Antonio | 10863 | 23 |  | 23 | 2.1
Guadalupe | 15378 | 27 |  | 27 | 1.8
Lower Colorado | 7513 | 7 | 26 | 33 | 4.4
Lower Brazos | 20473 | 17 |  | 17 | 0.8
Lower Trinity | 15836 | 12 |  | 12 | 0.8
Chart: Existing Flow Gauges / 1000 Sq Km
| San Antonio | Guadalupe | Lower Colorado | Lower Brazos | Lower Trinity
Gauges/1000 SqKm | 2.1173 | 1.7558 | 4.3924 | 0.83036 | 0.75777

## Slide 16: 100 Recon Sites After Field Visits

## Slide 17: Field Assessment of all Potential Sites in Middle Group

## Slide 18: 14 Operational Gauges, 30 Selected New Sites
StoryMap Demo by David Arctur
https://arcg.is/veW9T0

## Slide 19: Gauges in TxDOT Districts
Streamflow I 20 Gauges
Streamflow II, Phase 1 30 Gauges

## Slide 20: Field Reconnaissance for next 30 sites in Lower Basins
Potential gauge sites
identified by USGS
HUC6 Group | Number of Potential Gauge Sites
Lower | 60
Middle | 100
Upper | 240
Total | 400
Upper
Middle
Lower

## Slide 21: Task 2: Watershed Selection and Site Evaluation
Achievements during last Quarter
    Completed field reconnaissance of 100 potential sites in Middle Group of basins
    Identified first 30 gauging sites
Challenges for Next Quarter
    Identify second 30 gauging sites starting with Lower Group of basins
    Complete Technical Memorandum 2 by 31 July

## Slide 22: Streamflow II Overview Meeting Agenda
Task 1: Project Management
Task 2: Watershed Selection and Site Evaluation Task 3: Gauge Installation, Operation and Maintenance Task 4: Flood Forecast System Operation Task 5: Forecast Model Assessment
Task 6: Flood Manual and Training

## Slide 23
08031020 Cole Ck at I-10 nr Orange, TX
Installation and Lessons Learned
Requested by Beaumont District 31 March 2021
Data flowing
14 April 2021
Relocated Streamflow I Gauge

## Slide 24: Installation Day (and heaviest rainfall to date as of April 2021)

## Slide 25: Installation Day

## Slide 26
Gage Height is now being reported
through USGS National Water
Information System
Tidal Influence
Notes: Explain how we learned we could get well defined discharge here even in tidal flows.

## Slide 27: Relation between Stage Height and Velocity
Velocity
Stage
Height
(ft)
Velocity
(ft/sec)
Flow
pulse
Stage Height
Notes: As water level rises tidally, the velocity decreases and vice versa

## Slide 28: Relation between Stage Height and Velocity (Tehuacana Creek nr Waco)
Discharge Stg/Q
Discharge by velocity
Notes: As water level rises tidally, the velocity decreases and vice versa

## Slide 29: Cole Creek Data with Discharge Pulses for 16-29 May, 2021
Stage Height
Surface Velocity
Discharge

## Slide 30: Gauge Documentation

## Slide 31: Gauge Documentation
Detailed analysis for each visit-visit period.
Three-step approval process of stage data
- Evaluation of discharge hydrographs
Summary of any corrections or anomalies
- Hydrographic comparisons when available

## Slide 32: Task 3: Gauge Installation, Operation and Maintenance
Achievements during last Quarter
    -Cole Creek installation
    Advance preparation of streamflow II Installation equipment.
    Procedures for operations and maintenance outline for thoughtful evaluation of RQ-30.
Challenges for Next Quarter
    Efficient installation of 40+ Streamgages
    Continued coordination for permitting and traffic control
    Operations and Maintenance performed in tandem with installations

## Slide 33: Streamflow II Overview Meeting Agenda
Task 1: Project Management
Task 2: Watershed Selection and Site Evaluation Task 3: Gauge Installation, Operation and Maintenance Task 4: Flood Forecast System Operation Task 5: Forecast Model Assessment
Task 6: Flood Manual and Training

## Slide 34: KISTERS Datasphere Functions
Data Ingestion and Aggregation
NOAA Weather and Water Forecasting
Observation networks
  USGS
  TxDOT
  Others
Data Analytics
Discharge to water level using rating curves
Time Series at points from raster forecasts (e.g. precipitation)
Probabilistic times series forecasts from ensembles
Data Display and Access
Graphical User Interface
Application Programming Interface
Simulation Modeling
River routing by Muskingum-Cunge
River routing by HEC-RAS
Data Assimilation
Combining observations, modeling and forecasting to provide improved forecasts

## Slide 35: KISTERS Storages
Time Series Storage
Scalar time series in (No)SQL storages
Typically used for gauge observation sites
Time series analytics
Used when users define their own gauge locations
Array storage
Multidimensional storage (space, time, parameter, elevation, modelmember)
Geospatial analytics
Model results like stream forecasts can be supported using the “stationId“ as a dimension

## Slide 36: Raster Analytics
  Extraction of point time series per pixel
  Extraction of polygon statistics as point time series
  General in-storage analytics
    Aggregations and statistics
    e.g. min, max, mean, total, variance
Question: What rainfall is forecast over my District?

## Slide 37: Time Series Ensembles (multiple forecasts from a given time point)
Derive probabilistic forecasts (max, min, mean, etc)
Probabilistic forecasting
Today
NWM Medium Range Forecast Ensemble (7 Forecast Traces)

## Slide 38: Storages and Data Flow
NWM source
netcdf-CF by time step and ensemble member (as the model writes it)
NWM in datasphere spatial (Array Storage)
raster as zarr-CF in AWS S3 or Hadoop HBase with optimized chunking for balanced map and time series extraction use cases
Extract Transform, Load (ETL) through API
meteo: (ensemble x) time x latitude x longitude
derived data for fixed polygon such as HU6 and HU8 as (ensemble x) time x station-id
hydro: (ensemble x) time x station-id
datasphere spatial GUI
visualization of animated maps, (ensemble) time series at user-selected points / polygons on-the-fly
requests to API
maps as png, timeseries as JSON
Model Integration Framework
Hydraulic model derived from HEC-RAS and Muskingum-Cunge routing in variational data assimilation mode + forecast mode
Observations in datasphere sensor
scalar time series data: observations and forecasts at gauges in Hadoop HBase on Amazon Web Services
observations at gauges
for data assimilation
in JSON
NWM as forcing
results in NWM reference
datasphere sensor GUI
visualization of time series, statistics, alarm levels and notifications
requests to api
time series as JSON
requests to API
data by use case:
- forecast archive for individual locations
- aggregated data by shapes / polygons
- time-aggregated data (available soon)
supported formats: netcdf-CF, JSON, png, gif, jpg etc.
Observations sources
Time series data ingestion from observation networks (USGS, TxDOT, LCRA, others)
Extract Transform, Load (ETL) through API
requests to api

## Slide 39: Observation Networks in Datasphere

## Slide 40: Medium Range Forecast at Cole Creek

## Slide 41: Raster Data Viewer and Time Series at a Selected Point

## Slide 42: Global Forecast System (GFS) for Weather

## Slide 43: Observed Flows and Forecast Rainfall, Guadalupe River at Comfort

## Slide 44: Forecast Flows and Alarms, Pedernales River

## Slide 45: Forecasts at Concern Point M1 in Mason County (Demo by Matt Ables)

## Slide 46: Task 4: Flood Forecast System Operation
Achievements during last Quarter
    Enhancements to Datasphere
      Inclusion and dynamic display of NWM Results
      Addition of custom layers and map overlays
        TxDOT Districts, HUC Basins, Bridges, Streams, etc.
      Calculated time series in GUI
      Visualization of raster time series with sensor data
      Enhancements and alarming on Shared Channel data (LCRA, USGS)
      Addition of Concern Point virtual stations
    …..
Challenges for Next Quarter
    Planned enhancements to Datasphere
      Begin development on:
        Alarms on forecast data
        Visualization of HEC model schema
        Display and alarms on HEC results
        Visualization of bridge and sensor level alarms
        Add current and forecast radar to sensor maps
        Add NWM clone forecast

## Slide 47: Streamflow II Overview Meeting Agenda
Task 1: Project Management
Task 2: Watershed Selection and Site Evaluation Task 3: Gauge Installation, Operation and Maintenance Task 4: Flood Forecast System Operation Task 5: Forecast Model Assessment - Data Assimilation
Task 6: Flood Manual and Training

## Slide 48: Colorado Basin Prediction Testbed
75 USGS Stream gauges
50 LCRA (Lower Colorado River Authority) gauges separate from USGS
247 LCRA rain gauges
Austin
Streamflow Measurement
Precipitation Measurement

## Slide 49: HEC-RAS model of Lower Colorado
    Consistent unsteady-state model of about 300 km starting upstream of Austin covering the complete Colorado river reach up to Gulf of Mexico
    Simulations completed for flood events  HEC-RAS has some stability issues, which require very small time steps resulting in long computations, need for refined calibration for high flows
    Integration into KISTERS Operational Planning GUI for online execution and visualization
    Next steps:
      Real-Time Optimization model conversion and implementation of Data Assimilation mode and workflow for operational forecasting  will get rid of the stability issues
      Preparation of roll-out of the concept to other basins and systematic performance assessment

## Slide 50: HEC-RAS model of Lower Colorado – October 2018 flood
Wharton
Discharge
Water Level
Austin
Discharge
Water Level

## Slide 51: HEC-RAS model of Lower Colorado – HEC-RAS in Operational Planning GUI

## Slide 52: NWM model routing clone
    Clone can reproduce the results of the NWM routing to a very high degree
    Model is available for the complete Colorado basin including the integration of the lakes/reservoirs
    NWM data assimilation approach (nudging) is still not in and therefore results in different results downstream of NWM-considered gauges
    Next steps:
      Operational Planning GUI implementation, completion of Data Assimilation mode and workflow for operational forecasting
      Preparation of roll-out of the concept to other basins and systematic performance assessment

## Slide 53: Preliminary Data Assimilation Testing
Gap at Forecast Time for reach upstream of streamflow gauge:
NWM - does not consider any data assimilation due to the implemented approach
Clone - assimilation still not implemented
 very similar results of the models, clone will show significant improvement once data assimilation is implemented
Assimilation impact downstream of streamflow gauges
NWM implements some persistency of the change in its assimilation approach
Clone – assimilation still not implemented
 significant improvement of clone after implementation of approaching data assimilation approach

## Slide 54: Base Level Engineering Model
    Guadalupe model (short river reach represented in a single BLE model) as proof-of-concept
    Challenge: consolidation of all the individual models
    Conclusion: BLE models have significant potential due to state-wide coverage, but exploitation also requires significant effort
Guadalupe River at Comfort (Demo by Dirk Schwanenberg)

## Slide 55: Task 5: Data Assimilation
Achievements during last Quarter
    Assessment of BLE models (HEC-RAS)  initial work to make them suitable for unsteady state simulations
    Assessment of Lower Colorado model  suitable with some caveats and running in OP web GUI
    NWM Muskingum-Cunge clone available in simulation mode
    Implementation of data assimilation in both models is work in progress
Challenges for Next Quarter
    Completion of data assimilation mode in HEC-RAS and NWM clone models
    Full operational integration as forecasting models
    OP GUI integration of both models for scenario analysis
    Roll-out of the approach to other basins in Texas starting with Brazos
    Start of systematic performance assessment

## Slide 56: Streamflow II Overview Meeting Agenda
Task 1: Project Management
Task 2: Watershed Selection and Site Evaluation Task 3: Gauge Installation, Operation and Maintenance Task 4: Flood Forecast System Operation Task 5: Forecast Model Assessment
Task 6: Flood Manual and Training

## Slide 57: Austin District: Area Offices and Maintenance Sections
Burnet
South Travis
Georgetown
North Travis
Bastrop
Area Offices have equivalent lane miles of roads
Maintenance Sections by county in rural areas

## Slide 58: StoryMap of Concern Points for Hays County
Hays: https://arcg.is/111Cna1

## Slide 59: StoryMap of Concern Points for Mason County
Mason: https://arcg.is/1WWbH8

## Slide 60: Roadway Closure Information
DriveTexas.org
Roadway closures due to floodings, 2014-2020
Flooding on IH-10 during Hurricane Harvey
21,261 road closures from flooding

## Slide 61: TxDOT Recorded Flooded Roads, 2014 to 2020
Large differences in flood records at county lines, missing data in some metropolitan areas
Houston
San Antonio
Austin
Dallas – Fort Worth

## Slide 62: Low Water Crossing Measured by Emergency Services District 11 using Pin2Flood
Low Water Crossing, Normal Conditions
Low Water Crossing, Minor Flooding (ESD 11)

## Slide 63: Real-Time Inundation Mapping using Pin2Flood
Low Water Crossing, Minor Flooding (ESD 11)
Pin Drop by Public Safety
Flood Inundation Return

## Slide 64: Task 6: Flood Manual and Training
Achievements during last Quarter
    Interactions with the Austin District
        Discussed past events and how they dealt with them
        Discussed steps they take during a flooding event
        General staffing
    Concern Points established
        Austin District provided sites which are a concern in Hays and Mason County
        Mainly, these are low water crossings
        Create a Story Map
Challenges for Next Quarter
    Development of realistic HSEEP exercise
        Meetings with the Beaumont District
        Identify steps they take during a flooding event
        Identify flow of information
    Building a Concern Point template

## Slide 65: Concluding Remarks by Committee Members
Please introduce yourself and share how this project is relevant to the work that you do. (Is there anything we could do that would make it more valuable?)
Given your awareness of community needs, gaps, and work by others, what is the most strategic way that we can capitalize on the value of this work?
What do you see as the biggest challenges or areas of weakness that we should be considering?
Any additional comments, questions, words of wisdom, observations that you would offer to us?
Jason Johnson – NOAA/NWS
Jorge Urquidi – City of Austin
Justin Terry – HCFCD
Mark Lenz – NOAA/NWS
Paul Yura – NOA/NWS
Peter Smith – TxDOT TPP, ret
Sam Hermitte – TWDB