## Slide 1: Evaluate Improved Streamflow Measurement at TxDOT Bridges Project 0-7095 Being conducted for TxDOT by UT Austin and US Geological Survey with the support of Kisters North America and Aqua Strategies September 2020 to August 2023
Presentation for Fourth Quarterly Review Meeting, Friday 24 September 2021
Acknowledgements: Rose Marie Klee (H&H Director, TxDOT), Shelley Pridgen (RTI Project Manager), Matthew Heinze (MNT, TxDOT),
Joe Geossling (AUS, TxDOT); David Key, ESP Associates, NC; Dean Djokic and Chad Jennison, ESRI

## Slide 2: TxDOT Priorities
SAFETY
        Our staff, our community
        Emergency response
CONNECTIVITY
        Reliability of the transportation network
  Asset management
        *BRIDGES*
  Efficiency and efficacy
        For TxDOT
        For other/all jurisdictions
Slide: Rose Marie Klee, TxDOT

## Slide 3: TxDOT Project Management Committee
Rose Marie Klee H&H Section Director, DES
Abderrahmane Maamar-Tayeb
H&H Section Team Lead, DES
Adam Jack Dir of Trans Plan & Development, BMT
Andrew Lee District Bridge Engineer, BMT
Jared Browder Maintenance Assess Spec, MNT
Trent Ellis Bridge Scour Coordinator, BRG
Shelley Pridgen Research Project Manager, RTI
Joseph Goessling
Lead Hydraulics Engineer, AUS
Matthew Heinze TxDOT Emergency Mgmt Coordinator, MNT
Welcome to new member, Matthew Heinze!

## Slide 4: Project Advisory Committee
Jason Johnson, NOAA National Weather Service Mark Lenz, NOAA National Weather Service
Paul Yura, NOAA National Weather Service
Sam Marie Hermitte, Texas Water Development Board
Jorge Urquidi, City of Austin, Flood Early Warning System
Justin Terry, Harris County Flood Control District
Peter Smith, former TxDOT Dir of Trans Planning and Programming
+ other members of the H&H Section, TxDOT Design Division:
+ new member of the City of Austin FEWS group Christina Bryant
Welcome to
the Discussion!
Hiruy Berhe | Jaime Villena-Morales
Lucinda Soto | Sauda Ahmed
 | Zenia De Leon

## Slide 5: Streamflow II Overview Meeting Agenda
Task 1: Project Management
Task 2: Watershed Selection and Site Evaluation Task 3: Gauge Installation, Operation and Maintenance Task 4: Flood Forecast System Operation Task 5: Forecast Model Assessment
Task 6: Flood Manual and Training
Part 1 – Progress with Tasks
Part 2 – Proposed Flood Maps for TxDOT
Consideration of this proposal:

## Slide 6: Task 1: Project Management
Achievements during last Quarter
    Visit to Beaumont District on 28-30 July
    Developed plan for flood mapping
    Advanced collaboration with TxERA (TxDOT Emergency Response Application)
    Rapid Assessment process for culverts in Austin District
Challenges for Next Quarter
    Complete selection of second 30 gauge sites. Install as many new gauges as possible
    Continue collaboration with Beaumont and Austin Districts
    Begin flood map development if plan is approved by PMC
David Maidment, UT Austin

## Slide 7: Task 2: Watershed Selection and Site Evaluation
Achievements during last Quarter
    Completed Technical Memorandum 2 on Watershed Selection and Site Evaluation
Challenges for Next Quarter
    Complete field reconnaissance and selection of second 30 gauge sites

## Slide 8: Task 3: Gauge Installation, Operation and Maintenance
Achievements during last Quarter
    Installation of 36 stream gauges
    Streamlined site selection and procedures
    Reconned more than 40 additional sites for the second round of installation
Challenges for Next Quarter
    Continue installation of stream gauges
    Continued coordination for permitting and traffic control
    Operations and maintenance performed in tandem with installations
Scott Gryzb, US Geological Survey

## Slide 9
Chart: Field Recons and Installs since April
 | 1 | 25 | 50 | 75 | 100 | 125 | 150 | 168
Installations | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36

## Slide 10
Chart: Field Recons and Installs since June 1
| 44357 | 44357 | 44357 | 44357 | 44357 | 44357 | 44358 | 44362 | 44362 | 44362 | 44362 | 44362 | 44362 | 44363 | 44363 | 44363 | 44363 | 44446 | 44446 | 44446 | 44446 | 44446 | 44446 | 44446 | 44446 | 44446 | 44446 | 44446 | 44446 | 44446 | 44446 | 44446 | 44447 | 44447 | 44447 | 44447 | 44447 | 44447 | 44447 | 44447 | 44447 | 44447 | 44447 | 44447 | 44447 | 44460 | 44460 | 44460 | 44460 | 44460
Recons | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50
Installations | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36
copy2 | 1 | 17 | 18 | 45 | 46 | 50

## Slide 11: StoryMap for TxDOT RQ-30 Stream Gauging Sites
https://arcg.is/veW9T0
Streamflow I Refurbished Gauges: 12
Streamflow II New Gauges: 24
Total Gauges: 36
David Arctur

## Slide 12: StoryMap for Field Reconnaissance of Potential Sites
https://arcg.is/veW9T0

## Slide 13: Technical Highlight: How data gets into NWIS (National Water Information System)
R- script
NWISWEB Retrieval
Scott Gryzb
Notes: Data in FTP location is downloaded and ran through R Script on Virtual Machine creating a file that is then transferred into the Hot sync directory. Once in that directory the file is processed and ran through DECODES in which the file is DECODED for specific Time Series in AQ. Once the data in in AQ NWISWEB retrievals pick up the data and display it on the WEB

## Slide 14: On a Typical Day ….
    Check gauges
    Preliminary Quality assurance and Quality Control
    Field Trips, Measurements, or Records Computation

## Slide 15: Gauge Checks
Notes: Automatic fault detections, Look for elevated flows to get measurements.

## Slide 16: On a Typical Day …
    Check gauges
    Preliminary Quality Assurance and Quality Control (QA/QC)
    Field Trips, Measurements, or Records Computation

## Slide 17: Ongoing Quality Control
Automatic Filtering
Manual Filtering
Final Checks
Publish to NWIS as Provisional
Notes: Data does not always come in pretty. Wind spikes are common. Automated spike filtering, Manual spike deletion, before going to NWIS

## Slide 18: On a Typical Day ….
    Check gauges
    Preliminary Quality assurance and Quality Control
    Field Trips or Records Computation

## Slide 19: Types of Field Trips
Routine
    Operations and Maintenance
    Routine gauge height and/or discharge verification
    Cross section verification
Special
    Gauge repair
    Cross sections and Levels
    Storm events

## Slide 20: Types of Records Computation
    Gauge height corrections
    Discharge Rating Development
    Comparison of RQ-30 / Standard USGS methods
    Period Analysis for each gauge

## Slide 21: Task 4: Flood Forecast System Operation
Achievements during last Quarter
HEC-RAS model integration extended by data visualization of longitudinal and cross sections.
Evaluation of the use of BLE and Lower Colorado model completed (MSc thesis Alp Koyulhisarli). Models not suitable for unsteady flow hydrographs, lessons learned will contribute to future hydraulic modelling activities.
Addition of TxDOT Radar Gauges, JCDD6, and SRA gauges into Datasphere.
NWM Stage and Flow APIs for retrieval of data via COMID or lat/long.
Numerous Datasphere GUI and graph enhancements.
Challenges for Next Quarter
Continue ingestion of observations networks
    Complete USGS data for Texas
Begin development of thematic flood maps
    Observations map and Bridges map
Prepare data and maps for Beaumont District exercise in Feb 2022
Matt Ables

## Slide 22: Technical Highlight: Setup and Ingestion of Observation Networks
Jefferson County DD6
SHEF E
FTP
LCRA Web Service
XML
Datasphere Storage and Services
USGS NWIS
Web Service
text
KISTERS Distributed Services Manager (KiDSM)
KISTERS Data Acquisition &
Transformation (KiDAT)
Datasphere
The Datasphere process to manage, convert, and import observation networks

## Slide 23: KISTERS Distributed Services Manager (KiDSM)
Jefferson County DD6
SHEF E
FTP
LCRA Web Service
XML
USGS NWIS
Web Service
text
KISTERS Distributed Services Manager (KiDSM)
Key Features
Downloads data from Web, FTP, REST, and other APIs.
Source and Target location monitoring and notifications.
Data processing log and monitoring.
Monitor and gather data from observation networks

## Slide 24: KISTERS Data Acquisition and Transformation (KiDAT)
KISTERS Distributed Services Manager (KiDSM)
KISTERS Data Acquisition &Transformation (KiDAT)
Key Features
Quickly convert observation network formats and stream to Datasphere.
Automatically builds new stations and sensors in Datasphere on import.
Processes, cleans, and organizes high volumes of data and file formats.
Convert, clean, and import data from observation networks

## Slide 25: Representation of Multiple Networks in Datasphere
KISTERS Data Acquisition &
Transformation (KiDAT)
Datasphere
Key Features
Each observation network is organized with unique login and account.
Data shared from each observation network account to the TxDOT account.
Allows for better classifications, alarms, and general management of the data based on the observation network data characteristics.
Display data from observation networks

## Slide 26: Task 5: Forecast Model Assessment
Achievements during last Quarter
    Completed assessment of HEC-RAS models
    Operational integration of HEC-RAS and NWM clone extended by animated longitudinal and cross section views
    OP GUI integration of both models for scenario analysis in final stage
    Continuation of error analysis of NWM with stage height
Challenges for Next Quarter
    Set up Data Assimilation approach with Muskingum-Cunge
    Complete error analysis and analyze results (patterns, predictability)
    Implement error analysis within Datasphere as well
    Initiate river hydraulics analysis (additional student on project started Fall 2021)
Paola Passalacqua, UT Austin

## Slide 27: HEC-RAS Model Assessment
    - Assessment in MSc project by Alp Koyulhisarli under supervision by KISTERS and University of Texas
    - Significant manual work to enable the Lower Colorado model to simulate flood hydrographs
     various lessons learned, approach not scalable (for the time being)
2015 flood
2018 flood
Dirk Schwanenberg, KISTERS

## Slide 28: Visualization of Profiles and Cross-Sections
    Web-based visualization in Operations Planning GUI
    Animated visualization of level and streamflow in longitudinal section
    Animated visualization of level in cross section
    Future refinement for discussion:
    - Definition and visualization of warning/alarm levels

## Slide 29: Technical Highlight: RAS2FIM – Creation of Flood Inundation raster libraries and rating curves from HEC-RAS models
Create shapefiles
from directory of
HEC-RAS models
Conflate HEC-RAS
to National Water
Model
Get terrain data
for each HUC-12
Create FIM depth
rasters using
HEC-RAS Mapper +
HEC-RAS API
HEC-RAS
Files
National
Datasets
Watershed Boundary Dataset (WBD)
National Water Model flowlines (NWM)
Real-time mapping
of flooding events
3DEP Web Coverage Service
(or TNRIS, Fathom, etc..)
Cloud served
Terrain data
BLE, FEMA,
Municipality, USACE,
Etc…
Raster
Library
and
Rating
Curves
Cloud served
NWM flow rates
Stored per National Water Model
‘feature-id’
Per API service from the
National Water Model
(coming soon)
RAS2FIM scripts
Andy Carter, UT Austin

## Slide 30: Representation of River Channel in HEC-RAS and National Water Model Hydrofabric
Geospatial HEC-RAS 1D Models
Conflation to the National Water Model Hydro- Fabric

## Slide 31: Creating a Rating Curve at Half-ft Vertical Intervals for each Channel Reach
HEC-RAS conflated to National Water Model (NWM) Hydro-fabric
HEC-RAS Model ‘clipped’ to Corresponding NWM ‘COMID’
Compute a ‘reach averaged’ depth rating
curve for the ‘Feature-ID’
National Water Model ID number for reach

## Slide 32: Build an Inundation Map Stack as TIF files
Map library created per ‘feature-id’ with
Corresponding reach averaged
Indirect rating curve
Avg Depth = 12.5ft
Q = 5,867 cfs
Avg Depth = 16.0ft
Q = 9,499 cfs
Avg Depth = 27.5ft
Q = 83,958 cfs

## Slide 33: Example of Application of RAS2FIM for Denton Creek, HUC8 = 12030104
A HUC8 unit of Base Level Engineering Models
A Flood Inundation Map Library
and set of Rating Curves
519 HEC-RAS Models (611 Mb)
Drainage area = 719 sq miles
National Water Model Streams = 614
HEC-RAS Cross Sections = 13,299
Flood Inundation Library data (1.01 Gb)
Depth Rasters = 12,296
Rating curves PNG and CSV = 521
Depth Interval of GeoTIFFs = 0.5 ft
CSVs
GeoTIFFs
PNGs
Processed in 18 HUC12 units
HUC12 units

## Slide 34: Task 6: Flood Manual and Training
Achievements during last Quarter
Challenges for Next Quarter
    Development of realistic HSEEP exercise
      Continue meetings with the Beaumont District
          Identify flow of information from the bottom up and the top down
          Identify the types of useful maps needed for the BMT District
      Continue meetings with TxDOT Statewide Emergency Management
          Identify the most important map/data needs that would apply to all TxDOT districts
      Collaborate with Esri on TxERA
      Collaborate with Veoci on alerts and notifications
    Interactions with the Beaumont District
        Discussed past events and how they dealt with them
        Discussed steps they take during a flooding event
        Discussed the data and information needs during a flood event
        Field visits to flood prone roads
Interactions with TxDOT Statewide Emergency Management
        Discussions with VEOCI for alerts and notifications
        Discussions with Esri for TxERA
        Concern Points (Flood Points) Surveyed
        17 separate site surveys in Travis, Hays, Lee, Williamson, Burnet, Llano, Mason, Gillespie and Blanco Counties.
        Mainly, these are low water crossings
        Created a story map and Flood Point Template
Harry Evans, UT Austin

## Slide 35: Summary of Lessons Learned from Visit to Beaumont District (28-30 July)
Value of Local Intelligence!
Comprehensive understanding of BMT flood emergency response
Full integration into National Incident Management System (NIMS)
BMT Staffs a 24/7 Emergency Operations Center (EOC) during flood emergencies
Formal and defined lines of communication with Texas Division of Emergency Management (TDEM)
Maintenance Sections are the “tip of the spear” when a flood emergency occurs
What flood information is useful and useable to Maintenance in the EOC and the Field

## Slide 36
TxDOT BMT has a Detailed Hurricane Preparedness Plan
Uses National Incident Management System (NIMS) roles

## Slide 37: Daily Cycle of Information Development and Decision
Integration with TDEM State Operations Center

## Slide 38
Purpose:
Low Water Crossings are flood-prone
National Water Model forecasts flows at many of these sites
Austin District study in 2017 highlighted 153 “flood-points”, of which 20 are highest priority
Rapid Assessment Survey:
Minimizes the ‘time-on-target’ required for a field survey team to obtain the necessary data
Provides ‘just-enough’ appropriately attribute survey points, photos and site measurements to insert the hydraulic structure into HEC-RAS
Written procedure:
We field surveyed 17 sites of the top 20 in Austin District
We developed a written Rapid Assessment Survey for Culvert Crossings
Technical Highlight: Rapid Assessment of Low Water Crossings (Austin District)
Christine Thies, UT Austin

## Slide 39
For the test surveys, three classifications of survey points are requested.
They are (1) road edge, (2) pipe information and (3) staff gage [if available].
Road Edge – The field survey team acquires one (1) point on the edge of the roadway. This is used as a check against the site’s LiDAR terrain to determine any datum issues between the survey and the remote sensed data.
Pipe Information – One survey spot is acquired at the bottom center of each pipe/culvert on both the upstream and downstream face. The point data is attributed with the opening dimensions [height, width, radius] and material parameters [Reinforced Concrete Pipe, Corrugated Metal Pipe, etc..].
Staff / Flood Gage – One survey spot is acquired at the staff gage if one is installed at the crossing of concern. This point is recorded at the “zero” elevation of the staff gage.
Road Crossing Survey Components

## Slide 40
To detail the survey methods and locations, we have created two documents:
Documentation
https://arcg.is/10aXr0
“Rapid Assessment Survey for Culvert Crossings”
Background
Survey Point Collection Details
Survey Equipment
Data Collection Software (Collector)
How to Collect Survey Points
Story Map
Top 20 Sites
Tab for each site
Pictures, generalized detail about each site

## Slide 41: Discussion of Progress and Plans with the Project Management Committee
Your contributions are welcomed and appreciated!

## Slide 42: Streamflow II Overview Meeting Agenda
Task 1: Project Management
Task 2: Watershed Selection and Site Evaluation Task 3: Gauge Installation, Operation and Maintenance Task 4: Flood Forecast System Operation Task 5: Forecast Model Assessment
Task 6: Flood Manual and Training
Part 1 – Progress with Tasks
Part 2 – Proposed Flood Maps for TxDOT
Consideration of this proposal:

## Slide 43: Five Map Layers
Hydrology Base Map
Observation Gauges
Flooded Bridges
Flooded Roads
Inundation Extent

## Slide 44: 1. Hydrology Base Map
One map for each Maintenance Section
Hydrology Base Map
Observation Gauges
Flooded Bridges
Flooded Roads
Inundation Extent

## Slide 45: State-wide FATHOM 3m DEM of Texas
Image: Yan Liu, Oak Ridge National Laboratory
Seamless 3m Digital Elevation Model in 1º x 1º tiles
Built by compositing and resampling Texas 1m
LIDAR coverage, and filling some gaps. Has 11 times
cell density of National Elevation Dataset
Data provided by courtesy of:
https://web.corral.tacc.utexas.edu/nfiedata/fathom3m/
Hydrology Base Map
Observation Gauges
Flooded Bridges
Flooded Roads
Inundation Extent

## Slide 46: FATHOM 3m Topography southeast of Beaumont
Fathom 3m DEM
Imagery base map with streams
Roads base map with streams
Hydrology Base Map
Observation Gauges
Flooded Bridges
Flooded Roads
Inundation Extent

## Slide 47: National Water Model Hydrofabric for Texas
Geospatial framework for National Water Model provided by the National Water Center
Adapted from National Hydrography Dataset, Medium and High Resolutions

## Slide 48: 2. Observations Gauges Map
Data from multiple observation networks connected into the KISTERS Datasphere
Each gauge has several time series (water level, precipitation, ...)
Hydrology Base Map
Observation Gauges
Flooded Bridges
Flooded Roads
Inundation Extent
Thematic map: shows only data of one type across all networks
For example: the map of water level above geodetic datum ….
Color Code points according to degree of flood risk
Geodetic datum
Gauge datum
Stage Height
(local water level or depth)
1
2
3
4
5
6
Stage Height (ft)
Time

## Slide 49: Use of Two Water Level Scales (Intellisense Gauges)
https://flashflood.info:8080
Water Depth
Elevation Above
Geodetic Datum
125 water level sensors being installed
in Beaumont District
Hydrology Base Map
Observation Gauges
Flooded Bridges
Flooded Roads
Inundation Extent

## Slide 50: Reference Elevations (at Cole Creek Gauge Site)
Road Elevation = 23.24 ft
Low chord elevation = 15.84 ft
Crest stage gage elevation = 10.95 ft
Channel bottom = 0.71 ft
Mon 13-Sep
Tues 14-Sep
Weds 15-Sep
Thurs 16-Sep
Fri, 17-Sep
8
7
6
5
4
2
1
3
Water Level (ft)
Tropical Storm Nicholas (September, 2021)
Maximum water level 7.5 ft
Maximum Discharge 290 cfs
Hydrology Base Map
Observation Gauges
Flooded Bridges
Flooded Roads
Inundation Extent

## Slide 51: 3. Bridges and Culverts
Source: Sue Tidwell, TxDOT Beaumont District
Goal is to provide flood forecasting at all these locations
Hydrology Base Map
Observation Gauges
Flooded Bridges
Flooded Roads
Inundation Extent
These critical bridges and culverts were identified by BMT Maintenance staff

## Slide 52: 4. Flooded Roads
This map and summary table are drawn from the
FIMAN-T system developed by the North Carolina DOT
Source for Images: David Key, ESP Associates
Hydrology Base Map
Observation Gauges
Flooded Bridges
Flooded Roads
Inundation Extent

## Slide 53: 3D Road Map of North Carolina, State-Wide Extent
Hydrology Base Map
Observation Gauges
Flooded Bridges
Flooded Roads
Inundation Extent

## Slide 54: 3D Road Map of North Carolina, Local Extent
Hydrology Base Map
Observation Gauges
Flooded Bridges
Flooded Roads
Inundation Extent

## Slide 55: 5. Flood Inundation Mapping
Source of Image: Derek Giardino, West Gulf River Forecast Center, National Weather Service
Hydrology Base Map
Observation Gauges
Flooded Bridges
Flooded Roads
Inundation Extent
Inundation Extent
Flooded Roads Flooded Bridges Observation Gauges
all have to be consistent
Inundation Extent map
from NWS Agency Priority Goal exercise in Houston (2019)
Produced by National Water Center

## Slide 56: Technical Highlight: TxERA Field Operations Dashboard (TxDOT Emergency Response Application)
TS Nicholas, 13 September 2021
Source of Image: Chad Jennison, ESRI

## Slide 57: TxERA – Traffic Flow and Vehicle Locations at Regional Scale
Source of Image: Chad Jennison, ESRI

## Slide 58: Traffic Flow and Vehicle Locations at Local Scale
Source of Image: Chad Jennison, ESRI

## Slide 59: Texas Flood Impact Dashboard
Source of Image: Dean Djokic, ESRI
Developed by UT Austin, ESRI and KISTERS for Texas Division of Emergency Management to measure flood impact by number of flooded Address Points
Application was live during TS Nicholas, Sept 2021
9.3 million Address Points in Texas
Address Points
for homes

## Slide 60: Conversion to ESRI Dashboard Framework Application (Like TxERA)
Source of Image: Dean Djokic, ESRI
Application was live during TS Nicholas, Sept 2021

## Slide 61: Rhode Island DOT Dashboard Example
Source of Image: Dean Djokic, ESRI

## Slide 62: Concluding Thoughts
Rapid progress on Field Reconnaissance and
Gauge Installation in last Quarter (June to August)
Need to Get Gauges Done – research team proposes to coordinate with TxDOT biweekly until all gauges
are installed
List of web links for Datasphere and StoryMaps provided to TxDOT
Flood Gauging:
Flood Information:
Meeting with Beaumont District on 28-30 July was critical
TxDOT wants what everyone else wants
with more detail on flooding of roads and bridges
Does Project Management Committee approve in principle the idea
of presenting flood information as map layers?