## Slide 1: Evaluate Improved Streamflow Measurement at TxDOT Bridges Project 0-7095 Being conducted for TxDOT by UT Austin and US Geological Survey with the support of Kisters North America and Aqua Strategies September 2020 to August 2023
Presentation for Fifth Quarterly Review Meeting, Tuesday 7 December, 2021
Acknowledgements: Rose Marie Klee (H&H Director, TxDOT), Shelley Pridgen (RTI Project Manager, TxDOT),
Trenton Ellis (H&H, TxDOT), Matthew Heinze (MNT, TxDOT), Keith Horn (BMT, TxDOT)
Congratulations on his retirement: David Arctur

## Slide 2: TxDOT Priorities
SAFETY
        Our staff, our community
        Emergency response
CONNECTIVITY
        Reliability of the transportation network
  Asset management
        *BRIDGES*
  Efficiency and efficacy
        For TxDOT
        For other/all jurisdictions
Slide: Rose Marie Klee, TxDOT

## Slide 3: TxDOT Project Management Committee
Rose Marie Klee H&H Section Director DES
Abderrahmane Maamar-Tayeb
H&H Section Team Lead DES
Adam Jack Dir of Trans Plan & Dev BMT
Andrew Lee District Bridge Engineer BMT
Jared Browder Maintenance Assess Spec MNT
Trent Ellis H&H Engineer DES
Shelley Pridgen Research Project Manager RTI
Joseph Goessling
Lead Hydraulics Engineer
AUS
Matthew Heinze TxDOT Emerg Mgmt Coord MNT
Welcome to four new members,
Jennifer Lash and LaDonna Waters!
Ryan Eaves and Drake Builta!
Jennifer Lash GIS Program Leader TPP
LaDonna Waters Lead Hydraulics Engineer BMT
Ryan Eaves Geotech Brch Mgr BRG
Drake Builta
Bridge Info Grp Lead
BRG

## Slide 4: Project Advisory Committee
Welcome to
the Discussion!
Sauda Ahmed | Lucinda Soto
Hiruy Berhe | Jaime Villena-Morales
Zenia De Leon | Marissa Williams
NOAA National Weather Service | State and Local Agencies
Jason Johnson, West Gulf River Forecast Center | Sam Marie Hermitte, TWDB
Paul McKee, Southern Region HQ | Jorge Urquidi, City of Austin, Flood Early Warning System
Paul Yura, Austin/San Antonio Weather Forecast Office (WFO) | Christina Bryant, City of Austin, Flood Early Warning System
Katie Landry-Guyton, Houston/Galveston WFO | Justin Terry, Harris County Flood Control District
Amanda Schroeder, Dallas/Fort Worth WFO | Peter Smith, former TxDOT Director TPP
+ other members of the H&H Section,
TxDOT Design Division:
NOAA Weather Forecast Office Service Hydrologists*
Jonathan Brazzell, Lake Charles, LA, WFO
Melissa Huffman, Christina Barron, Corpus Christi WFO
* To discuss gauges in their area

## Slide 5: Streamflow II Overview Meeting Agenda
Task 1: Project Management
Task 2: Watershed Selection and Site Evaluation Task 3: Gauge Installation, Operation and Maintenance
Task 4: Flood Forecast System Operation Task 5: Forecast Model Assessment
Task 6: Flood Manual and Training
Part 1 – TxDOT-USGS
Flood Data
Part 2 – TxDOT Flood
Information

## Slide 6: Streamflow II Overview Meeting Agenda
Task 1: Project Management
Task 2: Watershed Selection and Site Evaluation Task 3: Gauge Installation, Operation and Maintenance
Task 4: Flood Forecast System Operation Task 5: Forecast Model Assessment
Task 6: Flood Manual and Training
Part 1 – TxDOT-USGS
Flood Data
Part 2 – TxDOT Flood
Information

## Slide 7: Task 1: Project Management
Achievements during last Quarter (September to November)
    Completed selection of Phase 2 Gauge Sites
    Developed Hydrology Base Map
    Mapping and charting of flooded roads data from HCRS
    Visit to Beaumont District on 16-17 November
Challenges for Next Quarter (December to February)
    Complete installations of most Phase 2 Gauges
    Complete Flood Maps for TS Imelda in BMT District
    Complete Flood Emergency Response Exercise in BMT
    Begin planning for September Exercise
David Maidment, UT Austin

## Slide 8: Task 2: Watershed Selection and Site Evaluation
Achievements during last Quarter
    Completed Phase 2 Gauge Site Selection
Challenges for Next Quarter
    Complete Amendment to TM2 that documents selection of Phase 2 Gauge sites

## Slide 9: Flood Risk Factors have a Combined Gradient from the Coast towards Inland
High
Rain
Poor Drainage
Flat
Slope

## Slide 10: Texas Drainage Basins – Two Types, Inland and Coastal Basins
Inland River Basins
Moderate slope
Well drained
Lesser rainfall
Coastal Basins
Low slope
Poor drainage
High rainfall

## Slide 11: How to Site TxDOT Gauges?
From RFP: “Determine spatial distribution between gauge locations with a gauge network that is distributed and spaced to better represent the flow in the system, which will produce and improve the TxDOT Flood Forecast System. The distribution should be scalable to other watersheds.”
Streamflow II: How do we place 80 gauges
to supplement the current USGS gauge network?
USGS Stream Gauges

## Slide 12: Previous Site Selection (Inland River Basins)
Installed in Streamflow I (2017– 2019)
Installed for Phase 1 of Streamflow II

## Slide 13: Phase 2 of Streamflow II Site Selection: Bridges Selected for Evaluation
Desktop Reconnaissance | 1402 | Bridges
Field Reconnaissance | 91 | Bridges
Selected Sites | 39 | Bridges
Chart: 
| Desktop Reconnaissance | Field Reconnaissance | Selected Sites
 | 1402 | 91 | 39
Jody Avant
Scott Grzyb
and their colleagues …
… thanks for all your hard work!
Scott Grzyb

## Slide 14: Field Reconnaissance Criteria
Speed tests for modem transmission
Cross-section / bridge deck views and pier configurations
Channel straightness and velocity sensor obstructions
Measurement section view
Channel identification

## Slide 15: Final Site Selections for Phase 2 of Streamflow II
7 Streamflow II Gauges
Corpus Christi
Victoria
6 Streamflow II Gauges
Yoakum
3 Streamflow II Gauges
North Houston
7 Streamflow II Gauges
South Houston
8 Streamflow II Gauges
USGS Gauges
Phase 2 Installs
Streamflow I Gauges
8 Streamflow II Gauges
Beaumont

## Slide 16: Final Selections – 80 sites
Combined Total of 80 Gauges
Phase 2 Installs
Streamflow I Gauges
Phase I Installs

## Slide 17: Two clusters of Streamflow II gauge sites
Coastal Cluster
Inland Cluster
Approximately doubles
USGS gauge density
in chosen watersheds
Provides coastal flow
gauging in Beaumont
District where none
exists now
Spacing is approximately
one gauge per HUC10
watershed considering
TxDOT and USGS
gauges together
Large riverine basins,
spatially lumped
Small coastal basins
spatially dispersed

## Slide 18: HUC10 Watersheds as Sampling Units
Priority HUC6 Basins
HUC10 Watersheds
HUC10 Centroids
Mean watershed area = 269 Sq. Mi.
= 16.4 Mi.
Spacing is approximately
one gauge per HUC10
watershed considering
TxDOT and USGS
gauges together

## Slide 19: Spatial Correlation of Streamflow
HUC10 Centroids with 15 Mile buffer zone
https://library.ctr.utexas.edu/ctr-publications/5-9054-01-1.pdf
Conclusion: A gauge density of one gauge/HUC10 unit
will show significant flow correlation among gauges

## Slide 20: Distribution of 80 New TxDOT Gauges
Chart: NWS Weather Forecast Offices
| Austin/San Antonio | Corpus Christi | Dallas/Fort Worth | Houston/Galveston | Lake Charles
FREQUENCY | 7 | 8 | 9 | 43 | 13
Chart: TxDOT Districts
| Austin | Beaumont | Bryan | Corpus Christi | Houston | Lufkin | San Antonio | Tyler | Waco | Yoakum
FREQUENCY | 1 | 15 | 15 | 7 | 17 | 5 | 3 | 2 | 3 | 12
25 TxDOT Districts 13 Weather Forecast Offices
form 82 distinct intersection areas
Need a Common Operating Picture
TxDOT Districts
NWS Weather Forecast Offices
Jonathan Brazzell
Katie Landry-Guyton
Amanda Schroeder
Paul Yura
Melissa Huffman, Christina Barron

## Slide 21: Task 3: Gauge Installation, Operation and Maintenance
Achievements during last Quarter
    77 recorded visits to installed gauges
    39 GNSS surveys performed
    Preliminary stage-discharge ratings started
Challenges for Next Quarter
    Complete preliminary ratings for all Tier 1 and Tier 2 gauges.
    Complete the installation of 43 gauges.
Scott Grzyb, US Geological Survey

## Slide 22: Gauge Visits
Number of Site Visits
    77 recorded visits to installed gauges
Station Number
0
2
1
3
4
5
6

## Slide 23: Gauge Height Verification
Gauge height (ft)
Date/Time

## Slide 24: Peak Verification

## Slide 25: Discharge Measurements
Handheld Acoustic Doppler velocimeter
Acoustic Doppler Current Profiler

## Slide 26: Preliminary Rating Development
Discharge Measurement
Rating Point

## Slide 27: Early discharge observations
November 2021 – Post Reconstruction
USGS Peak Discharge – 1,539 cfs
RQ-30 Peak Discharge – 1,500 cfs
July 2021 – Before Reconstruction
USGS Peak Discharge – 665 cfs
RQ-30 Peak Discharge – 680 cfs
Date
Discharge ( cfs )

## Slide 28: Early discharge observations
– Post Reconstruction
– Before Reconstruction
USGS Discharge
RQ-30 Discharge
Discharge ( cfs )
Date
USGS Discharge
RQ-30 Discharge

## Slide 29: Part 1: Topics for Discussion
Completed Field Reconnaissance and
for Phase 2 Gauge Sites (September to November)
Need to Get Gauges Done – research team coordinates with TxDOT biweekly until all gauges are installed
Does Project Management Committee approve proposed 42 gauge sites?
Gauge Siting:
Emerging TxDOT Streamflow Data
Could these data be used to improve flood briefings by NWS for TxDOT?

## Slide 30: Streamflow II Overview Meeting Agenda
Task 1: Project Management
Task 2: Watershed Selection and Site Evaluation Task 3: Gauge Installation, Operation and Maintenance
Task 4: Flood Forecast System Operation Task 5: Forecast Model Assessment
Task 6: Flood Manual and Training
Part 1 – TxDOT-USGS
Flood Data
Part 2 – TxDOT Flood
Information

## Slide 31: Geospatial Systems Are Helping Us Understand
. . . Helping Us Make Better Decisions
Data
Information
Knowledge
Understanding
Mapping
Integration
Sharing and Collaboration
Slide: Jack Dangermond

## Slide 32: Observation, Forecasting, Planning, Operations
Data
Information
Knowledge
Understanding
Mapping
Integration
Sharing and Collaboration
Kisters Datasphere
TxDOT - USGS Data
TxDOT Flood Maps
TxDOT Maintenance – TxERA
National Weather Service Maps

## Slide 33: TxDOT Flood Forecasting
National Weather Service
TxDOT Flood Information
TxERA – TxDOT Emergency
Response Application:
layers of map services
VEOCI: text alerts
Forecasting
Current
conditions
Hydrology Base Map
Observation Gauges
Flooded Bridges
Flooded Roads
Inundation Extent

## Slide 34: Flood Information: Five Map Layers
Hydrology Base Map
Observation Gauges
Flooded Bridges
Flooded Roads
Inundation Extent

## Slide 35: Task 4: Flood Forecast System Operation
Achievements during last Quarter
  Multiple enhancements to Datasphere API
    Inclusion of runtime calculations (transformations)
    Get Last Value csv
    Call NWM forecast by gauge, COMID, or Lat/Long
  Addition of NWM Forecast vs Gauge data time series
  Moved tested import sources and calculations from Dev system to Production
Challenges for Next Quarter
  Continue with enhancements to Datasphere API
    Allows better integration with TxERA / ESRI
  Expansion of NWM Forecast vs Gauge data time series
  Continue to move the system into production mode
  Add new TxDOT gauges
Matt Ables, KISTERS

## Slide 36: Observations Map of Water Levels
Web site of Jefferson County Drainage District 6
Color coded levels for map display
9:07AM, 7 Dec 2021
https://dd6.onerain.com/map/?view=46175b76-5b3a-4ea0-bdde-6e8475c64117
0
5
10
15
20
25
30
Elevation (ft)
Credit: Craig Cormier, Josh Broussard, Jefferson County DD6
Surveyed Elevations

## Slide 37: Datasphere to TxERA and VEOCI integration
API Call
Datasphere Channels allow the desired data
products to be published as a service
Datasphere API can call each channel and
transform the data as needed
To Map
API Enhancements

## Slide 38: Task 5: Forecast Model Assessment
Paola Passalacqua, UT Austin
Achievements during last Quarter
    Initiated analysis of stage-velocity relationship at sensors
    Getting familiar with ADCP data
    Developed HAND-based approach for storm surge inundation
Challenges for Next Quarter
    Automate detection of storm and analysis of stage-velocity relationship at sensors
    Analysis of ADCP data
    Validation of coastal HAND approach and integration with fluvial inundation approach GeoFlood
    Data Assimilation
    Building an Entwine point cloud at TACC to support 3D Bridges and Roads

## Slide 39: Investigating the stage-velocity relationship at radar stations

## Slide 40: Storm surge calculation
Coastal HAND approach was used to calculated storm surge
Storm surge was applied to the unfiltered “raw” DEM
Currently implemented in a Jupyter notebook with the rasterio and numpy python libraries

## Slide 41: Simulation of compound flooding
Classic GeoFlood riverine inundation map is combined with storm surge inundation
If a cell experiences both riverine and storm surge inundation, the greater value is chosen

## Slide 42: Bridge Characterization from a LIDAR Point Cloud
3
11,078 LiDAR points
on bridge deck
Plan
Profile
Plan
Deck point density
1 point per 2.6 sq feet
Perspective
Bridge over Shoal Creek at 15th St in Austin, Texas
Andy Carter, UT Austin

## Slide 43: Texas LIDAR Point Cloud Data Seamless point cloud service with consistent classification
325,000 tiles in 70 data collections
Some inconsistencies in classification
of types of points
Entwine is a data organization library for massive point clouds, designed to conquer datasets of trillions of points.

## Slide 44: Task 6: Flood Manual and Training
Achievements during last Quarter
Challenges for Next Quarter
    Interactions with the Beaumont District
      Continued HSEEP Exercise Planning
      Nov 16-17 In-Person Meeting
        Discussed logistics for Feb HSEEP
        Reviewed Hydrology Base Map for useability
        Presented new optional datasets (HCRS)
Interactions with TxDOT Statewide Emergency Management
      Discussions with TxDOT Statewide Emergency Management regarding needs and requirements for Hydrology Base Map
      Nov 30th In-Person Meeting
        Brief on Feb HSEEP Exercise
        Brief on what we are developing for Beaumont to make sure it is useful to the State (goal is to create something useful to entire State, not only Beaumont)
Harry Evans, UT Austin
Conduct a successful HSEEP Exercise in Beaumont
Objective of exercise is clear and concise Improvement Plan
Harry Evans
Christine Thies
Larry Jantzen
Flood Emergency Response Team

## Slide 45: TxDOT Priorities
SAFETY
        Our staff, our community
        Emergency response
CONNECTIVITY
        Reliability of the transportation network
  Asset management
        *BRIDGES*
  Efficiency and efficacy
        For TxDOT
        For other/all jurisdictions
Slide: Rose Marie Klee, TxDOT
How to implement these goals
during flood emergency response?

## Slide 46: Beaumont District Emergency Response Organization
Beaumont
(Kevin Emerson)
Kountze
(Steven Singleton)
Maintenance Sections
(Maintenance Supervisor)
Orange
(Jody Hand)
Port Arthur
(Carl Ray)
Anahuac
(Jake Taylor)
Liberty
(Tyrone Alexander)
Woodville
(Jay Castleberry)
Jasper
(JoEllen Miller)
Newton
(Cecil Wade)
Logistics
(Keith Horn /
Scott Estes)
Operations
(Brad Murray /
John Sudela)
Planning
(Adam Jack)
Administrative
(Heather Weeks)
Incident Command
(Chris Henry /
Kenneth Wiemers)
District Engineer (Martin Gonzalez)
(Day /
Night)
TxDOT Beaumont
Emergency
Operations Center
Maintenance Sections
TxDOT Austin
Emergency
Operations Center
(Matthew Heinze)
State
District
Local
Daytime Duty
(6 people)
(60 people)
12 hour shifts 7AM – 7PM
Operational briefings 6AM, 6PM
TxDOT Statewide Event (Weather) Call, 8AM
NWS BMT Weather briefings 10AM, 4PM
Requests for
assistance
Organized within

## Slide 47: HSEEP Exercise Homeland Security Exercise Evaluation Program
  HSEEP uses “best practices” to provide guiding principles for a common and professional approach to exercise design and development. This approach provides a format for product evaluation and improvement planning.
  These exercises will be the component to evaluate the usefulness of Streamflow II’s gauge data and the presentation of that data.
  The HSEEP exercise provides the opportunity to assess and validate the efficacy of the data and address areas for improvement in accessibility and presentation of the data.
Outcome: Improvement Plan
Lists corrective actions based on exercise findings
Lists responsible owner for corrective actions
Provides timeline for completion

## Slide 48: February HSEEP Exercise
Date: February 22, 2022
  4 hours
  Starting at 1:00pm
Storm: TS Imelda
Focus: Maintenance Sections’ data needs during event
Exercise Planning Team: Harry Evans, Larry Jantzen, Christine Thies
Exercise Roles:
  Facilitators – Provide exercise facilitation, situation updates, and moderate discussion. Runs the exercise. (Exercise Planning Team)
  Observers – Provides support during the exercise. They are TxDOT subject-matter experts and provide insight or questions to support players responses
  Players – Role is to use and evaluate product. Active role doing their “Regular Job” (BMT, NWS)
  Evaluators – Observe and document the exercise objectives
Computer screens in TxDOT BMT EOC

## Slide 49: Demo of Flood Map Overlays by Christine Thies
https://arcg.is/5zX0m0

## Slide 50: Exercise Maps
Hydrology Basemap: https://arcg.is/5zX0m0
Paper Maps:

## Slide 51
9/19/19
12:00 AM
Minor
Flooding

## Slide 52
9/19/19
6:00 PM
Max
Flooding

## Slide 53
9/22/19
6:00 PM
Recede

## Slide 54: Road Closure due to Flooding -- Visualized in DriveTexas.org
Duration = 7.83 hours
Length = 9.74 miles
Impact = 7.83 * 9.74 = 76.3 day- miles
IH-10 Closure
Road closure data in DriveTexas.org
are stored in the TxDOT Highway
Conditions Reporting System
Flood Closure

## Slide 55: Closure of IH-10 during TS Imelda
National Water Model Retrospective Simulation
IH-10 was closed
From 4:13 AM to 12 noon
on 19 September 2019
National Water Model
retrospective simulation
peaks then.
Road closure data from
TxDOT Highway Conditions Reporting System
which underlies “DriveTexas.org”
IH-10 Closure
Streamflow Hydrograph

## Slide 56: Flooded Roads “Hydrograph”
Chart: Water Level on Hillebrandt Bayou at Tx-124
Chart: Length of Flooded Roads
Quantifies the flood threat: How Large is it? Where is it? When is it?
TS Imelda
total impact = 1576 day-miles
of flooding on TxDOT roads
(area under curve)
Sum the length of road closures at each time point

## Slide 57: Cumulative Road Closures due to Flooding in Texas March 2014 to November 2021. Data from TxDOT Highway Conditions Reporting System (HCRS)
Chart: Years: 2014 to 2022
Aug 2017 Hurricane Harvey
Sept 2019 TS Imelda
May 2015 (Blanco and Regional Flood)
Oct 2018 Colorado Flood
May 2016 Brazos Flood
Sept 2014 (Hill Country Flood)
Oct 2015 Halloween Flood
May, July 2021
South, North Texas

## Slide 58: Demo by Tim Whiteaker – TxDOT Flooded Roads

## Slide 59: Part 2: Topics for Discussion
Is a system of sharing map services between NWS and TxDOT feasible?
How best should the content of those services be defined?
Could there be custom map layers defined directly from AssetWise?
Shared Map Services
Flooded Roads Hydrograph
Is this a useful concept?
Could it be forecast like a streamflow hydrograph?
September 2022 Flood Exercise
First plan was to engage Austin District
Instead, a regional exercise across several TxDOT Districts?
Bridge Characterization
LIDAR description of bridges in 3D
How to build a flood hydraulic model for each bridge?
Other Issues …
Implementation of Observations Map of Water Levels
Datasphere to TxERA and VEOCI?
Test in Beaumont Exercise in Feb 2022?