## Slide 1: Evaluate Improved Streamflow Measurement at TxDOT Bridges Project 0-7095 Being conducted for TxDOT by UT Austin and US Geological Survey with the support of Kisters North America and Aqua Strategies September 2020 to August 2023
Presentation for Second Quarterly Review Meeting, Monday 8 March 2021
Acknowledgements: Shelley Pridgen (RTI Project Manager), Rose Marie Klee (H&H Director, TxDOT),
Trent Ellis (BRG, TxDOT), Michael Cunningham (TPP, TxDOT)

## Slide 2: TxDOT Priorities
SAFETY
        Our staff, our community
        Emergency response
CONNECTIVITY
        Reliability of the transportation network
  Asset management
        *BRIDGES*
  Efficiency and efficacy
        For TxDOT
        For other/all jurisdictions
Slide: Rose Marie Klee, TxDOT

## Slide 3: TxDOT Project Management Committee
Rose Marie Klee H&H Section Director, DES
Abderrahmane Maamar-Tayeb
H&H Section Team Lead, DES
Adam Jack Dir of Trans Plan & Development, BMT
Andrew Lee District Bridge Engineer, BMT
Jared Browder Maintenance Assess Spec, MNT
Trent Ellis Bridge Scour Coordinator, BRG
Shelley Pridgen Research Project Manager, RTI
Joseph Goessling
Lead Hydraulics Engineer, AUS

## Slide 4: Project Advisory Committee
Jason Johnson, NOAA National Weather Service Mark Lenz, NOAA National Weather Service
Paul Yura, NOAA National Weather Service
Sam Marie Hermitte, Texas Water Development Board
Jorge Urquidi, City of Austin, Flood Early Warning System
Justin Terry, Harris County Flood Control District
Randy Charbeneau, UT Professor Emeritus of Civil Engineering Peter Smith, former TxDOT Dir of Trans Planning and Programs
Sauda Ahmed, H&H section, TxDOT Design Division Hiruy Berhe, H&H section, TxDOT Design Division
Lucinda Soto, H&H section, TxDOT Design Division
Jaime Villena-Morales, H&H section, TxDOT Design Division
Welcome to
the Discussion!

## Slide 5: Streamflow II Overview Meeting Agenda
1. Project Concept

## Slide 6: Streamflow II Overview Meeting Agenda
1. Project Concept
2. Site Selection and gauge installation
Scott Grzyb (USGS), David Arctur
and Tim Whiteaker (UT Austin)

## Slide 7: Streamflow II Overview Meeting Agenda
1. Project Concept
2. Site Selection 3. Data Assembly and Prediction Testbed
Paola Passalacqua (UT Austin)
and Dirk Schwanenberg (Kisters)
Scott Grzyb (USGS), David Arctur
and Tim Whiteaker (UT Austin)

## Slide 8: Streamflow II Overview Meeting Agenda
1. Project Concept
2. Site Selection and gauge installation 3. Data Assembly and Prediction Testbed 4. Streams to Roads and Bridges
Paola Passalacqua (UT Austin)
and Dirk Schwanenberg (Kisters)
Scott Grzyb (USGS), David Arctur
and Tim Whiteaker (UT Austin)
Andy Carter and
David Maidment (UT Austin)

## Slide 9: Streamflow II Overview Meeting Agenda
1. Project Concept
2. Site Selection and gage installation 3. Data Assembly and Prediction Testbed 4. Streams to Roads and Bridges
5. NWS Briefings and Flood Maps
Andy Carter and
David Maidment (UT Austin)
Paola Passalacqua (UT Austin)
and Dirk Schwanenberg (Kisters)
Mark Null (Aqua Strategies)
and Harry Evans (UT Austin)
Scott Grzyb (USGS), David Arctur
and Tim Whiteaker (UT Austin)

## Slide 10: Streamflow II Overview Meeting Agenda
1. Project Concept
2. Site Selection and gauge installation 3. Data Assembly and Prediction Testbed 4. Streams to Roads and Bridges
5. NWS Briefings and Flood Maps
6. Concluding Comments from Committee
Moderated by Rose Marie Klee (TxDOT)
Paola Passalacqua (UT Austin)
and Dirk Schwanenberg (Kisters)
Mark Null (Aqua Strategies)
and Harry Evans (UT Austin)
Scott Grzyb (USGS), David Arctur
and Tim Whiteaker (UT Austin)
Andy Carter and
David Maidment (UT Austin)

## Slide 11: Project Tasks
Task 1 Project Management
Task 2 Watershed Selection and Site Evaluation
Task 3 Gauge Installation, Operation and Maintenance
Task 4 Flood Forecast System Operation
Task 5 Forecast Model Assessment
Task 6 Flood Manual and Training
Project Concept
Site Selection and gauge installation
Data Assembly and Prediction Testbed
Streams to Roads and Bridges
NWS Briefings and Flood Maps
Topics Reported on during this Review:
David Maidment
Scott Grzyb, David Arctur, Tim Whiteaker
Scott Grzyb, …. USGS team
Matt Ables, Dirk Schwanenberg, … Kisters team
Paola Passalacqua, Andy Carter, David Maidment
Harry Evans, Christine Thies, Mark Null

## Slide 12: Streamflow II Overview Meeting Agenda
1. Project Concept
2. Site Selection and gauge installation
Scott Grzyb (USGS)
David Arctur and Tim Whiteaker (UT Austin)

## Slide 13
Progress Updates
January - Equipment starts arriving
February - Equipment set-up training
Now - Data Collector Set-up for installations

## Slide 14
Progress Updates
Structures for enclosure were designed and are being manufactured.
Redesigned for safer access and more robust attachments.
14 stands completed and sent for galvanizing.

## Slide 15
Progress Updates
Initial bridge permit package (10 Sites) sent in early February
Remaining Streamflow I permits nearing completion

## Slide 16
Progress Updates
13 sites set up in Aquarius program for USGS assessment.
Automated entry developed to expedite remaining project sites.
USGS Data
TxDOT Project Data

## Slide 17: Review: In Q1, we had prioritized watersheds for site selection

## Slide 18: On-System Bridges in Priority Watersheds with NBI and NHD attributes
National Bridge Inventory Criteria
National Hydrography Dataset Criteria
5,355 bridges

## Slide 19: Ranking of USGS HUC8 Subwatersheds in Priority Zone
Same weighting
scheme applied to
HUC8 subwatersheds

## Slide 20
USGS / RQ-30 needs
Higher Bridge,
no Inundation
Generally
Straight
Reach
Mostly
Contained
channel
Velocity
>1 ft/s
Ideal Measurement
Location
UT needs
Stream Network
Representation
Data For Forecast Model
Assimilation
TxDOT Needs
Bridge and
Roadway
Inundation
Early Warning
and Actionable Notification
Bridge
Inspection
Information Needs

## Slide 21
Higher Bridge,
no Inundation
Generally
Straight
Reach
Mostly
Contained
channel
Velocity
>1 ft/s
Ideal Measurement
Location
Stream Network
Representation
Data For Forecast Model
Assimilation
Bridge and
Roadway
Inundation
Early Warning
and Actionable Notification
Bridge
Inspection
Information Needs

## Slide 24
Notes: Fix legend.

## Slide 26
Proposed gauge locations for field recon
Notes: Add a legend. Change symbols.

## Slide 27
Field Recon Pilot
Proved usefulness of office recon Procedures

## Slide 28
Sharing the site selection process using a StoryMap
Demo by Tim Whiteaker
Credit: StoryMap prepared by David Arctur (UT Austin)

## Slide 29
Notes: To give TxDOT a view into our site selection process, we could create an interactive story map like this one.

## Slide 30
Notes: Tabs on the map focus on phase of the site selection process, such as watershed prioritization and identification of candidate bridges.

## Slide 31
Notes: You can zoom around and click features in the map to see details on existing and proposed gauges, bridges, streams, and more.

## Slide 32
Discussion
Is this process reasonable?
Is the format of the permit applications appropriate or could it be improved?
How does TxDOT want to be involved in site selection?

## Slide 33: Streamflow II Overview Meeting Agenda
1. Project Concept
2. Site Selection and gauge installation 3. Data Assembly and Prediction Testbed
Paola Passalacqua (UT Austin)
and Dirk Schwanenberg (KISTERS)

## Slide 34: Colorado Basin Prediction Testbed
75 USGS Stream gauges
50 LCRA (Lower Colorado River Authority) gauges separate from USGS
247 LCRA rain gauges
Austin

## Slide 35: Data Assembly and Prediction Testbed
UT Austin and KISTERS team
UT Austin
KISTERS
  is an international IT company with about 600 employees and its head office in Aachen, Germany
  KISTERS North America has been founded in 2004 and is the 2nd largest water entity
  The KISTERS TxDOT team supplied the hydromet tech stack for various international organizations including the European Flood Awareness System, national hydromet systems for UK, Sweden, Spain, Germany, among others
  Lower Colorado River Authority, City of Austin, Harris County Flood Control District, ...
Research collaboration initiated in Streamflow I

## Slide 36: Data Assembly and Prediction Testbed
Improve forecasts on local scale based on NWM input
Baseline:
NWM is an excellent start, but national scale. On local scale we may improve it in several ways:
Acquire and collect local data
Make use of local/regional models with higher degree of detail (nested into the NWM), e.g. the approaching HEC-RAS models for Texas
Make use of more enhanced data assimilation techniques (you cannot afford on national scale) to improve the skill of forecasts
Run models more frequently, more real-time (model execution cycle for local models in the order of 2-5 min instead of 1-1.5 hours for the national NWM)
 more accurate, more timely forecasts with higher spatial resolution

## Slide 37: Data Assembly and Prediction Testbed
Technology Stack / Approach
Clone of the NWM routing scheme + enhanced data assimilation  model schematization comes for free from NWM, highly scalable approach  pilot model available for Colorado River, setup of DA and integration in progress
HEC-RAS model integration  pilot model for Guadalupe River
datasphere as next generation cloud platform to
  integrate all scalar and raster data products
  structure and share data, provide alarming and notification features
  disseminate data through API and web widgets, e.g. for integration into inundation mapping or ESRI products
Credit: Wilken Steiner, KISTERS

## Slide 38
datasphere
Time series storage
Raster storage
datasphere
(cloud platform)
Network Store
Model schematization
Data Assimilation (Hydraulic)
NWM (Muskingum-Cunge routing)
Data Assimilation (Muskingum-Cunge)
HEC-RAS (Hydraulic routing)
Out-of-the-box visualization of (forecast) time series and model schematization
National and regional modelling
Assimilation of local data into regional models (NWM clone, HEC-RAS) to improve forecasts

## Slide 39
Sharing concept for private and public data, e.g.
- USGS
- LCRA
datasphere for visualization of time series data, alarming and notifications

## Slide 40
Raster data including the full extend of the NWM forcing and results
 live demonstration
datasphere for visualization of time-varying raster data

## Slide 41: Data Assembly and Prediction Testbed
Roadmap
next 1-2 months:
  remaining data integration tasks
  NWM streamflow reaches integrated as separate layer, all NWM forecasts (short-range, medium-range ensemble) fully supported in the cloud app
  NWM routing clone and HEC-RAS pilot models both integrated (without data assimilation)
  discussion of TxDOT user experience, setup and customization options
until June/July 2021:
  NWM routing clone operational including data assimilation
  customization such as the integration of the TxDOT Statewide Planning Map as map layer
  various other fine-tuning tasks regarding usability

## Slide 42: Data Assembly and Prediction Testbed
Questions for discussion
What expectations does TxDOT have for a flood data visualization system?
Should the TxDOT state planning map be used as the background?
Does TxDOT want this system to have “District-level” views or is one state-wide view sufficient?
How should alarms be set and to whom should the messages be directed?
Which data are most needed: current conditions, short-range forecast (18 hrs), medium range forecast (10 days)?

## Slide 43: Streamflow II Overview Meeting Agenda
1. Project Concept
2. Site Selection and gauge installation 3. Data Assembly and Prediction Testbed 4. Streams to Roads and Bridges
Andy Carter and
David Maidment(UT Austin)

## Slide 44
TxDOT Emergency Response Application (TxERA)
Traffic Flow Chart

## Slide 45: Streams to Roads and Bridges
Hydrology: Lines are streams and rivers
Flows are water
Transportation: Lines are roads and highways
Flows are traffic
Flood Information

## Slide 46: Linear Referencing using Measures for IH-20
Long.
Lat.
Long.
Lat.
Measure (M)
Measure (M)
634.692
0.000
4,746 vertices on IH-20 in Texas
Distance from Origin (DFO) ranges from :
M = 0.00 miles in West Texas to
M = 634.692 miles at TX/LA border

## Slide 47: Measure Values Near Trinity River
M = Distance from Origin (DFO) in miles
Measure increases going Eastwards
474.648
474.731
474.998
This is feature type PolylineM in GIS.
We would like to use PolylineMZ, which
also has a z-coordinate for each vertex

## Slide 48: Linear Referencing Demo
https://apps3.txdot.gov/eventmap.html?RIA_RTE_ID=IH0020-LG|474.637|475.363|#0000FF|5|Flooded%20Road&RIA_RTE_ID=IH0020-RG|474.467|475.191|#0000FF|5|Flooded%20Road&RIA_RTE_ID=IH0020-KG|474.404|475.13|#0000FF|5|Flooded%20Road
Credits: Michael Chamberlain, TxDOT TPP, Tim Whiteaker, UT Austin
RIA_RTE_ID=IH0020-KG|474.404|475.13|#0000FF|5|Flooded%20Road
An arbitrary flood polygon on IH-20 ….
…. is translated by route and measure
values in a TxDOT web app ….
…. to be depicted on the TxDOT state planning map
474.404
475.13
Route
Measure

## Slide 49: Flood Inundation Mapping (FIM)
National Water Model
Current Discharge
Forward Looking Discharge

## Slide 50: USGS Entwine LIDAR point cloud data service
https://usgs.entwine.io/
3.77 trillion LIDAR points for Texas
Only USGS 3DEP elevation data
Source: https://raw.githubusercontent.com/hobu/usgs-lidar/master/boundaries/boundaries.topojson
Date pulled: 5 March 2021
Data Gaps

## Slide 51: LIDAR Points for LBJ Freeway at Trinity River
Extraction of DEMs and LAS Point Clouds via Entwine pipeline (JSON) request
Bridge limits can be spatially queried
Point Cloud - Plan View
Point Cloud - Profile View
Point Cloud
Orthographic View
This bridge envelope is composed of
258,000 points
[of the 3.77 trillion points in Texas]

## Slide 52: Bridge Envelope for LBJ Freeway at Trinity River
NBI Structure Length = 2400 ft (732m)

## Slide 53: Profile along Trinity River at LBJ Freeway
Chart: Profile along the Waterway
Bridge Deck Width
Left = 70.9 ft
Right = 70.9 ft
NBI Attributes
Width = 21.6m
Width = 21.6m
LIDAR measured width
is close to that stored
in National Bridge Inventory

## Slide 54: Streams to Roads and Bridges
Questions:
Is the linear referencing approach appropriate for relating flood inundation to the road network?
Should we try to represent the road network in 3D?
Is this an appropriate way of characterizing bridges? What additional information about the bridge could be added to the Bridge Envelope?
How best can we present this information for flood decision-making at TxDOT? Create a flood water elevation line?

## Slide 55: Streamflow II Overview Meeting Agenda
1. Project Concept
2. Site Selection and gage installation 3. Data Assembly and Prediction Testbed 4. Streams to Roads and Bridges
5. NWS Briefings and Flood Maps
Mark Null (Aqua Strategies)
and Harry Evans (UT Austin)

## Slide 56: National Weather Service Offices
122 Weather Forecast Offices (WFO)
  Responsible for issuing Flood Watches, Flash Flood Watches, Flood Warnings, Flash Flood Warnings, and Flood Advisories for their local County Warning Area
13 River Forecast Centers (RFC)
  Provides hydrologic forecasting, hydrometeorologic analysis and support (HAS) functions and products.

## Slide 57
STRATEGIC
(State-wide EM Planning, Resource Allocation, Routing)
OPERATIONAL (Hydrologic Warning Area / Watershed Coordination)
TACTICAL (Neighborhood Level)
Weather Forecast Office
Emergency Management Decision Making

## Slide 58: Engagement With Emergency Managers
State/Regional Level:
NWS ROC / WGRFC
Deployments to the State Operations Center
Morning Briefings (Technical and Executive)
  State  Governor, TDEM
  FEMA
  “Deep” Core Partners
    USACE, USGS, River Authorities
Local Level:
Weather Forecast Offices (WFOs)
Assist WFO’s with local EM briefings and discussions
Outreach and training opportunities (i.e FloodAware)

## Slide 59
NWS Coordination with Texas Division of Emergency Management
Meteorology Message
Hydrology Message
WGRFC coordinates Hydro messaging across all impacted RFCs
SRH ROC coordinates weather messaging across all impacted WFOs
NWS Southern Region Headquarters
Regional Operations Center (Fort Worth)
TDEM State Operations Center
Austin, TX
Situational Weather Briefings
Daily high-level weather/hydro briefings to TDEM once SOC becomes activated.
Consolidated message across NWS offices. (One Forecast)
Deployments to the SOC as required

## Slide 60
Flood Messaging (Current and Future Services)
“This is a tool we just can’t afford to wait another 5 to 10 years to have…”
– Houston Office of Emergency Management

## Slide 61
Inundation maps are more useful than a hydrograph
Gaps are problematic
Hatch areas that are not modeled
Significant Finding #1: This is an Improvement and is Needed Now

## Slide 62: Homeland Security Exercise and Evaluation Program (HSEEP) Exercises
Scheduled for Sept 2021 and Sept 2022
What will we be testing?
HSEEP is an exercise to test a product or procedure. It provides a set of guiding principles to create an exercise which will evaluate, validate, and identify areas for improvement for preparedness.
We propose that Exercise 1 will involve collaboration with the National Weather and build on previous NWS flood inundation mapping exercises by adding TxDOT data and transportation information. The scope with be defined in consultation with the Project Management Committee.
What will Exercise tell us?
The Exercise outcomes will allow us to document what worked, what needs improvements, and develop an improvement plan. The improvement plan could be as simple as adding … to Datasphere or to the TxDOT Emergency Response Application, or as complex as updating operational guidelines within TxDOT’s emergency response.
What is HSEEP?
We will present a more detailed plan for consideration at the June Quarterly Review

## Slide 63: Homeland Security Exercise and Evaluation Program (HSEEP) Exercises
Scheduled for Sept 2021 and Sept 2022
Create HSEEP Exercise
Set
Exercise Date / Send out Invites
Test Exercise
(2-4 tests)
Hold Exercise (2-4 hrs)
Document Improvement Plan
Implement changes/
improvements

## Slide 64: NWS Briefings and Flood Mapping
Questions:
Could TxDOT personnel be more fully engaged in the state-wide flood briefings that NWS presents to TDEM?
How best could the bridge hydraulics work being done in this project be connected with the NWS flood inundation mapping services?
We have a flood exercise scheduled for September 2021. Could this be focused on a joint effort between NWS and TxDOT for forecasting flood impact on the transportation system?

## Slide 65: Streamflow II Overview Meeting Agenda
1. Project Concept
2. Site Selection and gauge installation 3. Data Assembly and Prediction Testbed 4. Streams to Roads and Bridges
5. NWS Briefings and Flood Maps
6. Concluding Comments from Committee
Moderated by Rose Marie Klee (TxDOT)

## Slide 66: Concluding Remarks by Committee Members
Please introduce yourself and share how this project is relevant to the work that you do.
What excites you most about the potential value?
Are there any particular aspects of this project that you would like to be more involved with?
Any comments, questions, words of wisdom, observations that you would offer to us?
      AN ASK (not for discussion): would you be willing to share a headshot that we could include in future presentations and a brief bio? (if so, please email!)
Randy Charbeneau – UT Professor Emeritus Sam Hermitte – TWDB
Jason Johnson – NOAA/NWS
Mark Lenz – NOAA/NWS
Paul McKee* – NOAA/NWS
Peter Smith – TxDOT TPP, ret
Justin Terry – HCFCD
Jorge Urquidi – City of Austin
Paul Yura – NOA/NWS
*special guest