## Slide 1: Evaluate Improved Streamflow Measurement at TxDOT Bridges Project 0-7095 Being conducted for TxDOT by UT Austin and US Geological Survey with the support of Kisters North America and Aqua Strategies September 2020 to August 2023
Presentation for Sixth Quarterly Review Meeting, Tuesday 8 March, 2022
Acknowledgements: Rose Marie Klee (H&H Director, TxDOT), Trenton Ellis (H&H, TxDOT), Shelley Pridgen (RTI Project Manager, TxDOT),
Matthew Heinze (MNT, TxDOT), Jared Browder (MNT, TxDOT), Chris Henry (BMT, TxDOT), Keith Horn (BMT, TxDOT)

## Slide 2: TxDOT Priorities
SAFETY
        Our staff, our community
        Emergency response
CONNECTIVITY
        Reliability of the transportation network
  Asset management
        *BRIDGES*
  Efficiency and efficacy
        For TxDOT
        For other/all jurisdictions
Slide: Rose Marie Klee, TxDOT

## Slide 3: TxDOT Project Management Committee
Rose Marie Klee H&H Section Director DES
Abderrahmane Maamar-Tayeb
H&H Section Team Lead DES
Adam Jack Dir of Trans Plan & Dev BMT
Andrew Lee District Bridge Engineer BMT
Jared Browder Maintenance Assess Spec MNT
Trent Ellis H&H Engineer DES
Shelley Pridgen Research Project Manager RTI
Joseph Goessling
Lead Hydraulics Engineer
AUS
Matthew Heinze TxDOT Emerg Mgmt Coord MNT
Jennifer Lash GIS Program Leader TPP
LaDonna Waters Lead Hydraulics Engineer BMT
Ryan Eaves Geotech Brch Mgr BRG
Drake Builta
Bridge Info Grp Lead
BRG

## Slide 4: Project Advisory Committee
Welcome to
the Discussion!
Sauda Ahmed | Lucinda Soto
Hiruy Berhe | Jaime Villena-Morales
Zenia De Leon | Marissa Williams
NOAA National Weather Service | State and Local Agencies
Jason Johnson, West Gulf River Forecast Center | Sam Marie Hermitte, TWDB
Paul McKee, Southern Region HQ | Jorge Urquidi, City of Austin, Flood Early Warning System
Paul Yura, Austin/San Antonio Weather Forecast Office (WFO) | Christina Bryant, City of Austin, Flood Early Warning System
 | Justin Terry, Harris County Flood Control District
 | Peter Smith, former TxDOT Director TPP
+ other members of the H&H Section,
TxDOT Design Division:
NOAA Weather Forecast Office Service Hydrologists*
Jonathan Brazzell, Lake Charles, LA, WFO
Katie Landry-Guyton, Houston/Galveston WFO
Amanda Schroeder, Dallas/Fort Worth WFO

## Slide 5: Meeting Agenda
Beaumont Flood Emergency Response Exercise
  Introduction and overview
  Review of maps presented
  Results of the exercise evaluation
  Proposed plan
  Discussion
Progress and Plans
  Gauge installation, operation and maintenance
  Flood forecast system operation
  Forecast model assessment
  Flood emergency response and flood manual
  Discussion

## Slide 6: Meeting Agenda
Beaumont Flood Emergency Response Exercise
  Introduction and overview
  Review of maps presented
  Results of the exercise evaluation
  Proposed plan
  Discussion
Progress and Plans
  Gauge installation, operation and maintenance
  Flood forecast system operation
  Forecast model assessment
  Flood emergency response and flood manual
  Discussion

## Slide 7: TxDOT BMT wants to move from Reactive response to Proactive response
Maintenance Staff
observing current
flood conditions
EOC staff
Decisions based on
current conditions
Reactive Response

## Slide 8: TxDOT BMT wants to move from Reactive response to Proactive response
Proactive Response
Maintenance Staff
observing current
flood conditions
Predictive Storm and Flood Maps
EOC staff
Advance warning of location, extent
and severity of flooding
Decisions based on
current and predicted conditions

## Slide 9: Some Thoughts I have Heard
“We want to move from being reactive to being proactive”
Chris Henry, Director of Maintenance, BMT
“It’s the guys in the field who tell us what’s going on”
Keith Horn, Logistics Coordinator, BMT
“I want technology to be my eyes on the landscape”
Martin Gonzalez, District Engineer, BMT
“We need all the data in one place”
Eliza Paul, District Engineer, HOU
“At the SOC, we need warning 24-48 hours in advance”
Jared Browder, Maintenance Assessment Specialist, MNT
“We could close IH-10 in 3-6 hours”
Chris Henry, Director of Maintenance, BMT
“I want to know if there’s going be another Harvey”
Eliza Paul, District Engineer, HOU

## Slide 10: Why so much about Beaumont?
from “Excessive Rainfall Outlook High Risks (2010-2020)”
Source: Jonathan Brazzell, NWS Lake Charles WFO
High risk of excessive rainfall causing flood deaths and damage
IH-10 closed three times in 2016 – 2021

## Slide 11: Districts, Maintenance Sections, Routes and Bridges
25 Districts
265 Maintenance Sections
13,784 Maintenance Routes
25,874 On-System Bridges over Water
101,187 miles of On-System Roads 268,820 square miles of Area
An average Maintenance Section
is responsible for approximately:
50 Routes
100 Bridges
400 miles of Roads
1000 square miles in Area

## Slide 12: TxDOT Beaumont District Emergency Response Organization
Beaumont
(Kevin Emerson)
Kountze
(Steven Singleton)
Maintenance Sections
(Maintenance Supervisor)
Orange
(Jody Hand)
Port Arthur
(Carl Ray)
Anahuac
(Jake Taylor)
Liberty
(Tyrone Alexander)
Woodville
(Jay Castleberry)
Jasper
(JoEllen Miller)
Newton
(Cecil Wade)
Logistics
(Keith Horn /
Scott Estes)
Operations
(Brad Murray /
John Sudela)
Planning
(Adam Jack)
Administrative
(Heather Weeks)
Incident Command
(Chris Henry /
Kenneth Wiemers)
District Engineer (Martin Gonzalez)
(Day /
Night)
TxDOT Beaumont
Emergency
Operations Center
Maintenance Sections
TxDOT Austin
Emergency
Operations Center
(Matthew Heinze)
State
District
Local
Daytime Duty
(6 people)
(60 people)
12 hour shifts 7AM – 7PM
Operational briefings 6AM, 6PM
TxDOT Statewide Event (Weather) Call, 8AM
NWS BMT Weather briefings 10AM, 4PM
Requests for
assistance
Organized within

## Slide 13: Spatial Scales and Forecast Lead Times
Decision units are Districts
Decision units are Sections
Decision units are Routes and Bridges
State scale
24-48 hours in advance
District scale
12-24 hours in advance
Section scale
3-6 hours in advance
Flood Risk: Regional Transportation System
Flood Risk: Local Transportation Infrastructure

## Slide 14: Geospatial Systems Are Helping Us Understand
. . . Helping Us Make Better Decisions
Data
Information
Knowledge
Understanding
Mapping
Integration
Sharing and Collaboration
Slide: Jack Dangermond

## Slide 15: A Proposal Discussed with NWS Southern Region Leadership on 18 Jan 2022
Shared Services
Flood Response Working Group
TxDOT
NWS
DriveTexas.org
Radar gauge data
Forecast
Map
Services
Arc GIS Online
NWS SRH and WGRFC
Service Hydrologists at
Weather Forecast Offices
Evaluation during 2022 Storm Season
Build on our Quarterly Review Meetings
Project 0-7095 Research Team
“I can’t see any downsides to this.”
Mike Coyne, Director NWS SRH

## Slide 16: Shared Map Services between NWS and TxDOT
Staff
EOC Staff and
Maintenance Supervisors
Forecasters at
WFO’s and RFC’s
TxERA
(TxDOT Emergency Response Application)
ArcGIS applications for IDSS
(Impact-Based Decision Support Services)
Map services for weather
and water forecasting at TxDOT
TxERA Map Server
(customized maps
for TxDOT)
KISTERS Datasphere
NWS Map Server
(Public and Prototype
Map Services)
Flood
data
services
Applications
Services Infrastructure
25 TxDOT Districts
13 Weather Forecast Offices
3 River Forecast Centers
Common
Operating
Picture
Forecast briefings
Field observations
of flooded roads
Forecast map services
DriveTexas.org service

## Slide 17
Forecast Rain Map
Observation Gauges
Bankfull Streams and
Flooded Roads (HCRS)
Flood Inundation Map
Web Communication
to TxDOT (TxERA)
Rainmap in the Sky to Floodmap on the Ground
Maps accessible through ESRI StoryMap
https://arcg.is/0LLLXX

## Slide 18
Streamflow II 0-7095
HSEEP Exercise Outcomes
Beaumont District
Maintenance Section
Center for Water and the Environment
Harry Evans
Christine Thies
Larry Jantzen
Flood Emergency Response Team
Notes: Larry

## Slide 19
Purpose
The Streamflow II Project Team have created several new products which we tested with the TxDOT Beaumont Maintenance District. The objectives of this exercise are to evaluate the effectiveness and access of these products.
      The new products are:
      Flooded Road Estimates (based on flood depth map)
      Flood Inundation (flood depth map)
      Gauge Water Level using Streamflow I and Drainage District 6 gauges
      Bridge Warnings using Streamflow I and Drainage District 6 gauges
      Bankfull Rivers (National Weather Service Product)
      Precipitation Forecast by Section (National Weather Service Product)
Notes: Larry

## Slide 20
Top New Products
Flooded Road Estimates
Precipitation Forecast by Section
Bridge Warnings
Estimated Depth
Ok (>10ft to bridge)
Concern (5 to 10ft to bridge)
Warning (< 5ft to bridge)
Out of Service (gauge not working)
X
Notes: Larry

## Slide 21
Top Reference Products
Flooded Inundation
Bankfull Rivers
Gauge Water Level
Flooded Roads (HCRS)
Ok (<5ft of water over normal level)
Concern (5-10ft of water over normal level)
Warning (>10ft of water over normal level)
Notes: Larry

## Slide 22
Participant Role | Assessment Factor |  |  |  | 
 | The exercise was well structured and organized. | The multimedia presentation helped the participants understand and become engaged in the scenario. | The facilitators were knowledgeable about the material, kept the exercise on target, and were sensitive to group dynamics. | Participation in the exercise was appropriate for someone in my position. | The participants included the right people in terms of level and mix of disciplines.
Observer | 5 | 5 | 5 | 5 | 5
Player | 5 | 5 | 5 | 5 | 5
Player | 5 | 5 | 5 | 5 | 5
Player | 5 | 4 | 5 | 4 | 5
Evaluator | 5 | 5 | 5 | 3 | 5
Player | 5 | 5 | 5 | 5 | 5
Player | 5 | 4 | 5 | 5 | 4
Player | 5 | 5 | 5 | 5 | 5
Evaluator | 5 | 5 | 5 | 5 | 5
Observer | 5 | 5 | 5 | 5 | 5
Player | 4 | 5 | 5 | 5 | 5
Player | 5 | 4 | 5 | 5 | 5
Average | 4.9 | 4.8 | 5.0 | 4.8 | 4.9
Exercise Feedback
The exercise was very well received in the Beaumont District
Notes: Larry

## Slide 23: Recommendations to TxDOT
Field Data Collection During Floods
  An automated method for field staff to record flood conditions is needed
  Possibilities:
Low Chord Elevation on Bridges
  Creating a bridge warning system requires a surveyed low chord elevation to serve as a reference point in (x,y,z)
+

## Slide 24: Spatial Scales of Flood Information
Around Gauge site
Downstream of Gauge
Gauged Watershed
TxDOT Districts

## Slide 25: FIMAN-T system from NCDOT
This map and summary table are drawn from the
FIMAN-T system developed by the North Carolina DOT
Source for Images: David Key, ESP Associates

## Slide 26: Proposed Plan
Prototype Map Products | At TxDOT Gauges | Downstream of TxDOT Gauges1 | Gauged Watersheds2 | Texas State-Wide
Flooded Road Estimate | 6 mo.3 | 12 mo. | 18 mo. | N. A.
Precipitation Forecast by Section | -- | -- | -- | 3 mo.
Bridge Warnings | 3 mo.4 | 6 mo.5 | 12 mo.5 | N. A.
Flood Inundation | 6 mo.3 | 12 mo. | 18 mo. | N. A.
Bankfull Rivers | -- | -- | -- | 3 mo.
Gauge Water Level | 3 mo. | -- | -- | N. A.
Notes:
Requires forecast adjustment and downstream routing
Requires forecast adjustment from routed reaches to all reaches
Requires hydraulic modeling of gauged bridge and its approach roads
Requires completion of gauge installation and a preliminary rating curve
Requires point cloud representation of bridge deck
Shared Services
Demonstration Prototype

## Slide 27: Shared Services Demonstration Prototype
Observation Gauges
Bankfull Streams
and Flooded Roads
Forecast Rain Maps
NWS Public
and Prototype
Map Services
Data and Map
services
Field
Observations
TxDOT Radar
Stream Gauges
Datasphere
Data and Map
services
Goal: A research prototype to be tested during the 2022 summer storm season
Observations
Forecasting

## Slide 28: Streamflow Measurement and Bridge Modeling at 80 TxDOT Gauges
“FIMAN-T for Texas”
Creates accurate measurement of flow conditions at bridges ….
….. and accurate mapping of flooded road depths near bridges

## Slide 29: Proposed Activities by Quarter
Second Quarter
Third Quarter
Dec 2021
Mar 2022
Jun 2022
Sept 2022
Fourth Quarter
Beaumont
Exercise
Austin
Exercise
Prep all products for
Austin exercise
Measurement and Modeling
at TxDOT Gauges
Shared Services
Demonstration Prototype
Prep all products for
Beaumont exercise
Fifth Quarterly Review
Sixth Quarterly Review
Seventh Quarterly Review
Eighth Quarterly Review
We are here now

## Slide 30: Discussion
We are asking for your approval of the proposed plan
Shared services demonstration prototype
Streamflow Measurement and Bridge Modeling at 80 TxDOT gauges

## Slide 31: Meeting Agenda
Beaumont Flood Emergency Response Exercise
  Introduction and overview
  Review of maps presented
  Results of the exercise evaluation
  Proposed plan
  Discussion
Progress and Plans
  Gauge installation, operation and maintenance
  Flood forecast system operation
  Forecast model assessment
  Flood emergency response and flood manual
  Discussion

## Slide 32: Task 3: Gauge Installation, Operation and Maintenance
Achievements during last Quarter
    55 recorded visits to installed gauges
    Finished site selection and permitting
    - Meaningful discharge verifications
    45 gauges installed and operating
Challenges for next Quarter
    Complete gage installations and documentation
    Continue developing and refining USGS rating models
    - 77 gauges installed and operating
Scott Grzyb, US Geological Survey

## Slide 33: Bridge permits, approvals, installations and visits
    December 3, 2021
    36 bridge permit requests sent
    December 16, 2021
    4 bridge permit requests sent
    February 9, 2022
    28 permits returned approved
    February 23, 2022
    Installation of new stream gauges begins
    7 new stream gauges installed since February 23, 2022
0
2
1
3
4
Number of Site Visits
    55 recorded visits to installed gauges
Station Number

## Slide 34: Gauge Visits - Observations
Corrections in gauge height

## Slide 35: Gauge Visits - Observations
July 2021
February 2022
Changes in vegetation in the channel

## Slide 36: Data Observations – Initial Velocity Wave
W Navidad Rv at I-10 nr Schulenburg, TX
Date/time
Stage Height (ft)
Velocity (ft/s)

## Slide 37: Data Observations – Initial Velocity Wave
W Navidad Rv at I-10 nr Schulenburg, TX
Date/time
Stage Height (ft)
Velocity (ft/s)

## Slide 38: Data Observations – Initial Velocity Wave
New Year Ck at FM 1155 nr Chappel Hill, TX
Chart: Peak Initial Pulse Velocity vs Water Level
| 2.11 | 2.11 | 2.2400000000000002 | 2.36 | 2.5499999999999998 | 2.78 | 2.09 | 2.0299999999999998
 | 156.78 | 156.44 | 162.02 | 160.1 | 162.84 | 164.1 | 156.15 | 156.44

## Slide 39: Rating 2.0 Development
Discharge Measurements
Rating Point
Tier 1 Site: New Year Ck at FM 1155 nr Chappel Hill, TX
Discharge Rating 2.0

## Slide 40: Discharge observations
Date/time
Discharge ( cfs )
Tier 1 Site: New Year Ck at FM 1155 nr Chappel Hill, TX
Measurements
USGS Discharge
RQ-30 Discharge
(uncalibrated)

## Slide 41: Task 4: Flood Forecast System Operation
Achievements during last Quarter
  Released the first versions of the Datasphere Command Line Interface (CLI) to research staff
  Provided CLI training and support to research staff
  Prepared Web Services for Beaumont Flood Emergency Response Exercise
  Imported and configured Llano Basin stations and data for Data Assimilation
Challenges for next Quarter
  Add new TxDOT Radar gauges to the system
  Establish TxDOT specific scheduling and data processing services in AWS / ArcGIS Online
  Enhance Datasphere APIs as needed
  Further develop the Operations vs Research and Planning environments
  Data Assimilation in the Llano River basin
Matt Ables, KISTERS

## Slide 42
Researchers, planners, and other users in need of additional tools and data are able to use the Datasphere interface to perform detailed graphing and analysis. Additional tools like the Cmd Line Interface all for easy bulk data retrieval and analysis.
Datasphere will work as an Operations Engine by collecting, processing, and distributing data directly to other TxDOT applications like TxERA. This allows for the datasphere products to be presented to Operations Staff through existing and familiar tool and eliminates the need to learn / use additional software.
Task 4: Flood Forecast System Operation
Operations Engine
Research & Planning Tools

## Slide 43
Datasphere
TxERA
The Scheduler / Data Processor is an AWS VM and collection of services used to analyze, build, and update feature services and layers in ArcGIS Online that are ultimately consumed by TxERA.
Datasphere APIs will supply time series data and graphs to TxERA or other TxDOT systems as needed.
Scheduler / Data Processor
ArcGIS Online Services
Operations Engine

## Slide 44
Datasphere
Data products and procedures designed by the Research Team could be operationalized if necessary once they pass the proof of concept stage.
Datasphere APIs will supply time series data and graphs to the KISTERS Water Information System which will allow greater access to historical data and statistics through web services and the ArcPro Extension.
Scheduler / Data Processor
Research & Planning Tools
KISTERS
Water Information System
Research Tools & Prototypes
Statistics &
time series
Web services
ArcPro
Extension
Python
Tools

## Slide 45: Task 5: Forecast Model Assessment
Paola Passalacqua, UT Austin
Achievements during last Quarter
Challenges for next Quarter
    Automated detection of storm and analysis of stage-velocity relationship at sensors from NWM retrospective data
    Analyzing ADCP data and comparing to RQ30
    Validating coastal HAND approach with ADCIRC model results
    Error analysis of NWM in SETx
    Identify patterns of stage-velocity relationships in space and time
    Analyzing ADCP data and comparing to RQ30
    Complete validation of coastal HAND approach, integrate with GeoFlood and finalize paper for submission
    Identify patterns in NWM errors and create uncertainty map

## Slide 46: Radar Measurements and River Hydraulics
Julia Ho – senior undergraduate student supervised by Paola Passalacqua on this project
What do stage-velocity relationships look like in the Texas streams where radar sensors are installed?
Do these relationships change through time?
How do the velocity measurements at radar sensors compare with ADCP measurements?
Velocity (ft/s)
Stage Height (ft)

## Slide 47: ADCP measurement and Isovel Contours
Smoothed contours created with USGS Velocity Measurement Tool and visualized with Python
Isovel
Contour of
Point velocity
Mean velocity

## Slide 48: RQ-30 Cross-Section Profile and K-Factor
Cross-Section, A
k-factor
Q = A*Vm= A*k*Vl
Can a predictive model for the
k-factor relationship with depth
be developed?
Stage Height (ft)
Stage Height (ft)

## Slide 49: Coastal HAND Approach
Coastal flooding plays a major role in SETx and coastal Texas in general – at this time, our flood inundation modeling approach does not account for this type of flooding
Currently performing comparison of our coastal HAND approach with ADCIRC model results for TS Imelda
Wang et al, in preparation
Mark Wang – MS/PhD student supervised by
Paola Passalacqua on a NOAA project

## Slide 50: Error Analysis and Validation of Data Assimilation Approach
Sujana Timilsina – PhD student supervised by Paola Passalacqua on this project
How do the predictions of the National Water Model compare to water level/discharge observations (at DD6 gauges and over the whole area?
Are there spatial patterns in the error and are those related to river network properties?
How to integrate this uncertainty into the flooded road maps?
Do DA techniques improve model forecasts? Does the operational DA approach improve the NWM performance on the Llano River?
Are there regions/watersheds or reaches that are more sensitive to model adjustments than others? Can we identify critical links of the network?

## Slide 51: Flood Inundation – 2D Hydraulic Modeling Andy Carter
80 TxDOT Radar
Stream Gauges
USGS Gage 08111110
New Year Ck at FM 1155 nr Chappel Hill, TX
30.21231, -96.24295
NBI #172390140504004
Goals:
Create “flood depth raster stacks” from HEC-RAS 2D models in compliance with FDST (Flood Decision Support Toolbox) criteria for each gauge location.
  Main stem (1 mile +/- upstream and downstream)
Create rating curve from 2D model and composite / compare with USGS ADCP data.
From raster stacks, determine limits of flooded roads.

## Slide 52: Flood Inundation – Rating Curves (USGS ADCP Integration)
USGS Gage 08111110
New Year Ck at FM 1155 nr Chappel Hill, TX
30.21231, -96.24295
NBI #172390140504004

## Slide 53: Flood Inundation – 2D Hydraulic Modeling
Bridge Modeling from Plans
In 2D grid mesh

## Slide 54: Flood Inundation – “Healing” Terrain with Bridges
Model on hydro-enforced
and map on “healed” terrain

## Slide 55: Flood Decision Support Toolbox (FDST) Compliant Products
A Flood Inundation Map Library
and set of Rating Curves
Draft 2D – FDST Guidance
Source: Jonathan Thomas (USGS)
Guadalupe River at Comfort, Tx

## Slide 56: Estimated Road Flooding Tim Whiteaker
Inputs:
Road network

## Slide 57: Estimated Road Flooding
Inputs:
Road network
Flooded area

## Slide 58: Estimated Road Flooding
Inputs:
Road network
Flooded area
Outputs:
Flooded road extent

## Slide 59: Estimated Road Flooding
Inputs:
Road network
Flooded area
Outputs:
Flooded road extent
Flooded road depth

## Slide 60: Task 6: Flood Emergency Response and Flood Manual
Achievements during last Quarter
Completion of Beaumont Flood Emergency Response Exercise
Harry Evans
Challenges for next Quarter
Improvement plan arising from Beaumont exercise
    Report P6A due 31 March
Preparation for Austin exercise (September 2022)
Harry Evans
Christine Thies
Larry Jantzen
Flood Emergency Response Team

## Slide 61: Discussion
Comments from all Committee members are encouraged
Questions for Discussion:
Does TxDOT want to participate in the Flood Decision Support Toolbox?
What survey measurements are needed at TxDOT bridges to support flood warning?
How to connect flow measurements and hydraulic modeling at gauged bridges?
How to connect inundation mapping done around bridges with regional scale inundation mapping?
How to define “bankfull flow”?
How to describe uncertainty in forecast information on the flood maps?
….