## Slide 1: Texas FLOG/FIM Subcommittee, Friday 27 Jan 2023
Summary of completion of FIM3 processing on 3m DEM for Texas (Yan Liu – ORNL)
FAST– Flood Assessment System for TxDOT and its roads and bridges representation (David Maidment – CWE)
Approaches to filling in 16,500 bridges in proposed NWC FIM4 coverage of Texas (Andy Carter – CWE)
Discussion
Agenda

## Slide 2: Computing 3-Meter HAND for the State of Texas
Yan Liu
Computational Scientist
Computational Sciences & Engineering Division
Oak Ridge National Laboratory
January 27, 2023

## Slide 3: Pin2Flood Data Production Workflow
Fathom 3m DEM
Full coverage of Texas
Projection: EPSG:4326
Size: 321GB
93 tiles, 176.36 billion raster cells
Application Environment
HUC8 hydrofabric
209 HUC8 units
Projection: EPSG:5070
For each HUC8:
  DEM: Fathom 3m
  NWM hydrofabric: NOAA NWC FIM3
3m HAND
Healed HAND raster
Stream network:
  287,535 streams
  ~1.5km/stream
Synthetic rating curve
Other byproducts
Size: 1.8TB
  Full package: 1.5TB
  Production package: 284GB
Watershed-based decomposition
NOAA NWC FIM3 workflow (full resolution mode)
ESRI flood slicing
App

## Slide 4: FIM3 Terrain Processing, Catchment and Stream Network Development for Texas
209 HUC8 units processed by Yan Liu at Oak Ridge National Laboratory in 4.28 days
This enables flood inundation map layers produced for the TxDOT Austin District
to be replicated across Texas when connected to forecasting from the
National Water Model
Supports Pin2Flood inundation map library development being done for TDEM
13 HUC8 units
processed for
Austin exercise

## Slide 5: Processing Bare-EarthDEM
Fathom 3m DEM for Texas (TWDB)
DEM-derived streams for Texas (TDEM)
(best elevation-derived stream hydrography that we have ever had)

## Slide 6: Texas FIM3 Results are Publicly Accessible
Results by HUC6 Units
Results by HUC8 Units
Metadata and Data
https://web.corral.tacc.utexas.edu/nfiedata/pin2flood/texas/

## Slide 7: Flood Response with Maps at the State Operations Center
West Gulf River
Forecast Center
Predictive Flood
Mapping
Observational
Flood Mapping
State Operations Center
State Operations Center
Local EOC
First responders in field
A common dataset for
predictive and
observational mapping

## Slide 8: FAST: Flood Assessment System for TxDOT
Asset Inventory
Precipitation
Flood Inundation
Streamflow Measurement
Bridge Warnings
Flooded Roads

## Slide 9: How to Move Forward: Two Challenges
How do we deal with lack of bridges in FIM
derived from bare-earth elevation models?
Real-time flood inundation
map services in 20 TxDOT Districts,
October 2023
Develop a quick solution based on tools
and data we have now
How can we improve FAST for the Austin District?
Develop a comprehensive solution starting with
“get the roads and bridges right first”

## Slide 10: RM 620 over Colorado River at Mansfield Dam
West bound RM 620 is where East bound RM 620 should be
East bound RM 620 is in the Colorado River in TxDOT Roadway Inventory

## Slide 11: Roads in the TxDOT Austin District
4400 miles On-System
18,000 miles TxDOT Roadway Inventory
Purchased by TxDOT RTI to support
our Streamflow II research project
Flood Emergency Response Exercise, Jan 2023
38,000 miles Ecopia road coverage
1600 miles of TxDOT Roadway Inventory
are not located on pavement as defined by
Ecopia roads coverage

## Slide 12: RM 620 over Colorado River at Mansfield Dam
Ecopia Road and Centerlines
LIDAR point cloud for bridge deck elevation
129,649 (x,y,z) points
on bridge
Road polygons and centerlines are correctly positioned in (x,y) and have correct elevation (z)

## Slide 13: Data Inputs for Road and Bridge Representation
Aerial Imagery (licensed from TNRIS)
Terrain from TWDB and Reaches from Pin2Flood (TDEM)

## Slide 14: Representation of East Slaughter Lane at Onion Creek
Ecopia Roads and Bridges (2D)
(interpreted by AI from TNRIS imagery)
LIDAR point cloud of bridge (3D)
(from TNRIS LIDAR data stored at TACC)

## Slide 15: Adding Attributes to a Geometrically Strong Roads and Bridges Dataset
AssetWise for Bridges
TxDOT Roadway Inventory for Roads

## Slide 16: How to Move Forward: Two Challenges
How do we deal with lack of bridges in FIM
derived from bare-earth elevation models?
Real-time flood inundation
map services in 20 TxDOT Districts,
October 2023
Develop a quick solution based on tools
and data we have now
How can we improve FAST for the Austin District?
Develop a comprehensive solution starting with
“get the roads and bridges right first”

## Slide 17: A Challenge: Real-Time Flood Inundation Mapping in October 2023
Inundation of a major highway
Source: Derek Giardino, National Weather Service
Coverage of NWS Flood Inundation Mapping
How can we use insights from FAST to include
the 16,500 bridges over water in these Districts?

## Slide 18: Getting the bridges back in National Weather Service’s real-time flood mapping products
GOAL: Create georeferenced bridge deck DEM’s from LiDAR point clouds to ‘correct’ the NWS‘ “relative elevation model” (REM) used in real-time flood mapping.
Crowd sourced bridge lines
National Bridge Inventory (NBI)
governmental dataset of points
Artificial intelligence polygons
extracted from 2D imagery
Classified LiDAR point clouds
Sources of Bridge locations
Linearly referenced bridge lines

## Slide 19: Creating bridge deck DEM’s
Method #1
Provided points, lines and polygons of expected bridge locations, examine the point clouds only at these locations.
Method #2
From cloud optimized point clouds (COPC), search the entire domain for classified bridges.
GOAL: Create georeferenced bridge deck DEM’s from LiDAR point clouds to ‘correct’ the NWS‘ “relative elevation model” (REM) used in real-time flood mapping.

## Slide 20: Bridge DEM from bulk LiDAR processing
Road pavement polygons
extracted from 2D imagery
Terrain DEM from point clouds
No infill of missing data
No “bridge” classifications used
Terrain DEM from points clouds
Infill of missing data
Use “bridge” classifications
Comparing ground w/o bridges
to ground w/ bridges
(assuming infill of both)
Detect differences
(Likely bridges with large clustering)