## Slide 1
David R. Maidment
Center for Water and Environment University of Texas at Austin
Prepared for presentation at Wharton County Commissioners Court, 13 June 2018
Acknowledgements: National Weather Service, Texas Division of Emergency Management,
Wharton County, USGS, Kisters, ESRI, FishView, Xing Zheng, David Arctur, Harry Evans.
Flood Inundation Mapping for Colorado, Wharton and Matagorda Counties

## Slide 2: Flood Inundation Mapping for Colorado, Wharton and Matagorda Counties
Three questions:
What has been done?
What needs to be done?
  Enhanced inundation mapping
  Flood impact assessment
  Densified Water Measurement
How much will it cost per county?

## Slide 3: Flood Inundation Mapping for Colorado, Wharton and Matagorda Counties
Three questions:
What has been done?
What needs to be done?
  Enhanced inundation mapping
  Flood impact assessment
  Densified Water Measurement
How much will it cost per county?

## Slide 4
Continuously forecasts flows over continental US

## Slide 5: Current Flood Inundation Maps in Texas
Colorado River
at Columbus
Maps at forecast points

## Slide 6
Minor Flooding (Stage Height 34 ft)
Moderate Flooding (Stage Height 39 ft)
Major Flooding (Stage Height 43 ft)
Highest Flooding (Stage Height 46.5 ft)

## Slide 7: Rating Curve: Relates Depth to Discharge
Streamflow
Measurement
Stream Depth
Forecasting
Stream
Depth
(ft)
Discharge (cubic feet per second)

## Slide 8: Method for Determining Flood Risk: Height Above Nearest Drainage (HAND)
HAND
Flood
Normal
Flooding occurs when Water Depth is greater than HAND
Address Point
Computed for continental US
Notes: How do we answer the question of how many people are going to be impacted, especially if large areas of the state are not covered by LIDAR or National Flood Hazard Layer? The researchers developed a process called Height Above Nearest Drainage or HAND.

## Slide 9: Modeled Rating Curves from HAND Data
Chart: Rating Curve for Eanes Creek, ComID = 5781289
| 0 | 607.56406134719555 | 2490.8796015163871 | 5785.1592347077603 | 10565.65567829302 | 16808.943658196451 | 24277.138771673799
Stage Height, h (ft) | 0 | 2.0669 | 3.937 | 5.807 | 7.6443 | 9.4159 | 10.9907
Chart: Rating Curve for Eanes Creek, ComID = 5781289
| 0 | 607.56406134719555 | 2490.8796015163871 | 5785.1592347077603 | 10565.65567829302 | 16808.943658196451 | 24277.138771673799
Stage Height, h (ft) | 0 | 2.0669 | 3.937 | 5.807 | 7.6443 | 9.4159 | 10.9907
Forecast Discharge
from National Water Model
Stream Depth (ft)
2.7 million stream reaches in continental US

## Slide 10: USGS Peak Stage Points from Harvey
152 peak stage points
used to calibrate
Manning roughness for
flood inundation mapping
Images: Kristine Blickenstaff, USGS

## Slide 11: Texas Address Points Use for Flood Impact Assessment
9.28 million points
Point on every building
for dispatching emergency
response vehicles by
911 systems
Notes: Over the summer we collected all 8.7million address points across Texas. Dr. David Arctur has assembled all the data and done some quality checks. When you have this much data from hundreds of sources, there are always some inconsistencies. However, in my opinion, for public safety this strategic snapshot is a good starting point for describing overall impact to a region or district.

## Slide 12: Flood Inundation and Impact
Discharge
Depth
Inundation
Impact
Transform discharge to depth by rating curve
or hydraulic model
Create flood inundation map from water depth
Assess impact on people and property
Take discharge forecast from the National Water Model
Flood emergency response depends on assessment of impact

## Slide 13: Inundation Map Produced After Harvey for Governor’s Office
Observations from the U.S. Geological Survey
Forecasting by NWS West Gulf River Forecast Center
Inundation Mapping by USACE, National Water Center and UT Austin
Map Synthesis by Texas Division of Emergency Management

## Slide 14: Goal: Real-Time Flood Inundation Mapping for Texas at Local Scale

## Slide 15: Flood Inundation Mapping for Colorado, Wharton and Matagorda Counties
Three questions:
What has been done?
What needs to be done?
  Enhanced inundation mapping
  Flood impact assessment
  Densified Water Measurement
How much will it cost per county?

## Slide 16: Lidar Data Collection in Texas
Available now
Collected in 2017
Available in 2018
Collected in 2018
Available in 2019
Colorado
Wharton
Matagorda
Counties
Colorado River
(154 miles)
2/3 of Texas is getting new LIDAR data over the period, 2017-2019!

## Slide 17: LIDAR Data in Three Counties
Flight Year
Collected in 2018
Available in 2019
Available now
Use northern Colorado County as a testbed

## Slide 18
An area of Columbus, Tx
(in Colorado County)
Colorado River
Fannin St

## Slide 19
National Elevation Dataset (10m cells)
used for existing flood inundation mapping

## Slide 20
New LIDAR data (1m cells)
Makes much better inundation maps

## Slide 21
New LIDAR data is 100 times denser
1 cell
10m x 10m
100 cells
1m x 1m
National Elevation
Dataset
New LIDAR for
Columbus
LIDAR is critical for accurate terrain description

## Slide 22: Surface Profile using LIDAR
Where is the
channel bed?
Water Surface
This LIDAR cannot see under water
We need a survey of Colorado river bathymetry

## Slide 23: Detailed Bathymetry Data Collected using Boats
Survey using sonar and couple with surface imagery

## Slide 24: HEC River Analysis System
1-D and 2-D Steady and
Unsteady Flow Analysis
Inundation Mapping
Apply at critical overflow locations on main rivers

## Slide 25: Flood Inundation Mapping for Colorado, Wharton and Matagorda Counties
Three questions:
What has been done?
What needs to be done?
  Enhanced inundation mapping
  Flood impact assessment
  Densified Water Measurement
How much will it cost per county?

## Slide 26: Flood Operational Maps
Flood depth in houses
3ft
6” – 3 ft
< 6”
Potentially flooded
neighborhoods

## Slide 27: Common Operating Picture for each County
Travis
Wharton
Identify neighborhoods at risk from flooding
using FEMA flood maps and interaction
with county Emergency Management Coordinator
Summarize information for
urban counties
Prepare information for
rural counties
… Buildings

## Slide 28
Wharton County Map
under glass:
Used for incident location, road closures, field notes…

## Slide 30: Strategic Flood Base Map for Wharton County

## Slide 31: Pin to Flood Map Application (for first responders)
Rock on road at current water level
Point location sent in by text
Inundation map
Chief Todd Pomroy, Austin Fire Department
Local Impact in this area

## Slide 32: Flood Inundation Mapping for Colorado, Wharton and Matagorda Counties
Three questions:
What has been done?
What needs to be done?
  Enhanced inundation mapping
  Flood impact assessment
  Densified Water Measurement
How much will it cost?

## Slide 33: Current and Forthcoming River Forecast Systems
Current
7 forecast points
3 inundation maps covering 35 river miles
Updated 6-hourly
Forthcoming
Forecasting and inundation mapping
covering 3274 river miles
Short-term forecast updated hourly
Medium-term forecast updated 6-hourly
Densified Forecasting Requires Densified Measurement

## Slide 34: Three Tier Water Measurement Plan
Tier 1: Gold Standard USGS Gages
– measure everything
Tier 2: Radar Sensors on Bridges (TxDOT)
– medium and high flows
Tier 3: Water Level Sensors
– low water crossings
Cost

## Slide 35: 27,000 Texas bridges on 15,700 stream reaches forecast by the National Water Model
Flood forecasting system
for Texas Bridges

## Slide 36: Radar Measurement Technologies
Densified forecasting requires densified measurement
Measures water level
Measures surface velocity

## Slide 37: Radar Measurement of Discharge
Combine with Acoustic Doppler Current Profiler
velocity profile
to get discharge
Measure velocity at one
point on water surface

## Slide 38: Radar Streamflow Measurement on I-10
20 Sensors from San Antonio
to LA border

## Slide 39: Real-Time Water Level Measurement in Hays County

## Slide 40: Flood Inundation Mapping for Colorado, Wharton and Matagorda Counties
Three questions:
What has been done?
What needs to be done?
  Enhanced inundation mapping
  Flood impact assessment
  Densified Water Measurement
How much will it cost per county?
Low 6-figures
High 6-figures
to low 7 figures