## Slide 1
Dr. David Maidment, Harry Evans, Dr. David Arctur, University of Texas at Austin
Center for Water and the Environment (CWE)
Presentation to TDEM, 3 August 2017
Acknowledgments: Texas Division of Emergency Management, City of Austin, Austin Fire Dept,
National Weather Service, West Gulf River Forecast Center, University of Texas at Austin
National Water Model
Texas Flood Response System:
Incorporating Predictions and Observations for Inundation Mapping

## Slide 2: Texas Flood Response System August 3rd Briefing
0900 – Opening and Introductions – Mike Ouimet
0905 – Review of Project status and directions – David Maidment
0910 – Ed Clark, Director National Water Center
0920 – WGRFC
0930 – Real-time Flood App “Point to Flood”
0945 – Best Available Flood Inundation Mapping for Texas
0955 – Questions/Comments
1000 – Discussion on Workflow NWS & TDEM CIS
1030 – Close Out

## Slide 3: Texas Flood Response System
May 2014
May 2015
May 2016
May 2017
May 2018
May 2019
Discharge
Inundation
Impact
Services
Deployment
Research and Development
Demonstration

## Slide 4: Recent Accomplishments
9.1 million Address Points statewide collected for impact assessment
TNRIS adoption of the Address Point Database
Process Review during 2017 Summer Institute at the NWC
Flood inundation mapping services from the NWC (in process)
Real-Time Point to Flood Map app created
Agency Collaboration – Over 40 different stakeholders
    6 Federal agencies / 8 State agencies / 10 Texas Counties / 12 Fire Departments / 5 City agencies … and others
TxDOT gage/sensor network (pending)
DHS Flood Apex Program – Texas Flood Response Testbed (pending)

## Slide 5: Three Themes for this Meeting:
Predictive flood mapping from the National Water Center
  Collaboration with WGRFC and TDEM
  What maps are needed?
  How will they be delivered?
Observational flood mapping at TDEM
  Point to Flood Map application
  Testing with first responders
  Building the mapping infrastructure at TDEM
Best available flood inundation maps for Texas
  Use engineering scale models where available, HAND elsewhere
  River Hydraulic Framework for combining maps from different sources

## Slide 6: Three Themes for this Meeting:
Predictive flood mapping from the National Water Center
  Collaboration with WGRFC and TDEM
  What maps are needed?
  How will they be delivered?
Observational flood mapping at TDEM
  Point to Flood Map application
  Testing with first responders
  Building the mapping infrastructure at TDEM
Best available flood inundation maps for Texas
  Use engineering scale models where available, HAND elsewhere
  River Hydraulic Framework for combining maps from different sources
Ed Clark leads discussion

## Slide 7: Three Themes for this Meeting:
Predictive flood mapping from the National Water Center
  Collaboration with WGRFC and TDEM
  What maps are needed?
  How will they be delivered?
Observational flood mapping at TDEM
  Point to Flood Map application
  Testing with first responders
  Building the mapping infrastructure at TDEM
Best available flood inundation maps for Texas
  Use engineering scale models where available, HAND elsewhere
  River Hydraulic Framework for combining maps from different sources

## Slide 8: First Responder Input to Inundation Mapping
Rock on road at current water level
Point location sent in by text
Inundation map
Chief Todd Pomroy, Austin Fire Department
Local Impact in this area

## Slide 9
Prepared for TFRS Status Briefing, Aug 3, 2017
Harry Evans, David Arctur, University of Texas at Austin
Jeanette Chamorro, TDEM Critical Information Systems
Acknowledgements:
David Maidment, Xing Zheng, University of Texas at Austin; Michael Ouimet, TDEM; Austin Fire Dept.
Texas Flood Response System:
Incorporating Observations for Real-Time Inundation Mapping

## Slide 10
Run mobile app on a phone or tablet in the field

## Slide 11
Map the mobile app photo & coordinates at TDEM CIS

## Slide 12
July 25 Testing
July 28 Testing
Test areas in Onion Creek Basin

## Slide 13
July 25 Testing: Topo basemap

## Slide 14
14 – Onion Creek’s edge
Pin – (lat,long) – potential addrs impacted
14 – (30.170799, -97.742204) – 0 addrs

## Slide 15
Pin – (lat,long) – potential addrs impacted
18 – (30.172203, -97.743922) – 38 addrs
18 – Vine Hill Dr near creek

## Slide 16
Pin – (lat,long) – potential addrs impacted
19 – (30.177183, -97.747903) – 79 addrs
19 – Onion Cr Dr & Pleasant Valley Rd

## Slide 17
Pin – (lat,long) – potential addrs impacted
17 – (30.173456, -97.747538) – 196 addrs
17 – Vine Hill Dr at Thatch Ln

## Slide 18
Pin – (lat,long) – potential addrs impacted
15 – (30.169338, -97.740908) – 677 addrs
15 – 6114 Orleans Dr

## Slide 19
20 – 7313 S Pleasant Valley Rd
Pin – (lat,long) – potential addrs impacted
20 – (30.17156, -97.752547) – 959 addrs

## Slide 20
Pin – (lat,long) – potential addrs impacted
20 – (30.17156, -97.752547) – 959 addrs
16 – (30.166610, -97.740116) – 202 addrs
16 – Orange Blossom Way at Green Grass Trail

## Slide 21
Comparison with FEMA National Flood Hazard Layer

## Slide 22
Comparison with AFD Operational Map

## Slide 23
July 25 Testing
July 28 Testing
Test Areas in Onion Creek Basin

## Slide 24
Pin – (lat,long) – potential addrs impacted
23 – (30.131581, -97.784074) – 53 addrs
27 – (30.141330, -97.779103) – 30 addrs
23 – Pinehurst Dr & Champions Ln
27 – Port Rush Ct

## Slide 25
Pin – (lat,long) – potential addrs impacted
24 – (30.133381, -97.785252) – 132 addrs
26 – (30.141835, -97.780748) – 45 addrs
24 – Merion Cricket Ct
26 – River Plantation at Interlachen

## Slide 26
Pin – (lat,long) – potential addrs impacted
25 – (30.134856, -97.786274) – 166 addrs
26 – (30.141835, -97.780748) – 45 addrs
25 – 4621 Pinehurst Dr S
26 – River Plantation at Interlachen

## Slide 27
Comparison with FEMA National Flood Hazard Layer

## Slide 28
Comparison with AFD Operational Map

## Slide 29
Live Demonstration:
Collecting Observations for Real-Time Inundation Mapping

## Slide 30
This testing was done in areas well understood, engineered and mapped
Some flood test mapping was over/under actual flooded extent due to differences in resolution between 10m NED and 30m NHDPlus
Flood test mapping from HAND calculation was bounded by NHD medium resolution catchments; this fragmented the result
Future stream reach delineation will use 10m (or better) catchments and river geometry, and will consider longer reaches than NHD, for greater usefulness in emergency response
Pin to Flood Summary

## Slide 31: Three Themes for this Meeting:
Predictive flood mapping from the National Water Center
  Collaboration with WGRFC and TDEM
  What maps are needed?
  How will they be delivered?
Observational flood mapping at TDEM
  Point to Flood Map application
  Testing with first responders
  Building the mapping infrastructure at TDEM
Best available flood inundation maps for Texas
  Use engineering scale models where available, HAND elsewhere
  River Hydraulic Framework for combining maps from different sources

## Slide 32: Existing Flood Maps from National Weather Service
http://water.weather.gov/ahps2/inundation/inundation_google.php?gage=atit2

## Slide 33: Continental-Scale Flood Inundation Mapping
Catchments and Flowlines
Digital Elevation Model
Height Above Nearest
Drainage (HAND) (relative elevation of land
surface cell above cell in
stream to which it flows)

## Slide 34: Detailed Flood Models of Main Stem Rivers
San Antonio River (from San Antonio River Authority)
Guadalupe River (from US Army Corps of Engineers,
Fort Worth District)

## Slide 35: Flood Models from FEMA Flood Mapping Studies
Harris County
Notes: Of the 254 counties in Texas about 120 have the FEMA Flood Hazard Layer. The National Flood Hazard Layer (NFHL) dataset represents the current effective flood data for the country, where maps have been modernized. The default base map is from a USGS service and conforms to FEMA's specification for horizontal accuracy. This is used by homeowners, engineers, architects, surveyors, insurance professionals, lenders, floodplain managers.

## Slide 36: Best Available Flood Inundation Mapping
National River Hydraulic Framework for Flood Inundation Mapping
Use mapping from
engineering scale models
where available,
HAND elsewhere
190,000 miles of
streams and rivers
in Texas

## Slide 37: Uncertainty Assessment Uncertainty in discharge – uncertainty in depth – uncertainty in inundation – uncertainty in impact (Monte Carlo simulation derived from USACE risk assessment procedure)
Impact
Inundation
Depth
Discharge
Flooded
Structures
Uncertainty in discharge
Rating curve
Discharge
Time
Discharge
Depth
Uncertainty in impact

## Slide 38: Three Themes for this Meeting:
Predictive flood mapping from the National Water Center
  Collaboration with WGRFC and TDEM
  What maps are needed?
  How will they be delivered?
Observational flood mapping at TDEM
  Point to Flood Map application
  Testing with first responders
  Building the mapping infrastructure at TDEM
Best available flood inundation maps for Texas
  Use engineering scale models where available, HAND elsewhere
  River Hydraulic Framework for combining maps from different sources